|  | University of Southampton · Department of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	s92

Empirical formula 	c19h26brn

Formula weight 	348.32

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	P21

Unit cell dimensions	a = 5.1549(2) Å	( = 90°

b = 31.1802(12) Å	( = 90.609(2)°

c = 5.4853(3) Å	(  = 90°

Volume	881.61(7) Å3

Z	2

Density (calculated)	1.312 Mg / m3

Absorption coefficient	2.326 mm(1

F(000)	364

Crystal	Block; Colourless

Crystal size	0.15 ( 0.10 ( 0.05 mm3

( range for data collection	3.71 ( 25.02°

Index ranges	(6 ( h ( 5, (26 ( k ( 37, (6 ( l ( 6

Reflections collected	3342

Independent reflections	2043 [Rint = 0.0390]

Completeness to ( = 25.02°	87.5 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.8926 and 0.7217

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	2043 / 1 / 190

Goodness-of-fit on F2	1.063

Final R indices [F2 > 2((F2)]	R1 = 0.0389, wR2 = 0.0883

R indices (all data)	R1 = 0.0425, wR2 = 0.0900

Absolute structure parameter	0.006(16)

Largest diff. peak and hole	0.678 and (0.574 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SORTAV (R. H. Blessing, Acta Cryst. A51 (1995) 33(37; R. H. Blessing, J. Appl. Cryst. 30 (1997) 421(426). Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: Cameron - A Molecular Graphics Package. (D. M. Watkin, L. Pearce and C. K. Prout, Chemical Crystallography Laboratory, University of Oxford, 1993).

Special details:

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

Br1	205(1)	7216(1)	2280(1)	27(1)	1

N1	(3289(8)	7291(2)	7214(6)	16(1)	1

C8	(4854(12)	6888(3)	7298(12)	23(2)	1

C7	(4882(13)	7687(3)	7266(12)	25(2)	1

C16	(15082(11)	4715(2)	12915(9)	21(1)	1

C10	(4876(11)	6089(2)	7250(9)	23(1)	1

C13	(9765(11)	5507(2)	11393(9)	21(1)	1

C9	(3210(14)	6494(2)	7335(12)	24(2)	1

C4	(73(13)	8797(2)	6082(10)	26(2)	1

C12	(8080(11)	5599(2)	9191(9)	20(1)	1

C19	(11519(11)	4839(2)	9286(9)	20(1)	1

C11	(6510(11)	6003(2)	9457(9)	20(1)	1

C1	(3211(13)	8081(2)	6835(11)	20(2)	1

C17	(15028(12)	4430(2)	10981(9)	23(1)	1

C14	(11554(10)	5122(2)	11208(9)	18(1)	1

C2	(1251(11)	8197(2)	8530(9)	22(1)	1

C15	(13359(11)	5051(2)	13039(9)	20(1)	1

C5	(1975(13)	8691(2)	4418(10)	28(2)	1

C18	(13244(12)	4501(2)	9155(9)	22(1)	1

C3	284(12)	8546(2)	8127(10)	25(2)	1

C6	(3529(12)	8339(2)	4786(9)	24(2)	1

Table 3. Bond lengths [Å] and angles [°].

N1(C7	1.484(11)

N1(C8	1.493(11)

C8(C9	1.494(12)

C7(C1	1.520(12)

C16(C15	1.376(8)

C16(C17	1.384(8)

C10(C11	1.506(7)

C10(C9	1.527(10)

C13(C14	1.517(8)

C13(C12	1.522(7)

C4(C5	1.373(9)

C4(C3	1.378(8)

C12(C11	1.504(8)

C19(C14	1.375(8)

C19(C18	1.381(8)

C1(C6	1.390(9)

C1(C2	1.413(9)

C17(C18	1.385(8)

C14(C15	1.393(7)

C2(C3	1.366(9)

C5(C6	1.376(9)

C7(N1(C8	113.6(5)

C9(C8(N1	112.7(6)

N1(C7(C1	110.8(6)

C15(C16(C17	120.6(5)

C11(C10(C9	116.2(5)

C14(C13(C12	116.6(4)

C8(C9(C10	111.2(6)

C5(C4(C3	119.6(6)

C11(C12(C13	113.0(4)

C14(C19(C18	121.1(5)

C12(C11(C10	112.1(5)

C6(C1(C2	117.5(6)

C6(C1(C7	122.1(6)

C2(C1(C7	120.4(6)

C16(C17(C18	118.1(6)

C19(C14(C15	117.8(5)

C19(C14(C13	123.1(5)

C15(C14(C13	119.1(5)

C3(C2(C1	120.6(5)

C16(C15(C14	121.4(5)

C4(C5(C6	120.4(5)

C19(C18(C17	121.1(5)

C2(C3(C4	120.8(6)

C5(C6(C1	121.1(6)

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

Br1	26(1) 	40(1)	14(1) 	1(1)	1(1) 	3(1)

N1	14(2) 	25(4)	9(2) 	(1(2)	1(1) 	(2(3)

C8	12(4) 	37(6)	21(3) 	3(3)	1(3) 	(4(3)

C7	27(5) 	29(6)	20(3) 	(4(3)	(1(3) 	8(3)

C16	24(4) 	22(4)	19(3) 	9(2)	5(2) 	5(3)

C10	26(4) 	17(4)	25(3) 	(5(2)	2(2) 	2(3)

C13	21(3) 	19(4)	22(3) 	(3(2)	(1(2) 	3(3)

C9	17(4) 	32(5)	23(3) 	(3(3)	2(3) 	(1(3)

C4	35(4) 	15(4)	28(3) 	1(3)	12(3) 	1(3)

C12	22(3) 	19(4)	19(3) 	2(2)	(4(2) 	2(3)

C19	19(3) 	25(4)	17(3) 	1(2)	5(2) 	2(3)

C11	17(3) 	23(4)	19(3) 	(3(2)	(5(2) 	3(3)

C1	16(4) 	25(5)	21(3) 	(3(3)	4(2) 	(1(3)

C17	21(3) 	23(4)	23(3) 	4(2)	(1(2) 	0(3)

C14	17(3) 	21(4)	16(2) 	4(2)	(8(2) 	(1(3)

C2	27(4) 	20(4)	19(3) 	4(2)	1(2) 	2(3)

C15	20(3) 	25(4)	16(2) 	(6(2)	(1(2) 	1(3)

C5	38(4) 	25(4)	20(3) 	9(3)	10(3) 	4(3)

C18	29(4) 	21(4)	15(3) 	0(2)	0(2) 	(1(3)

C3	26(4) 	26(4)	23(3) 	(5(3)	(3(2) 	3(3)

C6	25(3) 	30(4)	16(3) 	1(3)	(1(2) 	3(3)