|  | University of Southampton · School of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	2005src1222 / MIA69

Empirical formula 	C28H38N4O8S2

Formula weight 	622.74

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Triclinic

Space group 	P(1

Unit cell dimensions	a = 7.6356(3) Å	( = 102.333(2)°

b = 9.1896(4) Å	( = 105.058(3)°

c = 12.3286(5) Å	(  = 108.494(2)°

Volume	749.71(5) Å3

Z	1

Density (calculated)	1.379 Mg / m3

Absorption coefficient	0.233 mm(1

F(000)	330

Crystal	Cut Plate; Colourless

Crystal size	0.18 ( 0.12 ( 0.04 mm3

( range for data collection	3.40 ( 27.48°

Index ranges	(9 ( h ( 9, (11 ( k ( 11, (15 ( l ( 15

Reflections collected	14413

Independent reflections	3402 [Rint = 0.0574]

Completeness to ( = 27.48°	99.6 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9907 and 0.9592

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	3402 / 0 / 191

Goodness-of-fit on F2	1.061

Final R indices [F2 > 2((F2)]	R1 = 0.0441, wR2 = 0.1018

R indices (all data)	R1 = 0.0599, wR2 = 0.1104

Extinction coefficient	0.021(3)

Largest diff. peak and hole	0.299 and (0.379 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SADABS Version 2.10. (G. M. Sheldrick (2003)) Bruker AXS Inc., Madison, Wisconsin, USA. Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: ORTEP3 for Windows (L. J. Farrugia, J. Appl. Crystallogr. 1997, 30, 565).

Special details:

All hydrogen atoms were fixed.

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	2367(3)	9707(2)	9079(2)	24(1)	1

C2	4554(3)	10036(2)	9379(2)	27(1)	1

C3	1083(3)	11322(2)	7838(2)	22(1)	1

C4	2996(3)	12846(2)	8421(2)	28(1)	1

C5	2591(3)	14347(2)	8313(2)	32(1)	1

C6	1051(3)	14514(2)	8853(2)	33(1)	1

C7	(861(3)	12997(2)	8248(2)	29(1)	1

C8	(492(3)	11483(2)	8351(2)	24(1)	1

C9	(2135(3)	7836(2)	6170(2)	21(1)	1

C10	(3508(3)	6927(2)	6575(2)	22(1)	1

C11	(5519(3)	6492(2)	6056(2)	28(1)	1

C12	(6178(3)	7030(3)	5120(2)	32(1)	1

C13	(4849(3)	7959(3)	4716(2)	31(1)	1

C14	(2839(3)	8347(2)	5224(2)	26(1)	1

N1	1447(2)	9845(2)	7914(1)	22(1)	1

N2	(2900(2)	6440(2)	7628(1)	23(1)	1

O1	715(2)	6944(2)	7040(1)	27(1)	1

O2	1121(2)	8754(2)	5817(1)	29(1)	1

O3	(1813(2)	7529(2)	8565(1)	34(1)	1

O4	(3573(2)	5006(2)	7533(1)	37(1)	1

S1	453(1)	8297(1)	6727(1)	22(1)	1

Table 3. Bond lengths [Å] and angles [°].

C1(N1	1.477(2)

C1(C2	1.525(3)

C1(H1A	0.9900

C1(H1B	0.9900

C2(C2i	1.530(4)

C2(H2A	0.9900

C2(H2B	0.9900

C3(N1	1.486(2)

C3(C8	1.528(3)

C3(C4	1.529(3)

C3(H3	1.0000

C4(C5	1.531(3)

C4(H4A	0.9900

C4(H4B	0.9900

C5(C6	1.525(3)

C5(H5A	0.9900

C5(H5B	0.9900

C6(C7	1.527(3)

C6(H6A	0.9900

C6(H6B	0.9900

C7(C8	1.529(3)

C7(H7A	0.9900

C7(H7B	0.9900

C8(H8A	0.9900

C8(H8B	0.9900

C9(C14	1.393(3)

C9(C10	1.393(3)

C9(S1	1.7873(19)

C10(C11	1.385(3)

C10(N2	1.472(2)

C11(C12	1.388(3)

C11(H11	0.9500

C12(C13	1.379(3)

C12(H12	0.9500

C13(C14	1.391(3)

C13(H13	0.9500

C14(H14	0.9500

N1(S1	1.6095(16)

N2(O4	1.220(2)

N2(O3	1.227(2)

O1(S1	1.4342(13)

O2(S1	1.4337(14)

N1(C1(C2	113.35(16)

N1(C1(H1A	108.9

C2(C1(H1A	108.9

N1(C1(H1B	108.9

C2(C1(H1B	108.9

H1A(C1(H1B	107.7

C1(C2(C2i	110.8(2)

C1(C2(H2A	109.5

C2i(C2(H2A	109.5

C1(C2(H2B	109.5

C2i(C2(H2B	109.5

H2A(C2(H2B	108.1

N1(C3(C8	111.76(15)

N1(C3(C4	111.39(15)

C8(C3(C4	111.50(16)

N1(C3(H3	107.3

C8(C3(H3	107.3

C4(C3(H3	107.3

C3(C4(C5	110.47(16)

C3(C4(H4A	109.6

C5(C4(H4A	109.6

C3(C4(H4B	109.6

C5(C4(H4B	109.6

H4A(C4(H4B	108.1

C6(C5(C4	111.00(17)

C6(C5(H5A	109.4

C4(C5(H5A	109.4

C6(C5(H5B	109.4

C4(C5(H5B	109.4

H5A(C5(H5B	108.0

C5(C6(C7	110.22(17)

C5(C6(H6A	109.6

C7(C6(H6A	109.6

C5(C6(H6B	109.6

C7(C6(H6B	109.6

H6A(C6(H6B	108.1

C6(C7(C8	110.89(16)

C6(C7(H7A	109.5

C8(C7(H7A	109.5

C6(C7(H7B	109.5

C8(C7(H7B	109.5

H7A(C7(H7B	108.0

C3(C8(C7	110.83(16)

C3(C8(H8A	109.5

C7(C8(H8A	109.5

C3(C8(H8B	109.5

C7(C8(H8B	109.5

H8A(C8(H8B	108.1

C14(C9(C10	117.74(17)

C14(C9(S1	117.65(14)

C10(C9(S1	124.53(14)

C11(C10(C9	122.54(18)

C11(C10(N2	115.58(17)

C9(C10(N2	121.80(16)

C10(C11(C12	118.46(19)

C10(C11(H11	120.8

C12(C11(H11	120.8

C13(C12(C11	120.29(19)

C13(C12(H12	119.9

C11(C12(H12	119.9

C12(C13(C14	120.62(19)

C12(C13(H13	119.7

C14(C13(H13	119.7

C13(C14(C9	120.32(18)

C13(C14(H14	119.8

C9(C14(H14	119.8

C1(N1(C3	120.52(15)

C1(N1(S1	120.90(12)

C3(N1(S1	117.63(12)

O4(N2(O3	124.19(16)

O4(N2(C10	118.70(16)

O3(N2(C10	117.00(15)

O2(S1(O1	119.22(8)

O2(S1(N1	109.00(8)

O1(S1(N1	108.27(8)

O2(S1(C9	103.73(9)

O1(S1(C9	108.15(8)

N1(S1(C9	107.95(8)

Symmetry transformations used to generate equivalent atoms:

(i) (x+1,(y+2,(z+2

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	23(1) 	25(1)	24(1) 	11(1)	4(1) 	11(1)

C2	22(1) 	31(1)	28(1) 	13(1)	6(1) 	12(1)

C3	24(1) 	19(1)	22(1) 	9(1)	4(1) 	10(1)

C4	26(1) 	22(1)	33(1) 	10(1)	9(1) 	8(1)

C5	37(1) 	22(1)	37(1) 	12(1)	11(1) 	9(1)

C6	42(1) 	24(1)	36(1) 	11(1)	12(1) 	18(1)

C7	30(1) 	28(1)	31(1) 	9(1)	7(1) 	16(1)

C8	23(1) 	24(1)	24(1) 	7(1)	5(1) 	10(1)

C9	24(1) 	18(1)	20(1) 	3(1)	6(1) 	9(1)

C10	25(1) 	20(1)	19(1) 	3(1)	6(1) 	11(1)

C11	26(1) 	30(1)	27(1) 	5(1)	8(1) 	12(1)

C12	25(1) 	40(1)	26(1) 	3(1)	2(1) 	17(1)

C13	35(1) 	35(1)	22(1) 	8(1)	3(1) 	19(1)

C14	31(1) 	24(1)	21(1) 	6(1)	6(1) 	9(1)

N1	22(1) 	20(1)	23(1) 	8(1)	2(1) 	9(1)

N2	22(1) 	25(1)	25(1) 	9(1)	9(1) 	10(1)

O1	27(1) 	22(1)	35(1) 	11(1)	11(1) 	13(1)

O2	33(1) 	30(1)	31(1) 	13(1)	18(1) 	15(1)

O3	35(1) 	33(1)	22(1) 	9(1)	4(1) 	6(1)

O4	44(1) 	23(1)	43(1) 	14(1)	13(1) 	12(1)

S1	22(1) 	22(1)	24(1) 	9(1)	9(1) 	11(1)

Table 5. Hydrogen coordinates [( 104] and isotropic displacement parameters [Å2 ( 103].

Atom 	x	y	z	Ueq	S.o.f.

H1A	1658	8601	9083	29	1

H1B	2215	10483	9703	29	1

H2A	5265	11120	9341	32	1

H2B	4713	9220	8787	32	1

H3	566	11204	6977	26	1

H4A	3952	12735	8033	33	1

H4B	3585	12973	9269	33	1

H5A	3832	15327	8724	39	1

H5B	2114	14262	7465	39	1

H6A	788	15474	8755	40	1

H6B	1562	14673	9713	40	1

H7A	(1419	12883	7400	35	1

H7B	(1835	13106	8621	35	1

H8A	(55	11549	9196	29	1

H8B	(1736	10510	7919	29	1

H11	(6426	5841	6333	34	1

H12	(7550	6757	4757	39	1

H13	(5312	8338	4085	37	1

H14	(1942	8963	4923	31	1