|  | University of Southampton · School of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	2005src1385 / IAN3

Empirical formula 	C35H27Br2Cl5FeP2Pd

Formula weight 	1008.83

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Triclinic

Space group 	P(1

Unit cell dimensions	a = 10.6212(3) Å	( = 69.7780(10)°

b = 11.6023(3) Å	( = 81.3780(10)°

c = 16.3071(4) Å	(  = 73.0820(10)°

Volume	1801.33(8) Å3

Z	2

Density (calculated)	1.860 Mg / m3

Absorption coefficient	3.606 mm(1

F(000)	988

Crystal	Cut Slab; Red

Crystal size	0.24 ( 0.20 ( 0.08 mm3

( range for data collection	3.08 ( 27.48°

Index ranges	(13 ( h ( 13, (15 ( k ( 14, (21 ( l ( 20

Reflections collected	34771

Independent reflections	8237 [Rint = 0.0426]

Completeness to ( = 27.48°	99.8 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.7613 and 0.4782

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	8237 / 72 / 452

Goodness-of-fit on F2	1.034

Final R indices [F2 > 2((F2)]	R1 = 0.0398, wR2 = 0.0882

R indices (all data)	R1 = 0.0609, wR2 = 0.0972

Largest diff. peak and hole	1.684 and (1.308 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SADABS Version 2.10. (G. M. Sheldrick (2003)) Bruker AXS Inc., Madison, Wisconsin, USA. Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: ORTEP3 for Windows (L. J. Farrugia, J. Appl. Crystallogr. 1997, 30, 565).

Special details:

All hydrogen atoms were fixed.

There is a molecule of disordered chloroform in the asymmetric unit.

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	3474(4)	834(4)	1740(3)	25(1)	1

C2	4386(4)	827(4)	2313(3)	33(1)	1

C3	5668(4)	680(5)	1894(3)	40(1)	1

C4	5569(4)	601(5)	1065(3)	40(1)	1

C5	4247(4)	698(4)	957(3)	34(1)	1

C6	4100(4)	(2167(4)	2885(3)	30(1)	1

C7	4443(4)	(2369(4)	2053(3)	32(1)	1

C8	5829(4)	(2530(5)	1867(3)	42(1)	1

C9	6357(4)	(2437(5)	2576(4)	44(1)	1

C10	5313(4)	(2226(4)	3211(3)	36(1)	1

C11	1235(4)	1617(4)	746(3)	24(1)	1

C12	1317(4)	766(4)	305(3)	33(1)	1

C13	964(4)	1174(4)	(546(3)	34(1)	1

C14	493(5)	2435(5)	(972(3)	40(1)	1

C15	384(7)	3299(5)	(537(4)	60(2)	1

C16	763(5)	2894(5)	316(3)	45(1)	1

C17	1156(4)	2406(4)	2272(3)	24(1)	1

C18	1855(4)	3337(4)	1988(3)	29(1)	1

C19	1466(5)	4384(4)	2275(3)	38(1)	1

C20	375(5)	4524(5)	2839(3)	44(1)	1

C21	(342(6)	3622(5)	3113(3)	45(1)	1

C22	48(4)	2563(4)	2830(3)	33(1)	1

C23	2453(4)	(3678(4)	3946(3)	24(1)	1

C24	3276(4)	(4635(4)	3638(3)	31(1)	1

C25	3246(5)	(5888(4)	4058(3)	39(1)	1

C26	2437(5)	(6216(4)	4796(3)	38(1)	1

C27	1627(5)	(5281(5)	5110(3)	38(1)	1

C28	1613(4)	(4016(4)	4682(3)	33(1)	1

C29	2525(4)	(1528(4)	4380(3)	27(1)	1

C30	1673(4)	(396(4)	4443(3)	31(1)	1

C31	1685(4)	(3(5)	5157(3)	38(1)	1

C32	2530(4)	(758(5)	5814(3)	43(1)	1

C33	3344(5)	(1903(5)	5769(3)	45(1)	1

C34	3352(4)	(2295(5)	5057(3)	36(1)	1

Fe1	4906(1)	(814(1)	2045(1)	30(1)	1

Br1	4038(1)	1032(1)	3422(1)	37(1)	1

Br2	3290(1)	(2551(1)	1361(1)	38(1)	1

Cl1	(1146(1)	822(1)	1959(1)	26(1)	1

Cl2	(485(1)	(2097(1)	3265(1)	28(1)	1

Pd1	756(1)	(615(1)	2628(1)	19(1)	1

P1	1696(1)	1032(1)	1883(1)	21(1)	1

P2	2475(1)	(2009(1)	3433(1)	22(1)	1

C41	6831(16)	(6190(12)	1217(10)	63(3)	0.684(5)

Cl41	5475(6)	(5977(6)	1896(3)	102(2)	0.684(5)

Cl42	6502(3)	(6443(3)	296(2)	85(1)	0.684(5)

Cl43	7570(3)	(4910(3)	888(3)	98(1)	0.684(5)

C51	6760(20)	(6170(20)	1240(17)	72(7)	0.316(5)

Cl51	6769(10)	(5153(12)	206(6)	175(6)	0.316(5)

Cl52	7423(9)	(5562(8)	1855(8)	139(4)	0.316(5)

Cl53	5212(10)	(6171(13)	1767(10)	104(5)	0.316(5)

Table 3. Bond lengths [Å] and angles [°].

C1(C2	1.440(6)

C1(C5	1.442(6)

C1(P1	1.823(4)

C1(Fe1	2.023(4)

C2(C3	1.420(6)

C2(Br1	1.874(4)

C2(Fe1	2.003(4)

C3(C4	1.408(7)

C3(Fe1	2.045(4)

C3(H3	0.9500

C4(C5	1.409(6)

C4(Fe1	2.066(5)

C4(H4	0.9500

C5(Fe1	2.055(5)

C5(H5	0.9500

C6(C7	1.432(6)

C6(C10	1.440(6)

C6(P2	1.811(4)

C6(Fe1	2.005(4)

C7(C8	1.428(6)

C7(Br2	1.883(4)

C7(Fe1	1.999(4)

C8(C9	1.406(7)

C8(Fe1	2.046(5)

C8(H8	0.9500

C9(C10	1.426(7)

C9(Fe1	2.062(5)

C9(H9	0.9500

C10(Fe1	2.041(5)

C10(H10	0.9500

C11(C16	1.377(6)

C11(C12	1.386(5)

C11(P1	1.829(4)

C12(C13	1.374(6)

C12(H12	0.9500

C13(C14	1.360(7)

C13(H13	0.9500

C14(C15	1.385(7)

C14(H14	0.9500

C15(C16	1.387(7)

C15(H15	0.9500

C16(H16	0.9500

C17(C22	1.384(6)

C17(C18	1.397(5)

C17(P1	1.825(4)

C18(C19	1.382(6)

C18(H18	0.9500

C19(C20	1.374(7)

C19(H19	0.9500

C20(C21	1.383(7)

C20(H20	0.9500

C21(C22	1.390(6)

C21(H21	0.9500

C22(H22	0.9500

C23(C24	1.391(6)

C23(C28	1.396(6)

C23(P2	1.830(4)

C24(C25	1.384(6)

C24(H24	0.9500

C25(C26	1.377(7)

C25(H25	0.9500

C26(C27	1.374(7)

C26(H26	0.9500

C27(C28	1.387(6)

C27(H27	0.9500

C28(H28	0.9500

C29(C30	1.389(6)

C29(C34	1.392(6)

C29(P2	1.825(4)

C30(C31	1.392(6)

C30(H30	0.9500

C31(C32	1.380(7)

C31(H31	0.9500

C32(C33	1.378(7)

C32(H32	0.9500

C33(C34	1.383(6)

C33(H33	0.9500

C34(H34	0.9500

Cl1(Pd1	2.3439(10)

Cl2(Pd1	2.3343(10)

Pd1(P2	2.2816(10)

Pd1(P1	2.2944(10)

C41(Cl41	1.692(17)

C41(Cl42	1.729(13)

C41(Cl43	1.764(18)

C41(H41	1.0000

C51(Cl51	1.69(3)

C51(Cl52	1.72(2)

C51(Cl53	1.74(3)

C51(H51	1.0000

C2(C1(C5	105.7(3)

C2(C1(P1	130.4(3)

C5(C1(P1	123.9(3)

C2(C1(Fe1	68.3(2)

C5(C1(Fe1	70.5(2)

P1(C1(Fe1	127.5(2)

C3(C2(C1	109.1(4)

C3(C2(Br1	122.3(3)

C1(C2(Br1	128.5(3)

C3(C2(Fe1	71.1(3)

C1(C2(Fe1	69.8(2)

Br1(C2(Fe1	127.0(2)

C4(C3(C2	107.5(4)

C4(C3(Fe1	70.7(3)

C2(C3(Fe1	67.9(2)

C4(C3(H3	126.3

C2(C3(H3	126.3

Fe1(C3(H3	126.7

C3(C4(C5	109.1(4)

C3(C4(Fe1	69.2(3)

C5(C4(Fe1	69.6(3)

C3(C4(H4	125.4

C5(C4(H4	125.4

Fe1(C4(H4	127.4

C4(C5(C1	108.6(4)

C4(C5(Fe1	70.4(3)

C1(C5(Fe1	68.1(2)

C4(C5(H5	125.7

C1(C5(H5	125.7

Fe1(C5(H5	127.3

C7(C6(C10	106.2(4)

C7(C6(P2	125.5(3)

C10(C6(P2	128.1(3)

C7(C6(Fe1	68.8(2)

C10(C6(Fe1	70.5(3)

P2(C6(Fe1	129.1(2)

C8(C7(C6	109.0(4)

C8(C7(Br2	125.1(3)

C6(C7(Br2	125.6(3)

C8(C7(Fe1	71.1(3)

C6(C7(Fe1	69.3(2)

Br2(C7(Fe1	130.1(2)

C9(C8(C7	107.8(4)

C9(C8(Fe1	70.6(3)

C7(C8(Fe1	67.6(2)

C9(C8(H8	126.1

C7(C8(H8	126.1

Fe1(C8(H8	127.3

C8(C9(C10	108.5(4)

C8(C9(Fe1	69.4(3)

C10(C9(Fe1	68.8(3)

C8(C9(H9	125.7

C10(C9(H9	125.7

Fe1(C9(H9	127.6

C9(C10(C6	108.4(4)

C9(C10(Fe1	70.5(3)

C6(C10(Fe1	67.8(3)

C9(C10(H10	125.8

C6(C10(H10	125.8

Fe1(C10(H10	127.5

C16(C11(C12	118.3(4)

C16(C11(P1	121.6(3)

C12(C11(P1	120.1(3)

C13(C12(C11	121.5(4)

C13(C12(H12	119.2

C11(C12(H12	119.2

C14(C13(C12	120.3(4)

C14(C13(H13	119.9

C12(C13(H13	119.9

C13(C14(C15	119.0(4)

C13(C14(H14	120.5

C15(C14(H14	120.5

C14(C15(C16	120.9(5)

C14(C15(H15	119.5

C16(C15(H15	119.5

C11(C16(C15	119.9(4)

C11(C16(H16	120.1

C15(C16(H16	120.1

C22(C17(C18	119.0(4)

C22(C17(P1	121.4(3)

C18(C17(P1	119.6(3)

C19(C18(C17	120.6(4)

C19(C18(H18	119.7

C17(C18(H18	119.7

C20(C19(C18	120.1(4)

C20(C19(H19	120.0

C18(C19(H19	120.0

C19(C20(C21	120.0(4)

C19(C20(H20	120.0

C21(C20(H20	120.0

C20(C21(C22	120.2(5)

C20(C21(H21	119.9

C22(C21(H21	119.9

C17(C22(C21	120.1(4)

C17(C22(H22	120.0

C21(C22(H22	120.0

C24(C23(C28	118.5(4)

C24(C23(P2	122.0(3)

C28(C23(P2	119.4(3)

C25(C24(C23	120.0(4)

C25(C24(H24	120.0

C23(C24(H24	120.0

C26(C25(C24	121.1(4)

C26(C25(H25	119.5

C24(C25(H25	119.5

C27(C26(C25	119.4(4)

C27(C26(H26	120.3

C25(C26(H26	120.3

C26(C27(C28	120.3(4)

C26(C27(H27	119.8

C28(C27(H27	119.8

C27(C28(C23	120.6(4)

C27(C28(H28	119.7

C23(C28(H28	119.7

C30(C29(C34	119.2(4)

C30(C29(P2	119.0(3)

C34(C29(P2	121.7(3)

C29(C30(C31	120.5(4)

C29(C30(H30	119.8

C31(C30(H30	119.8

C32(C31(C30	119.7(5)

C32(C31(H31	120.2

C30(C31(H31	120.2

C33(C32(C31	120.0(4)

C33(C32(H32	120.0

C31(C32(H32	120.0

C32(C33(C34	120.7(5)

C32(C33(H33	119.6

C34(C33(H33	119.6

C33(C34(C29	119.8(5)

C33(C34(H34	120.1

C29(C34(H34	120.1

C7(Fe1(C2	149.17(17)

C7(Fe1(C6	41.92(17)

C2(Fe1(C6	114.19(18)

C7(Fe1(C1	116.89(16)

C2(Fe1(C1	41.92(16)

C6(Fe1(C1	107.73(16)

C7(Fe1(C10	69.29(19)

C2(Fe1(C10	106.34(19)

C6(Fe1(C10	41.71(17)

C1(Fe1(C10	130.78(18)

C7(Fe1(C3	169.60(18)

C2(Fe1(C3	41.06(17)

C6(Fe1(C3	146.06(19)

C1(Fe1(C3	69.90(17)

C10(Fe1(C3	113.02(19)

C7(Fe1(C8	41.32(17)

C2(Fe1(C8	167.35(19)

C6(Fe1(C8	70.17(18)

C1(Fe1(C8	149.92(19)

C10(Fe1(C8	68.5(2)

C3(Fe1(C8	129.05(18)

C7(Fe1(C5	111.14(18)

C2(Fe1(C5	68.94(18)

C6(Fe1(C5	133.28(17)

C1(Fe1(C5	41.40(16)

C10(Fe1(C5	171.92(17)

C3(Fe1(C5	68.11(19)

C8(Fe1(C5	117.5(2)

C7(Fe1(C9	68.63(19)

C2(Fe1(C9	128.8(2)

C6(Fe1(C9	69.73(18)

C1(Fe1(C9	169.32(19)

C10(Fe1(C9	40.69(19)

C3(Fe1(C9	106.09(19)

C8(Fe1(C9	40.0(2)

C5(Fe1(C9	147.37(19)

C7(Fe1(C4	132.87(19)

C2(Fe1(C4	68.17(19)

C6(Fe1(C4	172.57(18)

C1(Fe1(C4	68.97(17)

C10(Fe1(C4	145.44(18)

C3(Fe1(C4	40.07(19)

C8(Fe1(C4	109.11(19)

C5(Fe1(C4	40.01(17)

C9(Fe1(C4	114.77(19)

P2(Pd1(P1	99.98(4)

P2(Pd1(Cl2	88.81(4)

P1(Pd1(Cl2	171.20(4)

P2(Pd1(Cl1	173.24(4)

P1(Pd1(Cl1	83.18(4)

Cl2(Pd1(Cl1	88.10(3)

C1(P1(C17	101.49(18)

C1(P1(C11	101.35(18)

C17(P1(C11	105.85(18)

C1(P1(Pd1	122.98(14)

C17(P1(Pd1	115.39(13)

C11(P1(Pd1	107.86(12)

C6(P2(C29	107.45(19)

C6(P2(C23	101.10(19)

C29(P2(C23	102.00(19)

C6(P2(Pd1	117.00(15)

C29(P2(Pd1	108.40(14)

C23(P2(Pd1	119.40(13)

Cl41(C41(Cl42	112.3(10)

Cl41(C41(Cl43	112.8(6)

Cl42(C41(Cl43	108.9(9)

Cl41(C41(H41	107.5

Cl42(C41(H41	107.5

Cl43(C41(H41	107.5

Cl51(C51(Cl52	106.0(15)

Cl51(C51(Cl53	115.4(14)

Cl52(C51(Cl53	101.2(15)

Cl51(C51(H51	111.2

Cl52(C51(H51	111.2

Cl53(C51(H51	111.2

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	22(2) 	27(2)	32(2) 	(10(2)	(3(2) 	(12(2)

C2	32(2) 	39(3)	38(3) 	(18(2)	1(2) 	(17(2)

C3	23(2) 	48(3)	57(3) 	(20(2)	2(2) 	(20(2)

C4	29(2) 	48(3)	49(3) 	(20(2)	11(2) 	(20(2)

C5	27(2) 	39(3)	40(3) 	(16(2)	6(2) 	(14(2)

C6	23(2) 	28(2)	38(3) 	(12(2)	0(2) 	(6(2)

C7	28(2) 	34(2)	39(3) 	(17(2)	4(2) 	(9(2)

C8	29(2) 	44(3)	51(3) 	(22(2)	11(2) 	(5(2)

C9	21(2) 	46(3)	59(3) 	(16(3)	(3(2) 	(2(2)

C10	25(2) 	38(3)	45(3) 	(13(2)	(8(2) 	(5(2)

C11	22(2) 	30(2)	24(2) 	(10(2)	1(2) 	(11(2)

C12	38(2) 	30(2)	36(3) 	(16(2)	(5(2) 	(7(2)

C13	33(2) 	45(3)	33(2) 	(23(2)	(1(2) 	(10(2)

C14	46(3) 	53(3)	26(2) 	(14(2)	(8(2) 	(13(2)

C15	105(5) 	33(3)	38(3) 	(9(2)	(31(3) 	(1(3)

C16	72(4) 	34(3)	32(3) 	(13(2)	(15(2) 	(9(2)

C17	29(2) 	25(2)	24(2) 	(10(2)	(5(2) 	(8(2)

C18	34(2) 	28(2)	31(2) 	(9(2)	(8(2) 	(12(2)

C19	53(3) 	24(2)	43(3) 	(9(2)	(18(2) 	(14(2)

C20	70(4) 	30(3)	35(3) 	(18(2)	(10(2) 	(7(2)

C21	66(3) 	35(3)	35(3) 	(20(2)	12(2) 	(13(2)

C22	43(3) 	28(2)	29(2) 	(12(2)	0(2) 	(11(2)

C23	21(2) 	27(2)	25(2) 	(5(2)	(5(2) 	(7(2)

C24	28(2) 	33(2)	34(2) 	(14(2)	(3(2) 	(5(2)

C25	36(2) 	28(2)	56(3) 	(17(2)	(10(2) 	(4(2)

C26	45(3) 	29(2)	40(3) 	(2(2)	(14(2) 	(14(2)

C27	43(3) 	40(3)	28(2) 	(4(2)	(2(2) 	(16(2)

C28	34(2) 	32(2)	33(2) 	(10(2)	(2(2) 	(10(2)

C29	22(2) 	37(2)	28(2) 	(14(2)	0(2) 	(12(2)

C30	30(2) 	40(3)	29(2) 	(16(2)	(3(2) 	(12(2)

C31	30(2) 	54(3)	44(3) 	(32(2)	4(2) 	(16(2)

C32	32(2) 	78(4)	38(3) 	(33(3)	5(2) 	(25(3)

C33	35(3) 	72(4)	33(3) 	(18(3)	(10(2) 	(18(3)

C34	27(2) 	48(3)	36(3) 	(14(2)	(9(2) 	(8(2)

Fe1	18(1) 	37(1)	38(1) 	(16(1)	3(1) 	(10(1)

Br1	35(1) 	47(1)	41(1) 	(21(1)	(4(1) 	(17(1)

Br2	44(1) 	39(1)	36(1) 	(17(1)	(4(1) 	(12(1)

Cl1	18(1) 	30(1)	32(1) 	(11(1)	(5(1) 	(6(1)

Cl2	25(1) 	29(1)	33(1) 	(7(1)	(3(1) 	(14(1)

Pd1	16(1) 	23(1)	22(1) 	(10(1)	(1(1) 	(7(1)

P1	19(1) 	25(1)	25(1) 	(11(1)	(1(1) 	(9(1)

P2	18(1) 	25(1)	26(1) 	(10(1)	(3(1) 	(6(1)

C41	97(9) 	30(7)	53(6) 	(18(5)	(14(6) 	7(6)

Cl41	167(5) 	54(2)	44(2) 	(6(2)	31(2) 	3(3)

Cl42	119(2) 	90(2)	49(2) 	(31(2)	(5(1) 	(22(2)

Cl43	104(2) 	59(2)	140(4) 	(56(2)	21(2) 	(18(2)

C51	44(12) 	44(17)	100(12) 	22(10)	(5(12) 	(22(13)

Cl51	129(7) 	210(12)	92(5) 	48(7)	25(5) 	(34(7)

Cl52	134(7) 	88(5)	201(11) 	(31(6)	(63(7) 	(31(5)

Cl53	50(3) 	61(6)	157(11) 	7(6)	24(4) 	(15(3)

Table 5. Hydrogen coordinates [( 104] and isotropic displacement parameters [Å2 ( 103].

Atom 	x	y	z	Ueq	S.o.f.

H3	6450	643	2131	48	1

H4	6281	498	645	48	1

H5	3919	677	453	41	1

H8	6309	(2674	1356	50	1

H9	7258	(2503	2624	52	1

H10	5402	(2138	3756	44	1

H12	1624	(120	598	40	1

H13	1048	572	(838	41	1

H14	244	2720	(1559	48	1

H15	44	4181	(827	72	1

H16	698	3498	603	54	1

H18	2606	3249	1594	35	1

H19	1952	5009	2082	45	1

H20	113	5240	3040	52	1

H21	(1102	3726	3497	54	1

H22	(448	1946	3019	39	1

H24	3858	(4427	3139	37	1

H25	3794	(6531	3833	47	1

H26	2438	(7082	5085	46	1

H27	1075	(5502	5624	46	1

H28	1025	(3374	4891	39	1

H30	1078	113	3997	37	1

H31	1115	781	5191	45	1

H32	2551	(488	6299	52	1

H33	3907	(2429	6231	54	1

H34	3919	(3085	5030	43	1

H41	7490	(6967	1544	76	0.684(5)

H51	7288	(7045	1268	87	0.316(5)