|  | University of Southampton · Department of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	01SOT027r

Empirical formula 	C30H23N3O2

Formula weight 	457.51

Temperature 	150(2) K

Wavelength 	0.71073 Å

Crystal system 	Triclinic

Space group 	P-1

Unit cell dimensions	a = 9.4890(9) Å	( = 91.483(3)°

b = 9.4925(9) Å	( = 88.321(3)°

c = 27.4534(5) Å	(  = 73.520(4)°

Volume	2368.7(3) Å3

Z	4

Density (calculated)	1.283 Mg / m3

Absorption coefficient	0.082 mm(1

F(000)	960

Crystal	Colourless prism

Crystal size	0.10 ( 0.08 ( 0.03 mm3

( range for data collection	3.07 ( 23.26°

Index ranges	(10 ( h ( 10, (10 ( k ( 10, (28 ( l ( 30

Reflections collected	12778

Independent reflections	6387 [Rint = 0.0863]

Completeness to ( = 23.26°	93.5 %

Max. and min. transmission	0.9976 and 0.9919

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	6387 / 0 / 632

Goodness-of-fit on F2	1.016

Final R indices [F2 > 2((F2)]	R1 = 0.0622, wR2 = 0.1249

R indices (all data)	R1 = 0.1269, wR2 = 0.1625

Extinction coefficient	0.0027(9)

Largest diff. peak and hole	0.236 and (0.299 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill Ewald sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SORTAV (R. H. Blessing, Acta Cryst. A51 (1995) 33(37; R. H. Blessing, J. Appl. Cryst. 30 (1997) 421(426). Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: Cameron - A Molecular Graphics Package. (D. M. Watkin, L. Pearce and C. K. Prout, Chemical Crystallography Laboratory, University of Oxford, 1993).

Special details:  All hydrogen atoms were placed in idealised positions and refined using a riding model.

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

Molecule A

N1	8970(4)	7086(3)	1297(1)	30(1)	1

N2	7309(3)	8280(3)	155(1)	24(1)	1

N3	7679(3)	8730(3)	(1150(1)	30(1)	1

O1	6577(3)	7651(3)	1084(1)	35(1)	1

O2	5648(3)	9428(3)	(630(1)	34(1)	1

C1	7607(5)	6798(4)	2049(2)	32(1)	1

C2	7651(5)	6302(5)	2519(2)	40(1)	1

C3	8973(5)	5622(5)	2723(2)	38(1)	1

C4	10259(5)	5429(5)	2450(2)	38(1)	1

C5	10239(5)	5924(5)	1980(2)	35(1)	1

C6	8905(4)	6609(4)	1780(2)	26(1)	1

C7	7879(5)	7502(4)	979(2)	26(1)	1

C8	8363(4)	7736(4)	484(2)	24(1)	1

C9	9717(4)	7441(4)	243(2)	26(1)	1

C10	9464(4)	7791(4)	(250(2)	23(1)	1

C11	7944(4)	8339(4)	(294(2)	23(1)	1

C12	6980(4)	8882(4)	(702(2)	26(1)	1

C13	7117(4)	8963(4)	(1621(2)	29(1)	1

C14	8129(5)	8538(5)	(2010(2)	39(1)	1

C15	7686(5)	8713(5)	(2485(2)	40(1)	1

C16	6214(5)	9300(5)	(2574(2)	38(1)	1

C17	5206(5)	9723(4)	(2185(2)	37(1)	1

C18	5639(4)	9576(4)	(1708(2)	30(1)	1

C19	11222(4)	6867(4)	434(1)	22(1)	1

C20	11836(4)	7768(4)	710(2)	29(1)	1

C21	13279(5)	7284(5)	851(2)	33(1)	1

C22	14118(5)	5865(5)	726(2)	35(1)	1

C23	13510(5)	4956(5)	460(2)	41(1)	1

C24	12069(4)	5436(4)	314(2)	31(1)	1

C25	10662(4)	7686(4)	(622(1)	23(1)	1

C26	11571(4)	8605(4)	(578(2)	29(1)	1

C27	12740(4)	8475(4)	(904(2)	33(1)	1

C28	13031(4)	7432(4)	(1278(2)	32(1)	1

C29	12153(5)	6507(5)	(1328(2)	39(1)	1

C30	10986(4)	6621(4)	(998(2)	31(1)	1

Molecule B

N4	6928(3)	4187(3)	(3613(1)	27(1)	1

N5	8251(3)	2299(3)	(4777(1)	24(1)	1

N6	8581(3)	2367(3)	(6091(1)	29(1)	1

O3	7601(3)	1743(3)	(3828(1)	32(1)	1

O4	9401(3)	476(3)	(5578(1)	33(1)	1

C31	6727(4)	2948(4)	(2847(1)	26(1)	1

C32	6372(4)	3098(5)	(2351(2)	32(1)	1

C33	5858(4)	4451(5)	(2120(2)	33(1)	1

C34	5677(4)	5695(5)	(2382(2)	34(1)	1

C35	6010(4)	5573(4)	(2876(2)	31(1)	1

C36	6539(4)	4213(4)	(3111(1)	24(1)	1

C37	7416(4)	3033(5)	(3935(1)	24(1)	1

C38	7711(4)	3409(4)	(4441(1)	21(1)	1

C39	7426(4)	4733(4)	(4680(1)	23(1)	1

C40	7785(4)	4371(4)	(5181(2)	24(1)	1

C41	8309(4)	2838(4)	(5229(1)	21(1)	1

C42	8837(4)	1794(4)	(5642(2)	24(1)	1

C43	8687(4)	1627(4)	(6551(2)	27(1)	1

C44	7915(5)	2440(5)	(6923(2)	41(1)	1

C45	7954(5)	1811(5)	(7384(2)	47(1)	1

C46	8744(5)	355(5)	(7481(2)	40(1)	1

C47	9505(5)	(434(5)	(7109(2)	35(1)	1

C48	9495(4)	196(4)	(6650(2)	28(1)	1

C49	6892(4)	6268(4)	(4478(2)	26(1)	1

C50	7794(5)	6864(5)	(4197(2)	34(1)	1

C51	7344(5)	8319(5)	(4033(2)	39(1)	1

C52	5979(5)	9195(5)	(4149(2)	47(1)	1

C53	5072(5)	8623(5)	(4425(2)	46(1)	1

C54	5513(4)	7159(4)	(4595(2)	35(1)	1

C55	7635(4)	5502(4)	(5560(1)	22(1)	1

C56	8566(4)	6391(4)	(5565(2)	29(1)	1

C57	8387(5)	7496(4)	(5891(2)	30(1)	1

C58	7269(5)	7733(4)	(6220(2)	33(1)	1

C59	6325(4)	6871(4)	(6216(2)	28(1)	1

C60	6504(4)	5762(4)	(5884(2)	27(1)	1

Table 3. Bond lengths [Å] and angles [°].

Molecule A

N1(C7	1.351(5)

N1(C6	1.417(5)

N2(C11	1.365(4)

N2(C8	1.367(5)

N3(C12	1.364(5)

N3(C13	1.412(5)

O1(C7	1.228(4)

O2(C12	1.230(4)

C1(C6	1.382(5)

C1(C2	1.384(5)

C2(C3	1.380(6)

C3(C4	1.376(5)

C4(C5	1.385(5)

C5(C6	1.385(5)

C7(C8	1.466(5)

C8(C9	1.379(5)

C9(C10	1.414(5)

C9(C19	1.493(5)

C10(C11	1.398(5)

C10(C25	1.485(5)

C11(C12	1.477(5)

C13(C18	1.387(5)

C13(C14	1.387(5)

C14(C15	1.380(6)

C15(C16	1.381(6)

C16(C17	1.383(6)

C17(C18	1.384(5)

C19(C20	1.386(6)

C19(C24	1.393(5)

C20(C21	1.386(5)

C21(C22	1.385(6)

C22(C23	1.372(6)

C23(C24	1.389(6)

C25(C30	1.392(5)

C25(C26	1.395(5)

C26(C27	1.380(5)

C27(C28	1.374(6)

C28(C29	1.378(6)

C29(C30	1.387(5)

Molecule B

C31(C32	1.388(5)

C31(C36	1.389(5)

C32(C33	1.369(6)

C33(C34	1.370(5)

C34(C35	1.379(5)

C35(C36	1.379(5)

C36(N4	1.416(5)

C37(O3	1.231(4)

C37(N4	1.354(5)

C37(C38	1.481(5)

C38(N5	1.356(5)

C38(C39	1.393(5)

C39(C40	1.419(5)

C39(C49	1.487(5)

C40(C41	1.399(5)

C40(C55	1.495(5)

C41(N5	1.360(4)

C41(C42	1.465(5)

C42(O4	1.232(4)

C42(N6	1.362(5)

C43(C48	1.373(5)

C43(C44	1.392(5)

C43(N6	1.415(5)

C44(C45	1.381(6)

C45(C46	1.387(6)

C46(C47	1.377(6)

C47(C48	1.381(6)

C49(C50	1.392(6)

C49(C54	1.393(5)

C50(C51	1.384(6)

C51(C52	1.377(6)

C52(C53	1.375(6)

C53(C54	1.396(6)

C55(C56	1.384(5)

C55(C60	1.385(5)

C56(C57	1.375(5)

C57(C58	1.387(6)

C58(C59	1.374(6)

C59(C60	1.389(5)

Molecule A

C7(N1(C6	129.1(3)

C11(N2(C8	110.4(3)

C12(N3(C13	131.0(3)

C6(C1(C2	119.5(4)

C3(C2(C1	120.9(4)

C4(C3(C2	119.2(4)

C3(C4(C5	120.8(4)

C4(C5(C6	119.5(4)

C1(C6(C5	120.1(4)

C1(C6(N1	123.5(4)

C5(C6(N1	116.4(3)

O1(C7(N1	124.0(4)

O1(C7(C8	121.1(4)

N1(C7(C8	114.9(3)

N2(C8(C9	107.9(3)

N2(C8(C7	118.0(3)

C9(C8(C7	134.0(4)

C8(C9(C10	107.4(4)

C8(C9(C19	129.8(4)

C10(C9(C19	122.8(3)

C11(C10(C9	107.3(3)

C11(C10(C25	129.0(4)

C9(C10(C25	123.5(4)

N2(C11(C10	107.0(3)

N2(C11(C12	118.5(3)

C10(C11(C12	134.4(4)

O2(C12(N3	124.1(4)

O2(C12(C11	120.8(4)

N3(C12(C11	115.1(3)

C18(C13(C14	119.8(4)

C18(C13(N3	123.6(4)

C14(C13(N3	116.5(4)

C15(C14(C13	120.9(4)

C14(C15(C16	119.6(4)

C15(C16(C17	119.5(4)

C16(C17(C18	121.5(4)

C17(C18(C13	118.7(4)

C20(C19(C24	118.7(4)

C20(C19(C9	120.8(3)

C24(C19(C9	120.4(4)

C19(C20(C21	121.1(4)

C22(C21(C20	119.8(4)

C23(C22(C21	119.5(4)

C22(C23(C24	121.1(4)

C23(C24(C19	119.8(4)

C30(C25(C26	118.0(4)

C30(C25(C10	122.1(4)

C26(C25(C10	119.8(4)

C27(C26(C25	120.9(4)

C28(C27(C26	120.4(4)

C27(C28(C29	119.8(4)

C28(C29(C30	120.1(4)

C29(C30(C25	120.8(4)

Molecule B

C32(C31(C36	118.4(4)

C33(C32(C31	121.6(4)

C32(C33(C34	119.7(4)

C33(C34(C35	119.8(4)

C34(C35(C36	120.8(4)

C35(C36(C31	119.7(4)

C35(C36(N4	117.2(3)

C31(C36(N4	123.0(4)

O3(C37(N4	123.8(4)

O3(C37(C38	120.5(4)

N4(C37(C38	115.7(3)

N5(C38(C39	108.0(3)

N5(C38(C37	118.5(3)

C39(C38(C37	133.2(4)

C38(C39(C40	106.8(3)

C38(C39(C49	129.8(4)

C40(C39(C49	123.4(3)

C41(C40(C39	107.2(3)

C41(C40(C55	129.7(4)

C39(C40(C55	123.1(3)

N5(C41(C40	107.3(3)

N5(C41(C42	118.4(3)

C40(C41(C42	134.2(4)

O4(C42(N6	123.4(4)

O4(C42(C41	121.1(4)

N6(C42(C41	115.5(3)

C48(C43(C44	119.1(4)

C48(C43(N6	124.6(4)

C44(C43(N6	116.3(4)

C45(C44(C43	120.4(4)

C44(C45(C46	120.4(4)

C47(C46(C45	118.5(4)

C46(C47(C48	121.4(4)

C43(C48(C47	120.1(4)

C50(C49(C54	119.1(4)

C50(C49(C39	120.7(4)

C54(C49(C39	120.1(4)

C51(C50(C49	121.2(4)

C52(C51(C50	119.5(5)

C53(C52(C51	120.1(5)

C52(C53(C54	121.1(4)

C49(C54(C53	119.1(5)

C56(C55(C60	119.0(3)

C56(C55(C40	119.6(4)

C60(C55(C40	121.2(4)

C57(C56(C55	120.5(4)

C56(C57(C58	120.3(4)

C59(C58(C57	119.9(4)

C58(C59(C60	119.6(4)

C55(C60(C59	120.7(4)

C37(N4(C36	130.0(3)

C38(N5(C41	110.7(3)

C42(N6(C43	129.1(3)

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

Molecule A

N1	25(2) 	43(2)	25(2) 	6(2)	0(2) 	(14(2)

N2	19(2) 	31(2)	24(2) 	0(2)	2(2) 	(9(2)

N3	16(2) 	42(2)	28(2) 	0(2)	(2(2) 	(4(2)

O1	25(2) 	49(2)	28(2) 	5(1)	1(1) 	(6(1)

O2	23(2) 	46(2)	31(2) 	8(1)	0(1) 	(5(1)

C1	31(3) 	39(3)	25(3) 	(2(2)	0(2) 	(7(2)

C2	32(3) 	56(3)	28(3) 	2(2)	0(2) 	(9(2)

C3	46(3) 	44(3)	25(3) 	7(2)	(6(2) 	(13(2)

C4	34(3) 	45(3)	33(3) 	(1(2)	(11(2) 	(10(2)

C5	29(3) 	50(3)	27(3) 	(4(2)	(1(2) 	(11(2)

C6	29(3) 	32(3)	20(3) 	(4(2)	(2(2) 	(13(2)

C7	25(3) 	26(3)	26(3) 	(4(2)	2(2) 	(6(2)

C8	18(2) 	30(3)	22(3) 	(1(2)	(2(2) 	(7(2)

C9	25(2) 	29(3)	23(3) 	(4(2)	(3(2) 	(10(2)

C10	24(2) 	20(2)	25(3) 	(7(2)	1(2) 	(6(2)

C11	22(2) 	24(2)	24(3) 	3(2)	0(2) 	(5(2)

C12	23(3) 	28(3)	26(3) 	(3(2)	3(2) 	(8(2)

C13	26(3) 	39(3)	22(3) 	4(2)	(6(2) 	(10(2)

C14	34(3) 	54(3)	29(3) 	2(2)	1(2) 	(10(2)

C15	46(3) 	47(3)	27(3) 	1(2)	7(2) 	(12(2)

C16	46(3) 	40(3)	27(3) 	0(2)	(8(2) 	(14(2)

C17	38(3) 	35(3)	33(3) 	4(2)	(13(2) 	(2(2)

C18	30(3) 	28(3)	30(3) 	5(2)	0(2) 	(7(2)

C19	27(2) 	21(3)	20(3) 	2(2)	(1(2) 	(11(2)

C20	28(3) 	28(3)	31(3) 	(4(2)	(1(2) 	(7(2)

C21	33(3) 	36(3)	32(3) 	(2(2)	(9(2) 	(11(2)

C22	24(2) 	44(3)	36(3) 	8(2)	(11(2) 	(7(2)

C23	30(3) 	42(3)	46(3) 	(1(3)	(4(2) 	(3(2)

C24	30(3) 	30(3)	36(3) 	(2(2)	(8(2) 	(9(2)

C25	23(2) 	24(3)	20(3) 	2(2)	(2(2) 	(4(2)

C26	30(3) 	31(3)	24(3) 	(5(2)	2(2) 	(7(2)

C27	32(3) 	30(3)	38(3) 	0(2)	5(2) 	(10(2)

C28	30(3) 	38(3)	27(3) 	(5(2)	9(2) 	(8(2)

C29	39(3) 	38(3)	36(3) 	(10(2)	6(2) 	(8(2)

C30	26(3) 	35(3)	35(3) 	(5(2)	(1(2) 	(14(2)

Molecule B

C31	25(2) 	28(3)	24(3) 	(6(2)	(2(2) 	(5(2)

C32	35(3) 	28(3)	32(3) 	8(2)	3(2) 	(7(2)

C33	34(3) 	42(3)	22(3) 	0(2)	1(2) 	(9(2)

C34	40(3) 	30(3)	27(3) 	(5(2)	6(2) 	(1(2)

C35	31(3) 	28(3)	30(3) 	(2(2)	1(2) 	(3(2)

C36	20(2) 	26(3)	23(3) 	4(2)	(2(2) 	(3(2)

C37	21(2) 	29(3)	19(3) 	(4(2)	(1(2) 	(2(2)

C38	21(2) 	16(2)	21(3) 	(2(2)	(3(2) 	1(2)

C39	20(2) 	22(3)	24(3) 	(3(2)	0(2) 	(4(2)

C40	18(2) 	26(3)	28(3) 	(1(2)	(1(2) 	(7(2)

C41	24(2) 	25(3)	16(3) 	2(2)	(2(2) 	(8(2)

C42	24(2) 	21(3)	24(3) 	3(2)	(3(2) 	(4(2)

C43	30(3) 	34(3)	17(3) 	(3(2)	2(2) 	(9(2)

C44	46(3) 	44(3)	26(3) 	1(2)	(7(2) 	(3(2)

C45	42(3) 	65(4)	25(3) 	5(3)	(11(2) 	(2(3)

C46	39(3) 	52(3)	26(3) 	(12(2)	(4(2) 	(10(2)

C47	36(3) 	32(3)	36(3) 	(9(2)	9(2) 	(8(2)

C48	31(3) 	26(3)	26(3) 	(1(2)	2(2) 	(5(2)

C49	25(2) 	29(3)	21(3) 	(1(2)	7(2) 	(5(2)

C50	34(3) 	37(3)	30(3) 	(4(2)	(1(2) 	(11(2)

C51	41(3) 	34(3)	45(3) 	(16(2)	3(2) 	(16(2)

C52	48(3) 	34(3)	55(4) 	(15(3)	9(3) 	(8(3)

C53	32(3) 	39(3)	61(4) 	(8(3)	1(3) 	1(2)

C54	28(3) 	30(3)	44(3) 	(6(2)	1(2) 	(5(2)

C55	23(2) 	19(2)	21(3) 	5(2)	(1(2) 	(1(2)

C56	23(2) 	30(3)	34(3) 	8(2)	(7(2) 	(9(2)

C57	37(3) 	24(3)	34(3) 	6(2)	0(2) 	(14(2)

C58	36(3) 	32(3)	24(3) 	7(2)	1(2) 	0(2)

C59	25(2) 	33(3)	27(3) 	5(2)	(5(2) 	(9(2)

C60	28(2) 	28(3)	26(3) 	(2(2)	0(2) 	(10(2)

N4	36(2) 	20(2)	25(2) 	2(2)	2(2) 	(7(2)

N5	31(2) 	17(2)	24(2) 	0(2)	0(2) 	(8(2)

N6	38(2) 	25(2)	21(2) 	4(2)	(6(2) 	(5(2)

O3	41(2) 	22(2)	29(2) 	1(1)	1(1) 	(4(1)

O4	48(2) 	24(2)	24(2) 	1(1)	(1(1) 	(4(1)

Table 5. Hydrogen coordinates [( 104] and isotropic displacement parameters [Å2 ( 103].

Atom 	x	y	z	Ueq	S.o.f.

H1	9843	7114	1189	36	1

H2	6356	8555	223	29	1

H3	8645	8436	(1144	36	1

H1A	6691	7265	1912	39	1

H2A	6759	6431	2704	48	1

H3A	8996	5291	3047	46	1

H4A	11172	4949	2587	45	1

H5A	11133	5796	1796	42	1

H14	9140	8122	(1950	47	1

H15	8389	8431	(2749	48	1

H16	5896	9411	(2899	45	1

H17	4194	10124	(2247	44	1

H18	4938	9888	(1444	35	1

H20	11257	8734	804	35	1

H21	13692	7924	1033	40	1

H22	15106	5523	824	42	1

H23	14086	3982	375	49	1

H24	11663	4792	131	38	1

H26	11383	9330	(321	35	1

H27	13347	9110	(869	40	1

H28	13836	7348	(1502	38	1

H29	12347	5791	(1588	46	1

H30	10401	5963	(1030	38	1

H31	7091	2003	(3003	32	1

H32	6488	2241	(2167	39	1

H33	5627	4528	(1779	39	1

H34	5324	6637	(2224	41	1

H35	5874	6437	(3058	37	1

H44	7359	3434	(6859	49	1

H45	7436	2378	(7637	56	1

H46	8760	(88	(7796	48	1

H47	10048	(1433	(7171	42	1

H48	10048	(362	(6401	34	1

H50	8735	6261	(4117	40	1

H51	7971	8711	(3842	47	1

H52	5664	10196	(4039	56	1

H53	4130	9235	(4502	56	1

H54	4882	6776	(4787	42	1

H56	9335	6235	(5341	34	1

H57	9033	8100	(5891	36	1

H58	7156	8491	(6448	39	1

H59	5555	7033	(6440	34	1

H60	5842	5175	(5878	32	1

H4	6839	5054	(3735	33	1

H5	8527	1360	(4711	29	1

H6	8313	3333	(6097	34	1

Table 6. Hydrogen bonds [Å and °].

D(H···A	d(D(H)	d(H···A)	d(D···A)	((DHA)

N2(H2...O2i	0.88	2.50	3.238(4)	142.3

N5(H5...O4ii	0.88	2.40	3.127(4)	140.4

Symmetry transformations used to generate equivalent atoms:

(i) (x+1,(y+2,(z    (ii) (x+2,(y,(z(1

Molecular Structure of Molecule A

Hydrogen bonded dimers