|  | University of Southampton · School of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	2005src1387 / JEN1

Empirical formula 	C15H9N

Formula weight 	203.23

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Orthorhombic

Space group 	P212121

Unit cell dimensions	a = 3.83960(10) Å	( = 90°

b = 15.1075(8) Å	( = 90°

c = 17.1516(7) Å	(  = 90°

Volume	994.91(7) Å3

Z	4

Density (calculated)	1.357 Mg / m3

Absorption coefficient	0.079 mm(1

F(000)	424

Crystal	Rod; light yellow

Crystal size	0.28 ( 0.04 ( 0.03 mm3

( range for data collection	3.59 ( 27.47°

Index ranges	(4 ( h ( 4, (19 ( k ( 14, (22 ( l ( 22

Reflections collected	8466

Independent reflections	1361 [Rint = 0.1174]

Completeness to ( = 27.47°	99.5 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9976 and 0.9781

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	1361 / 0 / 146

Goodness-of-fit on F2	1.057

Final R indices [F2 > 2((F2)]	R1 = 0.0479, wR2 = 0.1035

R indices (all data)	R1 = 0.0641, wR2 = 0.1115

Absolute structure parameter	(10(10)

Extinction coefficient	0.035(10)

Largest diff. peak and hole	0.174 and (0.221 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SADABS Version 2.10. (G. M. Sheldrick (2003)) Bruker AXS Inc., Madison, Wisconsin, USA. Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: ORTEP3 for Windows (L. J. Farrugia, J. Appl. Crystallogr. 1997, 30, 565).

Special details:

All hydrogen atoms were fixed.

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	6424(6)	4349(1)	2402(1)	21(1)	1

C2	8044(6)	3654(1)	1993(1)	21(1)	1

C3	8727(6)	3684(1)	1179(1)	23(1)	1

C4	10272(6)	2991(1)	808(1)	26(1)	1

C5	11229(6)	2218(1)	1231(1)	25(1)	1

C6	10677(6)	2168(1)	2009(1)	25(1)	1

C7	9093(6)	2883(1)	2422(1)	21(1)	1

C8	8507(6)	2849(1)	3224(1)	23(1)	1

C9	6897(6)	3536(1)	3630(1)	22(1)	1

C10	6298(6)	3497(2)	4449(1)	26(1)	1

C11	4697(7)	4169(2)	4831(1)	30(1)	1

C12	3593(7)	4931(2)	4415(1)	28(1)	1

C13	4125(6)	5002(1)	3634(1)	25(1)	1

C14	5805(6)	4309(1)	3213(1)	21(1)	1

C15	5300(6)	5124(1)	1970(1)	24(1)	1

N1	4421(6)	5727(1)	1636(1)	34(1)	1

Table 3. Bond lengths [Å] and angles [°].

C1(C2	1.407(3)

C1(C14	1.413(3)

C1(C15	1.452(3)

C2(C3	1.423(3)

C2(C7	1.435(3)

C3(C4	1.362(3)

C3(H3	0.9500

C4(C5	1.423(3)

C4(H4	0.9500

C5(C6	1.354(3)

C5(H5	0.9500

C6(C7	1.427(3)

C6(H6	0.9500

C7(C8	1.395(3)

C8(C9	1.395(3)

C8(H8	0.9500

C9(C10	1.424(3)

C9(C14	1.432(3)

C10(C11	1.355(3)

C10(H10	0.9500

C11(C12	1.420(3)

C11(H11	0.9500

C12(C13	1.359(3)

C12(H12	0.9500

C13(C14	1.425(3)

C13(H13	0.9500

C15(N1	1.127(3)

C2(C1(C14	122.22(19)

C2(C1(C15	118.62(18)

C14(C1(C15	119.1(2)

C1(C2(C3	123.11(19)

C1(C2(C7	118.33(18)

C3(C2(C7	118.56(19)

C4(C3(C2	120.9(2)

C4(C3(H3	119.5

C2(C3(H3	119.5

C3(C4(C5	120.4(2)

C3(C4(H4	119.8

C5(C4(H4	119.8

C6(C5(C4	120.5(2)

C6(C5(H5	119.8

C4(C5(H5	119.8

C5(C6(C7	121.0(2)

C5(C6(H6	119.5

C7(C6(H6	119.5

C8(C7(C6	122.1(2)

C8(C7(C2	119.34(19)

C6(C7(C2	118.60(19)

C7(C8(C9	122.41(19)

C7(C8(H8	118.8

C9(C8(H8	118.8

C8(C9(C10	122.2(2)

C8(C9(C14	119.22(19)

C10(C9(C14	118.6(2)

C11(C10(C9	121.2(2)

C11(C10(H10	119.4

C9(C10(H10	119.4

C10(C11(C12	120.0(2)

C10(C11(H11	120.0

C12(C11(H11	120.0

C13(C12(C11	121.0(2)

C13(C12(H12	119.5

C11(C12(H12	119.5

C12(C13(C14	120.6(2)

C12(C13(H13	119.7

C14(C13(H13	119.7

C1(C14(C13	122.93(19)

C1(C14(C9	118.47(19)

C13(C14(C9	118.59(19)

N1(C15(C1	179.8(3)

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	19(1) 	17(1)	26(1) 	1(1)	(4(1) 	(1(1)

C2	14(1) 	20(1)	26(1) 	1(1)	(1(1) 	(4(1)

C3	20(1) 	20(1)	28(1) 	2(1)	(3(1) 	(1(1)

C4	21(1) 	29(1)	28(1) 	(4(1)	0(1) 	(2(1)

C5	21(1) 	21(1)	33(1) 	(6(1)	1(1) 	0(1)

C6	19(1) 	18(1)	36(1) 	(1(1)	(2(1) 	0(1)

C7	14(1) 	18(1)	31(1) 	0(1)	(3(1) 	(3(1)

C8	19(1) 	20(1)	32(1) 	4(1)	(5(1) 	(4(1)

C9	18(1) 	21(1)	28(1) 	1(1)	(2(1) 	(5(1)

C10	21(1) 	28(1)	29(1) 	4(1)	0(1) 	(4(1)

C11	25(1) 	40(1)	26(1) 	(1(1)	1(1) 	(7(1)

C12	22(1) 	30(1)	31(1) 	(8(1)	1(1) 	(1(1)

C13	20(1) 	23(1)	32(1) 	(3(1)	(3(1) 	0(1)

C14	14(1) 	21(1)	29(1) 	(2(1)	(4(1) 	(4(1)

C15	22(1) 	24(1)	25(1) 	(7(1)	(1(1) 	(1(1)

N1	42(1) 	26(1)	34(1) 	(3(1)	(5(1) 	5(1)

Table 5. Hydrogen coordinates [( 104] and isotropic displacement parameters [Å2 ( 103].

Atom 	x	y	z	Ueq	S.o.f.

H3	8096	4196	889	27	1

H4	10713	3023	263	31	1

H5	12262	1733	965	30	1

H6	11354	1650	2284	30	1

H8	9231	2338	3505	28	1

H10	7035	2991	4733	31	1

H11	4313	4130	5377	36	1

H12	2466	5398	4686	33	1

H13	3370	5518	3366	30	1