|  | University of Southampton · Department of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	03src0271

Empirical formula 	C32H26NO4P

Formula weight 	519.51

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	Cc

Unit cell dimensions	a = 13.4334(2) Å	( = 90°

b = 14.3903(2) Å	( = 90.4070(10)°

c = 13.7137(3) Å	(  = 90°

Volume	2650.94(8) Å3

Z	4

Density (calculated)	1.302 Mg / m3

Absorption coefficient	0.142 mm(1

F(000)	1088

Crystal	Block; Yellow

Crystal size	0.25 ( 0.18 ( 0.14 mm3

( range for data collection	3.20 ( 27.49°

Index ranges	(17 ( h ( 17, (18 ( k ( 18, (17 ( l ( 17

Reflections collected	22956

Independent reflections	6014 [Rint = 0.0463]

Completeness to ( = 27.49°	99.7 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9803 and 0.9653

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	6014 / 2 / 346

Goodness-of-fit on F2	1.014

Final R indices [F2 > 2((F2)]	R1 = 0.0333, wR2 = 0.0735

R indices (all data)	R1 = 0.0369, wR2 = 0.0758

Absolute structure parameter	0.02(6)

Extinction coefficient	0.0063(5)

Largest diff. peak and hole	0.189 and (0.191 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SORTAV (R. H. Blessing, Acta Cryst. A51 (1995) 33(37; R. H. Blessing, J. Appl. Cryst. 30 (1997) 421(426). Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: Cameron - A Molecular Graphics Package. (D. M. Watkin, L. Pearce and C. K. Prout, Chemical Crystallography Laboratory, University of Oxford, 1993).

Special details:

All hydrogen atoms were fixed.

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	9221(1)	5763(1)	1495(1)	19(1)	1

C2	9676(1)	5246(1)	761(1)	25(1)	1

C3	10522(1)	4739(1)	964(1)	28(1)	1

C4	10925(1)	4725(1)	1899(1)	27(1)	1

C5	10497(1)	5261(1)	2625(1)	22(1)	1

C6	9660(1)	5814(1)	2432(1)	17(1)	1

C7	9217(1)	6454(1)	3164(1)	17(1)	1

C8	9812(1)	6904(1)	3911(1)	17(1)	1

C9	10876(1)	6872(1)	3909(1)	18(1)	1

C10	9305(1)	7339(1)	4681(1)	17(1)	1

C11	9649(1)	7979(1)	5365(1)	17(1)	1

C12	10492(1)	8619(1)	5259(1)	19(1)	1

C13	11686(1)	9279(1)	4181(1)	28(1)	1

C14	11357(2)	10236(1)	3876(2)	36(1)	1

C15	9678(1)	7770(1)	7534(1)	17(1)	1

C16	10700(1)	7616(1)	7526(1)	21(1)	1

C17	11170(1)	7254(1)	8348(1)	25(1)	1

C18	10623(1)	7050(1)	9172(1)	27(1)	1

C19	9608(1)	7219(1)	9192(1)	30(1)	1

C20	9127(1)	7579(1)	8374(1)	23(1)	1

C21	8700(1)	9382(1)	6581(1)	18(1)	1

C22	8828(1)	9860(1)	7462(1)	23(1)	1

C23	8683(1)	10816(1)	7494(2)	29(1)	1

C24	8409(1)	11290(1)	6654(2)	31(1)	1

C25	8265(1)	10823(1)	5781(1)	29(1)	1

C26	8416(1)	9869(1)	5744(1)	24(1)	1

C27	7884(1)	7470(1)	6464(1)	15(1)	1

C28	6933(1)	7853(1)	6492(1)	19(1)	1

C29	6108(1)	7270(1)	6508(1)	21(1)	1

C30	6221(1)	6315(1)	6494(1)	21(1)	1

C31	7169(1)	5926(1)	6475(1)	22(1)	1

C32	7999(1)	6496(1)	6474(1)	20(1)	1

N1	11731(1)	6815(1)	3952(1)	28(1)	1

O1	8367(1)	6218(1)	1272(1)	25(1)	1

O2	8311(1)	6642(1)	3093(1)	23(1)	1

O3	10814(1)	9085(1)	5936(1)	24(1)	1

O4	10818(1)	8690(1)	4344(1)	26(1)	1

P1	8997(1)	8164(1)	6472(1)	15(1)	1

Table 3. Bond lengths [Å] and angles [°].

C1(O1	1.354(2)

C1(C2	1.396(2)

C1(C6	1.412(2)

C2(C3	1.378(3)

C2(H2	0.9500

C3(C4	1.388(3)

C3(H3	0.9500

C4(C5	1.387(2)

C4(H4	0.9500

C5(C6	1.402(2)

C5(H5	0.9500

C6(C7	1.490(2)

C7(O2	1.250(2)

C7(C8	1.447(2)

C8(C10	1.407(2)

C8(C9	1.430(2)

C9(N1	1.153(2)

C10(C11	1.392(2)

C10(H10	0.9500

C11(C12	1.467(2)

C11(P1	1.7777(15)

C12(O3	1.221(2)

C12(O4	1.3362(19)

C13(O4	1.461(2)

C13(C14	1.504(3)

C13(H13A	0.9900

C13(H13B	0.9900

C14(H14A	0.9800

C14(H14B	0.9800

C14(H14C	0.9800

C15(C16	1.390(2)

C15(C20	1.402(2)

C15(P1	1.8061(16)

C16(C17	1.390(2)

C16(H16	0.9500

C17(C18	1.384(3)

C17(H17	0.9500

C18(C19	1.385(3)

C18(H18	0.9500

C19(C20	1.390(2)

C19(H19	0.9500

C20(H20	0.9500

C21(C26	1.396(2)

C21(C22	1.400(2)

C21(P1	1.8042(16)

C22(C23	1.390(3)

C22(H22	0.9500

C23(C24	1.386(3)

C23(H23	0.9500

C24(C25	1.384(3)

C24(H24	0.9500

C25(C26	1.389(3)

C25(H25	0.9500

C26(H26	0.9500

C27(C28	1.392(2)

C27(C32	1.411(2)

C27(P1	1.7970(16)

C28(C29	1.390(2)

C28(H28	0.9500

C29(C30	1.383(2)

C29(H29	0.9500

C30(C31	1.391(2)

C30(H30	0.9500

C31(C32	1.384(2)

C31(H31	0.9500

C32(H32	0.9500

O1(H1	0.8400

O1(C1(C2	117.99(15)

O1(C1(C6	121.87(14)

C2(C1(C6	120.13(15)

C3(C2(C1	120.12(16)

C3(C2(H2	119.9

C1(C2(H2	119.9

C2(C3(C4	120.60(16)

C2(C3(H3	119.7

C4(C3(H3	119.7

C3(C4(C5	119.69(17)

C3(C4(H4	120.2

C5(C4(H4	120.2

C4(C5(C6	121.03(16)

C4(C5(H5	119.5

C6(C5(H5	119.5

C5(C6(C1	118.13(14)

C5(C6(C7	123.19(15)

C1(C6(C7	118.67(14)

O2(C7(C8	119.38(14)

O2(C7(C6	118.34(14)

C8(C7(C6	122.17(14)

C10(C8(C9	120.30(14)

C10(C8(C7	117.53(14)

C9(C8(C7	122.09(14)

N1(C9(C8	176.18(18)

C11(C10(C8	129.83(15)

C11(C10(H10	115.1

C8(C10(H10	115.1

C10(C11(C12	126.94(14)

C10(C11(P1	120.75(12)

C12(C11(P1	112.12(11)

O3(C12(O4	123.70(15)

O3(C12(C11	122.61(14)

O4(C12(C11	113.52(13)

O4(C13(C14	109.90(15)

O4(C13(H13A	109.7

C14(C13(H13A	109.7

O4(C13(H13B	109.7

C14(C13(H13B	109.7

H13A(C13(H13B	108.2

C13(C14(H14A	109.5

C13(C14(H14B	109.5

H14A(C14(H14B	109.5

C13(C14(H14C	109.5

H14A(C14(H14C	109.5

H14B(C14(H14C	109.5

C16(C15(C20	120.16(15)

C16(C15(P1	122.59(12)

C20(C15(P1	117.19(12)

C15(C16(C17	119.77(15)

C15(C16(H16	120.1

C17(C16(H16	120.1

C18(C17(C16	120.04(17)

C18(C17(H17	120.0

C16(C17(H17	120.0

C19(C18(C17	120.50(17)

C19(C18(H18	119.8

C17(C18(H18	119.8

C18(C19(C20	120.10(16)

C18(C19(H19	119.9

C20(C19(H19	119.9

C19(C20(C15	119.41(16)

C19(C20(H20	120.3

C15(C20(H20	120.3

C26(C21(C22	119.64(16)

C26(C21(P1	118.61(13)

C22(C21(P1	121.54(13)

C23(C22(C21	119.76(17)

C23(C22(H22	120.1

C21(C22(H22	120.1

C24(C23(C22	119.85(17)

C24(C23(H23	120.1

C22(C23(H23	120.1

C25(C24(C23	120.93(17)

C25(C24(H24	119.5

C23(C24(H24	119.5

C24(C25(C26	119.47(17)

C24(C25(H25	120.3

C26(C25(H25	120.3

C25(C26(C21	120.34(17)

C25(C26(H26	119.8

C21(C26(H26	119.8

C28(C27(C32	119.56(15)

C28(C27(P1	122.93(12)

C32(C27(P1	117.44(12)

C29(C28(C27	119.60(15)

C29(C28(H28	120.2

C27(C28(H28	120.2

C30(C29(C28	120.75(16)

C30(C29(H29	119.6

C28(C29(H29	119.6

C29(C30(C31	120.05(16)

C29(C30(H30	120.0

C31(C30(H30	120.0

C32(C31(C30	119.97(15)

C32(C31(H31	120.0

C30(C31(H31	120.0

C31(C32(C27	120.03(15)

C31(C32(H32	120.0

C27(C32(H32	120.0

C1(O1(H1	109.5

C12(O4(C13	117.09(13)

C11(P1(C27	109.08(7)

C11(P1(C21	109.05(7)

C27(P1(C21	110.84(7)

C11(P1(C15	113.04(8)

C27(P1(C15	104.35(7)

C21(P1(C15	110.40(7)

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	23(1) 	14(1)	20(1) 	1(1)	2(1) 	(5(1)

C2	33(1) 	23(1)	20(1) 	(5(1)	4(1) 	(8(1)

C3	35(1) 	22(1)	27(1) 	(9(1)	13(1) 	(6(1)

C4	26(1) 	19(1)	37(1) 	(3(1)	10(1) 	1(1)

C5	24(1) 	18(1)	24(1) 	1(1)	4(1) 	0(1)

C6	20(1) 	15(1)	17(1) 	1(1)	3(1) 	(4(1)

C7	19(1) 	17(1)	15(1) 	4(1)	3(1) 	0(1)

C8	17(1) 	18(1)	16(1) 	1(1)	2(1) 	(1(1)

C9	22(1) 	20(1)	13(1) 	(1(1)	3(1) 	(1(1)

C10	19(1) 	15(1)	16(1) 	2(1)	0(1) 	(2(1)

C11	19(1) 	16(1)	15(1) 	0(1)	4(1) 	(2(1)

C12	19(1) 	18(1)	19(1) 	0(1)	4(1) 	(2(1)

C13	26(1) 	32(1)	26(1) 	5(1)	4(1) 	(9(1)

C14	38(1) 	29(1)	41(1) 	6(1)	1(1) 	(10(1)

C15	20(1) 	14(1)	18(1) 	(1(1)	1(1) 	(1(1)

C16	20(1) 	22(1)	22(1) 	1(1)	2(1) 	0(1)

C17	19(1) 	26(1)	31(1) 	0(1)	(4(1) 	1(1)

C18	33(1) 	28(1)	22(1) 	(1(1)	(6(1) 	4(1)

C19	33(1) 	38(1)	18(1) 	5(1)	4(1) 	4(1)

C20	23(1) 	28(1)	19(1) 	(1(1)	4(1) 	4(1)

C21	19(1) 	14(1)	21(1) 	(1(1)	3(1) 	(2(1)

C22	22(1) 	21(1)	27(1) 	(5(1)	0(1) 	(1(1)

C23	24(1) 	22(1)	42(1) 	(14(1)	1(1) 	(3(1)

C24	24(1) 	16(1)	54(1) 	(1(1)	6(1) 	(2(1)

C25	25(1) 	20(1)	41(1) 	10(1)	4(1) 	1(1)

C26	24(1) 	23(1)	25(1) 	4(1)	1(1) 	(1(1)

C27	18(1) 	16(1)	11(1) 	(2(1)	1(1) 	(2(1)

C28	23(1) 	16(1)	18(1) 	(2(1)	(1(1) 	2(1)

C29	16(1) 	24(1)	24(1) 	(2(1)	0(1) 	1(1)

C30	19(1) 	23(1)	21(1) 	(1(1)	3(1) 	(6(1)

C31	25(1) 	14(1)	26(1) 	(1(1)	1(1) 	(1(1)

C32	17(1) 	17(1)	25(1) 	(1(1)	3(1) 	2(1)

N1	22(1) 	38(1)	25(1) 	2(1)	1(1) 	0(1)

O1	26(1) 	25(1)	24(1) 	(2(1)	(5(1) 	(1(1)

O2	18(1) 	28(1)	23(1) 	(4(1)	(1(1) 	1(1)

O3	27(1) 	23(1)	22(1) 	(3(1)	2(1) 	(8(1)

O4	32(1) 	26(1)	19(1) 	1(1)	7(1) 	(14(1)

P1	17(1) 	13(1)	14(1) 	(1(1)	2(1) 	(1(1)

Table 5. Hydrogen coordinates [( 104] and isotropic displacement parameters [Å2 ( 103].

Atom 	x	y	z	Ueq	S.o.f.

H2	9401	5243	121	30	1

H3	10833	4395	459	33	1

H4	11490	4351	2040	32	1

H5	10777	5252	3263	26	1

H10	8625	7170	4743	20	1

H13A	12107	9004	3666	33	1

H13B	12088	9320	4787	33	1

H14A	10949	10192	3282	53	1

H14B	11942	10622	3749	53	1

H14C	10964	10517	4398	53	1

H16	11075	7756	6960	26	1

H17	11868	7147	8345	30	1

H18	10945	6792	9728	33	1

H19	9241	7089	9765	35	1

H20	8431	7693	8385	28	1

H22	9014	9532	8037	28	1

H23	8772	11143	8089	35	1

H24	8319	11944	6677	37	1

H25	8064	11153	5213	34	1

H26	8325	9546	5146	29	1

H28	6848	8508	6499	23	1

H29	5459	7531	6529	26	1

H30	5651	5924	6496	25	1

H31	7246	5270	6463	26	1

H32	8647	6231	6481	24	1

H1	8072	6362	1789	38	1

Table 6. Hydrogen bonds [Å and °].

D(H···A	d(D(H)	d(H···A)	d(D···A)	((DHA)

O1(H1...O2	0.84	1.86	2.5726(17)	141.8

Symmetry transformations used to generate equivalent atoms: