|  | University of Southampton · School of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	2005src0502    (GM978)

Empirical formula 	C21H27NO4

Formula weight 	357.44

Temperature 	150(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	P21/c

Unit cell dimensions	a = 14.5879(19) Å	( = 90°

b = 10.4825(9) Å	( = 91.815(16)°

c = 12.641(2) Å	(  = 90°

Volume	1932.1(5) Å3

Z	4

Density (calculated)	1.229 Mg / m3

Absorption coefficient	0.084 mm(1

F(000)	768

Crystal	plate; colourless

Crystal size	0.34 ( 0.30 ( 0.01 mm3

( range for data collection	2.91 ( 27.50°

Index ranges	(15 ( h ( 18, (11 ( k ( 12, (14 ( l ( 16

Reflections collected	18917

Independent reflections	4288 [Rint = 0.0757]

Completeness to ( = 27.50°	96.6 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9992 and 0.9719

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	4288 / 0 / 246

Goodness-of-fit on F2	1.032

Final R indices [F2 > 2((F2)]	R1 = 0.0615, wR2 = 0.1343

R indices (all data)	R1 = 0.1023, wR2 = 0.1516

Extinction coefficient	0.005(2)

Largest diff. peak and hole	0.289 and (0.196 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SORTAV (R. H. Blessing, Acta Cryst. A51 (1995) 33(37; R. H. Blessing, J. Appl. Cryst. 30 (1997) 421(426). Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: Cameron - A Molecular Graphics Package. (D. M. Watkin, L. Pearce and C. K. Prout, Chemical Crystallography Laboratory, University of Oxford, 1993).

Special details:

Chirality: C8 = R

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	5087(2)	4528(2)	1624(2)	39(1)	1

C2	6410(2)	3201(2)	1887(2)	31(1)	1

C3	6105(2)	2729(2)	2843(2)	32(1)	1

C4	6652(2)	1845(2)	3402(2)	30(1)	1

C5	7481(1)	1433(2)	3036(2)	26(1)	1

C6	7781(2)	1940(2)	2098(2)	30(1)	1

C7	7255(2)	2819(2)	1531(2)	32(1)	1

C8	8029(1)	398(2)	3620(2)	28(1)	1

C9	9063(2)	615(2)	3631(2)	28(1)	1

C10	9654(2)	(142(2)	3062(2)	33(1)	1

C11	10590(2)	71(2)	3133(2)	36(1)	1

C12	10956(2)	1023(2)	3776(2)	32(1)	1

C13	10385(2)	1796(2)	4359(2)	26(1)	1

C14	9441(1)	1590(2)	4262(2)	26(1)	1

C15	8668(2)	3573(2)	4461(2)	34(1)	1

C16	10743(2)	2803(2)	5129(2)	31(1)	1

C17	12277(2)	3435(2)	4643(2)	26(1)	1

C18	13315(2)	3396(2)	4891(2)	29(1)	1

C19	13669(2)	2098(2)	4520(2)	43(1)	1

C20	13535(2)	3575(2)	6072(2)	40(1)	1

C21	13772(2)	4458(3)	4265(2)	48(1)	1

N1	11734(1)	2813(2)	5301(2)	29(1)	1

O1	5927(1)	4039(2)	1247(1)	41(1)	1

O2	7771(1)	(830(1)	3219(1)	34(1)	1

O3	8860(1)	2317(1)	4866(1)	28(1)	1

O4	11945(1)	4020(1)	3873(1)	32(1)	1

Table 3. Bond lengths [Å] and angles [°].

C1(O1	1.423(3)

C2(O1	1.374(3)

C2(C7	1.385(3)

C2(C3	1.392(3)

C3(C4	1.399(3)

C4(C5	1.378(3)

C5(C6	1.383(3)

C5(C8	1.525(3)

C6(C7	1.384(3)

C8(O2	1.429(3)

C8(C9	1.526(3)

C9(C10	1.389(3)

C9(C14	1.398(3)

C10(C11	1.384(3)

C11(C12	1.384(3)

C12(C13	1.389(3)

C13(C14	1.396(3)

C13(C16	1.517(3)

C14(O3	1.387(2)

C15(O3	1.437(3)

C16(N1	1.455(3)

C17(O4	1.236(3)

C17(N1	1.337(3)

C17(C18	1.536(3)

C18(C20	1.529(3)

C18(C21	1.531(3)

C18(C19	1.534(3)

O1(C2(C7	116.0(2)

O1(C2(C3	124.5(2)

C7(C2(C3	119.5(2)

C2(C3(C4	118.8(2)

C5(C4(C3	122.0(2)

C4(C5(C6	118.2(2)

C4(C5(C8	120.88(19)

C6(C5(C8	120.89(19)

C5(C6(C7	121.0(2)

C6(C7(C2	120.5(2)

O2(C8(C5	109.94(17)

O2(C8(C9	112.76(17)

C5(C8(C9	113.67(17)

C10(C9(C14	118.3(2)

C10(C9(C8	122.6(2)

C14(C9(C8	119.09(19)

C11(C10(C9	120.1(2)

C12(C11(C10	121.1(2)

C11(C12(C13	120.4(2)

C12(C13(C14	118.0(2)

C12(C13(C16	123.1(2)

C14(C13(C16	118.82(19)

O3(C14(C13	119.03(19)

O3(C14(C9	118.59(19)

C13(C14(C9	122.22(19)

N1(C16(C13	114.88(18)

O4(C17(N1	120.4(2)

O4(C17(C18	122.21(19)

N1(C17(C18	117.35(19)

C20(C18(C21	109.5(2)

C20(C18(C19	110.18(19)

C21(C18(C19	109.3(2)

C20(C18(C17	111.82(19)

C21(C18(C17	108.53(18)

C19(C18(C17	107.45(18)

C17(N1(C16	121.11(19)

C2(O1(C1	117.66(19)

C14(O3(C15	115.03(16)

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	33(1) 	35(1)	48(2) 	(6(1)	1(1) 	5(1)

C2	32(1) 	26(1)	36(1) 	(1(1)	2(1) 	0(1)

C3	28(1) 	33(1)	35(1) 	(4(1)	6(1) 	(2(1)

C4	28(1) 	33(1)	28(1) 	(1(1)	5(1) 	(7(1)

C5	29(1) 	24(1)	27(1) 	(4(1)	1(1) 	(6(1)

C6	30(1) 	29(1)	31(1) 	(1(1)	6(1) 	1(1)

C7	35(1) 	30(1)	33(1) 	3(1)	10(1) 	1(1)

C8	29(1) 	27(1)	27(1) 	(2(1)	1(1) 	(4(1)

C9	31(1) 	27(1)	24(1) 	2(1)	1(1) 	1(1)

C10	39(1) 	31(1)	29(1) 	(7(1)	(2(1) 	1(1)

C11	36(1) 	39(1)	34(1) 	(9(1)	5(1) 	6(1)

C12	29(1) 	35(1)	34(1) 	(3(1)	(1(1) 	2(1)

C13	30(1) 	24(1)	25(1) 	0(1)	(1(1) 	0(1)

C14	30(1) 	25(1)	23(1) 	1(1)	3(1) 	1(1)

C15	37(1) 	25(1)	39(1) 	(1(1)	6(1) 	1(1)

C16	29(1) 	31(1)	32(1) 	(4(1)	3(1) 	(3(1)

C17	31(1) 	22(1)	24(1) 	(4(1)	(2(1) 	(1(1)

C18	28(1) 	28(1)	32(1) 	2(1)	(2(1) 	1(1)

C19	35(1) 	46(2)	47(2) 	(11(1)	(1(1) 	7(1)

C20	36(1) 	44(2)	38(2) 	(4(1)	(8(1) 	(2(1)

C21	33(1) 	54(2)	57(2) 	22(1)	(4(1) 	(9(1)

N1	29(1) 	29(1)	28(1) 	3(1)	(4(1) 	(3(1)

O1	38(1) 	39(1)	46(1) 	9(1)	10(1) 	12(1)

O2	44(1) 	29(1)	27(1) 	0(1)	(3(1) 	(7(1)

O3	31(1) 	26(1)	28(1) 	(2(1)	7(1) 	1(1)

O4	36(1) 	31(1)	29(1) 	6(1)	(4(1) 	2(1)