|  | University of Southampton · Department of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	01SOT020

Empirical formula 	C23H26O8

Formula weight 	430.44

Temperature 	150(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	P21/n

Unit cell dimensions	a = 11.839(2) Å

b = 8.0773(10) Å	( = 91.84(3)°

c = 22.695(4) Å

Volume	2169.1(6) Å3

Z	4

Density (calculated)	1.318 Mg / m3

Absorption coefficient	0.100 mm(1

F(000)	912

Crystal	Colourless block

Crystal size	0.10 ( 0.10 ( 0.10 mm3

( range for data collection	3.05 ( 23.25°

Index ranges	(13 ( h ( 13, (8 ( k ( 8, (25 ( l ( 25

Reflections collected	13956

Independent reflections	2999 [Rint = 0.3615]

Completeness to ( = 23.25°	96.7 %

Max. and min. transmission	0.9901 and 0.9901

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	2999 / 0 / 281

Goodness-of-fit on F2	0.811

Final R indices [F2 > 2((F2)]	R1 = 0.0864, wR2 = 0.2145

R indices (all data)	R1 = 0.2721, wR2 = 0.3345

Extinction coefficient	0.005(3)

Largest diff. peak and hole	0.397 and (0.275 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill Ewald sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SORTAV (R. H. Blessing, Acta Cryst. A51 (1995) 33(37; R. H. Blessing, J. Appl. Cryst. 30 (1997) 421(426). Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: Cameron - A Molecular Graphics Package. (D. M. Watkin, L. Pearce and C. K. Prout, Chemical Crystallography Laboratory, University of Oxford, 1993).

Special details:  All hydrogen atoms were placed in idealised positions and refined using a riding model.

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	859(9)	3696(13)	602(5)	79(3)	1

C2	1774(15)	9100(20)	(272(10)	199(11)	1

C3	4607(14)	10700(16)	764(6)	150(7)	1

C4	2729(7)	5250(12)	1148(4)	50(3)	1

C5	2191(8)	5965(13)	668(4)	56(3)	1

C6	2495(11)	7514(15)	457(5)	91(4)	1

C7	3373(11)	8360(15)	754(5)	78(4)	1

C8	3924(8)	7692(13)	1245(5)	57(3)	1

C9	3603(7)	6112(12)	1432(4)	49(3)	1

C10	4171(7)	5431(11)	2002(4)	52(3)	1

C11	4271(7)	2760(14)	2384(5)	49(3)	1

C12	3704(7)	3793(12)	2854(4)	51(3)	1

C13	4501(8)	4393(14)	3378(5)	59(3)	1

C14	3720(8)	6745(13)	2974(4)	68(3)	1

C15	3380(7)	5391(13)	2529(4)	54(3)	1

C16	5580(8)	3500(12)	3478(4)	50(3)	1

C17	5734(9)	2389(13)	3942(4)	61(3)	1

C18	6743(8)	1513(12)	4042(5)	55(3)	1

C19	7611(7)	1771(12)	3676(5)	54(3)	1

C20	7496(8)	2892(13)	3197(4)	53(3)	1

C21	6506(8)	3757(12)	3113(4)	53(3)	1

C22	8290(8)	3968(13)	2333(5)	78(4)	1

C23	8817(9)	14(17)	4252(6)	120(6)	1

O1	1307(6)	5206(9)	360(3)	67(2)	1

O2	1940(14)	8101(16)	(14(5)	225(9)	1

O3	3652(9)	9851(11)	520(3)	134(4)	1

O4	4454(4)	3710(9)	1900(3)	54(2)	1

O5	4442(5)	1297(9)	2388(3)	56(2)	1

O6	4720(5)	6101(9)	3259(3)	65(2)	1

O7	8423(5)	2937(8)	2851(3)	63(2)	1

O8	8626(5)	989(8)	3730(3)	75(2)	1

Table 3. Bond lengths [Å] and angles [°].

C1(O1	1.446(11)

C2(O2	1.010(14)

C3(O3	1.420(13)

C4(C5	1.372(12)

C4(C9	1.388(12)

C5(O1	1.383(10)

C5(C6	1.391(13)

C6(O2	1.325(14)

C6(C7	1.399(14)

C7(O3	1.360(12)

C7(C8	1.383(13)

C8(C9	1.401(12)

C9(C10	1.540(13)

C10(O4	1.450(10)

C10(C15	1.542(13)

C11(O5	1.199(10)

C11(O4	1.363(11)

C11(C12	1.526(13)

C12(C15	1.530(13)

C12(C13	1.571(12)

C13(O6	1.431(10)

C13(C16	1.478(12)

C14(O6	1.430(10)

C14(C15	1.534(12)

C16(C17	1.392(12)

C16(C21	1.410(12)

C17(C18	1.401(12)

C18(C19	1.358(12)

C19(O8	1.360(10)

C19(C20	1.417(12)

C20(O7	1.371(10)

C20(C21	1.373(12)

C22(O7	1.446(10)

C23(O8	1.434(11)

C5(C4(C9	118.6(10)

C4(C5(O1	122.7(9)

C4(C5(C6	122.2(10)

O1(C5(C6	115.2(9)

O2(C6(C5	118.2(11)

O2(C6(C7	123.7(11)

C5(C6(C7	118.1(11)

O3(C7(C8	123.1(11)

O3(C7(C6	115.5(11)

C8(C7(C6	121.4(11)

C7(C8(C9	118.3(10)

C4(C9(C8	121.4(10)

C4(C9(C10	120.7(9)

C8(C9(C10	117.7(9)

O4(C10(C9	107.7(8)

O4(C10(C15	104.7(7)

C9(C10(C15	113.4(8)

O5(C11(O4	122.0(10)

O5(C11(C12	127.7(10)

O4(C11(C12	109.9(9)

C11(C12(C15	103.5(8)

C11(C12(C13	115.5(7)

C15(C12(C13	103.9(8)

O6(C13(C16	109.8(8)

O6(C13(C12	105.2(8)

C16(C13(C12	117.4(9)

O6(C14(C15	103.6(7)

C12(C15(C14	103.2(8)

C12(C15(C10	104.0(7)

C14(C15(C10	110.0(8)

C17(C16(C21	117.0(9)

C17(C16(C13	121.5(9)

C21(C16(C13	121.5(10)

C16(C17(C18	122.5(10)

C19(C18(C17	118.8(10)

C18(C19(O8	123.8(10)

C18(C19(C20	120.7(9)

O8(C19(C20	115.4(9)

O7(C20(C21	127.1(10)

O7(C20(C19	113.4(9)

C21(C20(C19	119.5(9)

C20(C21(C16	121.3(10)

C5(O1(C1	117.6(7)

C2(O2(C6	146.7(17)

C7(O3(C3	118.4(10)

C11(O4(C10	111.5(8)

C14(O6(C13	106.5(8)

C20(O7(C22	114.4(7)

C19(O8(C23	116.4(8)

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	95(8) 	66(8)	73(8) 	13(7)	(28(6) 	(11(7)

C2	158(15) 	170(20)	260(30) 	144(18)	(99(15) 	(60(14)

C3	236(17) 	118(13)	95(11) 	1(9)	1(11) 	(144(13)

C4	51(6) 	47(6)	53(7) 	(9(6)	11(5) 	(8(5)

C5	71(7) 	57(8)	40(7) 	5(6)	(7(6) 	(18(6)

C6	153(12) 	73(9)	43(8) 	25(7)	(25(8) 	(55(9)

C7	131(11) 	67(9)	37(7) 	17(7)	0(7) 	(23(8)

C8	53(6) 	51(7)	68(8) 	(14(6)	19(6) 	(18(5)

C9	38(6) 	49(7)	59(7) 	(11(6)	6(5) 	(3(5)

C10	43(6) 	30(6)	83(8) 	(22(5)	(3(6) 	(2(5)

C11	33(6) 	46(7)	68(8) 	(3(7)	(9(5) 	(9(5)

C12	43(6) 	55(7)	55(7) 	(7(6)	4(5) 	3(5)

C13	43(6) 	73(9)	61(8) 	(7(6)	(8(5) 	(2(6)

C14	67(7) 	79(9)	58(7) 	(15(6)	(13(6) 	31(6)

C15	42(6) 	68(8)	51(7) 	(19(6)	7(5) 	7(5)

C16	46(6) 	57(7)	46(7) 	(14(6)	(8(5) 	(1(6)

C17	63(7) 	73(8)	47(7) 	(14(6)	8(5) 	5(6)

C18	42(6) 	55(7)	69(8) 	(2(6)	(1(5) 	2(6)

C19	30(6) 	44(7)	88(9) 	3(6)	6(6) 	12(5)

C20	46(6) 	62(7)	53(7) 	2(6)	4(5) 	(7(6)

C21	47(6) 	42(6)	69(8) 	(14(6)	(17(6) 	0(6)

C22	56(7) 	79(9)	101(10) 	44(7)	12(6) 	2(6)

C23	69(8) 	165(14)	129(12) 	107(11)	37(8) 	52(8)

O1	97(5) 	66(5)	38(4) 	8(4)	(19(4) 	(21(4)

O2	400(20) 	159(12)	105(9) 	99(9)	(153(11) 	(165(13)

O3	239(11) 	102(7)	60(6) 	29(5)	(23(6) 	(90(8)

O4	46(4) 	62(5)	54(5) 	(12(4)	7(3) 	1(3)

O5	54(4) 	49(5)	66(5) 	(7(4)	(3(3) 	(3(4)

O6	51(4) 	79(6)	64(5) 	(26(4)	(18(3) 	13(4)

O7	40(4) 	63(5)	88(6) 	31(4)	5(4) 	6(3)

O8	43(4) 	85(6)	99(6) 	43(5)	22(4) 	15(4)

Table 5. Hydrogen coordinates [( 104] and isotropic displacement parameters [Å2 ( 103].

Atom 	x	y	z	Ueq	S.o.f.

H1A	236	3293	346	118	1

H1B	581	3916	997	118	1

H1C	1456	2857	628	118	1

H2A	1214	8795	(581	298	1

H2B	2470	9464	(454	298	1

H2C	1474	9993	(32	298	1

H3A	4704	11750	555	225	1

H3B	5283	10015	723	225	1

H3C	4493	10922	1183	225	1

H4	2509	4188	1283	60	1

H8	4506	8288	1450	68	1

H10	4869	6079	2106	62	1

H12	3021	3219	3002	61	1

H13	4069	4328	3749	71	1

H14A	3877	7803	2771	82	1

H14B	3118	6928	3260	82	1

H15	2562	5435	2406	65	1

H17	5131	2218	4202	73	1

H18	6819	751	4360	66	1

H21	6443	4543	2802	63	1

H22A	8984	3933	2110	117	1

H22B	8140	5111	2453	117	1

H22C	7656	3560	2086	117	1

H23A	9574	(475	4248	180	1

H23B	8251	(869	4264	180	1

H23C	8755	721	4601	180	1