|  | University of Southampton · Department of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	02src183

Empirical formula 	C8H10Cl2N2

Formula weight 	205.08

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	P21/c

Unit cell dimensions	a = 3.9283(10) Å	( = 90°

b = 18.273(4) Å	( = 97.462(10)°

c = 11.990(3) Å	(  = 90°

Volume	853.4(4) Å3

Z	4

Density (calculated)	1.596 Mg / m3

Absorption coefficient	0.700 mm(1

F(000)	424

Crystal	Needle; Colourless

Crystal size	0.18 ( 0.05 ( 0.05 mm3

( range for data collection	3.43 ( 25.03°

Index ranges	(4 ( h ( 4, (18 ( k ( 21, (12 ( l ( 12

Reflections collected	2747

Independent reflections	1192 [Rint = 0.0673]

Completeness to ( = 25.03°	79.2 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9658 and 0.8843

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	1192 / 0 / 109

Goodness-of-fit on F2	1.040

Final R indices [F2 > 2((F2)]	R1 = 0.0585, wR2 = 0.1098

R indices (all data)	R1 = 0.1208, wR2 = 0.1295

Largest diff. peak and hole	0.317 and (0.320 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SORTAV (R. H. Blessing, Acta Cryst. A51 (1995) 33(37; R. H. Blessing, J. Appl. Cryst. 30 (1997) 421(426). Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: Cameron - A Molecular Graphics Package. (D. M. Watkin, L. Pearce and C. K. Prout, Chemical Crystallography Laboratory, University of Oxford, 1993).

Special details:

All Hydrogen atoms were fixed.

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

Cl1	677(3)	7277(1)	2188(1)	38(1)	1

Cl2	5263(4)	8096(1)	4351(1)	43(1)	1

N2	896(10)	4897(2)	3285(4)	29(1)	1

C2	4351(14)	7176(3)	4241(5)	28(2)	1

C6	(1205(13)	5652(3)	1737(4)	30(2)	1

C4	4215(13)	5916(3)	4651(4)	31(2)	1

C3	5651(13)	6651(3)	5140(5)	32(2)	1

C7	(2264(13)	4867(3)	1410(5)	34(2)	1

N1	2285(10)	6104(2)	3541(4)	30(1)	1

C5	724(12)	5552(3)	2891(5)	27(1)	1

C1	2549(12)	6856(3)	3380(4)	29(2)	1

C8	(965(13)	4408(3)	2456(5)	35(2)	1

Table 3. Bond lengths [Å] and angles [°].

Cl1(C1	1.703(5)

Cl2(C2	1.720(5)

N2(C5	1.285(6)

N2(C8	1.461(6)

C2(C1	1.311(7)

C2(C3	1.483(7)

C6(C5	1.500(7)

C6(C7	1.529(7)

C4(N1	1.484(6)

C4(C3	1.543(7)

C7(C8	1.540(7)

N1(C5	1.370(6)

N1(C1	1.395(6)

C5(N2(C8	108.8(4)

C1(C2(C3	112.6(4)

C1(C2(Cl2	125.6(4)

C3(C2(Cl2	121.9(4)

C5(C6(C7	102.1(4)

N1(C4(C3	105.0(4)

C2(C3(C4	102.3(4)

C6(C7(C8	104.6(4)

C5(N1(C1	133.1(5)

C5(N1(C4	118.6(4)

C1(N1(C4	108.3(4)

N2(C5(N1	118.5(5)

N2(C5(C6	116.7(5)

N1(C5(C6	124.8(5)

C2(C1(N1	111.9(4)

C2(C1(Cl1	126.2(4)

N1(C1(Cl1	122.0(4)

N2(C8(C7	107.7(4)

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

Cl1	42(1) 	30(1)	39(1) 	6(1)	(2(1) 	0(1)

Cl2	49(1) 	26(1)	50(1) 	1(1)	(4(1) 	(5(1)

N2	26(3) 	25(3)	37(4) 	1(2)	4(2) 	(3(2)

C2	32(3) 	24(3)	28(4) 	5(3)	3(3) 	3(2)

C6	28(3) 	33(3)	29(4) 	2(3)	5(3) 	5(3)

C4	27(3) 	32(3)	31(4) 	7(3)	(4(3) 	3(2)

C3	27(3) 	32(3)	35(4) 	(5(3)	1(3) 	3(3)

C7	32(3) 	39(4)	30(4) 	(8(3)	2(3) 	(3(3)

N1	38(3) 	20(3)	31(3) 	0(2)	(1(2) 	(2(2)

C5	22(3) 	34(4)	27(4) 	(4(3)	7(3) 	1(3)

C1	26(3) 	35(3)	24(4) 	4(3)	(2(3) 	2(3)

C8	27(3) 	34(3)	43(4) 	(2(3)	1(3) 	(5(3)