|  | University of Southampton · School of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	2005src1160  (SeF2)

Empirical formula 	C26H32F2Se2

Formula weight 	540.44

Temperature 	121(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	P21/n

Unit cell dimensions	a = 11.3155(4) Å	( = 90°

b = 5.41330(10) Å	( = 91.099(2)°

c = 19.0117(7) Å	(  = 90°

Volume	1164.33(6) Å3

Z	2

Density (calculated)	1.542 Mg / m3

Absorption coefficient	3.202 mm(1

F(000)	548

Crystal	blade; pale yellow

Crystal size	0.38 ( 0.08 ( 0.02 mm3

( range for data collection	3.60 ( 27.49°

Index ranges	(14 ( h ( 14, (7 ( k ( 6, (24 ( l ( 24

Reflections collected	14057

Independent reflections	2665 [Rint = 0.0517]

Completeness to ( = 27.49°	99.7 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9387 and 0.3758

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	2665 / 0 / 137

Goodness-of-fit on F2	1.042

Final R indices [F2 > 2((F2)]	R1 = 0.0307, wR2 = 0.0717

R indices (all data)	R1 = 0.0403, wR2 = 0.0760

Largest diff. peak and hole	0.519 and (0.577 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SORTAV (R. H. Blessing, Acta Cryst. A51 (1995) 33(37; R. H. Blessing, J. Appl. Cryst. 30 (1997) 421(426). Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: Cameron - A Molecular Graphics Package. (D. M. Watkin, L. Pearce and C. K. Prout, Chemical Crystallography Laboratory, University of Oxford, 1993).

Special details:

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	4132(2)	6416(4)	4679(1)	21(1)	1

C2	4672(2)	4521(4)	4332(1)	21(1)	1

C3	5555(2)	3026(4)	4622(1)	19(1)	1

C4	6133(2)	1008(4)	4242(1)	19(1)	1

C5	7004(2)	(511(4)	4494(1)	19(1)	1

C6	7444(2)	(2335(4)	4023(1)	19(1)	1

C7	6911(2)	(2255(4)	3373(1)	24(1)	1

C8	8415(2)	(4087(4)	4247(1)	20(1)	1

C9	8843(2)	(5835(4)	3677(1)	20(1)	1

C10	9885(2)	(7419(4)	3927(1)	21(1)	1

C11	10324(2)	(9195(4)	3368(1)	21(1)	1

C12	11429(2)	(10609(4)	3600(1)	24(1)	1

C13	11836(2)	(12484(4)	3056(1)	26(1)	1

F1	4301(1)	4084(3)	3658(1)	32(1)	1

Se1	5761(1)	184(1)	3302(1)	23(1)	1

Table 3. Bond lengths [Å] and angles [°].

C1(C2	1.369(3)

C1(C3i	1.403(3)

C2(F1	1.361(2)

C2(C3	1.392(3)

C3(C1i	1.403(3)

C3(C4	1.470(3)

C4(C5	1.363(3)

C4(Se1	1.880(2)

C5(C6	1.430(3)

C6(C7	1.364(3)

C6(C8	1.507(3)

C7(Se1	1.857(2)

C8(C9	1.524(3)

C9(C10	1.527(3)

C10(C11	1.524(3)

C11(C12	1.524(3)

C12(C13	1.528(3)

C2(C1(C3i	120.8(2)

F1(C2(C1	116.82(19)

F1(C2(C3	118.5(2)

C1(C2(C3	124.7(2)

C2(C3(C1i	114.6(2)

C2(C3(C4	124.12(19)

C1i(C3(C4	121.30(19)

C5(C4(C3	126.91(19)

C5(C4(Se1	109.76(16)

C3(C4(Se1	123.33(15)

C4(C5(C6	117.0(2)

C7(C6(C5	113.10(19)

C7(C6(C8	125.66(19)

C5(C6(C8	121.23(19)

C6(C7(Se1	112.62(16)

C6(C8(C9	115.44(18)

C8(C9(C10	112.39(18)

C11(C10(C9	113.36(18)

C12(C11(C10	112.99(18)

C11(C12(C13	113.17(18)

C7(Se1(C4	87.50(9)

Symmetry transformations used to generate equivalent atoms:

(i) (x+1,(y+1,(z+1

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	21(1) 	25(1)	17(1) 	0(1)	(1(1) 	6(1)

C2	22(1) 	28(1)	12(1) 	(3(1)	(2(1) 	4(1)

C3	18(1) 	23(1)	15(1) 	(1(1)	1(1) 	1(1)

C4	20(1) 	22(1)	14(1) 	0(1)	2(1) 	1(1)

C5	19(1) 	24(1)	14(1) 	(1(1)	(1(1) 	2(1)

C6	21(1) 	18(1)	18(1) 	(1(1)	3(1) 	1(1)

C7	29(1) 	24(1)	18(1) 	(3(1)	1(1) 	6(1)

C8	24(1) 	22(1)	16(1) 	(1(1)	2(1) 	4(1)

C9	23(1) 	21(1)	16(1) 	(1(1)	1(1) 	3(1)

C10	24(1) 	21(1)	17(1) 	(1(1)	1(1) 	5(1)

C11	23(1) 	21(1)	21(1) 	(1(1)	0(1) 	3(1)

C12	24(1) 	26(1)	21(1) 	(2(1)	(2(1) 	6(1)

C13	25(1) 	27(1)	26(1) 	(1(1)	0(1) 	7(1)

F1	37(1) 	41(1)	18(1) 	(8(1)	(8(1) 	16(1)

Se1	27(1) 	28(1)	14(1) 	(4(1)	(3(1) 	9(1)