|  | University of Southampton · School of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	2005src1310 / PM004

Empirical formula 	C38H22CoN10NiS4

Formula weight 	864.54

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	C2

Unit cell dimensions	a = 34.2891(18) Å	( = 90°

b = 23.6591(13) Å	( = 97.920(2)°

c = 17.9551(10) Å	(  = 90°

Volume	14427.1(14) Å3

Z	16

Density (calculated)	1.592 Mg / m3

Absorption coefficient	1.259 mm(1

F(000)	7024

Crystal	Slab; Opaque Dark Red

Crystal size	0.20 ( 0.16 ( 0.08 mm3

( range for data collection	3.22 ( 27.48°

Index ranges	(44 ( h ( 37, (29 ( k ( 30, (21 ( l ( 23

Reflections collected	80809

Independent reflections	29975 [Rint = 0.0741]

Completeness to ( = 27.48°	96.0 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9060 and 0.7868

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	29975 / 3444 / 2414

Goodness-of-fit on F2	1.029

Final R indices [F2 > 2((F2)]	R1 = 0.0645, wR2 = 0.1206

R indices (all data)	R1 = 0.1699, wR2 = 0.1613

Absolute structure parameter	0.48(2)

Largest diff. peak and hole	0.715 and (0.784 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SADABS Version 2.10. (G. M. Sheldrick (2003)) Bruker AXS Inc., Madison, Wisconsin, USA. Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: ORTEP3 for Windows (L. J. Farrugia, J. Appl. Crystallogr. 1997, 30, 565).

Special details:

All hydrogen atoms were fixed.

Three of the four nickel (mnt) salts were disordered over 2 main sites each.

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	5384(4)	3477(6)	1034(6)	40(2)	1

C2	5536(4)	3626(7)	384(7)	53(3)	1

C3	5562(4)	4188(7)	156(6)	50(3)	1

C4	5459(3)	4592(6)	627(6)	42(3)	1

C5	5306(4)	4424(6)	1302(5)	32(2)	1

C6	5189(3)	4844(6)	1828(5)	32(2)	1

C7	5203(3)	5404(5)	1767(5)	36(2)	1

C8	5073(3)	5760(5)	2337(6)	36(2)	1

C9	4926(3)	5503(6)	2962(6)	37(2)	1

C10	4915(4)	4923(5)	2981(6)	33(2)	1

C11	4777(3)	4579(5)	3557(5)	29(2)	1

C12	4600(4)	4833(5)	4140(6)	37(2)	1

C13	4473(3)	4496(5)	4699(6)	40(2)	1

C14	4484(4)	3896(6)	4601(6)	40(2)	1

C15	4653(4)	3680(6)	3973(6)	43(3)	1

C16	5829(4)	3952(6)	3533(6)	40(2)	1

C17	6156(4)	3821(6)	4017(7)	47(3)	1

C18	6227(4)	3279(6)	4195(7)	44(3)	1

C19	5982(3)	2841(6)	3817(6)	34(2)	1

C20	5661(3)	3021(5)	3353(6)	32(2)	1

C21	5369(4)	2627(6)	2933(6)	34(2)	1

C22	5433(3)	2053(5)	2859(6)	32(2)	1

C23	5150(3)	1738(5)	2413(6)	36(2)	1

C24	4827(3)	2000(5)	2019(6)	30(2)	1

C25	4787(3)	2591(5)	2105(6)	28(2)	1

C26	4444(4)	2950(5)	1729(6)	31(2)	1

C27	4132(3)	2703(5)	1259(6)	34(2)	1

C28	3840(4)	3108(6)	983(6)	40(3)	1

C29	3864(4)	3663(6)	1188(6)	41(2)	1

C30	4192(3)	3839(6)	1683(6)	35(2)	1

N1	5272(3)	3878(5)	1496(5)	34(2)	1

N2	5035(3)	4584(4)	2413(5)	35(2)	1

N3	4786(3)	4029(5)	3490(5)	34(2)	1

N16	5597(3)	3582(4)	3217(5)	34(2)	1

N17	5059(3)	2895(4)	2525(5)	31(2)	1

N18	4473(3)	3500(4)	1925(5)	32(2)	1

Co1	5035(1)	3742(1)	2522(1)	31(1)	1

C31	3326(3)	1916(5)	7294(6)	33(2)	1

C32	3655(3)	2075(5)	7783(6)	35(2)	1

C33	3716(4)	2653(6)	7932(6)	42(3)	1

C34	3460(4)	3024(5)	7636(6)	39(2)	1

C35	3131(4)	2862(5)	7100(6)	35(2)	1

C36	2856(4)	3241(5)	6664(7)	37(2)	1

C37	2890(4)	3827(5)	6660(7)	55(3)	1

C38	2594(4)	4118(6)	6198(7)	61(3)	1

C39	2271(4)	3857(5)	5824(7)	56(3)	1

C40	2243(4)	3281(5)	5879(7)	43(2)	1

C41	1927(4)	2939(5)	5507(6)	34(2)	1

C42	1598(4)	3125(5)	4999(6)	40(2)	1

C43	1305(4)	2799(6)	4693(6)	44(3)	1

C44	1333(3)	2222(6)	4861(6)	42(2)	1

C45	1653(3)	2028(6)	5329(6)	40(2)	1

C46	2836(3)	2374(6)	4801(6)	39(2)	1

C47	2996(4)	2258(6)	4165(7)	47(3)	1

C48	3057(4)	1693(6)	4043(6)	51(3)	1

C49	2940(3)	1290(6)	4522(6)	44(3)	1

C50	2790(4)	1446(5)	5136(6)	36(2)	1

C51	2645(4)	1070(4)	5698(6)	33(2)	1

C52	2668(3)	468(5)	5666(6)	42(2)	1

C53	2531(3)	181(6)	6201(7)	48(3)	1

C54	2382(3)	430(5)	6751(7)	46(3)	1

C55	2370(4)	1028(5)	6764(7)	37(2)	1

C56	2208(3)	1367(5)	7358(6)	38(2)	1

C57	2067(4)	1164(6)	7961(7)	51(3)	1

C58	1928(4)	1554(7)	8436(7)	60(3)	1

C59	1983(4)	2102(7)	8363(8)	66(3)	1

C60	2151(4)	2284(6)	7769(7)	47(3)	1

N31	3050(3)	2313(4)	6939(5)	32(2)	1

N32	2532(3)	2982(4)	6302(5)	35(2)	1

N33	1957(3)	2383(4)	5664(5)	32(2)	1

N46	2730(3)	2014(4)	5307(5)	31(2)	1

N47	2505(3)	1312(4)	6251(5)	30(2)	1

N48	2265(3)	1957(4)	7215(5)	39(2)	1

Co2	2503(1)	2143(1)	6281(1)	28(1)	1

C61	3303(3)	2031(5)	2168(6)	36(2)	1

C62	3632(4)	2215(6)	2621(7)	42(2)	1

C63	3665(4)	2783(5)	2836(7)	39(2)	1

C64	3366(3)	3128(5)	2534(6)	36(2)	1

C65	3044(3)	2960(5)	2037(6)	28(2)	1

C66	2737(4)	3317(5)	1677(6)	35(2)	1

C67	2725(4)	3894(5)	1725(7)	47(3)	1

C68	2399(4)	4174(6)	1332(7)	56(3)	1

C69	2119(4)	3881(5)	869(8)	54(3)	1

C70	2134(3)	3292(5)	855(6)	33(2)	1

C71	1856(4)	2916(5)	438(6)	34(2)	1

C72	1534(3)	3093(5)	(128(7)	43(3)	1

C73	1261(4)	2736(5)	(410(6)	39(2)	1

C74	1316(3)	2161(6)	(228(6)	39(2)	1

C75	1641(3)	1985(5)	276(6)	33(2)	1

C76	2838(4)	2262(6)	(260(7)	45(3)	1

C77	2994(4)	2083(6)	(861(8)	54(3)	1

C78	3034(4)	1531(6)	(923(8)	55(3)	1

C79	2897(4)	1153(5)	(453(7)	46(3)	1

C80	2747(3)	1367(5)	147(6)	37(2)	1

C81	2599(3)	1027(4)	756(6)	33(2)	1

C82	2596(3)	440(5)	807(7)	44(2)	1

C83	2454(3)	173(5)	1338(7)	49(3)	1

C84	2318(3)	464(5)	1884(6)	42(2)	1

C85	2335(3)	1073(4)	1856(6)	30(2)	1

C86	2194(3)	1454(5)	2441(6)	31(2)	1

C87	2059(3)	1284(5)	3051(6)	41(2)	1

C88	1932(4)	1688(6)	3540(7)	50(3)	1

C89	1972(4)	2241(6)	3422(7)	48(3)	1

C90	2111(4)	2392(5)	2781(7)	38(2)	1

N61	3000(3)	2400(4)	1851(5)	31(2)	1

N62	2447(3)	3041(4)	1245(5)	30(2)	1

N63	1930(3)	2372(4)	599(5)	32(2)	1

N76	2705(3)	1941(4)	262(5)	36(2)	1

N77	2461(3)	1302(4)	1293(5)	30(2)	1

N78	2230(3)	2021(4)	2288(5)	31(2)	1

Co3	2462(1)	2171(1)	1252(1)	25(1)	1

C91	(356(3)	3565(5)	1432(6)	41(3)	1

C92	(514(4)	3739(6)	2071(6)	50(3)	1

C93	(555(4)	4319(6)	2234(7)	57(3)	1

C94	(444(4)	4703(6)	1740(6)	48(3)	1

C95	(272(3)	4497(5)	1111(5)	35(2)	1

C96	(145(3)	4883(5)	575(6)	33(2)	1

C97	(143(4)	5462(5)	582(7)	47(3)	1

C98	0	5785(8)	0	54(4)	1

C101	821(3)	3948(5)	950(6)	43(2)	1

C102	1149(3)	3788(6)	1451(7)	55(3)	1

C103	1198(3)	3240(5)	1636(6)	47(3)	1

C104	924(3)	2833(5)	1286(5)	37(2)	1

C105	609(3)	3053(4)	806(5)	33(2)	1

C106	292(3)	2674(4)	419(5)	31(2)	1

C107	304(4)	2098(5)	401(7)	58(3)	1

C108	0	1792(8)	0	78(5)	1

N91	(240(3)	3959(4)	977(4)	32(2)	1

N92	0	4599(5)	0	33(3)	1

N101	567(2)	3609(4)	657(4)	31(2)	1

N102	0	2960(5)	0	29(2)	1

Co4	0	3784(1)	0	29(1)	1

C111	362(3)	3567(5)	3536(5)	43(3)	1

C112	521(4)	3740(6)	2883(6)	50(3)	1

C113	544(4)	4331(6)	2721(7)	58(3)	1

C114	425(4)	4697(6)	3229(6)	55(3)	1

C115	266(4)	4492(5)	3878(5)	44(2)	1

C116	135(4)	4872(5)	4432(6)	43(2)	1

C117	138(4)	5449(5)	4403(6)	55(3)	1

C118	0	5768(8)	5000	68(5)	1

C121	(809(3)	3886(5)	4069(6)	39(2)	1

C122	(1140(3)	3746(6)	3579(6)	42(2)	1

C123	(1189(3)	3200(5)	3379(6)	43(3)	1

C124	(917(3)	2779(5)	3692(5)	37(2)	1

C125	(601(3)	2981(4)	4178(6)	35(2)	1

C126	(289(3)	2595(4)	4575(6)	46(3)	1

C127	(300(4)	2014(5)	4565(7)	82(4)	1

C128	0	1720(7)	5000	94(6)	1

N111	244(3)	3941(4)	4014(4)	34(2)	1

N112	0	4558(5)	5000	35(3)	1

N121	(558(2)	3532(4)	4353(5)	32(2)	1

N122	0	2896(5)	5000	39(3)	1

Co5	0	3731(1)	5000	33(1)	1

C201	6515(3)	(341(4)	3652(5)	32(2)	1

C202	6484(3)	146(4)	3250(5)	38(2)	1

C203	5807(3)	1403(4)	5645(5)	31(2)	1

C204	5819(3)	926(4)	6067(5)	30(2)	1

C205	6664(4)	(832(5)	3401(6)	41(2)	1

C206	6637(4)	177(5)	2517(5)	43(3)	1

C207	5618(4)	1910(5)	5874(7)	45(3)	1

C208	5634(4)	882(6)	6728(6)	39(3)	1

N201	6796(4)	(1246(5)	3178(6)	61(3)	1

N202	6775(3)	217(6)	1979(5)	67(4)	1

N203	5458(4)	2305(4)	6050(6)	69(3)	1

N204	5469(3)	840(5)	7243(5)	44(3)	1

S201	6372(1)	(326(1)	4549(1)	28(1)	1

S202	6296(1)	766(1)	3560(2)	39(1)	1

S203	5982(1)	1410(1)	4780(2)	39(1)	1

S204	6043(1)	328(1)	5787(1)	28(1)	1

Ni66	6179(1)	545(1)	4675(1)	27(1)	1

C211	3972(3)	10730(4)	9486(5)	30(2)	0.8980(18)

C212	4015(4)	11197(4)	9930(5)	33(2)	0.8980(18)

C213	3291(4)	10002(4)	12343(6)	33(2)	0.8980(18)

C214	3265(3)	9515(4)	11918(5)	30(2)	0.8980(18)

C215	4134(4)	10670(5)	8834(6)	31(2)	0.8980(18)

C216	4190(4)	11725(5)	9676(6)	32(2)	0.8980(18)

C217	3112(4)	10045(5)	13019(6)	28(2)	0.8980(18)

C218	3072(4)	9037(5)	12157(7)	35(3)	0.8980(18)

N211	4279(3)	10624(5)	8280(5)	41(3)	0.8980(18)

N212	4323(4)	12125(5)	9478(6)	46(3)	0.8980(18)

N213	2952(3)	10086(5)	13543(5)	38(3)	0.8980(18)

N214	2917(3)	8641(4)	12339(7)	49(3)	0.8980(18)

S211	3779(1)	10124(1)	9852(2)	35(1)	0.8980(18)

S212	3870(1)	11221(1)	10821(2)	33(1)	0.8980(18)

S213	3528(1)	10600(1)	12069(2)	30(1)	0.8980(18)

S214	3454(1)	9509(1)	11075(2)	35(1)	0.8980(18)

Ni77	3659(1)	10370(1)	10958(1)	25(1)	0.8980(18)

C311	4190(20)	10890(14)	8800(20)	31(4)	0.1020(18)

C312	4246(16)	11353(12)	9254(19)	31(4)	0.1020(18)

C313	3478(17)	10222(11)	11650(20)	26(3)	0.1020(18)

C314	3460(20)	9721(13)	11250(20)	28(4)	0.1020(18)

C315	4380(30)	10810(20)	8180(40)	31(5)	0.1020(18)

C316	4407(16)	11887(13)	8980(20)	32(5)	0.1020(18)

C317	3292(19)	10281(17)	12310(20)	28(4)	0.1020(18)

C318	3300(20)	9243(13)	11550(30)	31(4)	0.1020(18)

N311	4574(15)	10740(30)	7700(30)	32(9)	0.1020(18)

N312	4601(16)	12262(16)	8900(30)	37(9)	0.1020(18)

N313	3200(20)	10310(30)	12910(20)	38(7)	0.1020(18)

N314	3120(20)	8890(20)	11790(40)	33(7)	0.1020(18)

S311	3963(6)	10302(7)	9141(8)	36(3)	0.1020(18)

S312	4040(8)	11413(6)	10085(11)	28(3)	0.1020(18)

S313	3707(5)	10817(5)	11340(6)	21(3)	0.1020(18)

S314	3612(7)	9714(5)	10369(9)	36(3)	0.1020(18)

Ni37	3831(3)	10563(4)	10230(5)	31(2)	0.1020(18)

C221	1560(7)	(321(6)	6128(8)	38(3)	0.596(9)

C222	1521(6)	174(5)	5746(8)	39(3)	0.596(9)

C223	775(5)	1336(5)	8131(8)	37(3)	0.596(9)

C224	819(6)	867(5)	8571(8)	36(3)	0.596(9)

C225	1714(7)	(799(7)	5858(10)	42(3)	0.596(9)

C226	1665(6)	227(8)	5019(9)	43(3)	0.596(9)

C227	568(6)	1827(6)	8330(10)	41(3)	0.596(9)

C228	642(8)	816(10)	9232(12)	40(4)	0.596(9)

N221	1849(8)	(1208(9)	5674(18)	57(5)	0.596(9)

N222	1796(6)	300(9)	4485(9)	61(5)	0.596(9)

N223	405(6)	2222(6)	8493(12)	66(5)	0.596(9)

N224	473(6)	759(9)	9734(9)	56(5)	0.596(9)

S221	1399(4)	(336(3)	7011(4)	33(2)	0.596(9)

S222	1314(2)	773(3)	6076(3)	43(2)	0.596(9)

S223	952(2)	1364(2)	7277(4)	46(2)	0.596(9)

S224	1045(3)	278(3)	8254(4)	35(1)	0.596(9)

Ni88	1189(2)	516(2)	7161(3)	38(1)	0.596(9)

C321	1638(9)	(441(8)	5939(11)	39(3)	0.404(9)

C322	1618(9)	42(7)	5527(11)	41(3)	0.404(9)

C323	867(8)	1333(7)	7787(10)	41(3)	0.404(9)

C324	900(8)	879(6)	8252(11)	38(3)	0.404(9)

C325	1833(11)	(913(9)	5756(16)	40(4)	0.404(9)

C326	1788(10)	69(10)	4827(13)	47(4)	0.404(9)

C327	707(8)	1860(7)	7985(13)	41(4)	0.404(9)

C328	713(8)	855(10)	8902(13)	39(4)	0.404(9)

N321	1975(11)	(1327(11)	5620(20)	48(6)	0.404(9)

N322	1925(9)	99(12)	4299(13)	52(6)	0.404(9)

N323	561(8)	2268(7)	8143(14)	55(6)	0.404(9)

N324	553(12)	811(19)	9416(17)	53(6)	0.404(9)

S321	1471(5)	(403(4)	6813(8)	48(3)	0.404(9)

S322	1397(3)	656(4)	5772(6)	48(2)	0.404(9)

S323	1042(3)	1311(3)	6924(6)	44(2)	0.404(9)

S324	1097(4)	261(4)	7957(6)	44(2)	0.404(9)

Ni38	1253(2)	452(3)	6858(5)	45(1)	0.404(9)

C231	1713(5)	(514(5)	557(7)	37(3)	0.530(4)

C232	1680(7)	(27(5)	151(9)	36(3)	0.530(4)

C233	991(7)	1209(6)	2586(8)	46(3)	0.530(4)

C234	1029(6)	739(5)	3035(8)	45(3)	0.530(4)

C235	1897(6)	(993(6)	324(10)	42(4)	0.530(4)

C236	1894(10)	27(11)	(507(14)	41(4)	0.530(4)

C237	849(7)	1731(7)	2868(11)	45(4)	0.530(4)

C238	869(6)	702(8)	3717(9)	52(3)	0.530(4)

N231	2057(5)	(1378(6)	94(9)	46(4)	0.530(4)

N232	2055(5)	53(8)	(1021(8)	41(4)	0.530(4)

N233	742(8)	2172(7)	3030(12)	49(4)	0.530(4)

N234	725(5)	689(9)	4270(8)	53(5)	0.530(4)

S231	1509(2)	(519(2)	1398(3)	38(2)	0.530(4)

S232	1456(2)	580(2)	437(3)	36(1)	0.530(4)

S233	1141(2)	1224(2)	1704(4)	38(2)	0.530(4)

S234	1210(2)	133(3)	2667(3)	48(2)	0.530(4)

Ni99	1325(1)	358(2)	1548(2)	35(1)	0.530(4)

C331	1569(7)	(480(6)	1020(8)	40(3)	0.470(4)

C332	1551(6)	(16(5)	574(9)	47(3)	0.470(4)

C333	911(7)	1409(7)	2893(8)	52(3)	0.470(4)

C334	905(6)	958(5)	3369(9)	46(3)	0.470(4)

C335	1684(6)	(1008(6)	798(11)	49(4)	0.470(4)

C336	1712(8)	(51(9)	(149(10)	43(3)	0.470(4)

C337	744(11)	1938(9)	3097(15)	61(4)	0.470(4)

C338	716(7)	958(9)	4022(11)	53(4)	0.470(4)

N331	1805(6)	(1433(7)	591(12)	67(5)	0.470(4)

N332	1862(10)	(43(14)	(678(13)	56(6)	0.470(4)

N333	607(9)	2362(8)	3247(16)	93(8)	0.470(4)

N334	561(6)	939(10)	4563(9)	73(6)	0.470(4)

S331	1385(2)	(412(2)	1882(3)	36(1)	0.470(4)

S332	1366(2)	630(3)	816(4)	57(2)	0.470(4)

S333	1069(3)	1359(3)	2015(4)	61(2)	0.470(4)

S334	1091(2)	322(2)	3092(3)	39(1)	0.470(4)

Ni39	1229(1)	483(2)	1959(2)	41(1)	0.470(4)

Table 3. Bond lengths [Å] and angles [°].

C1(N1	1.350(14)

C1(C2	1.390(15)

C1(H1	0.9500

C2(C3	1.40(2)

C2(H2	0.9500

C3(C4	1.354(17)

C3(H3	0.9500

C4(C5	1.440(13)

C4(H4	0.9500

C5(N1	1.346(16)

C5(C6	1.465(16)

C6(C7	1.330(17)

C6(N2	1.384(13)

C7(C8	1.444(14)

C7(H7	0.9500

C8(C9	1.428(14)

C8(H8	0.9500

C9(C10	1.373(17)

C9(H9	0.9500

C10(N2	1.404(14)

C10(C11	1.446(14)

C11(N3	1.308(15)

C11(C12	1.416(14)

C12(C13	1.396(14)

C12(H12	0.9500

C13(C14	1.431(16)

C13(H13	0.9500

C14(C15	1.432(15)

C14(H14	0.9500

C15(N3	1.322(14)

C15(H15	0.9500

C16(N16	1.260(15)

C16(C17	1.359(17)

C16(H16	0.9500

C17(C18	1.335(18)

C17(H17	0.9500

C18(C19	1.444(17)

C18(H18	0.9500

C19(C20	1.358(16)

C19(H19	0.9500

C20(N16	1.361(15)

C20(C21	1.494(17)

C21(N17	1.363(15)

C21(C22	1.384(17)

C22(C23	1.386(15)

C22(H22	0.9500

C23(C24	1.377(14)

C23(H23	0.9500

C24(C25	1.415(16)

C24(H24	0.9500

C25(N17	1.327(14)

C25(C26	1.530(16)

C26(N18	1.348(15)

C26(C27	1.397(16)

C27(C28	1.425(16)

C27(H27	0.9500

C28(C29	1.364(18)

C28(H28	0.9500

C29(C30	1.397(16)

C29(H29	0.9500

C30(N18	1.283(14)

C30(H30	0.9500

N1(Co1	2.137(8)

N2(Co1	2.000(10)

N3(Co1	2.150(8)

N16(Co1	2.180(10)

N17(Co1	2.005(9)

N18(Co1	2.149(10)

C31(C32	1.383(15)

C31(N31	1.423(13)

C31(H31	0.9500

C32(C33	1.403(16)

C32(H32	0.9500

C33(C34	1.304(16)

C33(H33	0.9500

C34(C35	1.430(16)

C34(H34	0.9500

C35(N31	1.350(13)

C35(C36	1.451(16)

C36(N32	1.353(14)

C36(C37	1.391(16)

C37(C38	1.400(17)

C37(H37	0.9500

C38(C39	1.362(17)

C38(H38	0.9500

C39(C40	1.370(16)

C39(H39	0.9500

C40(N32	1.360(14)

C40(C41	1.443(16)

C41(N33	1.344(13)

C41(C42	1.419(15)

C42(C43	1.327(16)

C42(H42	0.9500

C43(C44	1.397(16)

C43(H43	0.9500

C44(C45	1.365(15)

C44(H44	0.9500

C45(N33	1.409(14)

C45(H45	0.9500

C46(N46	1.331(13)

C46(C47	1.363(14)

C46(H46	0.9500

C47(C48	1.375(18)

C47(H47	0.9500

C48(C49	1.379(17)

C48(H48	0.9500

C49(C50	1.331(14)

C49(H49	0.9500

C50(N46	1.400(13)

C50(C51	1.482(15)

C51(N47	1.293(13)

C51(C52	1.428(15)

C52(C53	1.315(14)

C52(H52	0.9500

C53(C54	1.311(15)

C53(H53	0.9500

C54(C55	1.417(16)

C54(H54	0.9500

C55(N47	1.278(13)

C55(C56	1.501(15)

C56(C57	1.334(15)

C56(N48	1.436(14)

C57(C58	1.386(17)

C57(H57	0.9500

C58(C59	1.319(18)

C58(H58	0.9500

C59(C60	1.350(16)

C59(H59	0.9500

C60(N48	1.359(13)

C60(H60	0.9500

N31(Co2	2.112(9)

N32(Co2	1.988(9)

N33(Co2	2.116(10)

N46(Co2	2.035(8)

N47(Co2	1.967(9)

N48(Co2	2.012(9)

C61(C62	1.368(15)

C61(N61	1.416(14)

C61(H61	0.9500

C62(C63	1.398(16)

C62(H62	0.9500

C63(C64	1.363(16)

C63(H63	0.9500

C64(C65	1.380(15)

C64(H64	0.9500

C65(N61	1.369(13)

C65(C66	1.433(16)

C66(N62	1.342(14)

C66(C67	1.369(16)

C67(C68	1.403(16)

C67(H67	0.9500

C68(C69	1.370(17)

C68(H68	0.9500

C69(C70	1.394(16)

C69(H69	0.9500

C70(N62	1.338(14)

C70(C71	1.435(16)

C71(N63	1.338(14)

C71(C72	1.455(16)

C72(C73	1.310(16)

C72(H72	0.9500

C73(C74	1.404(15)

C73(H73	0.9500

C74(C75	1.400(15)

C74(H74	0.9500

C75(N63	1.413(13)

C75(H75	0.9500

C76(N76	1.334(13)

C76(C77	1.338(15)

C76(H76	0.9500

C77(C78	1.318(17)

C77(H77	0.9500

C78(C79	1.357(16)

C78(H78	0.9500

C79(C80	1.354(15)

C79(H79	0.9500

C80(N76	1.386(14)

C80(C81	1.501(15)

C81(N77	1.303(13)

C81(C82	1.391(15)

C82(C83	1.294(15)

C82(H82	0.9500

C83(C84	1.334(15)

C83(H83	0.9500

C84(C85	1.443(14)

C84(H84	0.9500

C85(N77	1.274(13)

C85(C86	1.512(14)

C86(C87	1.309(14)

C86(N78	1.379(13)

C87(C88	1.407(16)

C87(H87	0.9500

C88(C89	1.337(18)

C88(H88	0.9500

C89(C90	1.352(14)

C89(H89	0.9500

C90(N78	1.349(12)

C90(H90	0.9500

N61(Co3	2.074(10)

N62(Co3	2.059(9)

N63(Co3	2.083(10)

N76(Co3	2.135(9)

N77(Co3	2.058(8)

N78(Co3	2.151(8)

C91(N91	1.338(11)

C91(C92	1.395(12)

C91(H91	0.9500

C92(C93	1.413(15)

C92(H92	0.9500

C93(C94	1.360(14)

C93(H93	0.9500

C94(C95	1.430(12)

C94(H94	0.9500

C95(N91	1.303(12)

C95(C96	1.437(12)

C96(C97	1.370(14)

C96(N92	1.380(10)

C97(C98	1.434(13)

C97(H97	0.9500

C98(C97i	1.434(13)

C98(H98	0.9500

C101(N101	1.246(11)

C101(C102	1.393(13)

C101(H101	0.9500

C102(C103	1.342(14)

C102(H102	0.9500

C103(C104	1.430(13)

C103(H103	0.9500

C104(C105	1.387(12)

C104(H104	0.9500

C105(N101	1.345(11)

C105(C106	1.504(12)

C106(N102	1.347(11)

C106(C107	1.363(13)

C107(C108	1.387(13)

C107(H107	0.9500

C108(C107i	1.387(13)

C108(H108	0.9500

N91(Co4	2.078(7)

N92(C96i	1.380(10)

N92(Co4	1.929(12)

N101(Co4	2.171(8)

N102(C106i	1.347(11)

N102(Co4	1.951(11)

Co4(N91i	2.078(7)

Co4(N101i	2.171(8)

C111(N111	1.334(11)

C111(C112	1.419(12)

C111(H111	0.9500

C112(C113	1.431(15)

C112(H112	0.9500

C113(C114	1.361(14)

C113(H113	0.9500

C114(C115	1.438(12)

C114(H114	0.9500

C115(N111	1.329(12)

C115(C116	1.456(13)

C116(C117	1.367(14)

C116(N112	1.391(11)

C117(C118	1.442(13)

C117(H117	0.9500

C118(C117ii	1.442(13)

C118(H118	0.9500

C121(N121	1.259(12)

C121(C122	1.377(13)

C121(H121	0.9500

C122(C123	1.345(14)

C122(H122	0.9500

C123(C124	1.425(13)

C123(H123	0.9500

C124(C125	1.380(12)

C124(H124	0.9500

C125(N121	1.343(12)

C125(C126	1.510(13)

C126(N122	1.365(11)

C126(C127	1.375(14)

C127(C128	1.389(13)

C127(H127	0.9500

C128(C127ii	1.389(13)

C128(H128	0.9500

N111(Co5	2.119(7)

N112(C116ii	1.391(11)

N112(Co5	1.957(11)

N121(Co5	2.148(8)

N122(C126ii	1.365(11)

N122(Co5	1.975(11)

Co5(N111ii	2.119(7)

Co5(N121ii	2.148(8)

C201(C202	1.356(9)

C201(C205	1.369(11)

C201(S201	1.748(7)

C202(C206	1.482(10)

C202(S202	1.727(9)

C203(C204	1.357(9)

C203(C207	1.449(11)

C203(S203	1.741(8)

C204(C208	1.426(11)

C204(S204	1.718(8)

C205(N201	1.172(11)

C206(N202	1.138(9)

C207(N203	1.150(10)

C208(N204	1.153(9)

S201(Ni66	2.186(3)

S202(Ni66	2.159(3)

S203(Ni66	2.173(3)

S204(Ni66	2.173(3)

C211(C212	1.359(9)

C211(C215	1.371(11)

C211(S211	1.744(7)

C212(C216	1.485(12)

C212(S212	1.743(8)

C213(C214	1.380(9)

C213(C217	1.436(12)

C213(S213	1.734(8)

C214(C218	1.405(12)

C214(S214	1.727(8)

C215(N211	1.175(10)

C216(N212	1.128(11)

C217(N213	1.156(10)

C218(N214	1.148(11)

S211(Ni77	2.162(3)

S212(Ni77	2.165(4)

S213(Ni77	2.174(3)

S214(Ni77	2.175(3)

C311(C312	1.361(13)

C311(C315	1.371(14)

C311(S311	1.743(10)

C312(C316	1.487(15)

C312(S312	1.743(10)

C313(C314	1.380(12)

C313(C317	1.438(14)

C313(S313	1.737(10)

C314(C318	1.408(14)

C314(S314	1.732(10)

C315(N311	1.174(14)

C316(N312	1.130(15)

C317(N313	1.160(14)

C318(N314	1.151(14)

S311(Ni37	2.158(8)

S312(Ni37	2.162(9)

S313(Ni37	2.178(8)

S314(Ni37	2.171(9)

C221(C222	1.354(10)

C221(C225	1.364(13)

C221(S221	1.750(9)

C222(C226	1.462(13)

C222(S222	1.726(9)

C223(C224	1.360(11)

C223(C227	1.432(13)

C223(S223	1.727(9)

C224(C228	1.411(13)

C224(S224	1.728(9)

C225(N221	1.141(13)

C226(N222	1.127(12)

C227(N223	1.147(12)

C228(N224	1.144(13)

S221(Ni88	2.170(5)

S222(Ni88	2.140(5)

S223(Ni88	2.183(5)

S224(Ni88	2.161(5)

C321(C322	1.357(12)

C321(C325	1.366(15)

C321(S321	1.745(9)

C322(C326	1.458(14)

C322(S322	1.722(10)

C323(C324	1.355(13)

C323(C327	1.427(14)

C323(S323	1.738(10)

C324(C328	1.409(15)

C324(S324	1.725(10)

C325(N321	1.136(14)

C326(N322	1.118(14)

C327(N323	1.141(14)

C328(N324	1.141(15)

S321(Ni38	2.162(7)

S322(Ni38	2.132(7)

S323(Ni38	2.165(7)

S324(Ni38	2.164(7)

C231(C232	1.360(12)

C231(C235	1.387(13)

C231(S231	1.749(9)

C232(C236	1.479(14)

C232(S232	1.741(10)

C233(C234	1.370(12)

C233(C237	1.445(14)

C233(S233	1.733(10)

C234(C238	1.413(13)

C234(S234	1.727(10)

C235(N231	1.168(12)

C236(N232	1.139(14)

C237(N233	1.156(14)

C238(N234	1.167(13)

S231(Ni99	2.195(5)

S232(Ni99	2.170(6)

S233(Ni99	2.173(6)

S234(Ni99	2.166(6)

C331(C332	1.356(13)

C331(C335	1.383(14)

C331(S331	1.757(10)

C332(C336	1.482(15)

C332(S332	1.734(10)

C333(C334	1.370(13)

C333(C337	1.444(15)

C333(S333	1.740(10)

C334(C338	1.414(15)

C334(S334	1.732(10)

C335(N331	1.169(14)

C336(N332	1.141(16)

C337(N333	1.155(15)

C338(N334	1.172(15)

S331(Ni39	2.191(6)

S332(Ni39	2.194(7)

S333(Ni39	2.152(6)

S334(Ni39	2.186(6)

N1(C1(C2	120.6(13)

N1(C1(H1	119.7

C2(C1(H1	119.7

C1(C2(C3	122.2(13)

C1(C2(H2	118.9

C3(C2(H2	118.9

C4(C3(C2	117.2(11)

C4(C3(H3	121.4

C2(C3(H3	121.4

C3(C4(C5	119.1(13)

C3(C4(H4	120.5

C5(C4(H4	120.5

N1(C5(C4	122.5(10)

N1(C5(C6	116.2(9)

C4(C5(C6	121.2(12)

C7(C6(N2	121.8(10)

C7(C6(C5	127.3(9)

N2(C6(C5	110.8(10)

C6(C7(C8	120.4(9)

C6(C7(H7	119.8

C8(C7(H7	119.8

C9(C8(C7	119.0(10)

C9(C8(H8	120.5

C7(C8(H8	120.5

C10(C9(C8	117.3(10)

C10(C9(H9	121.3

C8(C9(H9	121.3

C9(C10(N2	122.8(10)

C9(C10(C11	126.4(10)

N2(C10(C11	110.7(10)

N3(C11(C12	120.5(10)

N3(C11(C10	118.8(9)

C12(C11(C10	120.4(11)

C13(C12(C11	119.8(11)

C13(C12(H12	120.1

C11(C12(H12	120.1

C12(C13(C14	117.5(10)

C12(C13(H13	121.2

C14(C13(H13	121.2

C13(C14(C15	118.1(10)

C13(C14(H14	121.0

C15(C14(H14	121.0

N3(C15(C14	120.5(12)

N3(C15(H15	119.7

C14(C15(H15	119.7

N16(C16(C17	123.0(14)

N16(C16(H16	118.5

C17(C16(H16	118.5

C18(C17(C16	118.6(14)

C18(C17(H17	120.7

C16(C17(H17	120.7

C17(C18(C19	120.2(13)

C17(C18(H18	119.9

C19(C18(H18	119.9

C20(C19(C18	115.7(12)

C20(C19(H19	122.2

C18(C19(H19	122.2

C19(C20(N16	120.9(12)

C19(C20(C21	122.9(12)

N16(C20(C21	116.1(11)

N17(C21(C22	121.8(12)

N17(C21(C20	113.4(11)

C22(C21(C20	123.9(12)

C21(C22(C23	118.4(12)

C21(C22(H22	120.8

C23(C22(H22	120.8

C24(C23(C22	120.4(11)

C24(C23(H23	119.8

C22(C23(H23	119.8

C23(C24(C25	118.0(11)

C23(C24(H24	121.0

C25(C24(H24	121.0

N17(C25(C24	122.0(11)

N17(C25(C26	112.7(10)

C24(C25(C26	125.4(11)

N18(C26(C27	125.8(11)

N18(C26(C25	113.3(11)

C27(C26(C25	120.9(11)

C26(C27(C28	111.9(11)

C26(C27(H27	124.1

C28(C27(H27	124.1

C29(C28(C27	122.7(12)

C29(C28(H28	118.6

C27(C28(H28	118.6

C28(C29(C30	118.2(12)

C28(C29(H29	120.9

C30(C29(H29	120.9

N18(C30(C29	122.1(13)

N18(C30(H30	119.0

C29(C30(H30	119.0

C5(N1(C1	118.2(9)

C5(N1(Co1	115.2(7)

C1(N1(Co1	126.6(9)

C6(N2(C10	118.5(10)

C6(N2(Co1	121.5(7)

C10(N2(Co1	119.6(7)

C11(N3(C15	123.1(10)

C11(N3(Co1	113.8(7)

C15(N3(Co1	123.0(9)

C16(N16(C20	121.3(12)

C16(N16(Co1	126.1(9)

C20(N16(Co1	112.2(8)

C25(N17(C21	119.1(10)

C25(N17(Co1	121.1(8)

C21(N17(Co1	119.7(9)

C30(N18(C26	119.3(11)

C30(N18(Co1	125.6(9)

C26(N18(Co1	114.7(8)

N2(Co1(N17	173.8(3)

N2(Co1(N1	76.1(4)

N17(Co1(N1	97.7(4)

N2(Co1(N18	103.2(4)

N17(Co1(N18	76.6(4)

N1(Co1(N18	91.8(4)

N2(Co1(N3	76.8(4)

N17(Co1(N3	109.4(4)

N1(Co1(N3	152.9(4)

N18(Co1(N3	93.3(4)

N2(Co1(N16	102.5(4)

N17(Co1(N16	78.0(4)

N1(Co1(N16	96.3(4)

N18(Co1(N16	154.2(4)

N3(Co1(N16	90.6(4)

C32(C31(N31	122.6(11)

C32(C31(H31	118.7

N31(C31(H31	118.7

C31(C32(C33	118.3(12)

C31(C32(H32	120.8

C33(C32(H32	120.8

C34(C33(C32	120.3(12)

C34(C33(H33	119.9

C32(C33(H33	119.9

C33(C34(C35	121.1(12)

C33(C34(H34	119.4

C35(C34(H34	119.4

N31(C35(C34	121.6(11)

N31(C35(C36	112.1(11)

C34(C35(C36	126.2(11)

N32(C36(C37	120.8(12)

N32(C36(C35	114.2(10)

C37(C36(C35	124.7(12)

C36(C37(C38	116.0(13)

C36(C37(H37	122.0

C38(C37(H37	122.0

C39(C38(C37	122.9(13)

C39(C38(H38	118.6

C37(C38(H38	118.6

C38(C39(C40	118.3(13)

C38(C39(H39	120.8

C40(C39(H39	120.8

N32(C40(C39	120.3(13)

N32(C40(C41	114.2(10)

C39(C40(C41	125.4(12)

N33(C41(C42	118.1(11)

N33(C41(C40	114.8(10)

C42(C41(C40	127.1(11)

C43(C42(C41	125.0(11)

C43(C42(H42	117.5

C41(C42(H42	117.5

C42(C43(C44	117.0(12)

C42(C43(H43	121.5

C44(C43(H43	121.5

C45(C44(C43	119.1(12)

C45(C44(H44	120.4

C43(C44(H44	120.4

C44(C45(N33	123.2(12)

C44(C45(H45	118.4

N33(C45(H45	118.4

N46(C46(C47	128.5(12)

N46(C46(H46	115.8

C47(C46(H46	115.8

C46(C47(C48	114.6(12)

C46(C47(H47	122.7

C48(C47(H47	122.7

C47(C48(C49	120.6(11)

C47(C48(H48	119.7

C49(C48(H48	119.7

C50(C49(C48	120.3(12)

C50(C49(H49	119.9

C48(C49(H49	119.9

C49(C50(N46	122.2(11)

C49(C50(C51	127.1(11)

N46(C50(C51	110.6(9)

N47(C51(C52	120.1(10)

N47(C51(C50	116.9(9)

C52(C51(C50	123.0(10)

C53(C52(C51	117.3(11)

C53(C52(H52	121.4

C51(C52(H52	121.4

C54(C53(C52	122.3(12)

C54(C53(H53	118.9

C52(C53(H53	118.9

C53(C54(C55	118.3(12)

C53(C54(H54	120.8

C55(C54(H54	120.8

N47(C55(C54	120.0(11)

N47(C55(C56	116.0(10)

C54(C55(C56	124.0(11)

C57(C56(N48	124.6(11)

C57(C56(C55	126.5(12)

N48(C56(C55	108.7(9)

C56(C57(C58	117.0(13)

C56(C57(H57	121.5

C58(C57(H57	121.5

C59(C58(C57	121.8(13)

C59(C58(H58	119.1

C57(C58(H58	119.1

C58(C59(C60	118.3(14)

C58(C59(H59	120.9

C60(C59(H59	120.9

C59(C60(N48	126.4(13)

C59(C60(H60	116.8

N48(C60(H60	116.8

C35(N31(C31	115.7(10)

C35(N31(Co2	116.4(8)

C31(N31(Co2	127.6(8)

C36(N32(C40	121.3(10)

C36(N32(Co2	119.8(8)

C40(N32(Co2	118.5(8)

C41(N33(C45	117.5(10)

C41(N33(Co2	114.2(8)

C45(N33(Co2	127.8(8)

C46(N46(C50	113.7(9)

C46(N46(Co2	131.5(8)

C50(N46(Co2	114.7(7)

C55(N47(C51	122.0(10)

C55(N47(Co2	120.1(7)

C51(N47(Co2	117.9(7)

C60(N48(C56	111.3(10)

C60(N48(Co2	132.5(8)

C56(N48(Co2	116.2(7)

N47(Co2(N32	176.7(4)

N47(Co2(N48	79.0(4)

N32(Co2(N48	103.3(4)

N47(Co2(N46	79.7(4)

N32(Co2(N46	98.1(4)

N48(Co2(N46	158.6(4)

N47(Co2(N31	101.5(4)

N32(Co2(N31	76.1(4)

N48(Co2(N31	90.4(4)

N46(Co2(N31	95.4(3)

N47(Co2(N33	105.1(4)

N32(Co2(N33	77.3(4)

N48(Co2(N33	93.7(4)

N46(Co2(N33	90.3(3)

N31(Co2(N33	153.4(4)

C62(C61(N61	122.8(11)

C62(C61(H61	118.6

N61(C61(H61	118.6

C61(C62(C63	120.0(12)

C61(C62(H62	120.0

C63(C62(H62	120.0

C64(C63(C62	115.9(12)

C64(C63(H63	122.0

C62(C63(H63	122.0

C63(C64(C65	125.1(11)

C63(C64(H64	117.4

C65(C64(H64	117.4

N61(C65(C64	119.3(11)

N61(C65(C66	114.3(10)

C64(C65(C66	126.5(10)

N62(C66(C67	119.6(12)

N62(C66(C65	114.5(10)

C67(C66(C65	125.9(12)

C66(C67(C68	118.0(13)

C66(C67(H67	121.0

C68(C67(H67	121.0

C69(C68(C67	120.5(13)

C69(C68(H68	119.7

C67(C68(H68	119.7

C68(C69(C70	119.6(13)

C68(C69(H69	120.2

C70(C69(H69	120.2

N62(C70(C69	117.5(12)

N62(C70(C71	115.2(10)

C69(C70(C71	127.3(12)

N63(C71(C70	113.1(11)

N63(C71(C72	122.0(11)

C70(C71(C72	124.9(11)

C73(C72(C71	121.2(11)

C73(C72(H72	119.4

C71(C72(H72	119.4

C72(C73(C74	118.0(12)

C72(C73(H73	121.0

C74(C73(H73	121.0

C75(C74(C73	120.5(12)

C75(C74(H74	119.8

C73(C74(H74	119.8

C74(C75(N63	121.6(11)

C74(C75(H75	119.2

N63(C75(H75	119.2

N76(C76(C77	126.9(13)

N76(C76(H76	116.6

C77(C76(H76	116.6

C78(C77(C76	116.1(13)

C78(C77(H77	122.0

C76(C77(H77	122.0

C77(C78(C79	123.4(12)

C77(C78(H78	118.3

C79(C78(H78	118.3

C80(C79(C78	116.8(11)

C80(C79(H79	121.6

C78(C79(H79	121.6

C79(C80(N76	122.9(10)

C79(C80(C81	125.7(11)

N76(C80(C81	111.4(9)

N77(C81(C82	116.3(10)

N77(C81(C80	117.7(9)

C82(C81(C80	126.0(10)

C83(C82(C81	122.8(11)

C83(C82(H82	118.6

C81(C82(H82	118.6

C82(C83(C84	119.7(10)

C82(C83(H83	120.1

C84(C83(H83	120.1

C83(C84(C85	117.9(11)

C83(C84(H84	121.0

C85(C84(H84	121.0

N77(C85(C84	118.2(10)

N77(C85(C86	118.3(9)

C84(C85(C86	123.4(10)

C87(C86(N78	121.1(10)

C87(C86(C85	125.6(10)

N78(C86(C85	113.3(9)

C86(C87(C88	119.3(12)

C86(C87(H87	120.3

C88(C87(H87	120.3

C89(C88(C87	121.2(11)

C89(C88(H88	119.4

C87(C88(H88	119.4

C88(C89(C90	116.7(12)

C88(C89(H89	121.7

C90(C89(H89	121.7

N78(C90(C89	124.2(11)

N78(C90(H90	117.9

C89(C90(H90	117.9

C65(N61(C61	116.7(10)

C65(N61(Co3	116.1(8)

C61(N61(Co3	126.7(8)

C70(N62(C66	124.4(10)

C70(N62(Co3	117.7(8)

C66(N62(Co3	117.8(8)

C71(N63(C75	115.7(10)

C71(N63(Co3	117.8(8)

C75(N63(Co3	126.4(7)

C76(N76(C80	113.6(9)

C76(N76(Co3	130.6(8)

C80(N76(Co3	115.7(7)

C85(N77(C81	124.8(9)

C85(N77(Co3	117.1(7)

C81(N77(Co3	118.1(7)

C90(N78(C86	117.3(9)

C90(N78(Co3	129.9(7)

C86(N78(Co3	112.7(7)

N77(Co3(N62	177.6(3)

N77(Co3(N61	104.4(4)

N62(Co3(N61	76.2(4)

N77(Co3(N63	104.0(4)

N62(Co3(N63	75.5(4)

N61(Co3(N63	151.6(4)

N77(Co3(N76	77.1(4)

N62(Co3(N76	105.2(3)

N61(Co3(N76	94.4(4)

N63(Co3(N76	90.0(4)

N77(Co3(N78	78.6(3)

N62(Co3(N78	99.1(3)

N61(Co3(N78	90.3(4)

N63(Co3(N78	97.1(4)

N76(Co3(N78	155.7(4)

N91(C91(C92	118.6(11)

N91(C91(H91	120.7

C92(C91(H91	120.7

C91(C92(C93	121.2(10)

C91(C92(H92	119.4

C93(C92(H92	119.4

C94(C93(C92	118.0(10)

C94(C93(H93	121.0

C92(C93(H93	121.0

C93(C94(C95	117.9(11)

C93(C94(H94	121.0

C95(C94(H94	121.0

N91(C95(C94	122.3(9)

N91(C95(C96	117.1(8)

C94(C95(C96	120.5(10)

C97(C96(N92	119.4(10)

C97(C96(C95	129.1(9)

N92(C96(C95	111.4(8)

C96(C97(C98	121.9(11)

C96(C97(H97	119.1

C98(C97(H97	119.1

C97i(C98(C97	115.6(15)

C97i(C98(H98	122.2

C97(C98(H98	122.2

N101(C101(C102	123.6(12)

N101(C101(H101	118.2

C102(C101(H101	118.2

C103(C102(C101	119.0(12)

C103(C102(H102	120.5

C101(C102(H102	120.5

C102(C103(C104	119.3(11)

C102(C103(H103	120.4

C104(C103(H103	120.4

C105(C104(C103	115.4(10)

C105(C104(H104	122.3

C103(C104(H104	122.3

N101(C105(C104	122.9(10)

N101(C105(C106	116.2(9)

C104(C105(C106	120.9(10)

N102(C106(C107	120.8(10)

N102(C106(C105	113.1(9)

C107(C106(C105	125.7(10)

C106(C107(C108	120.7(13)

C106(C107(H107	119.7

C108(C107(H107	119.7

C107(C108(C107i	117.0(17)

C107(C108(H108	121.5

C107i(C108(H108	121.5

C95(N91(C91	121.8(8)

C95(N91(Co4	113.8(6)

C91(N91(Co4	124.3(7)

C96(N92(C96i	121.8(12)

C96(N92(Co4	119.1(6)

C96i(N92(Co4	119.1(6)

C101(N101(C105	119.8(10)

C101(N101(Co4	128.9(8)

C105(N101(Co4	110.9(7)

C106i(N102(C106	119.8(12)

C106i(N102(Co4	120.1(6)

C106(N102(Co4	120.1(6)

N92(Co4(N102	180.000(1)

N92(Co4(N91	78.5(3)

N102(Co4(N91	101.5(3)

N92(Co4(N91i	78.5(3)

N102(Co4(N91i	101.5(3)

N91(Co4(N91i	157.1(5)

N92(Co4(N101	101.0(2)

N102(Co4(N101	79.0(2)

N91(Co4(N101	90.5(3)

N91i(Co4(N101	93.9(3)

N92(Co4(N101i	101.0(2)

N102(Co4(N101i	79.0(2)

N91(Co4(N101i	93.9(3)

N91i(Co4(N101i	90.5(3)

N101(Co4(N101i	158.0(5)

N111(C111(C112	121.7(11)

N111(C111(H111	119.1

C112(C111(H111	119.1

C111(C112(C113	119.1(10)

C111(C112(H112	120.4

C113(C112(H112	120.4

C114(C113(C112	117.2(10)

C114(C113(H113	121.4

C112(C113(H113	121.4

C113(C114(C115	120.6(11)

C113(C114(H114	119.7

C115(C114(H114	119.7

N111(C115(C114	121.2(10)

N111(C115(C116	116.7(8)

C114(C115(C116	122.1(10)

C117(C116(N112	124.4(10)

C117(C116(C115	126.0(10)

N112(C116(C115	109.7(9)

C116(C117(C118	119.4(12)

C116(C117(H117	120.3

C118(C117(H117	120.3

C117(C118(C117ii	116.9(16)

C117(C118(H118	121.6

C117ii(C118(H118	121.6

N121(C121(C122	123.9(11)

N121(C121(H121	118.0

C122(C121(H121	118.0

C123(C122(C121	117.6(11)

C123(C122(H122	121.2

C121(C122(H122	121.2

C122(C123(C124	120.9(10)

C122(C123(H123	119.5

C124(C123(H123	119.5

C125(C124(C123	114.9(10)

C125(C124(H124	122.5

C123(C124(H124	122.5

N121(C125(C124	122.4(10)

N121(C125(C126	115.3(9)

C124(C125(C126	122.2(10)

N122(C126(C127	123.0(11)

N122(C126(C125	111.2(8)

C127(C126(C125	125.6(11)

C126(C127(C128	118.5(13)

C126(C127(H127	120.7

C128(C127(H127	120.7

C127ii(C128(C127	119.8(16)

C127ii(C128(H128	120.1

C127(C128(H128	120.1

C115(N111(C111	120.1(8)

C115(N111(Co5	115.0(6)

C111(N111(Co5	124.9(7)

C116(N112(C116ii	115.6(12)

C116(N112(Co5	122.2(6)

C116ii(N112(Co5	122.2(6)

C121(N121(C125	120.1(10)

C121(N121(Co5	125.6(8)

C125(N121(Co5	113.7(7)

C126ii(N122(C126	117.1(12)

C126ii(N122(Co5	121.5(6)

C126(N122(Co5	121.5(6)

N112(Co5(N122	180.000(2)

N112(Co5(N111ii	76.4(3)

N122(Co5(N111ii	103.6(3)

N112(Co5(N111	76.4(3)

N122(Co5(N111	103.6(3)

N111ii(Co5(N111	152.8(5)

N112(Co5(N121	102.7(3)

N122(Co5(N121	77.3(3)

N111ii(Co5(N121	94.5(3)

N111(Co5(N121	91.4(3)

N112(Co5(N121ii	102.7(3)

N122(Co5(N121ii	77.3(3)

N111ii(Co5(N121ii	91.4(3)

N111(Co5(N121ii	94.5(3)

N121(Co5(N121ii	154.6(5)

C202(C201(C205	123.4(8)

C202(C201(S201	117.6(7)

C205(C201(S201	119.0(7)

C201(C202(C206	120.2(8)

C201(C202(S202	123.7(7)

C206(C202(S202	116.0(7)

C204(C203(C207	120.7(8)

C204(C203(S203	121.2(7)

C207(C203(S203	117.9(7)

C203(C204(C208	122.9(9)

C203(C204(S204	120.2(6)

C208(C204(S204	116.9(8)

N201(C205(C201	178.7(13)

N202(C206(C202	175.5(14)

N203(C207(C203	178.1(15)

N204(C208(C204	177.0(13)

C201(S201(Ni66	104.0(3)

C202(S202(Ni66	102.6(3)

C203(S203(Ni66	102.6(3)

C204(S204(Ni66	103.6(3)

S202(Ni66(S203	87.22(13)

S202(Ni66(S204	178.27(14)

S203(Ni66(S204	91.96(12)

S202(Ni66(S201	92.02(12)

S203(Ni66(S201	178.91(15)

S204(Ni66(S201	88.77(11)

C212(C211(C215	124.0(8)

C212(C211(S211	117.6(7)

C215(C211(S211	117.2(8)

C211(C212(C216	121.4(8)

C211(C212(S212	122.9(7)

C216(C212(S212	115.6(7)

C214(C213(C217	121.6(8)

C214(C213(S213	121.4(7)

C217(C213(S213	117.0(7)

C213(C214(C218	120.1(8)

C213(C214(S214	119.3(7)

C218(C214(S214	120.6(8)

N211(C215(C211	179.0(14)

N212(C216(C212	179.4(13)

N213(C217(C213	177.0(14)

N214(C218(C214	178.5(13)

C211(S211(Ni77	104.8(3)

C212(S212(Ni77	102.4(4)

C213(S213(Ni77	102.8(3)

C214(S214(Ni77	104.0(3)

S211(Ni77(S212	92.16(13)

S211(Ni77(S213	178.55(15)

S212(Ni77(S213	89.17(13)

S211(Ni77(S214	86.67(13)

S212(Ni77(S214	178.77(14)

S213(Ni77(S214	92.00(12)

C312(C311(C315	123.2(19)

C312(C311(S311	117.8(11)

C315(C311(S311	117.2(16)

C311(C312(C316	121.2(15)

C311(C312(S312	122.5(12)

C316(C312(S312	114.9(14)

C314(C313(C317	121.4(14)

C314(C313(S313	121.3(11)

C317(C313(S313	117.3(14)

C313(C314(C318	118.9(14)

C313(C314(S314	118.9(12)

C318(C314(S314	121.9(14)

N311(C315(C311	174(9)

N312(C316(C312	164(6)

N313(C317(C313	169(7)

N314(C318(C314	172(7)

C311(S311(Ni37	104.4(7)

C312(S312(Ni37	101.9(7)

C313(S313(Ni37	102.8(7)

C314(S314(Ni37	104.3(7)

S311(Ni37(S312	92.4(4)

S311(Ni37(S314	87.6(5)

S312(Ni37(S314	179.2(12)

S311(Ni37(S313	178.9(10)

S312(Ni37(S313	87.9(5)

S314(Ni37(S313	92.0(4)

C222(C221(C225	123.6(10)

C222(C221(S221	117.0(9)

C225(C221(S221	119.4(9)

C221(C222(C226	120.3(10)

C221(C222(S222	123.5(9)

C226(C222(S222	116.1(9)

C224(C223(C227	122.4(11)

C224(C223(S223	121.5(9)

C227(C223(S223	116.0(9)

C223(C224(C228	122.1(12)

C223(C224(S224	119.0(9)

C228(C224(S224	118.3(11)

N221(C225(C221	176(2)

N222(C226(C222	175(2)

N223(C227(C223	179(2)

N224(C228(C224	175(3)

C221(S221(Ni88	104.3(4)

C222(S222(Ni88	102.9(4)

C223(S223(Ni88	103.3(4)

C224(S224(Ni88	105.0(5)

S222(Ni88(S224	178.0(3)

S222(Ni88(S221	92.2(2)

S224(Ni88(S221	89.6(2)

S222(Ni88(S223	87.1(2)

S224(Ni88(S223	91.1(2)

S221(Ni88(S223	177.3(6)

C322(C321(C325	123.2(13)

C322(C321(S321	116.7(10)

C325(C321(S321	119.3(12)

C321(C322(C326	120.7(12)

C321(C322(S322	124.1(10)

C326(C322(S322	115.2(11)

C324(C323(C327	122.7(13)

C324(C323(S323	121.0(10)

C327(C323(S323	116.2(12)

C323(C324(C328	122.3(13)

C323(C324(S324	119.1(11)

C328(C324(S324	117.5(13)

N321(C325(C321	175(3)

N322(C326(C322	178(4)

N323(C327(C323	177(3)

N324(C328(C324	177(4)

C321(S321(Ni38	103.8(6)

C322(S322(Ni38	102.0(5)

C323(S323(Ni38	103.7(5)

C324(S324(Ni38	105.0(6)

S322(Ni38(S321	93.0(3)

S322(Ni38(S324	178.7(5)

S321(Ni38(S324	88.2(3)

S322(Ni38(S323	87.7(3)

S321(Ni38(S323	178.9(7)

S324(Ni38(S323	91.1(3)

C232(C231(C235	122.4(11)

C232(C231(S231	117.1(8)

C235(C231(S231	120.5(10)

C231(C232(C236	119.4(13)

C231(C232(S232	123.2(9)

C236(C232(S232	116.8(12)

C234(C233(C237	119.9(11)

C234(C233(S233	122.5(10)

C237(C233(S233	117.4(10)

C233(C234(C238	122.9(12)

C233(C234(S234	117.4(10)

C238(C234(S234	118.9(11)

N231(C235(C231	176.2(19)

N232(C236(C232	178(3)

N233(C237(C233	173.5(19)

N234(C238(C234	177(2)

C231(S231(Ni99	104.9(4)

C232(S232(Ni99	103.2(5)

C233(S233(Ni99	103.1(5)

C234(S234(Ni99	105.7(5)

S234(Ni99(S232	178.5(3)

S234(Ni99(S233	91.1(2)

S232(Ni99(S233	89.4(2)

S234(Ni99(S231	88.5(2)

S232(Ni99(S231	90.9(2)

S233(Ni99(S231	179.6(3)

C332(C331(C335	123.5(12)

C332(C331(S331	116.9(10)

C335(C331(S331	119.2(11)

C331(C332(C336	118.7(12)

C331(C332(S332	123.7(10)

C336(C332(S332	117.6(12)

C334(C333(C337	118.5(13)

C334(C333(S333	123.1(11)

C337(C333(S333	118.2(12)

C333(C334(C338	124.4(13)

C333(C334(S334	117.4(11)

C338(C334(S334	117.8(12)

N331(C335(C331	175(2)

N332(C336(C332	174(3)

N333(C337(C333	179(4)

N334(C338(C334	178(2)

C331(S331(Ni39	105.3(5)

C332(S332(Ni39	103.1(5)

C333(S333(Ni39	102.8(6)

C334(S334(Ni39	104.6(5)

S333(Ni39(S334	91.9(3)

S333(Ni39(S331	179.0(4)

S334(Ni39(S331	88.7(2)

S333(Ni39(S332	88.8(3)

S334(Ni39(S332	179.2(3)

S331(Ni39(S332	90.6(3)

Symmetry transformations used to generate equivalent atoms:

(i) (x,y,(z    (ii) (x,y,(z+1

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	43(6) 	53(6)	20(4) 	0(4)	(5(4) 	3(5)

C2	53(6) 	77(6)	29(5) 	2(5)	3(5) 	6(6)

C3	48(6) 	89(7)	16(5) 	5(4)	9(4) 	(3(6)

C4	44(6) 	66(6)	18(4) 	11(4)	7(4) 	(1(5)

C5	35(5) 	52(5)	9(4) 	2(4)	1(4) 	(1(5)

C6	32(5) 	48(4)	14(4) 	7(4)	(2(3) 	0(5)

C7	33(5) 	50(5)	25(4) 	6(4)	5(4) 	5(5)

C8	33(6) 	33(5)	40(5) 	5(4)	(4(4) 	(1(5)

C9	31(5) 	47(5)	31(5) 	(5(4)	(2(4) 	(9(5)

C10	37(5) 	43(4)	17(4) 	(4(4)	0(4) 	(1(5)

C11	28(5) 	42(4)	17(4) 	(7(4)	2(3) 	(3(4)

C12	42(6) 	45(5)	22(4) 	0(4)	2(4) 	(4(5)

C13	46(6) 	42(5)	30(5) 	2(4)	3(4) 	(7(5)

C14	44(6) 	49(5)	27(5) 	9(4)	6(4) 	(8(5)

C15	45(6) 	51(6)	31(5) 	6(4)	3(4) 	(2(5)

C16	44(5) 	51(6)	24(5) 	1(5)	(2(4) 	(7(5)

C17	38(6) 	57(6)	41(6) 	(3(5)	(9(4) 	(11(5)

C18	29(5) 	66(6)	37(5) 	13(5)	3(4) 	(4(5)

C19	24(5) 	58(6)	21(4) 	7(4)	9(3) 	11(4)

C20	27(4) 	40(4)	29(5) 	(1(4)	8(3) 	2(4)

C21	34(5) 	40(4)	28(5) 	2(4)	3(4) 	0(4)

C22	25(4) 	43(5)	33(5) 	1(4)	24(4) 	1(4)

C23	24(4) 	37(5)	51(5) 	(2(4)	22(4) 	0(4)

C24	27(4) 	32(4)	36(5) 	(10(4)	20(4) 	(3(4)

C25	30(4) 	32(4)	21(4) 	6(4)	4(3) 	0(4)

C26	36(5) 	35(4)	20(4) 	5(4)	0(3) 	(2(4)

C27	39(5) 	37(5)	26(5) 	0(4)	4(4) 	(5(4)

C28	36(5) 	54(6)	27(5) 	(5(5)	(10(4) 	(2(5)

C29	37(5) 	47(5)	35(5) 	5(5)	(5(4) 	6(5)

C30	38(5) 	40(5)	26(5) 	8(4)	0(4) 	3(4)

N1	34(5) 	51(5)	17(4) 	2(3)	3(3) 	1(4)

N2	42(5) 	48(4)	16(4) 	3(3)	3(3) 	8(4)

N3	36(4) 	47(4)	18(4) 	(4(3)	2(3) 	(14(4)

N16	36(4) 	38(4)	25(4) 	7(4)	(3(3) 	(3(3)

N17	40(4) 	32(3)	20(4) 	3(3)	0(3) 	(1(3)

N18	39(4) 	33(4)	22(4) 	3(4)	(2(3) 	(3(3)

Co1	33(1) 	36(1)	21(1) 	0(1)	(2(1) 	0(1)

C31	39(5) 	30(5)	31(5) 	(7(4)	6(4) 	11(4)

C32	31(5) 	54(5)	24(5) 	(3(5)	15(4) 	10(5)

C33	39(6) 	59(6)	27(5) 	(10(5)	7(4) 	(6(5)

C34	48(6) 	40(5)	31(5) 	(11(4)	11(4) 	(8(4)

C35	44(5) 	28(4)	33(5) 	(12(4)	9(4) 	(3(4)

C36	41(5) 	27(4)	44(5) 	(15(4)	14(4) 	0(4)

C37	68(6) 	28(5)	66(7) 	(14(5)	0(5) 	(4(5)

C38	78(7) 	32(6)	71(7) 	(1(5)	11(6) 	5(4)

C39	84(7) 	33(5)	47(6) 	10(5)	(2(5) 	8(5)

C40	60(5) 	28(4)	41(5) 	16(4)	3(4) 	12(4)

C41	45(5) 	32(4)	29(5) 	14(4)	14(4) 	19(4)

C42	47(5) 	39(5)	37(5) 	23(4)	17(4) 	24(4)

C43	39(5) 	61(6)	36(5) 	15(5)	20(4) 	18(5)

C44	24(5) 	59(6)	44(6) 	6(5)	9(4) 	3(5)

C45	33(5) 	48(5)	42(6) 	10(5)	10(4) 	(6(4)

C46	30(5) 	49(5)	37(5) 	(2(4)	5(4) 	13(5)

C47	29(5) 	68(6)	44(5) 	5(5)	4(4) 	11(5)

C48	51(6) 	73(6)	29(5) 	(15(5)	3(4) 	19(6)

C49	43(6) 	47(5)	35(5) 	(14(4)	(17(4) 	18(5)

C50	31(5) 	33(4)	38(5) 	(9(4)	(15(4) 	13(4)

C51	31(5) 	19(4)	43(5) 	(3(4)	(19(4) 	11(4)

C52	33(5) 	26(4)	57(6) 	(10(4)	(24(4) 	6(5)

C53	41(6) 	24(5)	72(7) 	3(4)	(20(5) 	(4(4)

C54	37(6) 	28(5)	64(6) 	8(5)	(22(5) 	(12(5)

C55	28(5) 	28(4)	49(5) 	4(4)	(15(4) 	(7(4)

C56	26(5) 	40(5)	43(5) 	4(4)	(9(4) 	(10(4)

C57	48(6) 	58(6)	45(6) 	9(5)	(9(5) 	(11(5)

C58	40(6) 	86(7)	51(6) 	11(6)	(1(5) 	0(6)

C59	54(7) 	86(7)	58(6) 	(5(6)	7(5) 	11(7)

C60	36(6) 	51(6)	53(6) 	(9(5)	(2(5) 	5(5)

N31	33(4) 	35(4)	28(4) 	(3(4)	6(3) 	6(3)

N32	44(5) 	23(3)	40(5) 	4(3)	12(4) 	7(3)

N33	33(4) 	30(4)	33(4) 	14(4)	8(3) 	7(3)

N46	32(4) 	19(4)	39(4) 	1(3)	(10(3) 	13(4)

N47	32(5) 	18(3)	30(4) 	(1(3)	(24(3) 	5(3)

N48	37(5) 	35(4)	40(4) 	(4(3)	(9(4) 	0(4)

Co2	35(1) 	15(1)	32(1) 	0(1)	(1(1) 	2(1)

C61	43(5) 	31(5)	34(5) 	(6(4)	2(4) 	4(4)

C62	33(5) 	49(5)	44(6) 	(1(5)	7(4) 	0(5)

C63	37(5) 	47(6)	36(5) 	(6(5)	15(4) 	(9(5)

C64	46(5) 	29(5)	37(5) 	(19(4)	16(4) 	(13(4)

C65	36(4) 	27(4)	25(5) 	(13(4)	18(3) 	(12(3)

C66	42(5) 	27(4)	38(5) 	(9(4)	17(4) 	(8(4)

C67	56(6) 	29(5)	54(6) 	(7(5)	4(5) 	(1(4)

C68	63(7) 	28(5)	77(7) 	6(5)	2(5) 	3(4)

C69	58(6) 	25(4)	73(7) 	12(5)	(5(5) 	9(4)

C70	40(5) 	21(4)	40(5) 	12(4)	16(4) 	9(3)

C71	40(5) 	30(4)	33(5) 	7(4)	15(4) 	5(4)

C72	43(6) 	33(5)	51(6) 	21(5)	6(4) 	14(4)

C73	41(5) 	44(5)	32(5) 	5(4)	10(4) 	21(4)

C74	34(5) 	44(5)	39(5) 	1(5)	9(4) 	1(5)

C75	33(5) 	30(5)	34(5) 	1(4)	2(4) 	3(4)

C76	49(6) 	42(5)	42(6) 	0(4)	3(5) 	6(5)

C77	46(6) 	65(6)	51(6) 	(2(6)	10(5) 	4(6)

C78	44(6) 	65(6)	55(6) 	(16(5)	7(5) 	1(6)

C79	35(6) 	45(5)	55(6) 	(14(4)	(10(5) 	17(5)

C80	31(5) 	30(4)	46(5) 	0(4)	(11(4) 	13(4)

C81	27(5) 	17(4)	48(5) 	(7(4)	(15(4) 	6(4)

C82	37(5) 	18(4)	66(6) 	(7(4)	(32(4) 	11(4)

C83	42(6) 	7(4)	86(7) 	(7(4)	(34(5) 	(6(4)

C84	32(5) 	16(4)	67(6) 	9(4)	(32(4) 	(10(4)

C85	20(5) 	18(4)	46(5) 	1(4)	(15(4) 	(6(4)

C86	19(5) 	25(4)	46(5) 	4(4)	(6(4) 	(10(4)

C87	31(6) 	42(5)	47(5) 	5(4)	(7(4) 	(11(5)

C88	47(6) 	61(6)	41(6) 	1(5)	5(5) 	(10(5)

C89	43(6) 	60(6)	46(6) 	(14(5)	19(5) 	(10(6)

C90	37(6) 	32(5)	47(5) 	(9(4)	11(5) 	(2(5)

N61	35(4) 	25(4)	35(4) 	(15(4)	10(3) 	5(3)

N62	36(4) 	20(3)	36(5) 	2(3)	18(3) 	1(3)

N63	39(4) 	26(4)	32(4) 	8(4)	5(3) 	4(3)

N76	40(5) 	25(4)	42(4) 	0(3)	0(4) 	9(4)

N77	28(5) 	14(3)	42(4) 	(1(3)	(11(4) 	(2(3)

N78	36(5) 	21(4)	33(4) 	(4(3)	0(3) 	(6(4)

Co3	33(1) 	10(1)	30(1) 	(3(1)	1(1) 	3(1)

C91	37(6) 	52(6)	33(5) 	2(4)	(1(4) 	(13(5)

C92	34(6) 	84(6)	33(5) 	14(5)	7(4) 	(9(6)

C93	47(6) 	95(7)	33(5) 	(10(5)	20(5) 	(4(6)

C94	36(6) 	67(6)	45(6) 	(17(5)	14(5) 	(3(6)

C95	28(5) 	52(5)	25(4) 	(18(4)	2(4) 	(7(5)

C96	22(5) 	50(4)	25(4) 	(17(4)	(1(4) 	(6(5)

C97	41(6) 	47(5)	49(6) 	(18(5)	(8(5) 	(4(6)

C98	46(9) 	51(8)	60(9) 	0	(12(8) 	0

C101	45(5) 	55(6)	27(5) 	10(5)	(2(4) 	(1(5)

C102	43(6) 	76(6)	43(6) 	8(6)	(7(4) 	0(6)

C103	33(5) 	78(7)	30(5) 	12(5)	2(4) 	11(5)

C104	36(5) 	55(6)	23(5) 	6(4)	15(4) 	20(4)

C105	27(4) 	49(5)	24(4) 	2(4)	10(3) 	3(4)

C106	31(4) 	45(4)	22(4) 	(5(4)	17(3) 	7(4)

C107	74(7) 	43(5)	53(6) 	(8(5)	(5(5) 	18(5)

C108	102(12) 	32(8)	91(11) 	0	(19(9) 	0

N91	29(4) 	51(5)	15(4) 	(4(3)	3(3) 	(9(4)

N92	32(7) 	42(5)	26(6) 	0	13(5) 	0

N101	33(4) 	43(4)	19(4) 	5(4)	7(3) 	4(3)

N102	34(6) 	40(5)	13(5) 	0	6(4) 	0

Co4	26(1) 	45(2)	15(1) 	0	4(1) 	0

C111	37(6) 	67(6)	23(5) 	(4(4)	0(4) 	(12(5)

C112	39(6) 	88(7)	21(5) 	(10(5)	0(4) 	(11(6)

C113	46(6) 	96(7)	30(5) 	12(5)	(1(5) 	(20(6)

C114	53(7) 	72(7)	38(5) 	24(5)	(4(5) 	(9(6)

C115	48(6) 	64(5)	19(4) 	15(4)	0(4) 	(6(5)

C116	39(6) 	55(5)	31(4) 	12(4)	(9(4) 	(1(5)

C117	51(7) 	58(5)	47(6) 	19(5)	(22(5) 	(6(6)

C118	57(10) 	59(9)	75(9) 	0	(39(8) 	0

C121	37(5) 	41(5)	40(6) 	(14(5)	11(4) 	6(4)

C122	35(5) 	55(5)	37(5) 	(4(5)	7(4) 	0(5)

C123	41(6) 	60(6)	26(5) 	(6(5)	(6(4) 	(4(5)

C124	56(6) 	42(5)	15(4) 	1(4)	7(4) 	(7(4)

C125	48(5) 	35(4)	24(5) 	1(4)	10(4) 	1(4)

C126	78(6) 	32(4)	24(5) 	1(4)	(10(4) 	3(4)

C127	146(10) 	26(5)	56(7) 	0(5)	(49(7) 	(5(6)

C128	172(14) 	18(7)	71(10) 	0	(61(9) 	0

N111	38(5) 	58(5)	6(3) 	5(3)	(1(3) 	(2(4)

N112	36(7) 	41(5)	23(5) 	0	(7(5) 	0

N121	42(4) 	34(4)	22(4) 	0(4)	8(3) 	(6(3)

N122	70(7) 	30(5)	14(6) 	0	(1(5) 	0

Co5	44(1) 	40(2)	15(1) 	0	5(1) 	0

C201	29(5) 	45(5)	22(4) 	7(4)	2(4) 	(2(5)

C202	45(6) 	42(5)	23(4) 	20(4)	(6(4) 	(12(4)

C203	37(5) 	28(4)	26(4) 	(8(3)	(5(4) 	(5(4)

C204	33(5) 	39(5)	15(4) 	(11(4)	(9(3) 	(5(4)

C205	47(6) 	56(6)	17(5) 	6(4)	(1(4) 	2(5)

C206	42(6) 	66(7)	19(4) 	13(4)	(4(4) 	(7(5)

C207	49(6) 	41(5)	41(6) 	(3(5)	(5(5) 	5(5)

C208	36(6) 	44(6)	33(5) 	(10(5)	(5(4) 	5(5)

N201	61(7) 	74(7)	49(6) 	(15(6)	7(6) 	16(6)

N202	63(7) 	106(10)	33(5) 	15(6)	12(5) 	(9(7)

N203	90(9) 	54(7)	58(7) 	(19(6)	(11(6) 	23(6)

N204	49(6) 	47(6)	37(5) 	3(5)	9(5) 	20(5)

S201	39(2) 	26(2)	21(1) 	5(1)	6(1) 	(1(1)

S202	44(2) 	44(2)	29(2) 	21(1)	(1(1) 	(6(2)

S203	53(2) 	28(2)	33(2) 	9(1)	(2(2) 	(4(2)

S204	30(2) 	31(2)	22(1) 	1(1)	2(1) 	3(1)

Ni66	31(1) 	26(1)	23(1) 	7(1)	(2(1) 	(3(1)

C211	27(5) 	36(5)	26(4) 	5(4)	(3(4) 	(6(4)

C212	28(5) 	36(5)	32(5) 	2(4)	(2(4) 	(2(5)

C213	32(5) 	30(5)	38(5) 	(2(4)	7(4) 	(2(5)

C214	27(5) 	22(4)	39(5) 	(1(4)	(1(4) 	0(4)

C215	21(5) 	36(6)	34(5) 	0(4)	0(4) 	(8(5)

C216	33(5) 	35(5)	27(5) 	(5(4)	(1(4) 	5(5)

C217	27(6) 	15(5)	39(5) 	3(4)	0(4) 	(6(5)

C218	34(6) 	23(5)	46(6) 	(7(5)	(4(5) 	1(4)

N211	28(6) 	63(7)	29(5) 	(5(5)	(5(4) 	(12(5)

N212	62(7) 	44(6)	31(5) 	1(5)	(5(5) 	(2(6)

N213	30(6) 	48(7)	36(5) 	0(5)	2(4) 	(2(5)

N214	52(7) 	30(6)	64(7) 	(19(5)	8(6) 	(16(5)

S211	37(2) 	33(2)	32(2) 	(4(1)	2(2) 	(4(2)

S212	42(2) 	30(2)	25(2) 	4(1)	0(2) 	(3(2)

S213	37(2) 	24(2)	27(2) 	(3(1)	2(1) 	(5(2)

S214	39(2) 	24(2)	43(2) 	(8(2)	4(2) 	(2(2)

Ni77	25(1) 	26(1)	23(1) 	(1(1)	(2(1) 	1(1)

C311	26(8) 	39(8)	27(7) 	0(6)	4(7) 	(7(7)

C312	30(9) 	37(7)	26(8) 	3(6)	3(7) 	(5(7)

C313	29(7) 	19(6)	32(6) 	1(6)	8(6) 	(7(6)

C314	28(8) 	18(7)	38(7) 	0(6)	4(7) 	0(7)

C315	23(10) 	41(11)	29(9) 	(2(8)	5(8) 	(10(10)

C316	32(11) 	37(9)	29(10) 	0(9)	9(9) 	(2(9)

C317	32(8) 	21(8)	32(7) 	3(7)	9(6) 	(8(7)

C318	32(8) 	19(7)	40(8) 	0(7)	3(7) 	0(7)

N311	27(18) 	33(19)	37(17) 	(24(17)	6(13) 	(4(17)

N312	55(19) 	21(16)	39(19) 	(4(17)	17(18) 	(2(14)

N313	33(14) 	45(15)	39(11) 	3(14)	14(11) 	(1(14)

N314	30(14) 	29(14)	41(15) 	(5(13)	6(14) 	(6(12)

S311	21(7) 	44(7)	46(6) 	(6(6)	19(6) 	(5(6)

S312	23(7) 	24(6)	39(7) 	5(6)	12(6) 	10(7)

S313	26(6) 	11(5)	27(6) 	10(5)	6(5) 	(2(5)

S314	42(8) 	25(6)	41(7) 	(5(6)	11(7) 	(1(7)

Ni37	25(5) 	27(5)	47(5) 	4(4)	26(4) 	4(4)

C221	34(7) 	42(6)	37(6) 	12(5)	0(5) 	(7(5)

C222	36(7) 	37(6)	39(6) 	18(5)	(7(5) 	(10(5)

C223	41(7) 	30(5)	35(6) 	9(5)	(11(5) 	(5(5)

C224	37(8) 	33(5)	34(8) 	12(5)	(14(6) 	0(6)

C225	40(10) 	43(7)	40(7) 	8(6)	(3(6) 	(12(7)

C226	42(9) 	38(8)	45(7) 	7(6)	(1(6) 	(5(7)

C227	57(9) 	22(6)	41(8) 	11(6)	(8(6) 	(6(6)

C228	39(10) 	45(8)	31(9) 	9(7)	(13(7) 	0(7)

N221	56(14) 	58(11)	55(10) 	(2(10)	4(10) 	0(10)

N222	67(12) 	74(13)	41(8) 	16(9)	9(7) 	(16(10)

N223	77(12) 	30(8)	82(13) 	(6(8)	(23(9) 	(1(7)

N224	86(12) 	52(10)	27(9) 	8(9)	(2(7) 	15(9)

S221	30(4) 	37(3)	33(3) 	18(2)	6(3) 	3(2)

S222	55(4) 	44(3)	29(3) 	24(3)	1(3) 	(8(3)

S223	50(4) 	35(3)	50(4) 	21(3)	1(3) 	(3(2)

S224	45(3) 	26(2)	31(3) 	12(2)	(9(3) 	4(2)

Ni88	44(2) 	29(2)	36(2) 	19(2)	(6(2) 	(6(1)

C321	36(9) 	34(6)	43(7) 	13(6)	(9(6) 	(11(6)

C322	38(9) 	31(6)	47(7) 	10(6)	(16(6) 	(2(6)

C323	42(8) 	31(6)	45(8) 	17(6)	(15(7) 	(15(6)

C324	34(7) 	38(6)	35(7) 	18(6)	(20(6) 	(7(6)

C325	41(12) 	32(8)	43(8) 	11(8)	(8(7) 	(9(8)

C326	54(11) 	26(10)	56(9) 	9(7)	(5(7) 	1(8)

C327	46(9) 	35(7)	37(9) 	15(7)	(13(7) 	(4(7)

C328	37(10) 	39(8)	35(9) 	15(7)	(19(7) 	(6(7)

N321	59(17) 	49(11)	30(11) 	11(10)	(18(12) 	9(9)

N322	59(15) 	39(12)	56(11) 	6(11)	0(9) 	3(11)

N323	83(15) 	44(10)	35(12) 	(4(9)	4(10) 	(9(9)

N324	55(16) 	66(13)	35(14) 	10(14)	(7(10) 	(5(12)

S321	43(7) 	32(4)	67(7) 	14(4)	5(5) 	(8(4)

S322	45(5) 	34(4)	63(6) 	13(4)	2(4) 	(1(3)

S323	41(6) 	39(4)	48(6) 	20(4)	(11(4) 	4(3)

S324	38(5) 	48(4)	41(5) 	18(4)	(13(4) 	(6(3)

Ni38	39(3) 	35(2)	55(4) 	21(3)	(18(3) 	(5(2)

C231	36(6) 	27(5)	42(6) 	7(5)	(15(5) 	2(5)

C232	36(7) 	27(6)	41(7) 	10(6)	(10(6) 	3(6)

C233	35(7) 	42(6)	55(6) 	(5(5)	(11(6) 	(2(6)

C234	31(7) 	47(6)	51(6) 	1(5)	(17(5) 	1(6)

C235	45(8) 	25(6)	48(8) 	3(6)	(15(6) 	7(6)

C236	43(9) 	38(9)	38(9) 	8(7)	(13(7) 	4(8)

C237	38(8) 	47(8)	47(7) 	2(7)	(3(6) 	0(8)

C238	39(7) 	57(8)	53(7) 	(9(6)	(16(6) 	(2(7)

N231	50(9) 	35(8)	51(9) 	8(7)	4(7) 	4(7)

N232	40(10) 	40(9)	42(8) 	6(8)	(3(7) 	10(8)

N233	64(11) 	55(10)	32(9) 	7(10)	16(8) 	(3(11)

N234	37(9) 	67(12)	47(8) 	5(9)	(18(7) 	9(9)

S231	38(3) 	21(3)	51(4) 	10(2)	(12(3) 	(3(2)

S232	43(3) 	19(3)	41(3) 	7(2)	(11(3) 	9(2)

S233	25(3) 	41(3)	46(4) 	6(3)	(4(3) 	7(3)

S234	42(3) 	52(4)	46(3) 	12(3)	(7(3) 	3(3)

Ni99	32(2) 	25(2)	44(2) 	7(1)	(14(1) 	(3(1)

C331	38(7) 	41(5)	35(7) 	8(5)	(12(6) 	(3(6)

C332	44(7) 	48(5)	42(6) 	17(5)	(17(5) 	(5(6)

C333	43(7) 	38(6)	63(6) 	(10(6)	(34(6) 	1(7)

C334	39(7) 	34(6)	55(6) 	(16(5)	(33(6) 	2(6)

C335	46(8) 	47(6)	48(8) 	(5(6)	(7(7) 	0(7)

C336	39(7) 	40(7)	44(8) 	17(6)	(21(6) 	(10(6)

C337	65(10) 	35(8)	70(9) 	(7(8)	(40(8) 	6(9)

C338	44(9) 	45(9)	61(8) 	(23(7)	(23(7) 	12(8)

N331	62(11) 	71(10)	68(11) 	(17(10)	3(9) 	15(9)

N332	65(12) 	54(11)	43(11) 	6(10)	(16(9) 	(11(10)

N333	117(17) 	53(11)	87(15) 	(30(10)	(57(13) 	34(10)

N334	70(13) 	84(13)	58(10) 	(39(10)	(19(8) 	42(11)

S331	35(3) 	35(3)	41(3) 	12(3)	12(3) 	5(3)

S332	58(4) 	48(4)	58(4) 	30(3)	(15(4) 	(15(3)

S333	68(6) 	23(3)	81(6) 	9(4)	(33(4) 	(1(3)

S334	39(3) 	28(3)	44(3) 	(7(2)	(8(2) 	3(3)

Ni39	37(2) 	25(2)	54(2) 	13(2)	(13(2) 	(3(1)

Table 5. Hydrogen coordinates [( 104] and isotropic displacement parameters [Å2 ( 103].

Atom 	x	y	z	Ueq	S.o.f.

H1	5357	3089	1155	47	1

H2	5627	3336	84	64	1

H3	5647	4282	(309	60	1

H4	5487	4981	513	51	1

H7	5299	5570	1345	43	1

H8	5086	6160	2298	44	1

H9	4839	5724	3348	44	1

H12	4567	5231	4152	44	1

H13	4383	4659	5128	47	1

H14	4381	3648	4942	48	1

H15	4671	3283	3904	51	1

H16	5771	4338	3427	48	1

H17	6331	4109	4225	56	1

H18	6440	3182	4570	53	1

H19	6042	2451	3890	41	1

H22	5665	1879	3107	38	1

H23	5180	1340	2378	43	1

H24	4636	1790	1698	36	1

H27	4116	2312	1139	41	1

H28	3620	2986	641	48	1

H29	3663	3923	1001	49	1

H30	4207	4221	1846	42	1

H31	3284	1525	7190	40	1

H32	3835	1800	8013	42	1

H33	3946	2774	8249	50	1

H34	3492	3410	7780	47	1

H37	3102	4018	6953	66	1

H38	2620	4515	6143	73	1

H39	2070	4069	5532	67	1

H42	1588	3515	4867	48	1

H43	1085	2949	4375	53	1

H44	1133	1968	4651	50	1

H45	1671	1635	5433	49	1

H46	2794	2763	4897	46	1

H47	3061	2544	3832	56	1

H48	3181	1579	3626	61	1

H49	2967	900	4413	52	1

H52	2778	283	5275	50	1

H53	2540	(220	6189	57	1

H54	2283	213	7130	55	1

H57	2062	770	8059	62	1

H58	1789	1424	8825	72	1

H59	1907	2362	8720	79	1

H60	2194	2679	7736	57	1

H61	3276	1638	2063	43	1

H62	3838	1958	2789	51	1

H63	3883	2920	3172	47	1

H64	3381	3515	2676	43	1

H67	2931	4098	2016	56	1

H68	2373	4571	1388	68	1

H69	1916	4077	559	64	1

H72	1522	3474	(295	51	1

H73	1033	2862	(728	46	1

H74	1131	1890	(449	46	1

H75	1668	1596	405	39	1

H76	2819	2659	(200	54	1

H77	3073	2338	(1221	64	1

H78	3164	1391	(1319	66	1

H79	2906	758	(540	55	1

H82	2704	226	437	53	1

H83	2446	(228	1338	59	1

H84	2213	276	2280	51	1

H87	2047	892	3162	49	1

H88	1815	1564	3962	60	1

H89	1906	2515	3771	58	1

H90	2126	2783	2671	45	1

H91	(333	3174	1323	50	1

H92	(595	3463	2402	60	1

H93	(656	4436	2675	68	1

H94	(480	5097	1811	58	1

H97	(239	5655	983	56	1

H98	0	6187	0	65	1

H101	789	4337	826	51	1

H102	1335	4062	1659	66	1

H103	1413	3124	1994	57	1

H104	955	2439	1377	45	1

H107	524	1905	665	70	1

H108	0	1391	0	94	1

H111	339	3175	3636	52	1

H112	610	3467	2557	60	1

H113	638	4461	2278	69	1

H114	448	5093	3155	66	1

H117	229	5639	3994	66	1

H118	0	6170	5000	82	1

H121	(768	4272	4200	46	1

H122	(1327	4025	3388	50	1

H123	(1408	3093	3023	52	1

H124	(951	2389	3576	45	1

H127	(508	1819	4268	98	1

H128	0	1318	5000	113	1