|  | University of Southampton · Department of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	03src086    (300-475)

Empirical formula 	C42H86N18P6

Formula weight 	1029.11

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	P21/c

Unit cell dimensions	a = 30.586(10) Å	( = 90°

b = 9.660(2) Å	( = 94.599(10)°

c = 18.449(5) Å	(  = 90°

Volume	5433(3) Å3

Z	4

Density (calculated)	1.258 Mg / m3

Absorption coefficient	0.247 mm(1

F(000)	2216

Crystal	rod; colourless

Crystal size	0.24 ( 0.05 ( 0.03 mm3

( range for data collection	2.91 ( 27.02°

Index ranges	(38 ( h ( 38, (10 ( k ( 10, (20 ( l ( 23

Reflections collected	12154

Independent reflections	6215 [Rint = 0.1387]

Completeness to ( = 27.02°	52.3 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9926 and 0.9432

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	6215 / 6 / 596

Goodness-of-fit on F2	1.032

Final R indices [F2 > 2((F2)]	R1 = 0.1094, wR2 = 0.1958

R indices (all data)	R1 = 0.2656, wR2 = 0.2640

Extinction coefficient	0.0010(4)

Largest diff. peak and hole	0.216 and (0.277 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SORTAV (R. H. Blessing, Acta Cryst. A51 (1995) 33(37; R. H. Blessing, J. Appl. Cryst. 30 (1997) 421(426). Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: Cameron - A Molecular Graphics Package. (D. M. Watkin, L. Pearce and C. K. Prout, Chemical Crystallography Laboratory, University of Oxford, 1993).

Special details:

Very weak data, not good enough to experimentally find protons.

P1-P2 = 2.770, P2-P3 = 2.795, P1-P3 = 2.809, max deviation = 0.091 (P2), P4-P5 = 2.788, P5-P6 = 2.778, P4-P6 = 2.771, max deviation = 0.096 (N11).

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	3403(4)	(810(20)	(1193(6)	95(8)	1

C2	3104(6)	(1810(30)	(1613(9)	139(11)	1

C3	2894(6)	(2580(30)	(1103(10)	184(15)	1

C4	3072(5)	(2300(20)	(408(8)	119(10)	1

C5	4063(6)	(2550(20)	717(9)	111(9)	1

C6	4213(5)	(3220(30)	1384(9)	141(11)	1

C7	3978(5)	(2480(20)	1951(8)	130(11)	1

C8	3691(5)	(1480(20)	1613(7)	107(9)	1

C9	4040(4)	2590(20)	(1193(7)	83(8)	1

C10	4069(8)	3960(30)	(1606(12)	178(15)	1

C11	4251(11)	4880(30)	(1113(13)	250(20)	1

C12	4395(6)	4310(20)	(442(9)	105(9)	1

C13	4552(4)	2150(20)	1551(7)	100(8)	1

C14	4965(6)	1520(30)	1851(12)	260(20)	1

C15	5205(6)	1180(30)	1278(15)	194(15)	1

C16	4988(4)	1670(30)	603(10)	157(12)	1

C17	3193(4)	3688(19)	1974(7)	68(6)	1

C18	2821(3)	4476(17)	1562(6)	65(6)	1

C19	2855(3)	4395(18)	757(6)	66(6)	1

C20	2864(3)	3133(15)	(355(5)	56(5)	1

C21	2427(3)	3485(17)	(776(5)	73(6)	1

C22	2469(3)	3580(16)	(1591(6)	61(5)	1

C23	2061(3)	4053(16)	(2032(5)	64(6)	1

C24	2209(3)	5720(20)	(2943(6)	79(8)	1

C25	2368(3)	6027(17)	(3694(6)	67(6)	1

C26	2072(3)	5394(18)	(4304(7)	66(6)	1

C27	586(3)	3883(18)	(2075(6)	68(6)	1

C28	341(6)	5070(30)	(1741(9)	135(11)	1

C29	297(7)	6140(30)	(2246(9)	165(14)	1

C30	377(4)	5583(18)	(2971(6)	70(7)	1

C31	804(3)	3913(18)	(4868(6)	68(6)	1

C32	554(4)	3100(20)	(5420(7)	142(11)	1

C33	146(5)	2750(30)	(5154(8)	170(13)	1

C34	174(3)	2925(18)	(4369(7)	82(7)	1

C35	1548(4)	180(20)	(4530(8)	97(8)	1

C36	1445(5)	(960(20)	(5010(9)	129(11)	1

C37	1054(5)	(1600(20)	(4731(8)	125(10)	1

C38	1031(6)	(1210(20)	(3989(10)	146(11)	1

C39	1756(6)	(740(30)	(2308(10)	172(13)	1

C40	1686(6)	(1440(30)	(1617(11)	180(14)	1

C41	1354(6)	(740(30)	(1322(10)	166(13)	1

C42	1154(5)	230(20)	(1845(8)	160(13)	1

N1	3216(2)	512(14)	559(5)	50(4)	1

N2	4010(2)	484(13)	11(5)	47(4)	1

N3	3738(2)	2833(13)	655(5)	59(4)	1

N4	3216(2)	2291(15)	1684(5)	54(4)	1

N5	2867(2)	3041(16)	413(4)	61(5)	1

N6	3422(3)	(1292(16)	(453(5)	75(5)	1

N7	3729(3)	(1567(18)	847(6)	91(7)	1

N8	4267(3)	2820(19)	(488(6)	76(6)	1

N9	4557(2)	2249(14)	798(5)	61(5)	1

N10	1314(2)	4302(13)	(3419(5)	53(4)	1

N11	904(2)	1851(14)	(3175(5)	51(4)	1

N12	1791(2)	1924(14)	(3246(5)	51(3)	1

N13	2133(3)	4262(16)	(2794(5)	59(5)	1

N14	1989(3)	3941(15)	(4178(5)	54(5)	1

N15	519(2)	4139(15)	(2848(4)	53(4)	1

N16	583(2)	3716(13)	(4193(4)	55(4)	1

N17	1352(3)	(70(16)	(3864(5)	74(5)	1

N18	1379(3)	74(16)	(2481(5)	74(5)	1

P1	3286(1)	2094(5)	799(2)	50(1)	1

P2	3599(1)	(345(6)	246(2)	65(2)	1

P3	4115(1)	2043(6)	246(2)	57(2)	1

P4	1773(1)	3554(5)	(3402(2)	47(1)	1

P5	862(1)	3463(5)	(3411(2)	52(2)	1

P6	1353(1)	1055(5)	(3208(2)	60(2)	1

Table 3. Bond lengths [Å] and angles [°].

C1(N6	1.440(15)

C1(C2	1.51(2)

C1(H1A	0.9900

C1(H1B	0.9900

C2(C3	1.40(2)

C2(H2A	0.9900

C2(H2B	0.9900

C3(C4	1.378(19)

C3(H3A	0.9900

C3(H3B	0.9900

C4(N6	1.457(18)

C4(H4A	0.9900

C4(H4B	0.9900

C5(N7	1.43(2)

C5(C6	1.43(2)

C5(H5A	0.9900

C5(H5B	0.9900

C6(C7	1.50(2)

C6(H6A	0.9900

C6(H6B	0.9900

C7(C8	1.42(2)

C7(H7A	0.9900

C7(H7B	0.9900

C8(N7	1.429(15)

C8(H8A	0.9900

C8(H8B	0.9900

C9(N8	1.442(15)

C9(C10	1.54(3)

C9(H9A	0.9900

C9(H9B	0.9900

C10(C11	1.36(3)

C10(H10A	0.9900

C10(H10B	0.9900

C11(C12	1.39(3)

C11(H11A	0.9900

C11(H11B	0.9900

C12(N8	1.49(2)

C12(H12A	0.9900

C12(H12B	0.9900

C13(N9	1.392(14)

C13(C14	1.47(2)

C13(H13A	0.9900

C13(H13B	0.9900

C14(C15	1.37(3)

C14(H14A	0.9900

C14(H14B	0.9900

C15(C16	1.44(2)

C15(H15A	0.9900

C15(H15B	0.9900

C16(N9	1.504(15)

C16(H16A	0.9900

C16(H16B	0.9900

C17(N4	1.456(17)

C17(C18	1.521(17)

C17(H17A	0.9900

C17(H17B	0.9900

C18(C19	1.500(14)

C18(H18A	0.9900

C18(H18B	0.9900

C19(N5	1.456(19)

C19(H19A	0.9900

C19(H19B	0.9900

C20(N5	1.418(12)

C20(C21	1.531(12)

C20(H20A	0.9900

C20(H20B	0.9900

C21(C22	1.522(13)

C21(H21A	0.9900

C21(H21B	0.9900

C22(C23	1.507(13)

C22(H22A	0.9900

C22(H22B	0.9900

C23(N13	1.454(13)

C23(H23A	0.9900

C23(H23B	0.9900

C24(N13	1.461(19)

C24(C25	1.534(15)

C24(H24A	0.9900

C24(H24B	0.9900

C25(C26	1.517(16)

C25(H25A	0.9900

C25(H25B	0.9900

C26(N14	1.448(17)

C26(H26A	0.9900

C26(H26B	0.9900

C27(N15	1.446(13)

C27(C28	1.53(2)

C27(H27A	0.9900

C27(H27B	0.9900

C28(C29	1.39(3)

C28(H28A	0.9900

C28(H28B	0.9900

C29(C30	1.48(2)

C29(H29A	0.9900

C29(H29B	0.9900

C30(N15	1.473(19)

C30(H30A	0.9900

C30(H30B	0.9900

C31(C32	1.455(18)

C31(N16	1.477(12)

C31(H31A	0.9900

C31(H31B	0.9900

C32(C33	1.418(17)

C32(H32A	0.9900

C32(H32B	0.9900

C33(C34	1.453(16)

C33(H33A	0.9900

C33(H33B	0.9900

C34(N16	1.480(14)

C34(H34A	0.9900

C34(H34B	0.9900

C35(N17	1.429(15)

C35(C36	1.43(2)

C35(H35A	0.9900

C35(H35B	0.9900

C36(C37	1.475(19)

C36(H36A	0.9900

C36(H36B	0.9900

C37(C38	1.429(18)

C37(H37A	0.9900

C37(H37B	0.9900

C38(N17	1.480(18)

C38(H38A	0.9900

C38(H38B	0.9900

C39(N18	1.412(18)

C39(C40	1.47(2)

C39(H39A	0.9900

C39(H39B	0.9900

C40(C41	1.37(2)

C40(H40A	0.9900

C40(H40B	0.9900

C41(C42	1.44(2)

C41(H41A	0.9900

C41(H41B	0.9900

C42(N18	1.415(15)

C42(H42A	0.9900

C42(H42B	0.9900

N1(P2	1.581(11)

N1(P1	1.601(12)

N2(P2	1.578(10)

N2(P3	1.594(12)

N3(P1	1.596(9)

N3(P3	1.619(10)

N4(P1	1.673(9)

N4(H4	0.8800

N5(P1	1.685(11)

N6(P2	1.637(12)

N7(P2	1.647(14)

N8(P3	1.647(12)

N9(P3	1.638(9)

N10(P4	1.579(9)

N10(P5	1.603(9)

N11(P6	1.580(9)

N11(P5	1.619(12)

N12(P6	1.586(10)

N12(P4	1.601(13)

N13(P4	1.655(10)

N14(P4	1.666(9)

N14(H14	0.8800

N15(P5	1.666(9)

N16(P5	1.636(8)

N17(P6	1.627(12)

N18(P6	1.639(12)

N6(C1(C2	104.8(14)

N6(C1(H1A	110.8

C2(C1(H1A	110.8

N6(C1(H1B	110.8

C2(C1(H1B	110.8

H1A(C1(H1B	108.9

C3(C2(C1	106.9(15)

C3(C2(H2A	110.3

C1(C2(H2A	110.4

C3(C2(H2B	110.4

C1(C2(H2B	110.3

H2A(C2(H2B	108.6

C4(C3(C2	110.6(17)

C4(C3(H3A	109.5

C2(C3(H3A	109.5

C4(C3(H3B	109.5

C2(C3(H3B	109.5

H3A(C3(H3B	108.1

C3(C4(N6	108.5(14)

C3(C4(H4A	110.0

N6(C4(H4A	110.0

C3(C4(H4B	110.0

N6(C4(H4B	110.0

H4A(C4(H4B	108.4

N7(C5(C6	109.7(14)

N7(C5(H5A	109.8

C6(C5(H5A	109.7

N7(C5(H5B	109.7

C6(C5(H5B	109.7

H5A(C5(H5B	108.2

C5(C6(C7	104.4(16)

C5(C6(H6A	110.9

C7(C6(H6A	110.9

C5(C6(H6B	110.9

C7(C6(H6B	110.9

H6A(C6(H6B	108.9

C8(C7(C6	109.5(13)

C8(C7(H7A	109.8

C6(C7(H7A	109.8

C8(C7(H7B	109.8

C6(C7(H7B	109.8

H7A(C7(H7B	108.2

C7(C8(N7	107.2(14)

C7(C8(H8A	110.3

N7(C8(H8A	110.3

C7(C8(H8B	110.3

N7(C8(H8B	110.3

H8A(C8(H8B	108.5

N8(C9(C10	105.7(17)

N8(C9(H9A	110.6

C10(C9(H9A	110.6

N8(C9(H9B	110.6

C10(C9(H9B	110.6

H9A(C9(H9B	108.7

C11(C10(C9	106(2)

C11(C10(H10A	110.6

C9(C10(H10A	110.6

C11(C10(H10B	110.6

C9(C10(H10B	110.6

H10A(C10(H10B	108.8

C10(C11(C12	115(3)

C10(C11(H11A	108.6

C12(C11(H11A	108.5

C10(C11(H11B	108.5

C12(C11(H11B	108.6

H11A(C11(H11B	107.5

C11(C12(N8	105.5(16)

C11(C12(H12A	110.7

N8(C12(H12A	110.6

C11(C12(H12B	110.6

N8(C12(H12B	110.6

H12A(C12(H12B	108.8

N9(C13(C14	109.1(13)

N9(C13(H13A	109.9

C14(C13(H13A	109.8

N9(C13(H13B	109.9

C14(C13(H13B	109.9

H13A(C13(H13B	108.3

C15(C14(C13	107.8(18)

C15(C14(H14A	110.2

C13(C14(H14A	110.1

C15(C14(H14B	110.1

C13(C14(H14B	110.2

H14A(C14(H14B	108.5

C14(C15(C16	110.4(18)

C14(C15(H15A	109.6

C16(C15(H15A	109.6

C14(C15(H15B	109.6

C16(C15(H15B	109.6

H15A(C15(H15B	108.1

C15(C16(N9	105.5(14)

C15(C16(H16A	110.6

N9(C16(H16A	110.7

C15(C16(H16B	110.6

N9(C16(H16B	110.6

H16A(C16(H16B	108.8

N4(C17(C18	109.7(10)

N4(C17(H17A	109.7

C18(C17(H17A	109.7

N4(C17(H17B	109.7

C18(C17(H17B	109.7

H17A(C17(H17B	108.2

C19(C18(C17	111.1(10)

C19(C18(H18A	109.4

C17(C18(H18A	109.4

C19(C18(H18B	109.4

C17(C18(H18B	109.4

H18A(C18(H18B	108.0

N5(C19(C18	119.0(14)

N5(C19(H19A	107.6

C18(C19(H19A	107.6

N5(C19(H19B	107.5

C18(C19(H19B	107.6

H19A(C19(H19B	107.0

N5(C20(C21	117.1(8)

N5(C20(H20A	108.0

C21(C20(H20A	108.0

N5(C20(H20B	108.0

C21(C20(H20B	108.0

H20A(C20(H20B	107.3

C22(C21(C20	111.9(8)

C22(C21(H21A	109.2

C20(C21(H21A	109.2

C22(C21(H21B	109.2

C20(C21(H21B	109.2

H21A(C21(H21B	107.9

C23(C22(C21	114.8(9)

C23(C22(H22A	108.6

C21(C22(H22A	108.6

C23(C22(H22B	108.6

C21(C22(H22B	108.6

H22A(C22(H22B	107.5

N13(C23(C22	112.3(9)

N13(C23(H23A	109.1

C22(C23(H23A	109.1

N13(C23(H23B	109.1

C22(C23(H23B	109.1

H23A(C23(H23B	107.9

N13(C24(C25	114.9(14)

N13(C24(H24A	108.5

C25(C24(H24A	108.5

N13(C24(H24B	108.6

C25(C24(H24B	108.6

H24A(C24(H24B	107.5

C26(C25(C24	112.3(10)

C26(C25(H25A	109.2

C24(C25(H25A	109.1

C26(C25(H25B	109.1

C24(C25(H25B	109.2

H25A(C25(H25B	107.9

N14(C26(C25	111.9(11)

N14(C26(H26A	109.2

C25(C26(H26A	109.2

N14(C26(H26B	109.2

C25(C26(H26B	109.2

H26A(C26(H26B	107.9

N15(C27(C28	103.5(12)

N15(C27(H27A	111.1

C28(C27(H27A	111.0

N15(C27(H27B	111.1

C28(C27(H27B	111.1

H27A(C27(H27B	109.0

C29(C28(C27	108.0(15)

C29(C28(H28A	110.1

C27(C28(H28A	110.1

C29(C28(H28B	110.1

C27(C28(H28B	110.1

H28A(C28(H28B	108.4

C28(C29(C30	109(2)

C28(C29(H29A	109.9

C30(C29(H29A	109.9

C28(C29(H29B	109.9

C30(C29(H29B	109.9

H29A(C29(H29B	108.3

C29(C30(N15	105.8(12)

C29(C30(H30A	110.6

N15(C30(H30A	110.6

C29(C30(H30B	110.6

N15(C30(H30B	110.6

H30A(C30(H30B	108.7

C32(C31(N16	105.6(11)

C32(C31(H31A	110.6

N16(C31(H31A	110.6

C32(C31(H31B	110.6

N16(C31(H31B	110.6

H31A(C31(H31B	108.8

C33(C32(C31	108.2(12)

C33(C32(H32A	110.0

C31(C32(H32A	110.1

C33(C32(H32B	110.1

C31(C32(H32B	110.0

H32A(C32(H32B	108.4

C32(C33(C34	109.5(11)

C32(C33(H33A	109.8

C34(C33(H33A	109.8

C32(C33(H33B	109.8

C34(C33(H33B	109.8

H33A(C33(H33B	108.2

C33(C34(N16	105.0(10)

C33(C34(H34A	110.8

N16(C34(H34A	110.7

C33(C34(H34B	110.7

N16(C34(H34B	110.8

H34A(C34(H34B	108.8

N17(C35(C36	108.2(16)

N17(C35(H35A	110.0

C36(C35(H35A	110.0

N17(C35(H35B	110.1

C36(C35(H35B	110.1

H35A(C35(H35B	108.4

C35(C36(C37	104.7(14)

C35(C36(H36A	110.8

C37(C36(H36A	110.8

C35(C36(H36B	110.8

C37(C36(H36B	110.8

H36A(C36(H36B	108.9

C38(C37(C36	109.0(14)

C38(C37(H37A	109.9

C36(C37(H37A	109.9

C38(C37(H37B	109.9

C36(C37(H37B	109.9

H37A(C37(H37B	108.3

C37(C38(N17	105.2(12)

C37(C38(H38A	110.7

N17(C38(H38A	110.7

C37(C38(H38B	110.7

N17(C38(H38B	110.7

H38A(C38(H38B	108.8

N18(C39(C40	106.2(12)

N18(C39(H39A	110.5

C40(C39(H39A	110.5

N18(C39(H39B	110.5

C40(C39(H39B	110.5

H39A(C39(H39B	108.7

C41(C40(C39	106.2(17)

C41(C40(H40A	110.5

C39(C40(H40A	110.5

C41(C40(H40B	110.5

C39(C40(H40B	110.5

H40A(C40(H40B	108.7

C40(C41(C42	110.2(16)

C40(C41(H41A	109.6

C42(C41(H41A	109.7

C40(C41(H41B	109.6

C42(C41(H41B	109.6

H41A(C41(H41B	108.1

N18(C42(C41	106.0(14)

N18(C42(H42A	110.6

C41(C42(H42A	110.6

N18(C42(H42B	110.5

C41(C42(H42B	110.5

H42A(C42(H42B	108.7

P2(N1(P1	121.0(6)

P2(N2(P3	123.6(7)

P1(N3(P3	121.7(8)

C17(N4(P1	118.5(11)

C17(N4(H4	120.7

P1(N4(H4	120.7

C20(N5(C19	112.4(13)

C20(N5(P1	113.6(7)

C19(N5(P1	110.4(7)

C1(N6(C4	107.3(10)

C1(N6(P2	123.4(13)

C4(N6(P2	121.9(9)

C5(N7(C8	108.9(12)

C5(N7(P2	120.0(10)

C8(N7(P2	126.0(14)

C9(N8(C12	107.9(15)

C9(N8(P3	121.6(11)

C12(N8(P3	118.8(11)

C13(N9(C16	107.0(11)

C13(N9(P3	122.6(7)

C16(N9(P3	120.1(10)

P4(N10(P5	122.4(8)

P6(N11(P5	120.5(6)

P6(N12(P4	120.8(6)

C23(N13(C24	110.8(13)

C23(N13(P4	116.9(8)

C24(N13(P4	112.3(8)

C26(N14(P4	116.2(10)

C26(N14(H14	121.9

P4(N14(H14	121.9

C27(N15(C30	109.3(11)

C27(N15(P5	120.0(8)

C30(N15(P5	117.9(9)

C34(N16(C31	108.6(8)

C34(N16(P5	119.2(8)

C31(N16(P5	121.4(6)

C35(N17(C38	108.2(11)

C35(N17(P6	123.3(13)

C38(N17(P6	125.0(8)

C39(N18(C42	108.4(11)

C39(N18(P6	119.5(9)

C42(N18(P6	128.4(12)

N3(P1(N1	118.6(5)

N3(P1(N4	106.9(5)

N1(P1(N4	110.7(7)

N3(P1(N5	109.0(6)

N1(P1(N5	108.7(6)

N4(P1(N5	101.5(5)

N1(P2(N2	117.6(7)

N1(P2(N6	111.8(5)

N2(P2(N6	106.7(5)

N1(P2(N7	106.0(6)

N2(P2(N7	113.3(6)

N6(P2(N7	100.2(8)

N2(P3(N3	115.8(5)

N2(P3(N9	115.0(6)

N3(P3(N9	103.6(5)

N2(P3(N8	105.7(7)

N3(P3(N8	115.3(8)

N9(P3(N8	100.6(5)

N10(P4(N12	118.0(5)

N10(P4(N13	111.6(6)

N12(P4(N13	105.8(6)

N10(P4(N14	107.1(5)

N12(P4(N14	111.4(6)

N13(P4(N14	101.6(5)

N10(P5(N11	116.0(5)

N10(P5(N16	107.7(5)

N11(P5(N16	113.9(6)

N10(P5(N15	113.2(6)

N11(P5(N15	104.5(6)

N16(P5(N15	100.5(5)

N11(P6(N12	119.0(7)

N11(P6(N17	113.7(6)

N12(P6(N17	105.8(5)

N11(P6(N18	103.6(5)

N12(P6(N18	110.9(6)

N17(P6(N18	102.7(7)

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	127(12) 	130(30)	29(9) 	4(11)	10(6) 	(15(12)

C2	171(17) 	170(30)	72(14) 	(28(16)	(9(11) 	(86(17)

C3	165(18) 	280(50)	100(18) 	(20(20)	(40(13) 	(110(20)

C4	147(14) 	140(30)	74(13) 	(5(14)	18(9) 	(78(15)

C5	168(17) 	70(30)	94(15) 	22(14)	9(11) 	47(15)

C6	132(14) 	200(30)	88(15) 	(11(17)	(6(10) 	78(15)

C7	134(14) 	200(30)	50(11) 	45(14)	(1(8) 	69(16)

C8	121(12) 	150(30)	47(11) 	9(12)	10(7) 	21(13)

C9	132(12) 	80(30)	36(10) 	(11(11)	10(7) 	(17(11)

C10	270(30) 	180(50)	85(19) 	60(20)	(5(15) 	(40(20)

C11	500(50) 	140(50)	100(20) 	20(20)	(80(30) 	(150(40)

C12	176(16) 	60(30)	89(14) 	(36(14)	40(10) 	(59(15)

C13	66(9) 	150(30)	83(12) 	0(12)	(17(7) 	(2(10)

C14	81(14) 	530(70)	150(20) 	130(30)	(38(12) 	30(20)

C15	98(16) 	240(40)	240(30) 	40(30)	(13(17) 	69(19)

C16	54(9) 	280(40)	140(17) 	(107(19)	1(9) 	30(13)

C17	77(8) 	90(20)	41(9) 	(24(10)	13(5) 	(27(9)

C18	56(7) 	70(20)	65(9) 	(16(9)	7(5) 	3(7)

C19	41(6) 	120(20)	40(9) 	(4(9)	0(5) 	(1(7)

C20	42(6) 	84(18)	42(8) 	9(8)	5(4) 	7(6)

C21	44(6) 	140(20)	34(8) 	0(9)	1(4) 	3(7)

C22	50(7) 	72(18)	59(9) 	(12(8)	(4(5) 	(6(7)

C23	75(8) 	100(20)	14(7) 	5(8)	2(4) 	(22(8)

C24	37(6) 	140(30)	52(9) 	(38(11)	(20(5) 	0(9)

C25	52(7) 	80(20)	66(9) 	8(9)	5(5) 	(13(7)

C26	42(7) 	90(20)	65(9) 	16(11)	1(5) 	10(8)

C27	76(8) 	80(20)	54(9) 	22(9)	17(5) 	37(8)

C28	202(18) 	140(40)	65(14) 	(44(16)	40(11) 	77(18)

C29	250(20) 	200(40)	50(14) 	29(17)	26(12) 	90(20)

C30	91(9) 	80(20)	42(8) 	31(9)	14(6) 	54(10)

C31	69(7) 	110(20)	29(7) 	20(9)	9(5) 	(7(8)

C32	78(10) 	270(30)	79(13) 	(64(15)	26(8) 	(60(13)

C33	128(14) 	300(40)	79(14) 	(62(17)	(1(9) 	(97(17)

C34	50(7) 	120(20)	72(10) 	11(10)	(20(5) 	(27(8)

C35	110(11) 	100(30)	84(12) 	(62(13)	36(8) 	(44(11)

C36	127(14) 	150(40)	110(16) 	(42(17)	26(10) 	(60(14)

C37	113(12) 	180(30)	85(13) 	(50(15)	29(9) 	(53(13)

C38	166(17) 	110(30)	170(20) 	(63(18)	92(14) 	(108(17)

C39	173(18) 	230(40)	126(18) 	90(20)	91(13) 	100(20)

C40	194(19) 	170(40)	190(20) 	100(20)	114(17) 	124(19)

C41	200(20) 	200(40)	98(16) 	59(18)	43(13) 	130(20)

C42	160(15) 	250(40)	75(13) 	85(16)	66(10) 	129(17)

N1	56(6) 	31(14)	64(7) 	(19(7)	5(4) 	(11(5)

N2	51(5) 	19(13)	71(7) 	4(7)	1(4) 	(16(5)

N3	33(5) 	56(14)	88(8) 	(33(8)	5(4) 	(8(5)

N4	73(6) 	51(16)	37(7) 	11(7)	(1(4) 	(7(6)

N5	47(5) 	130(18)	6(6) 	(10(7)	8(3) 	(13(6)

N6	79(7) 	110(19)	34(7) 	5(7)	(2(4) 	(25(7)

N7	93(8) 	140(20)	44(8) 	10(9)	2(5) 	38(9)

N8	83(7) 	90(20)	57(8) 	(14(9)	17(5) 	(39(8)

N9	49(5) 	79(15)	56(7) 	(7(7)	2(4) 	12(6)

N10	38(5) 	75(15)	44(6) 	6(7)	(2(3) 	4(5)

N11	61(6) 	40(14)	52(7) 	29(7)	11(4) 	25(5)

N12	51(3) 	51(3)	51(3) 	0(1)	4(1) 	0(1)

N13	39(5) 	85(18)	52(7) 	14(8)	(5(4) 	(11(6)

N14	68(6) 	61(16)	34(6) 	0(7)	18(4) 	2(6)

N15	51(5) 	82(16)	28(6) 	6(6)	11(3) 	15(6)

N16	36(5) 	94(15)	34(5) 	7(6)	1(3) 	(3(5)

N17	113(8) 	85(18)	30(7) 	(31(7)	42(5) 	(29(8)

N18	90(8) 	85(18)	53(8) 	31(8)	31(5) 	31(7)

P1	42(2) 	65(5)	42(2) 	1(2)	(3(1) 	1(2)

P2	64(2) 	90(6)	41(2) 	3(3)	(2(1) 	(1(2)

P3	46(2) 	75(5)	49(2) 	(6(2)	2(1) 	(9(2)

P4	35(2) 	67(5)	39(2) 	(3(2)	(2(1) 	4(2)

P5	39(2) 	86(5)	31(2) 	(2(2)	2(1) 	5(2)

P6	56(2) 	77(6)	47(2) 	2(2)	13(1) 	3(2)

Table 5. Torsion angles [°].

N6(C1(C2(C3	13(3)

C1(C2(C3(C4	(8(3)

C2(C3(C4(N6	0(3)

N7(C5(C6(C7	(5(3)

C5(C6(C7(C8	2(3)

C6(C7(C8(N7	1(2)

N8(C9(C10(C11	(7(3)

C9(C10(C11(C12	7(4)

C10(C11(C12(N8	(4(4)

N9(C13(C14(C15	(3(3)

C13(C14(C15(C16	5(4)

C14(C15(C16(N9	(5(3)

N4(C17(C18(C19	(51.8(16)

C17(C18(C19(N5	56.4(14)

N5(C20(C21(C22	178.9(13)

C20(C21(C22(C23	(174.6(13)

C21(C22(C23(N13	174.0(13)

N13(C24(C25(C26	53.0(15)

C24(C25(C26(N14	(50.7(16)

N15(C27(C28(C29	(21(2)

C27(C28(C29(C30	17(3)

C28(C29(C30(N15	(6(2)

N16(C31(C32(C33	15(2)

C31(C32(C33(C34	(18(3)

C32(C33(C34(N16	14(2)

N17(C35(C36(C37	21(2)

C35(C36(C37(C38	(21(3)

C36(C37(C38(N17	12(3)

N18(C39(C40(C41	(17(3)

C39(C40(C41(C42	10(4)

C40(C41(C42(N18	1(3)

C18(C17(N4(P1	57.7(11)

C21(C20(N5(C19	(75.6(14)

C21(C20(N5(P1	158.1(11)

C18(C19(N5(C20	175.3(8)

C18(C19(N5(P1	(56.7(10)

C2(C1(N6(C4	(13(2)

C2(C1(N6(P2	(163.6(13)

C3(C4(N6(C1	9(2)

C3(C4(N6(P2	159.9(15)

C6(C5(N7(C8	6(3)

C6(C5(N7(P2	162.2(14)

C7(C8(N7(C5	(4(2)

C7(C8(N7(P2	(158.7(13)

C10(C9(N8(C12	4.9(19)

C10(C9(N8(P3	147.4(15)

C11(C12(N8(C9	(1(2)

C11(C12(N8(P3	(145.0(19)

C14(C13(N9(C16	0(2)

C14(C13(N9(P3	144.6(16)

C15(C16(N9(C13	3(2)

C15(C16(N9(P3	(142.7(17)

C22(C23(N13(C24	(98.2(14)

C22(C23(N13(P4	131.5(11)

C25(C24(N13(C23	169.8(8)

C25(C24(N13(P4	(57.5(12)

C25(C26(N14(P4	56.7(12)

C28(C27(N15(C30	17.5(16)

C28(C27(N15(P5	158.4(12)

C29(C30(N15(C27	(8.1(16)

C29(C30(N15(P5	(149.9(11)

C33(C34(N16(C31	(3.9(18)

C33(C34(N16(P5	(148.8(13)

C32(C31(N16(C34	(6.7(18)

C32(C31(N16(P5	137.3(12)

C36(C35(N17(C38	(14(2)

C36(C35(N17(P6	(173.8(12)

C37(C38(N17(C35	1(2)

C37(C38(N17(P6	160.2(13)

C40(C39(N18(C42	17(3)

C40(C39(N18(P6	177.5(17)

C41(C42(N18(C39	(11(3)

C41(C42(N18(P6	(169.3(15)

P3(N3(P1(N1	2.5(10)

P3(N3(P1(N4	128.5(8)

P3(N3(P1(N5	(122.6(8)

P2(N1(P1(N3	5.1(10)

P2(N1(P1(N4	(119.1(7)

P2(N1(P1(N5	130.3(7)

C17(N4(P1(N3	59.7(9)

C17(N4(P1(N1	(169.7(8)

C17(N4(P1(N5	(54.4(9)

C20(N5(P1(N3	63.4(11)

C19(N5(P1(N3	(64.0(9)

C20(N5(P1(N1	(67.2(11)

C19(N5(P1(N1	165.4(8)

C20(N5(P1(N4	176.0(10)

C19(N5(P1(N4	48.7(10)

P1(N1(P2(N2	(13.7(9)

P1(N1(P2(N6	(137.7(8)

P1(N1(P2(N7	114.1(9)

P3(N2(P2(N1	15.7(10)

P3(N2(P2(N6	142.2(8)

P3(N2(P2(N7	(108.5(9)

C1(N6(P2(N1	89.8(11)

C4(N6(P2(N1	(56.4(17)

C1(N6(P2(N2	(40.1(12)

C4(N6(P2(N2	173.7(14)

C1(N6(P2(N7	(158.3(10)

C4(N6(P2(N7	55.5(15)

C5(N7(P2(N1	178.6(15)

C8(N7(P2(N1	(29.6(14)

C5(N7(P2(N2	(51.1(18)

C8(N7(P2(N2	100.8(12)

C5(N7(P2(N6	62.2(16)

C8(N7(P2(N6	(145.9(12)

P2(N2(P3(N3	(8.4(10)

P2(N2(P3(N9	112.6(7)

P2(N2(P3(N8	(137.4(7)

P1(N3(P3(N2	(1.0(10)

P1(N3(P3(N9	(127.9(8)

P1(N3(P3(N8	123.2(8)

C13(N9(P3(N2	(87.2(14)

C16(N9(P3(N2	53.3(15)

C13(N9(P3(N3	40.3(16)

C16(N9(P3(N3	(179.2(14)

C13(N9(P3(N8	159.8(15)

C16(N9(P3(N8	(59.7(16)

C9(N8(P3(N2	42.3(16)

C12(N8(P3(N2	(179.2(13)

C9(N8(P3(N3	(87.0(16)

C12(N8(P3(N3	51.5(15)

C9(N8(P3(N9	162.3(14)

C12(N8(P3(N9	(59.2(15)

P5(N10(P4(N12	(9.8(8)

P5(N10(P4(N13	(132.7(7)

P5(N10(P4(N14	116.9(7)

P6(N12(P4(N10	7.6(9)

P6(N12(P4(N13	133.3(6)

P6(N12(P4(N14	(117.0(6)

C23(N13(P4(N10	69.6(12)

C24(N13(P4(N10	(60.0(10)

C23(N13(P4(N12	(60.0(12)

C24(N13(P4(N12	170.4(9)

C23(N13(P4(N14	(176.5(11)

C24(N13(P4(N14	53.9(11)

C26(N14(P4(N10	61.4(9)

C26(N14(P4(N12	(168.1(7)

C26(N14(P4(N13	(55.7(10)

P4(N10(P5(N11	15.3(8)

P4(N10(P5(N16	(113.7(7)

P4(N10(P5(N15	136.2(7)

P6(N11(P5(N10	(19.2(9)

P6(N11(P5(N16	106.8(7)

P6(N11(P5(N15	(144.6(6)

C34(N16(P5(N10	172.7(10)

C31(N16(P5(N10	32.4(14)

C34(N16(P5(N11	42.5(11)

C31(N16(P5(N11	(97.9(13)

C34(N16(P5(N15	(68.7(12)

C31(N16(P5(N15	151.0(13)

C27(N15(P5(N10	(78.8(14)

C30(N15(P5(N10	58.8(10)

C27(N15(P5(N11	48.4(13)

C30(N15(P5(N11	(174.0(10)

C27(N15(P5(N16	166.6(12)

C30(N15(P5(N16	(55.7(11)

P5(N11(P6(N12	17.8(9)

P5(N11(P6(N17	(107.9(9)

P5(N11(P6(N18	141.4(8)

P4(N12(P6(N11	(11.7(9)

P4(N12(P6(N17	117.8(8)

P4(N12(P6(N18	(131.6(7)

C35(N17(P6(N11	101.7(13)

C38(N17(P6(N11	(54.7(18)

C35(N17(P6(N12	(30.7(14)

C38(N17(P6(N12	172.8(16)

C35(N17(P6(N18	(147.0(12)

C38(N17(P6(N18	56.5(17)

C39(N18(P6(N11	(176.5(16)

C42(N18(P6(N11	(20.8(18)

C39(N18(P6(N12	(47.8(18)

C42(N18(P6(N12	108.0(17)

C39(N18(P6(N17	64.9(17)

C42(N18(P6(N17	(139.4(17)

Symmetry transformations used to generate equivalent atoms: