|  | University of Southampton · School of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	2007src0194  (306-310-1)

Empirical formula 	C6H4Cl4F8N3O2P3

Formula weight 	536.83

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	P21/c

Unit cell dimensions	a = 6.0475(4) Å	( = 90°

b = 27.1376(15) Å	( = 96.177(3)°

c = 10.4986(7) Å	(  = 90°

Volume	1712.97(19) Å3

Z	4

Density (calculated)	2.082 Mg / m3

Absorption coefficient	1.062 mm(1

F(000)	1048

Crystal	plate; colourless

Crystal size	0.10 ( 0.06 ( 0.02 mm3

( range for data collection	3.39 ( 27.50°

Index ranges	(7 ( h ( 7, (35 ( k ( 35, (12 ( l ( 13

Reflections collected	17197

Independent reflections	3849 [Rint = 0.0523]

Completeness to ( = 27.50°	98.0 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9791 and 0.9012

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	3849 / 0 / 235

Goodness-of-fit on F2	1.100

Final R indices [F2 > 2((F2)]	R1 = 0.0633, wR2 = 0.1287

R indices (all data)	R1 = 0.0771, wR2 = 0.1381

Largest diff. peak and hole	0.767 and (0.509 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SADABS Version 2.10. (G. M. Sheldrick (2003)) Bruker AXS Inc., Madison, Wisconsin, USA. Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: PLATON  (A.L. Spek, J. Appl. Crystallogr. 2003, 36, 7).

Special details:

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	6334(9)	6977(2)	3420(5)	34(1)	1

C2	8465(8)	6740(2)	4034(5)	32(1)	1

C3	9046(8)	6201(2)	3679(5)	33(1)	1

C4	7654(8)	5797(2)	4280(5)	35(1)	1

C5	7482(8)	5284(2)	3583(5)	35(1)	1

C6	5571(8)	5205(2)	2540(5)	31(1)	1

N1	4078(6)	6274(1)	1455(4)	25(1)	1

N2	5445(7)	5891(1)	(716(4)	30(1)	1

N3	5639(7)	6879(1)	(310(4)	34(1)	1

O1	6485(6)	7049(1)	2070(3)	32(1)	1

O2	6039(5)	5425(1)	1363(3)	30(1)	1

F1	10223(5)	7011(1)	3736(3)	49(1)	1

F2	8435(5)	6765(1)	5319(3)	44(1)	1

F3	8845(4)	6151(1)	2387(3)	32(1)	1

F4	11193(5)	6115(1)	4112(3)	50(1)	1

F5	5566(4)	5967(1)	4339(3)	33(1)	1

F6	8557(5)	5730(1)	5499(3)	45(1)	1

F7	9460(5)	5179(1)	3163(3)	43(1)	1

F8	7176(6)	4952(1)	4518(3)	46(1)	1

P1	4714(2)	6812(1)	1035(1)	27(1)	1

P2	4459(2)	5811(1)	611(1)	25(1)	1

P3	5964(2)	6423(1)	(1201(1)	28(1)	1

Cl1	2066(2)	7245(1)	1082(1)	41(1)	1

Cl2	1572(2)	5456(1)	317(1)	38(1)	1

Cl3	4185(2)	6529(1)	(2895(1)	37(1)	1

Cl4	9045(2)	6442(1)	(1700(1)	42(1)	1

Table 3. Bond lengths [Å] and angles [°].

C1(O1	1.443(6)

C1(C2	1.520(7)

C2(F2	1.352(5)

C2(F1	1.357(5)

C2(C3	1.558(7)

C3(F4	1.349(6)

C3(F3	1.355(6)

C3(C4	1.558(7)

C4(F6	1.349(6)

C4(F5	1.352(5)

C4(C5	1.572(7)

C5(F7	1.349(5)

C5(F8	1.358(6)

C5(C6	1.519(7)

C6(O2	1.428(5)

N1(P2	1.571(4)

N1(P1	1.584(4)

N2(P3	1.575(4)

N2(P2	1.588(4)

N3(P3	1.576(4)

N3(P1	1.584(4)

O1(P1	1.578(4)

O2(P2	1.572(3)

P1(Cl1	1.9911(17)

P2(Cl2	1.9876(17)

P3(Cl4	1.9899(17)

P3(Cl3	1.9979(18)

O1(C1(C2	109.5(4)

F2(C2(F1	107.3(4)

F2(C2(C1	107.4(4)

F1(C2(C1	108.8(4)

F2(C2(C3	108.3(4)

F1(C2(C3	104.5(4)

C1(C2(C3	119.9(4)

F4(C3(F3	107.4(4)

F4(C3(C2	108.5(4)

F3(C3(C2	109.6(4)

F4(C3(C4	106.4(4)

F3(C3(C4	109.9(4)

C2(C3(C4	114.7(4)

F6(C4(F5	106.7(4)

F6(C4(C3	107.4(4)

F5(C4(C3	109.0(4)

F6(C4(C5	108.8(4)

F5(C4(C5	108.0(4)

C3(C4(C5	116.5(4)

F7(C5(F8	106.9(4)

F7(C5(C6	111.6(4)

F8(C5(C6	106.0(4)

F7(C5(C4	108.8(4)

F8(C5(C4	104.9(4)

C6(C5(C4	117.8(4)

O2(C6(C5	111.0(4)

P2(N1(P1	121.8(2)

P3(N2(P2	121.0(2)

P3(N3(P1	121.2(2)

C1(O1(P1	120.7(3)

C6(O2(P2	123.1(3)

O1(P1(N1	110.5(2)

O1(P1(N3	106.8(2)

N1(P1(N3	118.2(2)

O1(P1(Cl1	103.33(14)

N1(P1(Cl1	108.49(15)

N3(P1(Cl1	108.45(18)

N1(P2(O2	111.6(2)

N1(P2(N2	118.5(2)

O2(P2(N2	105.41(19)

N1(P2(Cl2	107.19(15)

O2(P2(Cl2	103.42(14)

N2(P2(Cl2	109.67(17)

N2(P3(N3	119.1(2)

N2(P3(Cl4	109.50(16)

N3(P3(Cl4	108.42(18)

N2(P3(Cl3	108.21(17)

N3(P3(Cl3	109.04(18)

Cl4(P3(Cl3	101.04(7)

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	45(3) 	30(2)	27(3) 	(5(2)	10(2) 	0(2)

C2	33(3) 	40(3)	25(2) 	(7(2)	8(2) 	(12(2)

C3	21(2) 	48(3)	30(3) 	(3(2)	6(2) 	0(2)

C4	33(3) 	43(3)	30(3) 	5(2)	8(2) 	8(2)

C5	32(3) 	32(2)	43(3) 	5(2)	8(2) 	8(2)

C6	40(3) 	26(2)	27(2) 	4(2)	8(2) 	0(2)

N1	29(2) 	22(2)	25(2) 	2(1)	9(2) 	0(2)

N2	39(2) 	25(2)	27(2) 	(4(2)	10(2) 	3(2)

N3	48(3) 	26(2)	30(2) 	3(2)	16(2) 	(3(2)

O1	40(2) 	27(2)	30(2) 	(4(1)	7(2) 	(10(1)

O2	34(2) 	26(2)	32(2) 	2(1)	12(1) 	6(1)

F1	42(2) 	61(2)	44(2) 	(11(2)	8(2) 	(25(2)

F2	48(2) 	55(2)	30(2) 	(7(1)	7(1) 	(8(2)

F3	29(1) 	40(2)	30(2) 	0(1)	11(1) 	0(1)

F4	25(2) 	75(2)	49(2) 	3(2)	2(1) 	2(2)

F5	26(1) 	36(2)	39(2) 	4(1)	14(1) 	6(1)

F6	49(2) 	58(2)	27(2) 	4(1)	4(1) 	9(2)

F7	37(2) 	49(2)	46(2) 	9(2)	13(1) 	16(1)

F8	58(2) 	43(2)	38(2) 	11(1)	9(2) 	13(2)

P1	34(1) 	20(1)	28(1) 	1(1)	9(1) 	(1(1)

P2	27(1) 	21(1)	28(1) 	0(1)	7(1) 	(1(1)

P3	28(1) 	30(1)	26(1) 	2(1)	9(1) 	(1(1)

Cl1	48(1) 	31(1)	45(1) 	4(1)	10(1) 	14(1)

Cl2	34(1) 	32(1)	49(1) 	(5(1)	7(1) 	(10(1)

Cl3	32(1) 	51(1)	31(1) 	5(1)	7(1) 	3(1)

Cl4	26(1) 	62(1)	38(1) 	6(1)	10(1) 	(1(1)