|  | University of Southampton · School of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	2007src0354  (TG 3.399)

Empirical formula 	C14H15F9NP

Formula weight 	399.24

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	P21/c

Unit cell dimensions	a = 18.5797(5) Å	( = 90°

b = 10.6257(3) Å	( = 98.718(2)°

c = 8.38670(10) Å	(  = 90°

Volume	1636.59(7) Å3

Z	4

Density (calculated)	1.620 Mg / m3

Absorption coefficient	0.260 mm(1

F(000)	808

Crystal	block; colourless

Crystal size	0.50 ( 0.20 ( 0.10 mm3

( range for data collection	2.93 ( 27.49°

Index ranges	(23 ( h ( 24, (12 ( k ( 13, (10 ( l ( 10

Reflections collected	19829

Independent reflections	3737 [Rint = 0.0411]

Completeness to ( = 27.49°	99.5 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9745 and 0.8810

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	3737 / 0 / 226

Goodness-of-fit on F2	1.047

Final R indices [F2 > 2((F2)]	R1 = 0.0395, wR2 = 0.0978

R indices (all data)	R1 = 0.0530, wR2 = 0.1047

Largest diff. peak and hole	0.328 and (0.442 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SADABS Version 2.10. (G. M. Sheldrick (2003)) Bruker AXS Inc., Madison, Wisconsin, USA. Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: PLATON  (A.L. Spek, J. Appl. Crystallogr. 2003, 36, 7).

Special details:

Chirality: C2 = S.

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	727(1)	(1336(2)	8711(2)	32(1)	1

C2	1163(1)	(514(2)	7734(2)	22(1)	1

C3	826(1)	790(2)	7369(2)	28(1)	1

C4	1162(1)	1603(2)	8795(2)	30(1)	1

C5	1935(1)	1102(2)	9224(2)	23(1)	1

C6	2418(1)	(1030(2)	8872(2)	18(1)	1

C7	3121(1)	(768(2)	9732(2)	19(1)	1

C8	3640(1)	(1664(2)	9809(2)	20(1)	1

C9	4386(1)	(1573(2)	10632(2)	19(1)	1

C10	4642(1)	(547(2)	11617(2)	23(1)	1

C11	5364(1)	(508(2)	12334(2)	26(1)	1

C12	5839(1)	(1474(2)	12086(2)	28(1)	1

C13	5595(1)	(2485(2)	11113(2)	28(1)	1

C14	4870(1)	(2536(2)	10399(2)	24(1)	1

N1	1882(1)	(232(1)	8680(2)	18(1)	1

F1	2456(1)	976(1)	5693(1)	34(1)	1

F2	3301(1)	(168(1)	4637(2)	40(1)	1

F3	2573(1)	1180(1)	3070(1)	44(1)	1

F4	2418(1)	(935(1)	2728(1)	36(1)	1

F5	1581(1)	209(1)	3791(2)	47(1)	1

F6	2320(1)	(1137(1)	5358(1)	32(1)	1

F7	1030(1)	(2469(1)	9007(2)	50(1)	1

F8	645(1)	(838(1)	10133(1)	43(1)	1

F9	57(1)	(1528(1)	7902(2)	50(1)	1

P1	2440(1)	24(1)	4207(1)	21(1)	1

Table 3. Bond lengths [Å] and angles [°].

C1(F8	1.334(2)

C1(F7	1.335(2)

C1(F9	1.340(2)

C1(C2	1.514(2)

C2(N1	1.4784(19)

C2(C3	1.532(2)

C3(C4	1.530(2)

C4(C5	1.521(2)

C5(N1	1.487(2)

C6(N1	1.299(2)

C6(C7	1.419(2)

C7(C8	1.351(2)

C8(C9	1.455(2)

C9(C14	1.396(2)

C9(C10	1.407(2)

C10(C11	1.386(2)

C11(C12	1.389(3)

C12(C13	1.384(3)

C13(C14	1.390(2)

F1(P1	1.6026(10)

F2(P1	1.5990(11)

F3(P1	1.5979(11)

F4(P1	1.6009(10)

F5(P1	1.5940(12)

F6(P1	1.6027(10)

F8(C1(F7	107.06(16)

F8(C1(F9	106.81(15)

F7(C1(F9	106.84(15)

F8(C1(C2	113.48(15)

F7(C1(C2	112.08(15)

F9(C1(C2	110.22(15)

N1(C2(C1	109.90(13)

N1(C2(C3	103.47(13)

C1(C2(C3	113.19(14)

C4(C3(C2	104.38(13)

C5(C4(C3	104.27(14)

N1(C5(C4	104.22(13)

N1(C6(C7	124.26(15)

C8(C7(C6	118.74(15)

C7(C8(C9	126.72(15)

C14(C9(C10	118.83(15)

C14(C9(C8	118.21(14)

C10(C9(C8	122.94(14)

C11(C10(C9	119.84(15)

C10(C11(C12	120.50(16)

C13(C12(C11	120.29(15)

C12(C13(C14	119.54(16)

C13(C14(C9	120.99(16)

C6(N1(C2	123.22(13)

C6(N1(C5	124.80(13)

C2(N1(C5	111.68(12)

F5(P1(F3	90.86(7)

F5(P1(F2	179.53(7)

F3(P1(F2	89.56(7)

F5(P1(F4	90.10(6)

F3(P1(F4	90.87(6)

F2(P1(F4	90.10(6)

F5(P1(F1	89.55(6)

F3(P1(F1	89.56(6)

F2(P1(F1	90.25(6)

F4(P1(F1	179.45(6)

F5(P1(F6	90.02(7)

F3(P1(F6	179.11(7)

F2(P1(F6	89.56(6)

F4(P1(F6	89.29(6)

F1(P1(F6	90.28(6)

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	18(1) 	23(1)	52(1) 	3(1)	4(1) 	0(1)

C2	18(1) 	23(1)	24(1) 	(2(1)	1(1) 	1(1)

C3	22(1) 	26(1)	35(1) 	5(1)	(1(1) 	2(1)

C4	25(1) 	20(1)	46(1) 	(3(1)	3(1) 	4(1)

C5	24(1) 	17(1)	27(1) 	(4(1)	2(1) 	0(1)

C6	20(1) 	16(1)	20(1) 	2(1)	7(1) 	(1(1)

C7	20(1) 	19(1)	19(1) 	1(1)	4(1) 	(1(1)

C8	21(1) 	19(1)	19(1) 	1(1)	5(1) 	(2(1)

C9	19(1) 	20(1)	19(1) 	4(1)	5(1) 	(1(1)

C10	25(1) 	22(1)	22(1) 	3(1)	4(1) 	1(1)

C11	26(1) 	29(1)	22(1) 	2(1)	1(1) 	(6(1)

C12	19(1) 	40(1)	24(1) 	7(1)	2(1) 	(3(1)

C13	22(1) 	32(1)	29(1) 	4(1)	6(1) 	7(1)

C14	24(1) 	25(1)	24(1) 	(1(1)	5(1) 	1(1)

N1	18(1) 	18(1)	18(1) 	1(1)	4(1) 	(1(1)

F1	45(1) 	29(1)	29(1) 	(13(1)	7(1) 	(2(1)

F2	25(1) 	34(1)	61(1) 	(2(1)	7(1) 	0(1)

F3	81(1) 	22(1)	29(1) 	6(1)	8(1) 	(6(1)

F4	64(1) 	25(1)	22(1) 	(6(1)	13(1) 	(5(1)

F5	28(1) 	38(1)	67(1) 	(14(1)	(12(1) 	8(1)

F6	46(1) 	26(1)	25(1) 	4(1)	12(1) 	(4(1)

F7	33(1) 	23(1)	97(1) 	17(1)	15(1) 	2(1)

F8	38(1) 	50(1)	46(1) 	8(1)	23(1) 	(2(1)

F9	21(1) 	40(1)	84(1) 	2(1)	(3(1) 	(10(1)

P1	27(1) 	17(1)	18(1) 	(1(1)	3(1) 	1(1)