|  | University of Southampton · School of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	2007src0399  (307-MAG-12-04)

Empirical formula 	C12H12Cl8N8OP6

Formula weight 	753.72

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	Cc

Unit cell dimensions	a = 14.6358(2) Å	( = 90°

b = 16.3497(2) Å	( = 107.4550(10)°

c = 12.34480(10) Å	(  = 90°

Volume	2817.98(6) Å3

Z	4

Density (calculated)	1.777 Mg / m3

Absorption coefficient	1.167 mm(1

F(000)	1496

Crystal	needle; colourless

Crystal size	0.50 ( 0.02 ( 0.01 mm3

( range for data collection	2.92 ( 27.50°

Index ranges	(18 ( h ( 18, (21 ( k ( 21, (15 ( l ( 16

Reflections collected	23887

Independent reflections	6203 [Rint = 0.0516]

Completeness to ( = 27.50°	99.6 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9884 and 0.5931

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	6203 / 2 / 324

Goodness-of-fit on F2	1.037

Final R indices [F2 > 2((F2)]	R1 = 0.0303, wR2 = 0.0663

R indices (all data)	R1 = 0.0333, wR2 = 0.0677

Absolute structure parameter	0.24(5)

Largest diff. peak and hole	0.353 and (0.401 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SADABS Version 2.10. (G. M. Sheldrick (2003)) Bruker AXS Inc., Madison, Wisconsin, USA. Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: PLATON  (A.L. Spek, J. Appl. Crystallogr. 2003, 36, 7).

Special details:

P1-P2 = 2.742, P2-P3 = 2.771, P1-P3 = 2.784, max deviation from mean plane = 0.107 (N1), P4-P5= 2.782, P5-P6 = 2.758, P4-P6 = 2.773, max deviation from mean plane = 0.042 (N7).

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	4118(2)	5148(2)	9129(2)	15(1)	1

C2	4570(2)	5225(2)	8296(3)	24(1)	1

C3	5461(2)	5594(2)	8545(3)	27(1)	1

C4	5912(2)	5896(2)	9623(3)	27(1)	1

C5	5455(2)	5815(2)	10449(3)	29(1)	1

C6	4562(2)	5445(2)	10220(3)	24(1)	1

C7	159(2)	5555(2)	10363(2)	15(1)	1

C8	(169(2)	5716(2)	9202(2)	19(1)	1

C9	(1138(2)	5603(2)	8618(3)	22(1)	1

C10	(1763(2)	5334(2)	9187(3)	27(1)	1

C11	(1438(2)	5179(2)	10326(3)	31(1)	1

C12	(474(2)	5283(2)	10928(3)	23(1)	1

N1	1601(2)	3005(1)	10073(2)	19(1)	1

N2	2792(2)	4302(1)	10743(2)	17(1)	1

N3	1487(2)	4294(1)	8648(2)	14(1)	1

N4	3214(2)	4749(1)	8835(2)	15(1)	1

N5	1143(2)	5658(1)	11004(2)	15(1)	1

N6	2843(2)	6315(1)	11706(2)	14(1)	1

N7	2779(2)	7967(1)	11380(2)	21(1)	1

N8	1493(2)	6988(1)	9915(2)	17(1)	1

O1	2225(1)	5644(1)	9691(2)	14(1)	1

P1	1050(1)	3463(1)	8942(1)	14(1)	1

P2	2400(1)	3455(1)	11035(1)	16(1)	1

P3	2422(1)	4697(1)	9514(1)	12(1)	1

P4	1933(1)	6192(1)	10613(1)	12(1)	1

P5	3295(1)	7196(1)	12067(1)	15(1)	1

P6	1906(1)	7868(1)	10258(1)	17(1)	1

Cl1	890(1)	2687(1)	7644(1)	18(1)	1

Cl2	(308(1)	3628(1)	8906(1)	23(1)	1

Cl3	1933(1)	3589(1)	12385(1)	33(1)	1

Cl4	3475(1)	2671(1)	11617(1)	37(1)	1

Cl5	3443(1)	7357(1)	13712(1)	22(1)	1

Cl6	4661(1)	7211(1)	12084(1)	31(1)	1

Cl7	866(1)	8622(1)	10366(1)	30(1)	1

Cl8	2262(1)	8362(1)	8956(1)	29(1)	1

Table 3. Bond lengths [Å] and angles [°].

C1(C2	1.385(4)

C1(C6	1.395(4)

C1(N4	1.422(3)

C2(C3	1.385(4)

C3(C4	1.387(5)

C4(C5	1.384(5)

C5(C6	1.391(4)

C7(C12	1.390(4)

C7(C8	1.394(4)

C7(N5	1.429(3)

C8(C9	1.398(4)

C9(C10	1.382(5)

C10(C11	1.367(5)

C11(C12	1.394(4)

N1(P1	1.576(2)

N1(P2	1.577(2)

N2(P2	1.580(2)

N2(P3	1.587(2)

N3(P1	1.590(2)

N3(P3	1.603(2)

N4(P3	1.623(2)

N5(P4	1.634(2)

N6(P5	1.592(2)

N6(P4	1.599(2)

N7(P5	1.580(2)

N7(P6	1.586(2)

N8(P6	1.569(2)

N8(P4	1.587(2)

O1(P3	1.6022(19)

O1(P4	1.604(2)

P1(Cl2	1.9935(10)

P1(Cl1	2.0009(10)

P2(Cl4	1.9894(11)

P2(Cl3	1.9936(11)

P5(Cl5	1.9943(10)

P5(Cl6	1.9943(10)

P6(Cl7	1.9938(11)

P6(Cl8	2.0027(10)

C2(C1(C6	119.8(3)

C2(C1(N4	117.9(2)

C6(C1(N4	122.3(3)

C1(C2(C3	120.2(3)

C2(C3(C4	120.9(3)

C5(C4(C3	118.4(3)

C4(C5(C6	121.7(3)

C5(C6(C1	118.9(3)

C12(C7(C8	120.1(3)

C12(C7(N5	118.2(3)

C8(C7(N5	121.7(3)

C7(C8(C9	119.3(3)

C10(C9(C8	120.3(3)

C11(C10(C9	120.2(3)

C10(C11(C12	120.7(3)

C7(C12(C11	119.5(3)

P1(N1(P2	120.77(14)

P2(N2(P3	122.08(15)

P1(N3(P3	121.35(14)

C1(N4(P3	130.2(2)

C7(N5(P4	125.7(2)

P5(N6(P4	121.34(14)

P5(N7(P6	121.13(15)

P6(N8(P4	123.01(15)

P3(O1(P4	137.22(13)

N1(P1(N3	118.32(12)

N1(P1(Cl2	109.03(10)

N3(P1(Cl2	110.25(9)

N1(P1(Cl1	108.29(10)

N3(P1(Cl1	108.53(9)

Cl2(P1(Cl1	101.00(4)

N1(P2(N2	118.38(12)

N1(P2(Cl4	107.34(10)

N2(P2(Cl4	110.21(10)

N1(P2(Cl3	108.51(10)

N2(P2(Cl3	109.48(10)

Cl4(P2(Cl3	101.59(5)

N2(P3(O1	106.65(12)

N2(P3(N3	116.63(12)

O1(P3(N3	109.57(11)

N2(P3(N4	115.09(13)

O1(P3(N4	101.83(11)

N3(P3(N4	106.02(12)

N8(P4(N6	117.08(12)

N8(P4(O1	103.01(12)

N6(P4(O1	109.66(12)

N8(P4(N5	112.97(13)

N6(P4(N5	107.54(12)

O1(P4(N5	105.94(11)

N7(P5(N6	118.76(13)

N7(P5(Cl5	109.22(10)

N6(P5(Cl5	108.30(9)

N7(P5(Cl6	108.18(11)

N6(P5(Cl6	110.17(9)

Cl5(P5(Cl6	100.71(4)

N8(P6(N7	118.28(12)

N8(P6(Cl7	110.18(10)

N7(P6(Cl7	108.07(10)

N8(P6(Cl8	108.98(10)

N7(P6(Cl8	108.90(11)

Cl7(P6(Cl8	101.04(5)

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	12(1) 	13(1)	20(2) 	1(1)	6(1) 	1(1)

C2	20(2) 	33(2)	18(2) 	1(1)	5(1) 	0(1)

C3	19(2) 	36(2)	31(2) 	6(1)	13(1) 	(2(1)

C4	16(2) 	20(2)	45(2) 	(6(1)	11(1) 	(6(1)

C5	16(2) 	34(2)	37(2) 	(17(1)	6(1) 	(4(1)

C6	19(2) 	30(2)	25(2) 	(11(1)	9(1) 	(7(1)

C7	14(1) 	10(1)	20(1) 	(2(1)	4(1) 	(1(1)

C8	18(1) 	15(1)	23(2) 	0(1)	4(1) 	(1(1)

C9	21(2) 	14(1)	26(2) 	(1(1)	(2(1) 	5(1)

C10	10(1) 	25(2)	42(2) 	(7(1)	2(1) 	0(1)

C11	19(2) 	37(2)	41(2) 	(7(2)	17(1) 	(11(1)

C12	20(2) 	29(2)	18(2) 	(2(1)	6(1) 	(5(1)

N1	26(1) 	12(1)	18(1) 	2(1)	4(1) 	(7(1)

N2	18(1) 	18(1)	13(1) 	3(1)	2(1) 	(2(1)

N3	13(1) 	14(1)	12(1) 	(1(1)	1(1) 	(2(1)

N4	15(1) 	16(1)	15(1) 	(5(1)	4(1) 	(4(1)

N5	15(1) 	16(1)	13(1) 	1(1)	5(1) 	(1(1)

N6	13(1) 	14(1)	13(1) 	0(1)	0(1) 	0(1)

N7	28(1) 	11(1)	19(1) 	0(1)	(1(1) 	(3(1)

N8	18(1) 	14(1)	16(1) 	0(1)	2(1) 	0(1)

O1	18(1) 	9(1)	16(1) 	0(1)	6(1) 	0(1)

P1	14(1) 	12(1)	15(1) 	(2(1)	4(1) 	(3(1)

P2	20(1) 	14(1)	13(1) 	2(1)	4(1) 	(1(1)

P3	12(1) 	12(1)	12(1) 	0(1)	3(1) 	(1(1)

P4	12(1) 	11(1)	13(1) 	(1(1)	3(1) 	(1(1)

P5	15(1) 	14(1)	15(1) 	(2(1)	3(1) 	(3(1)

P6	22(1) 	11(1)	16(1) 	0(1)	4(1) 	(1(1)

Cl1	20(1) 	17(1)	18(1) 	(5(1)	6(1) 	(4(1)

Cl2	15(1) 	22(1)	35(1) 	(6(1)	11(1) 	(4(1)

Cl3	56(1) 	29(1)	21(1) 	(5(1)	21(1) 	(15(1)

Cl4	32(1) 	30(1)	40(1) 	14(1)	(1(1) 	11(1)

Cl5	29(1) 	19(1)	15(1) 	(3(1)	3(1) 	(4(1)

Cl6	18(1) 	36(1)	43(1) 	(11(1)	13(1) 	(10(1)

Cl7	37(1) 	20(1)	31(1) 	1(1)	8(1) 	11(1)

Cl8	37(1) 	29(1)	22(1) 	5(1)	9(1) 	(12(1)