|  | University of Southampton · School of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	2007src0400  (306-MAG-11-01)

Empirical formula 	C12H26Cl8N8P6

Formula weight 	751.83

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	P21/c

Unit cell dimensions	a = 8.65180(10) Å	( = 90°

b = 11.36330(10) Å	( = 102.0060(10)°

c = 16.0178(2) Å	(  = 90°

Volume	1540.31(3) Å3

Z	2

Density (calculated)	1.621 Mg / m3

Absorption coefficient	1.064 mm(1

F(000)	760

Crystal	block; colourless

Crystal size	0.55 ( 0.30 ( 0.30 mm3

( range for data collection	3.16 ( 27.50°

Index ranges	(11 ( h ( 10, (14 ( k ( 13, (20 ( l ( 20

Reflections collected	20502

Independent reflections	3526 [Rint = 0.0284]

Completeness to ( = 27.50°	99.5 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.7408 and 0.5922

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	3526 / 0 / 155

Goodness-of-fit on F2	1.070

Final R indices [F2 > 2((F2)]	R1 = 0.0284, wR2 = 0.0705

R indices (all data)	R1 = 0.0321, wR2 = 0.0726

Largest diff. peak and hole	0.545 and (0.483 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SADABS Version 2.10. (G. M. Sheldrick (2003)) Bruker AXS Inc., Madison, Wisconsin, USA. Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: PLATON  (A.L. Spek, J. Appl. Crystallogr. 2003, 36, 7).

Special details:

P1-P2 = 2.783, P2-P3 = 2.736, P1-P3 = 2.781, max deviation from mean plane = 0.038 (N1).

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	2772(2)	5801(2)	632(1)	18(1)	1

C2	2030(2)	6983(2)	354(1)	19(1)	1

C3	445(2)	7106(2)	623(1)	21(1)	1

C4	(413(2)	8233(2)	319(1)	29(1)	1

C5	(2025(2)	8312(2)	564(1)	35(1)	1

C6	(2926(3)	9413(2)	240(2)	50(1)	1

N1	7284(2)	5194(1)	1214(1)	18(1)	1

N2	7511(2)	3621(1)	2514(1)	26(1)	1

N3	4978(2)	3584(1)	1179(1)	19(1)	1

N4	4231(2)	5595(1)	314(1)	15(1)	1

P1	5667(1)	4639(1)	706(1)	14(1)	1

P2	8255(1)	4658(1)	2069(1)	17(1)	1

P3	5886(1)	3057(1)	2051(1)	16(1)	1

Cl1	10372(1)	4124(1)	1885(1)	29(1)	1

Cl2	8893(1)	5946(1)	2913(1)	36(1)	1

Cl3	6227(1)	1336(1)	1903(1)	39(1)	1

Cl4	4444(1)	3037(1)	2876(1)	30(1)	1

Table 3. Bond lengths [Å] and angles [°].

C1(N4	1.475(2)

C1(C2	1.515(2)

C2(C3	1.527(2)

C3(C4	1.509(2)

C4(C5	1.528(3)

C5(C6	1.508(3)

N1(P2	1.5723(14)

N1(P1	1.5954(14)

N2(P2	1.5813(15)

N2(P3	1.5823(15)

N3(P3	1.5720(14)

N3(P1	1.5975(14)

N4(P1	1.6718(14)

N4(P1i	1.6748(13)

P1(N4i	1.6748(13)

P1(P1i	2.4562(8)

P2(Cl2	1.9910(6)

P2(Cl1	2.0085(6)

P3(Cl4	1.9974(6)

P3(Cl3	1.9990(6)

N4(C1(C2	112.27(13)

C1(C2(C3	110.40(14)

C4(C3(C2	113.43(15)

C3(C4(C5	112.44(17)

C6(C5(C4	113.24(19)

P2(N1(P1	122.94(9)

P2(N2(P3	119.70(9)

P3(N3(P1	122.69(9)

C1(N4(P1	126.57(11)

C1(N4(P1i	125.79(11)

P1(N4(P1i	94.43(7)

N1(P1(N3	115.40(7)

N1(P1(N4	116.02(7)

N3(P1(N4	110.10(7)

N1(P1(N4i	110.01(7)

N3(P1(N4i	116.37(7)

N4(P1(N4i	85.57(7)

N1(P1(P1i	122.14(6)

N3(P1(P1i	122.46(6)

N4(P1(P1i	42.83(5)

N4i(P1(P1i	42.74(5)

N1(P2(N2	119.18(8)

N1(P2(Cl2	109.17(6)

N2(P2(Cl2	108.84(6)

N1(P2(Cl1	109.14(6)

N2(P2(Cl1	108.07(6)

Cl2(P2(Cl1	100.87(3)

N3(P3(N2	119.57(8)

N3(P3(Cl4	109.09(6)

N2(P3(Cl4	108.10(6)

N3(P3(Cl3	109.06(6)

N2(P3(Cl3	108.26(7)

Cl4(P3(Cl3	101.21(3)

Symmetry transformations used to generate equivalent atoms:

(i) (x+1,(y+1,(z

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	19(1) 	21(1)	15(1) 	2(1)	6(1) 	2(1)

C2	20(1) 	20(1)	16(1) 	1(1)	4(1) 	3(1)

C3	18(1) 	26(1)	19(1) 	(2(1)	3(1) 	2(1)

C4	31(1) 	34(1)	23(1) 	5(1)	10(1) 	14(1)

C5	27(1) 	44(1)	35(1) 	2(1)	9(1) 	9(1)

C6	44(1) 	59(2)	50(2) 	6(1)	15(1) 	28(1)

N1	19(1) 	19(1)	13(1) 	4(1)	0(1) 	(2(1)

N2	21(1) 	37(1)	16(1) 	13(1)	(2(1) 	(4(1)

N3	19(1) 	21(1)	14(1) 	6(1)	(1(1) 	(3(1)

N4	17(1) 	19(1)	9(1) 	2(1)	2(1) 	4(1)

P1	16(1) 	15(1)	9(1) 	3(1)	1(1) 	1(1)

P2	16(1) 	21(1)	12(1) 	2(1)	(1(1) 	(1(1)

P3	19(1) 	18(1)	12(1) 	6(1)	3(1) 	1(1)

Cl1	18(1) 	32(1)	36(1) 	8(1)	5(1) 	3(1)

Cl2	45(1) 	35(1)	23(1) 	(11(1)	(7(1) 	0(1)

Cl3	63(1) 	21(1)	30(1) 	3(1)	2(1) 	12(1)

Cl4	26(1) 	45(1)	20(1) 	7(1)	10(1) 	(1(1)