|  | University of Southampton · Department of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	02SRC017

Empirical formula 	C16H24O8

Formula weight 	344.35

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	P21

Unit cell dimensions	a = 8.1183(7) Å

b = 5.9280(5) Å	( = 113.000(7)°

c = 9.0398(7) Å

Volume	400.46(6) Å3

Z	1

Density (calculated)	1.428 Mg / m3

Absorption coefficient	0.115 mm(1

F(000)	184

## Crystal	Colourless Plate

Crystal size	0.20 ( 0.15 ( 0.02 mm3

( range for data collection	4.22 ( 25.01°

Index ranges	(9 ( h ( 9, (6 ( k ( 7, (10 ( l ( 10

Reflections collected	3809

Independent reflections	1360 [Rint = 0.0637]

Completeness to ( = 25.01°	99.2 %

Max. and min. transmission	0.9886 and 0.9774

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	1360 / 1 / 158

Goodness-of-fit on F2	0.995

Final R indices [F2 > 2((F2)]	R1 = 0.0374, wR2 = 0.0680

R indices (all data)	R1 = 0.0609, wR2 = 0.0751

Absolute structure parameter	not reliably determined

Extinction coefficient	0.048(6)

Largest diff. peak and hole	0.178 and (0.184 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SORTAV (R. H. Blessing, Acta Cryst. A51 (1995) 33(37; R. H. Blessing, J. Appl. Cryst. 30 (1997) 421(426). Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: Cameron - A Molecular Graphics Package. (D. M. Watkin, L. Pearce and C. K. Prout, Chemical Crystallography Laboratory, University of Oxford, 1993).

Special details: All hydrogen atoms were located from the difference map and fully refined.

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	3783(4)	1865(6)	6855(3)	25(1)	1

C2	5490(4)	(1168(5)	8780(3)	25(1)	1

C3	5575(3)	781(4)	7769(3)	20(1)	1

C4	7453(4)	3655(5)	7753(3)	21(1)	1

C5	7175(3)	2034(4)	6332(3)	19(1)	1

C6	9110(3)	1649(5)	6537(3)	19(1)	1

C7	10003(4)	5269(5)	7330(3)	26(1)	1

C8	9471(3)	3881(5)	8482(3)	21(1)	1

O1	6808(2)	2410(3)	8764(2)	22(1)	1

O2	6406(2)	58(3)	6700(2)	20(1)	1

O3	10064(2)	1650(3)	8225(2)	21(1)	1

O4	9667(2)	3692(3)	6012(2)	22(1)	1

Table 3. Bond lengths [Å] and angles [°].

C1(C3	1.507(4)

C2(C3	1.491(4)

C3(O1	1.429(3)

C3(O2	1.443(3)

C4(O1	1.424(3)

C4(C8	1.514(4)

C4(C5	1.548(3)

C5(O2	1.426(3)

C5(C6	1.525(4)

C6(O3	1.416(3)

C6(O4	1.437(3)

C7(O4	1.453(3)

C7(C8	1.517(4)

C8(O3	1.456(3)

O1(C3(O2	103.08(19)

O1(C3(C2	109.1(2)

O2(C3(C2	109.0(2)

O1(C3(C1	110.2(2)

O2(C3(C1	111.25(19)

C2(C3(C1	113.6(2)

O1(C4(C8	111.9(2)

O1(C4(C5	103.9(2)

C8(C4(C5	101.42(19)

O2(C5(C6	111.9(2)

O2(C5(C4	104.57(18)

C6(C5(C4	100.52(19)

O3(C6(O4	104.19(19)

O3(C6(C5	103.59(17)

O4(C6(C5	106.0(2)

O4(C7(C8	101.6(2)

O3(C8(C4	102.7(2)

O3(C8(C7	100.5(2)

C4(C8(C7	107.4(2)

C4(O1(C3	106.80(18)

C5(O2(C3	105.91(19)

C6(O3(C8	95.54(18)

C6(O4(C7	104.70(17)

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	18(2) 	29(2)	27(2) 	(3(2)	9(1) 	(1(1)

C2	27(2) 	27(2)	24(2) 	(1(1)	13(1) 	(2(2)

C3	20(2) 	25(2)	17(1) 	(5(1)	10(1) 	(1(1)

C4	22(2) 	20(2)	25(1) 	0(1)	12(1) 	0(1)

C5	22(2) 	17(2)	19(1) 	2(1)	9(1) 	(2(1)

C6	21(2) 	22(2)	19(1) 	3(1)	12(1) 	(3(1)

C7	27(2) 	20(2)	33(2) 	(1(1)	14(1) 	(4(2)

C8	21(2) 	21(2)	20(1) 	(6(1)	8(1) 	(1(1)

O1	21(1) 	29(1)	18(1) 	(5(1)	10(1) 	(4(1)

O2	23(1) 	21(1)	19(1) 	(3(1)	13(1) 	(3(1)

O3	21(1) 	22(1)	19(1) 	0(1)	8(1) 	3(1)

O4	26(1) 	20(1)	23(1) 	3(1)	12(1) 	0(1)

Table 5. Hydrogen coordinates [( 104] and isotropic displacement parameters [Å2 ( 103].

Atom 	x	y	z	Ueq	S.o.f.

H2B	6680(40)	(1800(60)	9450(30)	50(9)	1

H2C	4920(40)	(620(40)	9540(30)	35(8)	1

H4	6850(30)	5120(50)	7410(30)	26(7)	1

H5	6400(30)	2680(40)	5270(30)	17(6)	1

H6	9390(30)	200(50)	5950(30)	20(6)	1

H7A	9240(30)	6570(50)	6920(30)	18(7)	1

H7B	11230(40)	5680(50)	7760(30)	35(8)	1

H8	9990(30)	4320(40)	9550(30)	24(8)	1

H1A	3880(40)	3120(60)	6210(30)	36(8)	1

H1B	3260(30)	2380(50)	7710(30)	31(7)	1

H1C	2990(30)	790(50)	6230(30)	27(8)	1

H2A	4780(30)	(2250(50)	8100(30)	20(7)	1