|  | University of Southampton · School of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	00tam081

Empirical formula 	C15H25Cl8N9P6S

Formula weight 	832.92

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Orthorhombic

Space group 	P212121

Unit cell dimensions	a = 8.5829(17) Å	( = 90°

b = 15.587(3) Å	( = 90°

c = 25.277(5) Å	(  = 90°

Volume	3381.6(12) Å3

Z	4

Density (calculated)	1.636 Mg / m3

Absorption coefficient	1.039 mm(1

F(000)	1680

Crystal	rod; colourless

Crystal size	0.68 ( 0.20 ( 0.18 mm3

( range for data collection	3.07 ( 27.48°

Index ranges	(11 ( h ( 11, (20 ( k ( 20, (31 ( l ( 32

Reflections collected	20485

Independent reflections	7560 [Rint = 0.0819]

Completeness to ( = 27.48°	99.0 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.8351 and 0.5386

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	7560 / 0 / 356

Goodness-of-fit on F2	1.033

Final R indices [F2 > 2((F2)]	R1 = 0.0453, wR2 = 0.1003

R indices (all data)	R1 = 0.0665, wR2 = 0.1127

Absolute structure parameter	0.12(7)

Largest diff. peak and hole	0.793 and (0.974 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SADABS Version 2.10. (G. M. Sheldrick (2003)) Bruker AXS Inc., Madison, Wisconsin, USA. Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: PLATON  (A.L. Spek, J. Appl. Crystallogr. 2003, 36, 7).

Special details:

P1-P2 = 2.791, P2-P3 = 2.722, P1-P3 = 2.781, P4-P5 = 2.816, P5-P6 = 2.713, P4-P6 = 2.828.

Max deviation from mean plane = 0.042 (P3), 0.066 (N9).

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	7803(5)	(2622(2)	(3259(2)	33(1)	1

C2	6727(5)	(2822(3)	(3649(2)	39(1)	1

C3	7271(7)	(2923(3)	(4164(2)	50(1)	1

C4	8819(7)	(2807(3)	(4294(2)	56(1)	1

C5	9879(7)	(2628(3)	(3896(2)	59(2)	1

C6	9368(6)	(2536(3)	(3373(2)	47(1)	1

C7	5021(6)	(2908(4)	(3544(2)	60(1)	1

C8	9358(10)	(2835(4)	(4867(3)	93(3)	1

C9	5001(5)	(3323(3)	(1621(2)	37(1)	1

C10	4714(5)	(2614(3)	(1228(2)	33(1)	1

C11	5061(4)	(2861(2)	(660(2)	27(1)	1

C12	4490(4)	(2174(3)	(274(1)	27(1)	1

C13	4213(5)	(3150(2)	496(2)	31(1)	1

C14	4906(13)	(3408(4)	994(2)	135(5)	1

C15	5274(6)	(2843(3)	1387(2)	45(1)	1

N1	9248(4)	(3890(2)	(2196(1)	28(1)	1

N2	9003(4)	(5282(2)	(2839(2)	45(1)	1

N3	6463(4)	(4307(2)	(2631(1)	32(1)	1

N4	6687(4)	(3494(2)	(1694(1)	30(1)	1

N5	4910(4)	(2367(2)	281(1)	28(1)	1

N6	5665(4)	(1968(2)	1232(1)	31(1)	1

N7	6554(3)	(955(2)	430(1)	31(1)	1

N8	4829(4)	500(2)	352(2)	39(1)	1

N9	3595(3)	(971(2)	752(1)	29(1)	1

P1	7439(1)	(3642(1)	(2274(1)	25(1)	1

P2	10028(1)	(4674(1)	(2477(1)	33(1)	1

P3	7206(1)	(5119(1)	(2885(1)	34(1)	1

P4	5175(1)	(1538(1)	670(1)	24(1)	1

P5	6436(1)	15(1)	294(1)	31(1)	1

P6	3368(1)	(33(1)	550(1)	27(1)	1

S1	7208(1)	(2429(1)	(2593(1)	35(1)	1

Cl1	11100(2)	(5370(1)	(1922(1)	57(1)	1

Cl2	11862(1)	(4292(1)	(2901(1)	61(1)	1

Cl3	6113(2)	(6166(1)	(2618(1)	64(1)	1

Cl4	6630(2)	(5167(1)	(3650(1)	51(1)	1

Cl5	8042(1)	668(1)	697(1)	47(1)	1

Cl6	7183(1)	204(1)	(450(1)	49(1)	1

Cl7	1762(1)	(14(1)	(29(1)	40(1)	1

Cl8	2278(1)	646(1)	1109(1)	41(1)	1

Table 3. Bond lengths [Å] and angles [°].

C1(C6	1.380(6)

C1(C2	1.386(6)

C1(S1	1.785(4)

C2(C3	1.392(6)

C2(C7	1.494(7)

C3(C4	1.381(8)

C4(C5	1.384(9)

C4(C8	1.521(7)

C5(C6	1.401(7)

C9(N4	1.483(5)

C9(C10	1.506(6)

C10(C11	1.517(6)

C11(C12	1.530(5)

C12(N5	1.480(5)

C13(C14	1.451(7)

C13(N5	1.463(5)

C14(C15	1.365(7)

C15(N6	1.458(5)

N1(P2	1.565(3)

N1(P1	1.612(3)

N2(P3	1.567(4)

N2(P2	1.584(4)

N3(P3	1.557(3)

N3(P1	1.610(3)

N4(P1	1.618(3)

N5(P4	1.639(3)

N6(P4	1.628(3)

N7(P5	1.554(3)

N7(P4	1.610(3)

N8(P5	1.580(3)

N8(P6	1.585(3)

N9(P6	1.560(3)

N9(P4	1.632(3)

P1(S1	2.0644(14)

P2(Cl2	1.9949(16)

P2(Cl1	1.9983(16)

P3(Cl4	1.9975(16)

P3(Cl3	2.0002(16)

P5(Cl5	1.9924(15)

P5(Cl6	2.0090(16)

P6(Cl8	1.9982(14)

P6(Cl7	2.0099(14)

C6(C1(C2	121.5(4)

C6(C1(S1	117.3(4)

C2(C1(S1	121.2(3)

C1(C2(C3	117.8(4)

C1(C2(C7	123.2(4)

C3(C2(C7	119.0(5)

C4(C3(C2	122.1(5)

C3(C4(C5	119.1(5)

C3(C4(C8	121.0(6)

C5(C4(C8	119.8(6)

C4(C5(C6	120.1(5)

C1(C6(C5	119.4(5)

N4(C9(C10	111.9(3)

C9(C10(C11	113.9(4)

C10(C11(C12	111.3(3)

N5(C12(C11	112.6(3)

C14(C13(N5	112.7(4)

C15(C14(C13	123.2(6)

C14(C15(N6	117.5(4)

P2(N1(P1	122.9(2)

P3(N2(P2	119.5(2)

P3(N3(P1	122.8(2)

C9(N4(P1	121.8(3)

C13(N5(C12	114.9(3)

C13(N5(P4	119.5(3)

C12(N5(P4	116.1(3)

C15(N6(P4	124.1(3)

P5(N7(P4	125.74(19)

P5(N8(P6	118.00(19)

P6(N9(P4	124.7(2)

N3(P1(N1	114.58(17)

N3(P1(N4	113.08(19)

N1(P1(N4	107.88(19)

N3(P1(S1	108.64(14)

N1(P1(S1	111.10(13)

N4(P1(S1	100.71(14)

N1(P2(N2	119.53(19)

N1(P2(Cl2	110.40(14)

N2(P2(Cl2	107.87(16)

N1(P2(Cl1	107.54(14)

N2(P2(Cl1	109.65(16)

Cl2(P2(Cl1	100.11(7)

N3(P3(N2	120.29(19)

N3(P3(Cl4	109.14(14)

N2(P3(Cl4	108.03(16)

N3(P3(Cl3	109.40(14)

N2(P3(Cl3	107.72(17)

Cl4(P3(Cl3	100.43(7)

N7(P4(N6	111.79(18)

N7(P4(N9	110.68(16)

N6(P4(N9	109.06(18)

N7(P4(N5	108.75(17)

N6(P4(N5	103.53(16)

N9(P4(N5	112.86(17)

N7(P5(N8	120.11(17)

N7(P5(Cl5	109.83(14)

N8(P5(Cl5	108.22(14)

N7(P5(Cl6	109.16(14)

N8(P5(Cl6	107.18(16)

Cl5(P5(Cl6	100.55(6)

N9(P6(N8	119.70(16)

N9(P6(Cl8	108.88(13)

N8(P6(Cl8	108.38(14)

N9(P6(Cl7	109.74(13)

N8(P6(Cl7	107.77(15)

Cl8(P6(Cl7	100.69(6)

C1(S1(P1	100.82(13)

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	48(2) 	23(2)	28(2) 	4(2)	9(2) 	7(2)

C2	56(3) 	31(2)	30(2) 	9(2)	1(2) 	6(2)

C3	89(4) 	31(2)	30(3) 	7(2)	(1(3) 	10(2)

C4	103(4) 	22(2)	43(3) 	9(2)	28(3) 	(2(2)

C5	68(3) 	33(3)	75(4) 	5(3)	39(3) 	(3(2)

C6	58(3) 	31(2)	53(3) 	2(2)	8(2) 	(4(2)

C7	53(3) 	76(4)	51(3) 	6(3)	(12(3) 	13(3)

C8	180(8) 	39(3)	60(4) 	3(3)	64(5) 	(3(4)

C9	26(2) 	59(3)	26(2) 	(9(2)	4(2) 	(1(2)

C10	31(2) 	42(2)	24(2) 	(4(2)	2(2) 	5(2)

C11	25(2) 	28(2)	28(2) 	0(2)	4(2) 	(2(2)

C12	32(2) 	31(2)	19(2) 	(1(2)	0(2) 	2(2)

C13	35(2) 	24(2)	32(2) 	(2(2)	7(2) 	(1(2)

C14	304(13) 	56(4)	46(4) 	26(3)	(68(6) 	(84(6)

C15	63(3) 	34(2)	37(3) 	12(2)	(14(2) 	(7(2)

N1	29(2) 	26(2)	30(2) 	(5(1)	(2(1) 	1(1)

N2	52(2) 	38(2)	44(2) 	(18(2)	(2(2) 	6(2)

N3	31(2) 	35(2)	28(2) 	(7(2)	(1(1) 	(6(1)

N4	34(2) 	41(2)	16(2) 	(3(2)	(2(1) 	10(2)

N5	42(2) 	20(2)	20(2) 	0(1)	1(1) 	1(1)

N6	39(2) 	29(2)	24(2) 	(2(1)	(6(1) 	(2(1)

N7	31(2) 	22(2)	41(2) 	0(2)	5(2) 	2(1)

N8	36(2) 	21(2)	61(3) 	7(2)	6(2) 	4(1)

N9	31(2) 	21(2)	34(2) 	3(1)	4(1) 	4(1)

P1	29(1) 	25(1)	20(1) 	(4(1)	2(1) 	0(1)

P2	36(1) 	31(1)	31(1) 	(5(1)	4(1) 	5(1)

P3	47(1) 	28(1)	25(1) 	(6(1)	1(1) 	(7(1)

P4	28(1) 	21(1)	24(1) 	(2(1)	2(1) 	1(1)

P5	29(1) 	24(1)	39(1) 	1(1)	7(1) 	(1(1)

P6	27(1) 	23(1)	31(1) 	(1(1)	1(1) 	3(1)

S1	51(1) 	26(1)	28(1) 	0(1)	3(1) 	6(1)

Cl1	69(1) 	50(1)	53(1) 	2(1)	(8(1) 	25(1)

Cl2	47(1) 	67(1)	70(1) 	(1(1)	27(1) 	6(1)

Cl3	99(1) 	43(1)	50(1) 	(2(1)	3(1) 	(33(1)

Cl4	78(1) 	49(1)	27(1) 	(13(1)	(6(1) 	2(1)

Cl5	42(1) 	40(1)	58(1) 	(5(1)	3(1) 	(15(1)

Cl6	59(1) 	45(1)	42(1) 	10(1)	14(1) 	5(1)

Cl7	44(1) 	39(1)	36(1) 	2(1)	(10(1) 	4(1)

Cl8	45(1) 	37(1)	41(1) 	(11(1)	3(1) 	10(1)