|  | University of Southampton · School of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	2007src1029   (EV_062_5)

Empirical formula 	C14H15F6N2O2P

Formula weight 	388.25

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	P21/n

Unit cell dimensions	a = 7.916(5) Å	( = 90.000(5)°

b = 9.901(5) Å	( = 99.445(5)°

c = 20.661(5) Å	(  = 90.000(5)°

Volume	1597.4(13) Å3

Z	4

Density (calculated)	1.614 Mg / m3

Absorption coefficient	0.249 mm(1

F(000)	792

Crystal	rod; colourless

Crystal size	0.20 ( 0.04 ( 0.04 mm3

( range for data collection	2.87 ( 27.50°

Index ranges	(9 ( h ( 10, (12 ( k ( 12, (26 ( l ( 26

Reflections collected	25553

Independent reflections	3630 [Rint = 0.2237]

Completeness to ( = 27.50°	99.1 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9901 and 0.9519

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	3630 / 0 / 226

Goodness-of-fit on F2	1.042

Final R indices [F2 > 2((F2)]	R1 = 0.1137, wR2 = 0.3083

R indices (all data)	R1 = 0.2326, wR2 = 0.3783

Largest diff. peak and hole	0.720 and (0.451 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SADABS Version 2.10. (G. M. Sheldrick (2003)) Bruker AXS Inc., Madison, Wisconsin, USA. Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: PLATON  (A.L. Spek, J. Appl. Crystallogr. 2003, 36, 7).

Special details:

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	5260(10)	857(7)	4109(3)	48(2)	1

C2	5051(9)	(609(8)	3923(3)	44(2)	1

C3	4624(10)	(2428(8)	3099(4)	55(2)	1

C4	4514(8)	(1(8)	2759(4)	46(2)	1

C5	4805(10)	1460(8)	2945(3)	49(2)	1

C6	3753(9)	2893(7)	3724(3)	43(2)	1

C7	3491(9)	3388(8)	4347(3)	48(2)	1

C8	2670(9)	4596(8)	4380(3)	45(2)	1

C9	2301(9)	5233(7)	4973(3)	44(2)	1

C10	1493(9)	6471(8)	4921(3)	48(2)	1

C11	1060(10)	7113(8)	5467(4)	53(2)	1

C12	1421(10)	6492(9)	6074(4)	58(2)	1

C13	2209(10)	5269(9)	6129(4)	53(2)	1

C14	2654(9)	4605(8)	5587(4)	52(2)	1

N1	4499(7)	1793(6)	3606(2)	43(1)	1

N2	4723(7)	(963(6)	3261(3)	44(1)	1

O1	5229(6)	(1474(5)	4343(2)	51(1)	1

O2	4221(6)	(330(5)	2185(2)	49(1)	1

F1	(1148(6)	(565(6)	3885(2)	79(2)	1

F2	(1316(7)	780(5)	3021(3)	92(2)	1

F3	(1659(6)	(1421(6)	2864(2)	78(2)	1

F4	708(6)	(423(5)	2630(2)	66(1)	1

F5	870(7)	(1800(5)	3480(2)	78(2)	1

F6	1222(7)	428(7)	3648(3)	109(2)	1

P1	(222(2)	(501(2)	3263(1)	50(1)	1

Table 3. Bond lengths [Å] and angles [°].

C1(N1	1.448(9)

C1(C2	1.503(10)

C2(O1	1.211(8)

C2(N2	1.395(9)

C3(N2	1.487(10)

C4(O2	1.214(8)

C4(N2	1.397(9)

C4(C5	1.505(11)

C5(N1	1.465(8)

C6(N1	1.281(9)

C6(C7	1.424(9)

C7(C8	1.368(10)

C8(C9	1.448(10)

C9(C10	1.379(10)

C9(C14	1.401(11)

C10(C11	1.386(10)

C11(C12	1.385(11)

C12(C13	1.359(11)

C13(C14	1.392(10)

F1(P1	1.582(5)

F2(P1	1.570(6)

F3(P1	1.579(5)

F4(P1	1.604(5)

F5(P1	1.573(5)

F6(P1	1.577(5)

N1(C1(C2	114.8(6)

O1(C2(N2	120.3(7)

O1(C2(C1	120.3(6)

N2(C2(C1	119.3(6)

O2(C4(N2	121.4(7)

O2(C4(C5	120.2(7)

N2(C4(C5	118.1(6)

N1(C5(C4	114.4(6)

N1(C6(C7	127.2(7)

C8(C7(C6	119.1(7)

C7(C8(C9	125.9(7)

C10(C9(C14	119.1(7)

C10(C9(C8	118.5(6)

C14(C9(C8	122.4(7)

C9(C10(C11	121.2(7)

C12(C11(C10	119.5(7)

C13(C12(C11	119.7(7)

C12(C13(C14	121.8(7)

C13(C14(C9	118.7(8)

C6(N1(C1	124.0(6)

C6(N1(C5	121.4(6)

C1(N1(C5	114.4(6)

C2(N2(C4	122.4(6)

C2(N2(C3	117.4(6)

C4(N2(C3	120.2(6)

F2(P1(F5	178.1(3)

F2(P1(F6	90.3(4)

F5(P1(F6	90.8(4)

F2(P1(F3	89.3(3)

F5(P1(F3	89.6(3)

F6(P1(F3	178.9(3)

F2(P1(F1	89.2(3)

F5(P1(F1	92.4(3)

F6(P1(F1	90.4(3)

F3(P1(F1	90.6(3)

F2(P1(F4	90.3(3)

F5(P1(F4	88.1(3)

F6(P1(F4	89.5(3)

F3(P1(F4	89.4(3)

F1(P1(F4	179.5(3)

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	51(4) 	47(5)	45(4) 	(5(3)	7(3) 	1(4)

C2	41(4) 	50(5)	43(4) 	(1(4)	12(3) 	(1(3)

C3	59(5) 	57(5)	49(4) 	(1(4)	12(4) 	2(4)

C4	32(4) 	58(5)	50(5) 	3(4)	12(3) 	(4(3)

C5	60(4) 	55(5)	32(4) 	1(3)	10(3) 	3(4)

C6	47(4) 	38(4)	41(4) 	(2(3)	5(3) 	(5(3)

C7	43(4) 	58(5)	44(4) 	0(3)	10(3) 	0(4)

C8	44(4) 	48(5)	42(4) 	4(3)	8(3) 	0(3)

C9	42(4) 	46(5)	43(4) 	(2(3)	7(3) 	0(3)

C10	48(4) 	53(5)	43(4) 	0(3)	11(3) 	(2(4)

C11	54(4) 	48(5)	57(5) 	(3(4)	11(3) 	2(4)

C12	56(5) 	63(6)	58(5) 	(12(4)	15(4) 	(6(4)

C13	51(4) 	69(6)	41(4) 	(6(4)	9(3) 	1(4)

C14	38(4) 	60(5)	58(5) 	(3(4)	9(3) 	2(4)

N1	40(3) 	52(4)	36(3) 	0(3)	8(2) 	(5(3)

N2	43(3) 	49(4)	39(3) 	(2(3)	8(2) 	(7(3)

O1	55(3) 	50(3)	50(3) 	7(3)	12(2) 	7(2)

O2	49(3) 	62(4)	37(3) 	(6(2)	8(2) 	(5(2)

F1	64(3) 	119(5)	59(3) 	(7(3)	24(2) 	(5(3)

F2	84(4) 	65(4)	134(5) 	13(3)	40(3) 	29(3)

F3	49(3) 	99(4)	90(4) 	(34(3)	20(2) 	(10(3)

F4	71(3) 	66(3)	69(3) 	11(2)	29(2) 	5(2)

F5	91(4) 	73(4)	71(3) 	21(3)	22(3) 	27(3)

F6	61(3) 	150(6)	123(5) 	(84(4)	31(3) 	(40(4)

P1	43(1) 	54(1)	56(1) 	(7(1)	16(1) 	2(1)