|  | University of Southampton · School of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	2006src0567   (306-131-A)

Empirical formula 	C4H8Cl4N3O2P3

Formula weight 	364.84

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	Cc

Unit cell dimensions	a = 14.8296(9) Å	( = 90°

b = 6.0926(3) Å	( = 109.500(3)°

c = 15.4113(12) Å	(  = 90°

Volume	1312.56(14) Å3

Z	4

Density (calculated)	1.846 Mg / m3

Absorption coefficient	1.255 mm(1

F(000)	728

Crystal	block; colourless

Crystal size	0.40 ( 0.20 ( 0.20 mm3

( range for data collection	3.30 ( 27.50°

Index ranges	(19 ( h ( 17, (7 ( k ( 7, (18 ( l ( 18

Reflections collected	2043

Independent reflections	1519 [Rint = 0.0445]

Completeness to ( = 27.50°	77.7 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.7875 and 0.6338

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	1519 / 14 / 146

Goodness-of-fit on F2	1.165

Final R indices [F2 > 2((F2)]	R1 = 0.0658, wR2 = 0.1561

R indices (all data)	R1 = 0.0961, wR2 = 0.1817

Absolute structure parameter	0.4(3)

Largest diff. peak and hole	0.792 and (0.866 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SORTAV (R. H. Blessing, Acta Cryst. A51 (1995) 33(37; R. H. Blessing, J. Appl. Cryst. 30 (1997) 421(426). Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: Cameron - A Molecular Graphics Package. (D. M. Watkin, L. Pearce and C. K. Prout, Chemical Crystallography Laboratory, University of Oxford, 1993).

Special details:

Chiral space group, -only 1 enantiomer crystallises.

P1-P2 = 2.754, P2-P3 = 2.741, P1-P3 = 2.775, max dev = 0.077 (N2)

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	10951(8)	(7820(20)	10453(11)	21(3)	1

C2	11840(8)	(6674(18)	11073(10)	14(3)	1

C3	12128(9)	(7560(20)	12034(10)	19(3)	1

C4	11644(9)	(4240(20)	11082(10)	21(3)	1

N1	10408(7)	(3660(20)	8437(9)	24(3)	1

N2	8556(7)	(2234(18)	8043(8)	19(3)	1

N3	9534(7)	(3800(18)	9750(9)	23(3)	1

O1	10630(6)	(6940(14)	9529(6)	15(2)	1

O2	11364(6)	(3288(13)	10137(7)	21(2)	1

P1	10440(2)	(4381(5)	9435(3)	15(1)	1

P2	9484(2)	(2545(6)	7744(3)	16(1)	1

P3	8622(2)	(2633(6)	9065(2)	15(1)	1

Cl1	9087(2)	(4228(5)	6555(2)	22(1)	1

Cl2	9842(2)	346(6)	7333(3)	25(1)	1

Cl3	8416(2)	229(5)	9607(2)	22(1)	1

Cl4	7461(2)	(4297(6)	9053(3)	24(1)	1

Table 3. Bond lengths [Å] and angles [°].

C1(O1	1.445(18)

C1(C2	1.515(17)

C2(C3	1.499(19)

C2(C4	1.511(16)

C4(O2	1.492(18)

N1(P2	1.580(12)

N1(P1	1.586(12)

N2(P3	1.563(12)

N2(P2	1.602(10)

N3(P3	1.579(11)

N3(P1	1.614(11)

O1(P1	1.582(9)

O2(P1	1.581(9)

P2(Cl2	2.003(5)

P2(Cl1	2.009(5)

P3(Cl4	1.994(4)

P3(Cl3	2.000(5)

O1(C1(C2	112.5(10)

C3(C2(C4	109.6(12)

C3(C2(C1	111.0(10)

C4(C2(C1	109.1(10)

O2(C4(C2	111.4(11)

P2(N1(P1	120.9(6)

P3(N2(P2	120.0(7)

P3(N3(P1	120.7(8)

C1(O1(P1	116.4(8)

C4(O2(P1	113.5(7)

O2(P1(O1	105.4(5)

O2(P1(N1	106.6(6)

O1(P1(N1	108.1(6)

O2(P1(N3	108.6(6)

O1(P1(N3	109.2(5)

N1(P1(N3	118.2(6)

N1(P2(N2	119.4(6)

N1(P2(Cl2	109.2(5)

N2(P2(Cl2	109.3(4)

N1(P2(Cl1	108.8(5)

N2(P2(Cl1	107.7(4)

Cl2(P2(Cl1	100.8(2)

N2(P3(N3	119.7(6)

N2(P3(Cl4	107.8(4)

N3(P3(Cl4	108.7(5)

N2(P3(Cl3	108.5(4)

N3(P3(Cl3	109.2(5)

Cl4(P3(Cl3	101.23(19)

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	14(6) 	17(7)	35(11) 	(7(7)	10(7) 	0(5)

C2	11(5) 	4(4)	21(7) 	6(5)	(1(5) 	1(4)

C3	29(7) 	13(6)	9(9) 	(1(5)	0(6) 	(1(5)

C4	19(5) 	20(5)	18(7) 	(7(5)	(3(5) 	(10(5)

N1	21(6) 	38(7)	20(8) 	7(6)	15(5) 	8(5)

N2	16(5) 	28(6)	13(7) 	1(5)	6(5) 	11(5)

N3	19(5) 	29(6)	24(8) 	2(5)	10(5) 	11(5)

O1	22(4) 	15(4)	9(6) 	4(4)	4(4) 	0(4)

O2	17(4) 	12(4)	31(7) 	4(4)	3(5) 	(6(3)

P1	12(1) 	18(2)	12(2) 	1(1)	3(1) 	5(1)

P2	14(1) 	24(2)	11(2) 	1(1)	4(2) 	5(1)

P3	12(1) 	23(2)	9(2) 	1(2)	1(1) 	4(1)

Cl1	29(2) 	27(2)	12(2) 	(5(1)	8(2) 	(1(1)

Cl2	31(2) 	20(2)	23(2) 	3(2)	6(2) 	(2(1)

Cl3	25(2) 	20(2)	21(2) 	(2(1)	8(2) 	(1(1)

Cl4	17(1) 	30(2)	25(2) 	(7(2)	8(2) 	(5(1)