|  | Departmental Single Crystal X-Ray Diffraction Service School of Chemistry - University of Southampton Contact: Dr Mark E Light, light@soton.ac.uk, ex 29429 |
| --- | --- |

Table 1. Crystal data and structure refinement details.

Identification code 	07skc0003cmcm

Empirical formula 	C5H10NO2.50

Formula weight 	116.14

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Orthorhombic

Space group 	Cmcm

Unit cell dimensions	a = 6.8156(6) Å	( = 90°

b = 12.7537(12) Å	( = 90°

c = 14.1899(11) Å	(  = 90°

Volume	1233.44(19) Å3

Z	8

Density (calculated)	1.337 Mg / m3

Absorption coefficient	0.107 mm(1

F(000)	536

Crystal	plate; colourless

Crystal size	0.15 ( 0.07 ( 0.01 mm3

( range for data collection	3.19 ( 27.48°

Index ranges	(8 ( h ( 8, (16 ( k ( 11, (18 ( l ( 16

Reflections collected	4539

Independent reflections	800 [Rint = 0.0636]

Completeness to ( = 27.48°	99.4 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9989 and 0.9842

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	800 / 0 / 58

Goodness-of-fit on F2	1.167

Final R indices [F2 > 2((F2)]	R1 = 0.0587, wR2 = 0.1116

R indices (all data)	R1 = 0.0893, wR2 = 0.1283

Largest diff. peak and hole	0.309 and (0.292 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit ). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: Sheldrick, G. M. SADABS - Bruker Nonius area detector scaling and absorption correction - V2.10 Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: Cameron - A Molecular Graphics Package. (D. M. Watkin, L. Pearce and C. K. Prout, Chemical Crystallography Laboratory, University of Oxford, 1993).

Special details:

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	0	3041(2)	4852(2)	26(1)	1

C2	0	3750(2)	5698(2)	26(1)	1

C3	0	3141(2)	6618(2)	24(1)	1

C4	0	3831(3)	7500	25(1)	1

O1B	0	2091(2)	4899(1)	36(1)	1

O1A	0	3565(2)	4042(1)	32(1)	1

C22	0	1399(3)	2500	25(1)	1

C25	0	(314(2)	3045(2)	34(1)	1

N21	0	798(2)	3274(2)	29(1)	1

O22	0	2392(2)	2500	26(1)	1

Table 3. Bond lengths [Å] and angles [°].

C1(O1B	1.213(3)

C1(O1A	1.329(3)

C1(C2	1.503(4)

C2(C3	1.519(3)

C2(H2A	0.9900

C2(H2B	0.9900

C3(C4	1.530(3)

C3(H3A	0.9900

C3(H3B	0.9900

C4(C3i	1.530(3)

C4(H4A	0.9900

C4(H4B	0.9900

O1A(H1	0.8400

C22(O22	1.267(5)

C22(N21ii	1.339(3)

C22(N21	1.339(3)

C25(N21	1.456(4)

C25(C25ii	1.546(6)

C25(H25A	0.9900

C25(H25B	0.9900

N21(H21	0.8800

O1B(C1(O1A	123.4(3)

O1B(C1(C2	123.8(2)

O1A(C1(C2	112.8(2)

C1(C2(C3	112.2(2)

C1(C2(H2A	109.2

C3(C2(H2A	109.2

C1(C2(H2B	109.2

C3(C2(H2B	109.2

H2A(C2(H2B	107.9

C2(C3(C4	114.2(2)

C2(C3(H3A	108.7

C4(C3(H3A	108.7

C2(C3(H3B	108.7

C4(C3(H3B	108.7

H3A(C3(H3B	107.6

C3(C4(C3i	109.8(3)

C3(C4(H4A	109.7

C3i(C4(H4A	109.7

C3(C4(H4B	109.7

C3i(C4(H4B	109.7

H4A(C4(H4B	108.2

C1(O1A(H1	109.5

O22(C22(N21ii	124.90(17)

O22(C22(N21	124.90(17)

N21ii(C22(N21	110.2(3)

N21(C25(C25ii	102.92(15)

N21(C25(H25A	111.2

C25ii(C25(H25A	111.2

N21(C25(H25B	111.2

C25ii(C25(H25B	111.2

H25A(C25(H25B	109.1

C22(N21(C25	112.0(2)

C22(N21(H21	124.0

C25(N21(H21	124.0

Symmetry transformations used to generate equivalent atoms:

(i) x,y,(z+3/2    (ii) x,y,(z+1/2

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	29(2) 	27(2)	23(1) 	1(1)	0 	0

C2	31(2) 	24(2)	22(1) 	1(1)	0 	0

C3	30(2) 	22(1)	19(1) 	1(1)	0 	0

C4	29(2) 	25(2)	21(2) 	0	0 	0

O1B	61(2) 	24(1)	24(1) 	(1(1)	0 	0

O1A	53(1) 	25(1)	19(1) 	(1(1)	0 	0

C22	28(2) 	21(2)	26(2) 	0	0 	0

C25	46(2) 	22(2)	34(2) 	1(1)	0 	0

N21	41(2) 	23(1)	24(1) 	0(1)	0 	0

O22	38(2) 	21(2)	20(1) 	0	0 	0

Table 5. Hydrogen bonds [Å and °].

D(H···A	d(D(H)	d(H···A)	d(D···A)	((DHA)

O1A(H1...O22	0.84	1.82	2.651(2)	171.3

N21(H21...O1B	0.88	1.99	2.834(3)	159.2

Symmetry transformations used to generate equivalent atoms:

(i) x,y,(z+3/2    (ii) x,y,(z+1/2