|  | Departmental Single Crystal X-Ray Diffraction Service School of Chemistry - University of Southampton Contact: Dr Mark E Light, light@soton.ac.uk, ex 29429 |
| --- | --- |

Table 1. Crystal data and structure refinement details.

Identification code 	07skc0018pna21

Empirical formula 	C15H31NO4

Formula weight 	289.41

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Orthorhombic

Space group 	Pna21

Unit cell dimensions	a = 11.5504(7) Å	( = 90°

b = 22.2264(10) Å	( = 90°

c = 6.6309(4) Å	(  = 90°

Volume	1702.31(16) Å3

Z	4

Density (calculated)	1.129 Mg / m3

Absorption coefficient	0.080 mm(1

F(000)	640

Crystal	block; colourless

Crystal size	0.18 ( 0.10 ( 0.04 mm3

( range for data collection	3.21 ( 27.48°

Index ranges	(14 ( h ( 13, (28 ( k ( 28, (5 ( l ( 8

Reflections collected	9877

Independent reflections	2855 [Rint = 0.0628]

Completeness to ( = 27.48°	99.5 %

Max. and min. transmission	0.9968 and 0.9857

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	2855 / 1 / 192

Goodness-of-fit on F2	1.111

Final R indices [F2 > 2((F2)]	R1 = 0.0635, wR2 = 0.1191

R indices (all data)	R1 = 0.0883, wR2 = 0.1345

Absolute structure parameter	1(2)

Largest diff. peak and hole	0.260 and (0.234 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit ). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: Sheldrick, G. M. SADABS - Bruker Nonius area detector scaling and absorption correction - V2.10 Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: Cameron - A Molecular Graphics Package. (D. M. Watkin, L. Pearce and C. K. Prout, Chemical Crystallography Laboratory, University of Oxford, 1993).

Special details:

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	1631(3)	1594(2)	(1509(6)	28(1)	1

C2	2626(3)	1909(2)	(492(7)	28(1)	1

C3	2477(4)	1958(2)	1762(7)	46(1)	1

C4	3492(4)	2258(2)	2866(7)	41(1)	1

C5	3596(3)	2929(2)	2420(6)	28(1)	1

C6	4425(3)	3234(1)	3873(6)	24(1)	1

C7	4550(3)	3913(2)	3630(6)	24(1)	1

O1A	747(2)	1446(1)	(670(5)	42(1)	1

O1B	1842(2)	1471(1)	(3425(4)	34(1)	1

O7A	3959(2)	4187(1)	2373(4)	28(1)	1

O7B	5252(2)	4173(1)	4852(4)	26(1)	1

C21	995(4)	3242(2)	(2924(8)	38(1)	1

C22	1121(3)	3930(2)	(3186(7)	29(1)	1

C23	2342(3)	4083(1)	(2332(6)	24(1)	1

C24	2772(3)	4736(2)	(2049(6)	23(1)	1

C26	130(3)	4230(2)	(2050(7)	36(1)	1

C27	1020(3)	4071(2)	(5442(7)	33(1)	1

C28	2204(3)	5057(2)	(280(6)	30(1)	1

C29	2751(3)	5126(2)	(3928(6)	29(1)	1

N25	4041(2)	4665(1)	(1476(5)	24(1)	1

Table 3. Bond lengths [Å] and angles [°].

C1(O1A	1.208(5)

C1(O1B	1.322(5)

C1(C2	1.506(5)

C2(C3	1.508(6)

C2(H2A	0.9900

C2(H2B	0.9900

C3(C4	1.535(6)

C3(H3A	0.9900

C3(H3B	0.9900

C4(C5	1.526(5)

C4(H4A	0.9900

C4(H4B	0.9900

C5(C6	1.519(5)

C5(H5A	0.9900

C5(H5B	0.9900

C6(C7	1.523(4)

C6(H6A	0.9900

C6(H6B	0.9900

C7(O7A	1.238(4)

C7(O7B	1.284(4)

O1B(H1	0.8400

C21(C22	1.544(5)

C21(H21A	0.9800

C21(H21B	0.9800

C21(H21C	0.9800

C22(C26	1.525(5)

C22(C27	1.533(6)

C22(C23	1.557(5)

C23(C24	1.546(4)

C23(H23A	0.9900

C23(H23B	0.9900

C24(C29	1.519(5)

C24(C28	1.521(5)

C24(N25	1.523(4)

C26(H26A	0.9800

C26(H26B	0.9800

C26(H26C	0.9800

C27(H27A	0.9800

C27(H27B	0.9800

C27(H27C	0.9800

C28(H28A	0.9800

C28(H28B	0.9800

C28(H28C	0.9800

C29(H29A	0.9800

C29(H29B	0.9800

C29(H29C	0.9800

N25(H25A	0.9100

N25(H25B	0.9100

N25(H25C	0.9100

O1A(C1(O1B	122.9(4)

O1A(C1(C2	124.4(4)

O1B(C1(C2	112.7(3)

C1(C2(C3	113.0(4)

C1(C2(H2A	109.0

C3(C2(H2A	109.0

C1(C2(H2B	109.0

C3(C2(H2B	109.0

H2A(C2(H2B	107.8

C2(C3(C4	114.6(4)

C2(C3(H3A	108.6

C4(C3(H3A	108.6

C2(C3(H3B	108.6

C4(C3(H3B	108.6

H3A(C3(H3B	107.6

C5(C4(C3	113.1(4)

C5(C4(H4A	109.0

C3(C4(H4A	109.0

C5(C4(H4B	109.0

C3(C4(H4B	109.0

H4A(C4(H4B	107.8

C6(C5(C4	111.3(3)

C6(C5(H5A	109.4

C4(C5(H5A	109.4

C6(C5(H5B	109.4

C4(C5(H5B	109.4

H5A(C5(H5B	108.0

C5(C6(C7	115.7(3)

C5(C6(H6A	108.3

C7(C6(H6A	108.3

C5(C6(H6B	108.3

C7(C6(H6B	108.3

H6A(C6(H6B	107.4

O7A(C7(O7B	123.5(3)

O7A(C7(C6	120.4(3)

O7B(C7(C6	116.0(3)

C1(O1B(H1	109.5

C22(C21(H21A	109.5

C22(C21(H21B	109.5

H21A(C21(H21B	109.5

C22(C21(H21C	109.5

H21A(C21(H21C	109.5

H21B(C21(H21C	109.5

C26(C22(C27	109.6(3)

C26(C22(C21	107.9(3)

C27(C22(C21	107.8(3)

C26(C22(C23	113.9(3)

C27(C22(C23	112.3(3)

C21(C22(C23	105.1(3)

C24(C23(C22	122.7(3)

C24(C23(H23A	106.7

C22(C23(H23A	106.7

C24(C23(H23B	106.7

C22(C23(H23B	106.7

H23A(C23(H23B	106.6

C29(C24(C28	111.0(3)

C29(C24(N25	106.2(3)

C28(C24(N25	105.7(3)

C29(C24(C23	115.6(3)

C28(C24(C23	113.3(3)

N25(C24(C23	104.1(3)

C22(C26(H26A	109.5

C22(C26(H26B	109.5

H26A(C26(H26B	109.5

C22(C26(H26C	109.5

H26A(C26(H26C	109.5

H26B(C26(H26C	109.5

C22(C27(H27A	109.5

C22(C27(H27B	109.5

H27A(C27(H27B	109.5

C22(C27(H27C	109.5

H27A(C27(H27C	109.5

H27B(C27(H27C	109.5

C24(C28(H28A	109.5

C24(C28(H28B	109.5

H28A(C28(H28B	109.5

C24(C28(H28C	109.5

H28A(C28(H28C	109.5

H28B(C28(H28C	109.5

C24(C29(H29A	109.5

C24(C29(H29B	109.5

H29A(C29(H29B	109.5

C24(C29(H29C	109.5

H29A(C29(H29C	109.5

H29B(C29(H29C	109.5

C24(N25(H25A	109.5

C24(N25(H25B	109.5

H25A(N25(H25B	109.5

C24(N25(H25C	109.5

H25A(N25(H25C	109.5

H25B(N25(H25C	109.5

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	30(2) 	23(2)	31(2) 	2(2)	4(2) 	3(2)

C2	28(2) 	26(2)	31(2) 	(6(2)	1(2) 	0(2)

C3	66(3) 	38(2)	35(3) 	0(2)	(1(2) 	(26(2)

C4	64(3) 	30(2)	28(2) 	0(2)	(9(2) 	(10(2)

C5	31(2) 	26(2)	27(2) 	(2(2)	(1(2) 	(1(2)

C6	24(2) 	21(2)	25(2) 	3(2)	(1(2) 	4(1)

C7	25(2) 	24(2)	21(2) 	1(2)	6(2) 	5(2)

O1A	33(2) 	55(2)	38(2) 	(11(2)	7(2) 	(13(1)

O1B	31(2) 	40(2)	31(2) 	(4(1)	0(1) 	(7(1)

O7A	34(1) 	27(1)	24(2) 	4(1)	0(1) 	4(1)

O7B	30(1) 	23(1)	26(2) 	1(1)	(3(1) 	(1(1)

C21	35(2) 	26(2)	53(3) 	7(2)	(8(2) 	(3(2)

C22	26(2) 	26(2)	36(2) 	4(2)	(2(2) 	0(2)

C23	25(2) 	23(2)	23(2) 	5(2)	0(2) 	2(1)

C24	20(2) 	25(2)	25(2) 	3(2)	(2(2) 	(1(1)

C26	28(2) 	37(2)	43(3) 	0(2)	2(2) 	(6(2)

C27	33(2) 	36(2)	30(2) 	(4(2)	(8(2) 	0(2)

C28	30(2) 	30(2)	29(2) 	0(2)	3(2) 	0(2)

C29	31(2) 	24(2)	32(2) 	2(2)	(1(2) 	0(2)

N25	27(2) 	22(1)	24(2) 	(2(2)	0(2) 	(2(1)

Table 5. Hydrogen bonds [Å and °].

D(H···A	d(D(H)	d(H···A)	d(D···A)	((DHA)

N25(H25A...O7A	0.91	1.90	2.766(4)	158.5

O1B(H1...O7Bi	0.84	1.76	2.593(4)	171.6

N25(H25B...O7Bii	0.91	1.95	2.849(4)	167.4

N25(H25C...O7Biii	0.91	2.11	3.014(4)	173.4

Symmetry transformations used to generate equivalent atoms:

(i) x(1/2,(y+1/2,z(1    (ii) (x+1,(y+1,z(1/2    (iii) x,y,z(1