|  | Departmental Single Crystal X-Ray Diffraction Service School of Chemistry - University of Southampton Contact: Dr Mark E Light, light@soton.ac.uk, ex 29429 |
| --- | --- |

Table 1. Crystal data and structure refinement details.

Identification code 	06skc0012p212121

Empirical formula 	C5H7NO3

Formula weight 	129.12

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Orthorhombic

Space group 	P212121

Unit cell dimensions	a = 8.1972(10) Å	( = 90°

b = 14.340(2) Å	( = 90°

c = 14.6661(15) Å	(  = 90°

Volume	1724.0(4) Å3

Z	12

Density (calculated)	1.492 Mg / m3

Absorption coefficient	0.125 mm(1

F(000)	816

Crystal	block; colourless

Crystal size	0.22 ( 0.10 ( 0.06 mm3

( range for data collection	3.12 ( 23.37°

Index ranges	(9 ( h ( 8, (15 ( k ( 15, (16 ( l ( 16

Reflections collected	23141

Independent reflections	2495 [Rint = 0.1562]

Completeness to ( = 23.37°	99.2 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9926 and 0.9731

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	2495 / 0 / 247

Goodness-of-fit on F2	1.012

Final R indices [F2 > 2((F2)]	R1 = 0.0518, wR2 = 0.0942

R indices (all data)	R1 = 0.1088, wR2 = 0.1118

Absolute structure parameter	0(2)

Largest diff. peak and hole	0.218 and (0.268 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit ). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: Sheldrick, G. M. SADABS - Bruker Nonius area detector scaling and absorption correction - V2.10 Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: Cameron - A Molecular Graphics Package. (D. M. Watkin, L. Pearce and C. K. Prout, Chemical Crystallography Laboratory, University of Oxford, 1993).

Special details:

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C2	(1812(6)	2133(3)	329(3)	39(1)	1

C3	(2817(6)	1266(3)	214(3)	40(1)	1

C4	(2970(6)	884(3)	1184(3)	42(1)	1

C5	(1449(5)	1262(3)	1670(3)	41(1)	1

C6	(1747(5)	1469(4)	2670(3)	39(1)	1

N1	(1108(5)	2104(3)	1150(2)	42(1)	1

O2	(1615(4)	2784(2)	(219(2)	48(1)	1

O6A	(2011(4)	693(2)	3129(2)	44(1)	1

O6B	(1727(4)	2239(2)	2995(2)	49(1)	1

C22	2288(5)	3428(3)	4687(3)	37(1)	1

C23	3654(5)	2732(3)	4788(3)	42(1)	1

C24	3899(5)	2340(3)	3822(3)	38(1)	1

C25	2220(6)	2483(3)	3386(3)	39(1)	1

C26	2243(6)	2660(4)	2378(3)	39(1)	1

N21	1569(5)	3277(2)	3884(2)	40(1)	1

O22	1877(4)	4034(2)	5244(2)	41(1)	1

O26A	3019(4)	1991(2)	1941(2)	55(1)	1

O26B	1573(3)	3313(2)	2010(2)	43(1)	1

C32	3212(6)	94(3)	9219(3)	41(1)	1

C33	1421(5)	285(3)	9343(3)	41(1)	1

C34	802(5)	440(3)	8368(3)	43(1)	1

C35	2309(5)	829(3)	7877(3)	39(1)	1

C36	2468(6)	614(3)	6872(3)	39(1)	1

N31	3631(4)	410(2)	8394(2)	40(1)	1

O32	4155(4)	(288(2)	9754(2)	46(1)	1

O36A	1035(4)	650(2)	6457(2)	48(1)	1

O36B	3750(4)	467(2)	6499(2)	43(1)	1

Table 3. Bond lengths [Å] and angles [°].

C2(O2	1.243(5)

C2(N1	1.335(5)

C2(C3	1.501(6)

C3(C4	1.529(5)

C3(H3A	0.9900

C3(H3B	0.9900

C4(C5	1.535(6)

C4(H4A	0.9900

C4(H4B	0.9900

C5(N1	1.456(5)

C5(C6	1.516(6)

C5(H5	1.0000

C6(O6B	1.202(5)

C6(O6A	1.318(5)

N1(H1	0.8800

O6A(H6A	0.8400

C22(O22	1.239(5)

C22(N21	1.335(5)

C22(C23	1.507(6)

C23(C24	1.537(5)

C23(H23A	0.9900

C23(H23B	0.9900

C24(C25	1.531(6)

C24(H24A	0.9900

C24(H24B	0.9900

C25(N21	1.454(5)

C25(C26	1.501(5)

C25(H25	1.0000

C26(O26B	1.213(5)

C26(O26A	1.317(5)

N21(H21	0.8800

O26A(H26A	0.8400

C32(O32	1.230(5)

C32(N31	1.337(5)

C32(C33	1.505(6)

C33(C34	1.533(6)

C33(H33A	0.9900

C33(H33B	0.9900

C34(C35	1.535(6)

C34(H34A	0.9900

C34(H34B	0.9900

C35(N31	1.452(5)

C35(C36	1.511(6)

C35(H35	1.0000

C36(O36B	1.204(5)

C36(O36A	1.325(5)

N31(H31	0.8800

O36A(H36A	0.8400

O2(C2(N1	123.4(4)

O2(C2(C3	128.4(4)

N1(C2(C3	108.2(4)

C2(C3(C4	103.7(3)

C2(C3(H3A	111.0

C4(C3(H3A	111.0

C2(C3(H3B	111.0

C4(C3(H3B	111.0

H3A(C3(H3B	109.0

C3(C4(C5	103.8(4)

C3(C4(H4A	111.0

C5(C4(H4A	111.0

C3(C4(H4B	111.0

C5(C4(H4B	111.0

H4A(C4(H4B	109.0

N1(C5(C6	112.1(4)

N1(C5(C4	101.9(3)

C6(C5(C4	112.8(4)

N1(C5(H5	109.9

C6(C5(H5	109.9

C4(C5(H5	109.9

O6B(C6(O6A	125.1(4)

O6B(C6(C5	124.1(4)

O6A(C6(C5	110.8(4)

C2(N1(C5	114.5(4)

C2(N1(H1	122.7

C5(N1(H1	122.7

C6(O6A(H6A	109.5

O22(C22(N21	125.1(4)

O22(C22(C23	127.0(4)

N21(C22(C23	107.9(4)

C22(C23(C24	104.4(3)

C22(C23(H23A	110.9

C24(C23(H23A	110.9

C22(C23(H23B	110.9

C24(C23(H23B	110.9

H23A(C23(H23B	108.9

C25(C24(C23	102.6(3)

C25(C24(H24A	111.2

C23(C24(H24A	111.2

C25(C24(H24B	111.2

C23(C24(H24B	111.2

H24A(C24(H24B	109.2

N21(C25(C26	111.5(4)

N21(C25(C24	103.0(4)

C26(C25(C24	114.9(4)

N21(C25(H25	109.0

C26(C25(H25	109.0

C24(C25(H25	109.0

O26B(C26(O26A	124.3(4)

O26B(C26(C25	124.3(5)

O26A(C26(C25	111.3(5)

C22(N21(C25	114.1(4)

C22(N21(H21	123.0

C25(N21(H21	123.0

C26(O26A(H26A	109.5

O32(C32(N31	124.5(4)

O32(C32(C33	128.1(4)

N31(C32(C33	107.4(4)

C32(C33(C34	103.6(3)

C32(C33(H33A	111.0

C34(C33(H33A	111.0

C32(C33(H33B	111.0

C34(C33(H33B	111.0

H33A(C33(H33B	109.0

C33(C34(C35	102.9(3)

C33(C34(H34A	111.2

C35(C34(H34A	111.2

C33(C34(H34B	111.2

C35(C34(H34B	111.2

H34A(C34(H34B	109.1

N31(C35(C36	111.1(4)

N31(C35(C34	101.8(3)

C36(C35(C34	116.9(4)

N31(C35(H35	108.9

C36(C35(H35	108.9

C34(C35(H35	108.9

O36B(C36(O36A	124.9(4)

O36B(C36(C35	123.7(4)

O36A(C36(C35	111.4(4)

C32(N31(C35	114.9(4)

C32(N31(H31	122.5

C35(N31(H31	122.5

C36(O36A(H36A	109.5

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C2	36(3) 	48(3)	31(3) 	(8(3)	(4(2) 	2(3)

C3	39(3) 	47(3)	33(3) 	(3(2)	(3(2) 	(1(3)

C4	44(3) 	48(3)	35(3) 	0(2)	(4(2) 	(5(3)

C5	38(3) 	48(3)	36(3) 	1(3)	2(2) 	1(2)

C6	35(3) 	42(3)	40(4) 	8(3)	3(2) 	2(3)

N1	48(3) 	45(3)	31(2) 	(2(2)	(4(2) 	(8(2)

O2	63(2) 	47(2)	33(2) 	5(2)	(5(2) 	(8(2)

O6A	56(2) 	44(2)	31(2) 	1(2)	3(2) 	(2(2)

O6B	68(2) 	42(2)	38(2) 	(2(2)	0(2) 	(3(2)

C22	30(3) 	47(3)	33(3) 	12(3)	0(3) 	(7(3)

C23	40(3) 	44(3)	42(3) 	2(3)	(2(2) 	0(3)

C24	34(3) 	49(3)	31(3) 	2(2)	(5(2) 	8(2)

C25	47(3) 	41(3)	31(3) 	(1(2)	0(2) 	(2(2)

C26	33(3) 	49(4)	36(3) 	(3(3)	(5(3) 	(12(3)

N21	40(2) 	48(3)	32(2) 	4(2)	(5(2) 	2(2)

O22	44(2) 	44(2)	34(2) 	(4(2)	1(2) 	4(2)

O26A	71(2) 	62(2)	31(2) 	0(2)	5(2) 	19(2)

O26B	45(2) 	50(2)	33(2) 	6(2)	(4(2) 	7(2)

C32	41(3) 	49(3)	32(3) 	(6(3)	5(3) 	(2(3)

C33	34(3) 	52(3)	35(3) 	3(2)	0(2) 	(1(3)

C34	34(3) 	53(3)	42(3) 	2(3)	0(2) 	0(3)

C35	39(3) 	46(3)	30(3) 	(1(2)	(2(2) 	0(2)

C36	46(4) 	30(3)	41(3) 	5(2)	(7(3) 	(1(3)

N31	29(2) 	60(3)	31(2) 	(1(2)	3(2) 	4(2)

O32	43(2) 	63(2)	32(2) 	6(2)	(3(2) 	8(2)

O36A	43(2) 	67(3)	32(2) 	(4(2)	(2(2) 	2(2)

O36B	36(2) 	57(2)	37(2) 	(2(2)	5(2) 	3(2)

Table 5. Hydrogen bonds [Å and °].

D(H···A	d(D(H)	d(H···A)	d(D···A)	((DHA)

N1(H1...O26B	0.88	2.22	3.070(5)	161.5

O6A(H6A...O22i	0.84	1.79	2.585(4)	158.5

N21(H21...O36Bi	0.88	2.12	2.983(5)	166.4

O26A(H26A...O2ii	0.84	1.74	2.563(4)	167.4

O36A(H36A...O32iii	0.84	1.74	2.556(4)	163.6

N31(H31...O26Biv	0.88	2.49	3.086(5)	125.7

N31(H31...O6Av	0.88	2.47	3.214(5)	142.0

Symmetry transformations used to generate equivalent atoms:

(i) x(1/2,(y+1/2,(z+1    (ii) x+1/2,(y+1/2,(z    (iii) (x+1/2,(y,z(1/2

(iv)  x+1/2,(y+1/2,(z+1    (v) (x+1/2,(y,z+1/2