|  | University of Southampton · Department of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	00mau005

Empirical formula 	C6H9N3O3

Formula weight 	171.16

Temperature 	150(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	P21/c

Unit cell dimensions	a = 6.9056(14) Å	( = 90°

b = 8.6519(17) Å	( = 94.41(3)°

c = 12.818(3) Å	(  = 90°

Volume	763.6(3) Å3

Z	4

Density (calculated)	1.489 Mg / m3

Absorption coefficient	0.121 mm(1

F(000)	360

Crystal	needle; orange

Crystal size	0.40 ( 0.12 ( 0.08 mm3

( range for data collection	2.96 ( 27.48°

Index ranges	(8 ( h ( 8, (11 ( k ( 11, (16 ( l ( 16

Reflections collected	6083

Independent reflections	1725 [Rint = 0.0378]

Completeness to ( = 27.48°	98.8 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9904 and 0.9532

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	1725 / 0 / 112

Goodness-of-fit on F2	1.021

Final R indices [F2 > 2((F2)]	R1 = 0.0397, wR2 = 0.1010

R indices (all data)	R1 = 0.0547, wR2 = 0.1099

Extinction coefficient	0.042(10)

Largest diff. peak and hole	0.202 and (0.242 e Å(3

Diffractometer: Enraf Nonius KappaCCD area detector (( scans and ( scans to fill Ewald sphere). Data collection and cell

refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography,

part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SORTAV (R. H. Blessing,

Acta Cryst. A51 (1995) 33(37; R. H. Blessing, J. Appl. Cryst. 30 (1997) 421(426). Program used to solve structure:

SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Program used to refine structure: SHELXL97 (G. M. Sheldrick

(1997), University of Göttingen, Germany).

Further information:  http://www.soton.ac.uk/~xservice/strat.htm

Special details:

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	2166(2)	2124(2)	5360(1)	23(1)	1

C2	2125(2)	3687(2)	5820(1)	34(1)	1

C3	3710(2)	832(2)	6964(1)	26(1)	1

C4	2276(2)	253(2)	7713(1)	28(1)	1

C5	2685(2)	(331(2)	5153(1)	21(1)	1

C6	1859(2)	257(2)	4243(1)	24(1)	1

N1	1534(2)	1790(1)	4373(1)	26(1)	1

N2	2882(1)	859(1)	5874(1)	21(1)	1

N3	3227(2)	(1891(1)	5351(1)	26(1)	1

O1	606(1)	1200(1)	7701(1)	31(1)	1

O2	3036(2)	(2783(1)	4603(1)	39(1)	1

O3	3849(2)	(2284(1)	6232(1)	39(1)	1

Table 3. Bond lengths [Å] and angles [°].

C1(N1	1.3378(17)

C1(N2	1.3514(16)

C1(C2	1.477(2)

C3(N2	1.4696(16)

C3(C4	1.5159(19)

C4(O1	1.4133(17)

C5(C6	1.3577(18)

C5(N2	1.3826(16)

C5(N3	1.4181(18)

C6(N1	1.3580(19)

N3(O3	1.2248(15)

N3(O2	1.2300(15)

N1(C1(N2	111.49(11)

N1(C1(C2	124.10(12)

N2(C1(C2	124.40(12)

N2(C3(C4	112.46(10)

O1(C4(C3	111.94(11)

C6(C5(N2	107.93(12)

C6(C5(N3	126.72(12)

N2(C5(N3	125.34(11)

C5(C6(N1	108.86(11)

C1(N1(C6	106.37(11)

C1(N2(C5	105.34(10)

C1(N2(C3	125.24(11)

C5(N2(C3	129.41(10)

O3(N3(O2	123.60(12)

O3(N3(C5	119.87(11)

O2(N3(C5	116.53(11)

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	22(1) 	24(1)	24(1) 	3(1)	3(1) 	(2(1)

C2	42(1) 	24(1)	37(1) 	(1(1)	2(1) 	0(1)

C3	28(1) 	32(1)	18(1) 	(2(1)	(5(1) 	(1(1)

C4	37(1) 	28(1)	20(1) 	(1(1)	0(1) 	2(1)

C5	20(1) 	22(1)	21(1) 	(1(1)	2(1) 	(2(1)

C6	23(1) 	29(1)	19(1) 	(1(1)	2(1) 	(5(1)

N1	26(1) 	28(1)	22(1) 	4(1)	1(1) 	(1(1)

N2	22(1) 	22(1)	19(1) 	(1(1)	0(1) 	(1(1)

N3	26(1) 	26(1)	26(1) 	(2(1)	3(1) 	0(1)

O1	32(1) 	36(1)	24(1) 	(8(1)	0(1) 	1(1)

O2	56(1) 	27(1)	34(1) 	(11(1)	3(1) 	0(1)

O3	52(1) 	33(1)	31(1) 	4(1)	(7(1) 	12(1)

Table 5. Hydrogen coordinates [( 104] and isotropic displacement parameters [Å2 ( 103].

Atom 	x	y	z	Ueq	S.o.f.

H2A	1516	4408	5304	51	1

H2B	3455	4026	6022	51	1

H2C	1377	3666	6439	51	1

H3A	4132	1889	7173	31	1

H3B	4871	157	7017	31	1

H4A	1880	(814	7518	34	1

H4B	2916	226	8431	34	1

H6	1557	(312	3618	28	1

H1	748	1853	8186	46	1