|  | Single Crystal X-Ray Diffraction Service National Crystallography Service Contact: Dr S.K.Callear, S.K.Callear@soton.ac.uk |
| --- | --- |

Table 4. Crystal data and structure refinement details.

Identification code 	2008src0980  (SM 108-111)

Empirical formula 	C14H16Cl2N2O2Si

Formula weight 	343.28

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Triclinic

Space group 	P(1

Unit cell dimensions	a = 8.1291(3) Å	( = 109.321(2)°

b = 10.8097(4) Å	( = 103.396(2)°

c = 11.8595(5) Å	(  = 100.002(2)°

Volume	920.42(6) Å3

Z	2

Density (calculated)	1.239 Mg / m3

Absorption coefficient	0.422 mm(1

F(000)	356

Crystal	block; colourless

Crystal size	0.22 ( 0.13 ( 0.06 mm3

( range for data collection	3.33 ( 27.48°

Index ranges	(10 ( h ( 10, (14 ( k ( 13, (15 ( l ( 15

Reflections collected	18586

Independent reflections	4196 [Rint = 0.0652]

Completeness to ( = 27.48°	99.6 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9751 and 0.9129

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	4196 / 43 / 214

Goodness-of-fit on F2	1.036

Final R indices [F2 > 2((F2)]	R1 = 0.0560, wR2 = 0.1436

R indices (all data)	R1 = 0.0808, wR2 = 0.1558

Extinction coefficient	0.016(4)

Largest diff. peak and hole	0.513 and (0.320 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: Sheldrick, G. M. SADABS - Bruker Nonius area detector scaling and absorption correction - V2.10 Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: ORTEP-3 (L.G. Farrugia, J. Appl. Cryst. (1997) 30, 565).

Special details:

SQUEEZE was used to remove severely disordered solvent (PLATON output noted 10.8 electrons removed).

The methyl and chloro groups are disordered with chlorine bonded to C6 38.2% of the time and methyl 61.8%, and chlorine bonded to C26 55.3% of the time and methyl 44.7%.

All hydrogens fixed using a standard riding model.

Table 5. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C28	2120(20)	2696(19)	(2002(19)	24(3)	0.447(6)

Cl26	1790(6)	2765(6)	(2044(5)	53(1)	0.553(6)

C8	2832(18)	4382(15)	5604(14)	56(6)	0.618(6)

Cl6	2929(5)	4636(6)	5839(6)	33(1)	0.382(6)

C2	139(3)	1685(2)	2572(2)	28(1)	1

C3	(1549(3)	1400(3)	2689(3)	35(1)	1

C4	(1801(3)	2114(3)	3801(3)	38(1)	1

C5	(422(4)	3108(3)	4798(3)	37(1)	1

C6	1214(3)	3378(2)	4662(2)	30(1)	1

C7	3176(3)	2860(3)	3325(2)	30(1)	1

C22	5300(3)	2902(2)	916(2)	29(1)	1

C23	6904(3)	3472(3)	797(3)	34(1)	1

C24	6909(4)	3787(3)	(220(3)	40(1)	1

C25	5343(4)	3559(3)	(1146(3)	47(1)	1

C26	3778(4)	3016(3)	(1017(3)	38(1)	1

C27	2159(3)	2151(2)	267(2)	28(1)	1

C31	3271(4)	(30(3)	1350(3)	39(1)	1

N1	1482(3)	2645(2)	3565(2)	27(1)	1

N21	3763(3)	2697(2)	8(2)	29(1)	1

O2	520(2)	1077(2)	1563(2)	32(1)	1

O22	5127(2)	2543(2)	1828(2)	31(1)	1

Si1	2851(1)	1667(1)	1660(1)	27(1)	1

Cl2	11552(1)	5172(1)	2437(1)	40(1)	1

Table 6. Bond lengths [Å] and angles [°].

C28(C26	1.462(15)

C28(H28A	0.9800

C28(H28B	0.9800

C28(H28C	0.9800

Cl26(C26	1.699(6)

C8(C6	1.476(11)

C8(H8A	0.9800

C8(H8B	0.9800

C8(H8C	0.9800

Cl6(C6	1.710(6)

C2(O2	1.297(3)

C2(N1	1.363(3)

C2(C3	1.402(3)

C3(C4	1.373(4)

C3(H3	0.9500

C4(C5	1.391(4)

C4(H4	0.9500

C5(C6	1.369(4)

C5(H5	0.9500

C6(N1	1.370(3)

C7(N1	1.465(3)

C7(Si1	1.894(2)

C7(H7A	0.9900

C7(H7B	0.9900

C22(O22	1.292(3)

C22(N21	1.375(3)

C22(C23	1.401(3)

C23(C24	1.358(4)

C23(H23	0.9500

C24(C25	1.397(4)

C24(H24	0.9500

C25(C26	1.370(4)

C25(H25	0.9500

C26(N21	1.371(3)

C27(N21	1.477(3)

C27(Si1	1.887(3)

C27(H27A	0.9900

C27(H27B	0.9900

C31(Si1	1.857(3)

C31(H31A	0.9800

C31(H31B	0.9800

C31(H31C	0.9800

O2(Si1	1.8553(17)

O22(Si1	1.8584(17)

C26(C28(H28A	109.5

C26(C28(H28B	109.5

C26(C28(H28C	109.5

C6(C8(H8A	109.5

C6(C8(H8B	109.5

H8A(C8(H8B	109.5

C6(C8(H8C	109.5

H8A(C8(H8C	109.5

H8B(C8(H8C	109.5

O2(C2(N1	116.9(2)

O2(C2(C3	123.7(2)

N1(C2(C3	119.4(2)

C4(C3(C2	118.7(2)

C4(C3(H3	120.7

C2(C3(H3	120.7

C3(C4(C5	121.2(2)

C3(C4(H4	119.4

C5(C4(H4	119.4

C6(C5(C4	119.2(2)

C6(C5(H5	120.4

C4(C5(H5	120.4

N1(C6(C5	119.8(2)

N1(C6(C8	112.9(7)

C5(C6(C8	127.3(7)

N1(C6(Cl6	119.4(3)

C5(C6(Cl6	120.8(3)

C8(C6(Cl6	6.8(9)

N1(C7(Si1	108.09(16)

N1(C7(H7A	110.1

Si1(C7(H7A	110.1

N1(C7(H7B	110.1

Si1(C7(H7B	110.1

H7A(C7(H7B	108.4

O22(C22(N21	115.8(2)

O22(C22(C23	125.2(2)

N21(C22(C23	119.0(2)

C24(C23(C22	119.4(3)

C24(C23(H23	120.3

C22(C23(H23	120.3

C23(C24(C25	121.1(3)

C23(C24(H24	119.4

C25(C24(H24	119.4

C26(C25(C24	119.2(3)

C26(C25(H25	120.4

C24(C25(H25	120.4

C25(C26(N21	120.0(3)

C25(C26(C28	120.5(10)

N21(C26(C28	119.4(10)

C25(C26(Cl26	123.3(3)

N21(C26(Cl26	116.6(3)

C28(C26(Cl26	6.1(10)

N21(C27(Si1	107.86(15)

N21(C27(H27A	110.1

Si1(C27(H27A	110.1

N21(C27(H27B	110.1

Si1(C27(H27B	110.1

H27A(C27(H27B	108.4

Si1(C31(H31A	109.5

Si1(C31(H31B	109.5

H31A(C31(H31B	109.5

Si1(C31(H31C	109.5

H31A(C31(H31C	109.5

H31B(C31(H31C	109.5

C2(N1(C6	121.7(2)

C2(N1(C7	114.27(19)

C6(N1(C7	124.0(2)

C26(N21(C22	121.2(2)

C26(N21(C27	124.7(2)

C22(N21(C27	114.0(2)

C2(O2(Si1	114.76(15)

C22(O22(Si1	115.48(15)

O2(Si1(C31	94.97(10)

O2(Si1(O22	170.57(8)

C31(Si1(O22	94.43(10)

O2(Si1(C27	90.62(9)

C31(Si1(C27	117.38(12)

O22(Si1(C27	85.69(9)

O2(Si1(C7	86.00(9)

C31(Si1(C7	120.22(12)

O22(Si1(C7	88.65(9)

C27(Si1(C7	122.39(11)

Symmetry transformations used to generate equivalent atoms:

Table 7. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C28	20(6) 	30(5)	22(6) 	9(4)	7(4) 	6(4)

Cl26	44(2) 	75(2)	38(1) 	33(1)	2(1) 	7(1)

C8	72(6) 	40(7)	37(8) 	(8(4)	25(4) 	5(4)

Cl6	39(1) 	30(2)	18(2) 	2(2)	7(1) 	2(1)

C2	30(1) 	29(1)	28(1) 	12(1)	9(1) 	9(1)

C3	28(1) 	41(2)	35(1) 	16(1)	12(1) 	7(1)

C4	33(1) 	51(2)	41(2) 	24(1)	17(1) 	17(1)

C5	43(2) 	43(2)	31(1) 	15(1)	19(1) 	18(1)

C6	40(1) 	29(1)	23(1) 	11(1)	11(1) 	10(1)

C7	28(1) 	36(1)	25(1) 	12(1)	10(1) 	6(1)

C22	33(1) 	28(1)	26(1) 	7(1)	12(1) 	9(1)

C23	33(1) 	31(1)	39(2) 	11(1)	16(1) 	6(1)

C24	41(2) 	38(2)	47(2) 	17(1)	24(1) 	8(1)

C25	55(2) 	51(2)	43(2) 	23(2)	25(2) 	13(2)

C26	48(2) 	39(2)	31(1) 	14(1)	16(1) 	12(1)

C27	28(1) 	30(1)	23(1) 	6(1)	9(1) 	7(1)

C31	37(1) 	39(2)	46(2) 	18(1)	17(1) 	14(1)

N1	29(1) 	29(1)	24(1) 	11(1)	9(1) 	7(1)

N21	34(1) 	26(1)	25(1) 	8(1)	12(1) 	8(1)

O2	26(1) 	37(1)	26(1) 	7(1)	9(1) 	2(1)

O22	28(1) 	41(1)	26(1) 	14(1)	9(1) 	6(1)

Si1	25(1) 	31(1)	24(1) 	10(1)	9(1) 	6(1)

Cl2	52(1) 	35(1)	38(1) 	14(1)	25(1) 	11(1)