|  | Single Crystal X-Ray Diffraction Service National Crystallography Service Contact: Dr S.K.Callear, S.K.Callear@soton.ac.uk |
| --- | --- |

Table 1. Crystal data and structure refinement details.

Identification code 	2008src1284 (HP1232(7))

Empirical formula 	C10H20N4O6S2

Formula weight 	356.42

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	P21/c

Unit cell dimensions	a = 13.2331(6) Å	( = 90°

b = 11.7105(6) Å	( = 99.664(3)°

c = 10.2193(5) Å	(  = 90°

Volume	1561.17(13) Å3

Z	4

Density (calculated)	1.516 Mg / m3

Absorption coefficient	0.375 mm(1

F(000)	752

Crystal	lath; colourless

Crystal size	0.07 ( 0.02 ( 0.01 mm3

( range for data collection	2.91 ( 27.48°

Index ranges	(17 ( h ( 17, (15 ( k ( 15, (11 ( l ( 13

Reflections collected	15777

Independent reflections	3546 [Rint = 0.0994]

Completeness to ( = 27.48°	99.2 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9963 and 0.9742

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	3546 / 3 / 209

Goodness-of-fit on F2	1.182

Final R indices [F2 > 2((F2)]	R1 = 0.0893, wR2 = 0.1383

R indices (all data)	R1 = 0.1496, wR2 = 0.1625

Largest diff. peak and hole	0.459 and (0.438 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: Sheldrick, G. M. SADABS - Bruker Nonius area detector scaling and absorption correction - V2.10 Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: ORTEP-3 (L.G. Farrugia, J. Appl. Cryst. (1997) 30, 565).

Special details:

All hydrogens fixed using a standard riding model.

In spite of the short contact H8A..H55, an electron density peak was found next to N5 in accordance with its being protonated. When this peak was assigned as a hydrogen, the hydrogen was freely refined and remained in this position. This nitrogen being protonated also concurs with the charge balancing of the structure.

balancing of the structure.

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C2	(2535(4)	6226(4)	2815(5)	24(1)	1

C3	(1883(4)	5837(4)	3935(5)	26(1)	1

C4	(1518(4)	4763(4)	3871(5)	24(1)	1

C6	(2519(3)	4519(4)	1752(5)	17(1)	1

C8	(2587(4)	2640(4)	599(5)	26(1)	1

C9	(3543(4)	1911(4)	260(5)	21(1)	1

C11	(4488(4)	3562(4)	(792(5)	20(1)	1

C12	(3531(4)	4287(4)	(477(5)	21(1)	1

C13	(6035(4)	1447(4)	(680(5)	23(1)	1

N1	(2853(3)	5604(4)	1744(4)	22(1)	1

N5	(1832(3)	4103(3)	2783(4)	19(1)	1

N7	(2862(3)	3848(3)	712(4)	21(1)	1

N10	(4177(3)	2364(3)	(959(4)	19(1)	1

O1	(4638(3)	409(3)	(1753(3)	27(1)	1

O2	(5528(3)	2064(3)	(2924(3)	24(1)	1

S1	(5091(1)	1520(1)	(1698(1)	20(1)	1

C21	1225(4)	4151(5)	644(5)	32(1)	1

O21	1314(3)	3364(3)	3002(3)	26(1)	1

O22	256(3)	5036(3)	2391(4)	32(1)	1

O23	2103(3)	5203(3)	2765(3)	26(1)	1

S2	1228(1)	4467(1)	2330(1)	21(1)	1

O1W	532(3)	7358(3)	1853(4)	33(1)	1

Table 3. Bond lengths [Å] and angles [°].

C2(N1	1.323(6)

C2(C3	1.390(7)

C2(H2	0.9500

C3(C4	1.353(7)

C3(H3	0.9500

C4(N5	1.361(6)

C4(H4	0.9500

C6(N7	1.338(6)

C6(N1	1.345(6)

C6(N5	1.361(6)

C8(N7	1.470(6)

C8(C9	1.518(7)

C8(H8A	0.9900

C8(H8B	0.9900

C9(N10	1.478(6)

C9(H9A	0.9900

C9(H9B	0.9900

C11(N10	1.480(6)

C11(C12	1.513(7)

C11(H11A	0.9900

C11(H11B	0.9900

C12(N7	1.470(6)

C12(H12A	0.9900

C12(H12B	0.9900

C13(S1	1.756(5)

C13(H13A	0.9800

C13(H13B	0.9800

C13(H13C	0.9800

N5(H55	0.8800

N10(S1	1.645(4)

O1(S1	1.438(4)

O2(S1	1.438(3)

C21(S2	1.762(5)

C21(H21A	0.9800

C21(H21B	0.9800

C21(H21C	0.9800

O21(S2	1.459(4)

O22(S2	1.459(4)

O23(S2	1.452(4)

O1W(H1W	0.849(19)

O1W(H2W	0.841(19)

N1(C2(C3	124.6(5)

N1(C2(H2	117.7

C3(C2(H2	117.7

C4(C3(C2	116.2(5)

C4(C3(H3	121.9

C2(C3(H3	121.9

C3(C4(N5	120.3(5)

C3(C4(H4	119.8

N5(C4(H4	119.9

N7(C6(N1	118.8(4)

N7(C6(N5	119.9(4)

N1(C6(N5	121.3(4)

N7(C8(C9	110.6(4)

N7(C8(H8A	109.5

C9(C8(H8A	109.5

N7(C8(H8B	109.5

C9(C8(H8B	109.5

H8A(C8(H8B	108.1

N10(C9(C8	108.8(4)

N10(C9(H9A	109.9

C8(C9(H9A	109.9

N10(C9(H9B	109.9

C8(C9(H9B	109.9

H9A(C9(H9B	108.3

N10(C11(C12	108.5(4)

N10(C11(H11A	110.0

C12(C11(H11A	110.0

N10(C11(H11B	110.0

C12(C11(H11B	110.0

H11A(C11(H11B	108.4

N7(C12(C11	110.3(4)

N7(C12(H12A	109.6

C11(C12(H12A	109.6

N7(C12(H12B	109.6

C11(C12(H12B	109.6

H12A(C12(H12B	108.1

S1(C13(H13A	109.5

S1(C13(H13B	109.5

H13A(C13(H13B	109.5

S1(C13(H13C	109.5

H13A(C13(H13C	109.5

H13B(C13(H13C	109.5

C2(N1(C6	117.1(4)

C6(N5(C4	120.2(4)

C6(N5(H55	119.9

C4(N5(H55	119.9

C6(N7(C8	124.9(4)

C6(N7(C12	121.8(4)

C8(N7(C12	113.2(4)

C9(N10(C11	111.9(4)

C9(N10(S1	116.1(3)

C11(N10(S1	115.2(3)

O1(S1(O2	118.4(2)

O1(S1(N10	106.4(2)

O2(S1(N10	106.9(2)

O1(S1(C13	108.8(2)

O2(S1(C13	108.5(2)

N10(S1(C13	107.4(2)

S2(C21(H21A	109.5

S2(C21(H21B	109.5

H21A(C21(H21B	109.5

S2(C21(H21C	109.5

H21A(C21(H21C	109.5

H21B(C21(H21C	109.5

O23(S2(O21	112.7(2)

O23(S2(O22	112.3(2)

O21(S2(O22	112.5(2)

O23(S2(C21	107.2(2)

O21(S2(C21	105.2(2)

O22(S2(C21	106.3(3)

H1W(O1W(H2W	105(3)

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C2	22(3) 	22(3)	29(3) 	(2(2)	6(2) 	(2(2)

C3	27(3) 	26(3)	26(3) 	(6(2)	5(2) 	(4(2)

C4	24(3) 	28(3)	17(2) 	1(2)	(1(2) 	(6(2)

C6	17(2) 	18(2)	19(2) 	2(2)	8(2) 	(4(2)

C8	25(3) 	19(3)	31(3) 	(4(2)	1(2) 	6(2)

C9	26(3) 	18(2)	16(2) 	(4(2)	(2(2) 	2(2)

C11	24(3) 	19(3)	18(2) 	2(2)	4(2) 	6(2)

C12	26(3) 	18(3)	19(2) 	2(2)	0(2) 	(2(2)

C13	24(3) 	24(3)	22(2) 	(1(2)	3(2) 	(7(2)

N1	21(2) 	21(2)	24(2) 	1(2)	5(2) 	(2(2)

N5	16(2) 	19(2)	21(2) 	1(2)	0(2) 	0(2)

N7	24(2) 	19(2)	18(2) 	(4(2)	(1(2) 	(1(2)

N10	20(2) 	16(2)	20(2) 	(1(2)	(3(2) 	4(2)

O1	30(2) 	22(2)	26(2) 	(9(2)	(1(2) 	4(2)

O2	30(2) 	26(2)	16(2) 	3(2)	1(2) 	2(2)

S1	24(1) 	19(1)	16(1) 	(1(1)	2(1) 	1(1)

C21	30(3) 	43(4)	24(3) 	(2(3)	4(2) 	(2(3)

O21	29(2) 	22(2)	26(2) 	3(2)	0(2) 	0(2)

O22	21(2) 	28(2)	47(2) 	6(2)	8(2) 	6(2)

O23	27(2) 	24(2)	28(2) 	(4(2)	4(2) 	(4(2)

S2	22(1) 	19(1)	22(1) 	1(1)	3(1) 	1(1)

O1W	24(2) 	20(2)	51(3) 	(2(2)	(3(2) 	2(2)

Table 5. Hydrogen bonds [Å and °].

D(H···A	d(D(H)	d(H···A)	d(D···A)	((DHA)

O1W(H2W...O22	0.841(19)	1.99(3)	2.811(5)	165(7)

O1W(H2W...S2	0.841(19)	2.77(3)	3.521(4)	149(5)

N5(H55...O1Wi	0.88	1.86	2.658(5)	150.4

O1W(H1W...O21ii	0.849(19)	1.89(2)	2.738(5)	174(6)

O1W(H1W...S2ii	0.849(19)	2.85(3)	3.588(4)	147(5)

Symmetry transformations used to generate equivalent atoms:

(i) (x,y(1/2,(z+1/2    (ii) (x,y+1/2,(z+1/2