|  | Single Crystal X-Ray Diffraction Service National Crystallography Service Contact: Dr S.K.Callear, S.K.Callear@soton.ac.uk |
| --- | --- |

Table 1. Crystal data and structure refinement details.

Identification code 	2009src0082 (TM1)

Empirical formula 	C9H14O3

Formula weight 	170.20

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	P21/n

Unit cell dimensions	a = 5.8119(2) Å	( = 90°

b = 12.9400(5) Å	( = 95.045(2)°

c = 11.9303(4) Å	(  = 90°

Volume	893.75(6) Å3

Z	4

Density (calculated)	1.265 Mg / m3

Absorption coefficient	0.094 mm(1

F(000)	368

Crystal	block; colourless

Crystal size	0.14 ( 0.08 ( 0.02 mm3

( range for data collection	3.15 ( 27.47°

Index ranges	(7 ( h ( 7, (16 ( k ( 16, (14 ( l ( 15

Reflections collected	10346

Independent reflections	2059 [Rint = 0.0449]

Completeness to ( = 27.47°	99.8 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9981 and 0.9870

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	2059 / 0 / 113

Goodness-of-fit on F2	1.081

Final R indices [F2 > 2((F2)]	R1 = 0.0545, wR2 = 0.0975

R indices (all data)	R1 = 0.0737, wR2 = 0.1074

Largest diff. peak and hole	0.319 and (0.220 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: Sheldrick, G. M. SADABS - Bruker Nonius area detector scaling and absorption correction - V2.10 Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: ORTEP-3 (L.G. Farrugia, J. Appl. Cryst. (1997) 30, 565).

Special details:

All hydrogens fixed using a standard riding model.

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	2193(3)	9072(1)	(1786(1)	20(1)	1

C2	1469(3)	8954(1)	(586(1)	18(1)	1

C3	(426(3)	8192(1)	(427(1)	19(1)	1

C4	284(3)	7114(1)	(841(1)	20(1)	1

C5	794(3)	7191(1)	(2087(2)	22(1)	1

C6	2628(3)	7986(2)	(2248(1)	22(1)	1

C7	221(3)	9597(2)	(2526(2)	25(1)	1

C8	(1671(3)	6341(1)	(749(2)	26(1)	1

C9	2417(3)	6742(2)	(111(2)	24(1)	1

O1	4195(2)	9676(1)	(1810(1)	30(1)	1

O2	2499(2)	9432(1)	177(1)	25(1)	1

O6	4377(2)	7795(1)	(2689(1)	33(1)	1

Table 3. Bond lengths [Å] and angles [°].

C1(O1	1.404(2)

C1(C2	1.535(2)

C1(C6	1.539(3)

C1(C7	1.542(2)

C2(O2	1.213(2)

C2(C3	1.503(2)

C3(C4	1.549(2)

C3(H3A	0.9900

C3(H3B	0.9900

C4(C8	1.525(2)

C4(C9	1.529(2)

C4(C5	1.544(2)

C5(C6	1.505(3)

C5(H5A	0.9900

C5(H5B	0.9900

C6(O6	1.210(2)

C7(H7A	0.9800

C7(H7B	0.9800

C7(H7C	0.9800

C8(H8A	0.9800

C8(H8B	0.9800

C8(H8C	0.9800

C9(H9A	0.9800

C9(H9B	0.9800

C9(H9C	0.9800

O1(H1	0.8400

O1(C1(C2	111.70(14)

O1(C1(C6	109.83(14)

C2(C1(C6	108.06(14)

O1(C1(C7	108.58(14)

C2(C1(C7	109.08(14)

C6(C1(C7	109.56(14)

O2(C2(C3	123.94(16)

O2(C2(C1	119.42(15)

C3(C2(C1	116.55(14)

C2(C3(C4	109.39(14)

C2(C3(H3A	109.8

C4(C3(H3A	109.8

C2(C3(H3B	109.8

C4(C3(H3B	109.8

H3A(C3(H3B	108.2

C8(C4(C9	108.94(15)

C8(C4(C5	108.65(14)

C9(C4(C5	110.74(14)

C8(C4(C3	110.29(14)

C9(C4(C3	109.09(14)

C5(C4(C3	109.13(14)

C6(C5(C4	111.43(14)

C6(C5(H5A	109.3

C4(C5(H5A	109.3

C6(C5(H5B	109.3

C4(C5(H5B	109.3

H5A(C5(H5B	108.0

O6(C6(C5	123.23(18)

O6(C6(C1	120.79(17)

C5(C6(C1	115.96(15)

C1(C7(H7A	109.5

C1(C7(H7B	109.5

H7A(C7(H7B	109.5

C1(C7(H7C	109.5

H7A(C7(H7C	109.5

H7B(C7(H7C	109.5

C4(C8(H8A	109.5

C4(C8(H8B	109.5

H8A(C8(H8B	109.5

C4(C8(H8C	109.5

H8A(C8(H8C	109.5

H8B(C8(H8C	109.5

C4(C9(H9A	109.5

C4(C9(H9B	109.5

H9A(C9(H9B	109.5

C4(C9(H9C	109.5

H9A(C9(H9C	109.5

H9B(C9(H9C	109.5

C1(O1(H1	109.5

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	19(1) 	20(1)	20(1) 	1(1)	1(1) 	(3(1)

C2	18(1) 	17(1)	20(1) 	(1(1)	2(1) 	4(1)

C3	19(1) 	20(1)	18(1) 	(1(1)	3(1) 	(2(1)

C4	19(1) 	19(1)	20(1) 	(1(1)	1(1) 	1(1)

C5	27(1) 	19(1)	21(1) 	(2(1)	1(1) 	1(1)

C6	23(1) 	28(1)	15(1) 	2(1)	0(1) 	3(1)

C7	29(1) 	23(1)	21(1) 	3(1)	(3(1) 	1(1)

C8	25(1) 	21(1)	32(1) 	(1(1)	3(1) 	(5(1)

C9	22(1) 	25(1)	24(1) 	2(1)	2(1) 	2(1)

O1	28(1) 	37(1)	23(1) 	1(1)	2(1) 	(14(1)

O2	25(1) 	28(1)	23(1) 	(6(1)	1(1) 	(4(1)

O6	32(1) 	39(1)	31(1) 	3(1)	15(1) 	7(1)

Table 5. Hydrogen bonds [Å and °].

D(H···A	d(D(H)	d(H···A)	d(D···A)	((DHA)

O1(H1...O2	0.84	2.18	2.6646(18)	117.1

O1(H1...O2i	0.84	2.15	2.8575(18)	141.6

Symmetry transformations used to generate equivalent atoms:

(i) (x+1,(y+2,(z