|  | Single Crystal X-Ray Diffraction Service National Crystallography Service Contact: Dr S.K.Callear, S.K.Callear@soton.ac.uk |
| --- | --- |

Table 1. Crystal data and structure refinement details.

Identification code 	2009src0172 (DMF 313)

Empirical formula 	C20H26O4S2Se2

Formula weight 	552.45

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	P21/n

Unit cell dimensions	a = 13.0885(2) Å	( = 90°

b = 12.5754(3) Å	( = 110.7530(10)°

c = 14.4854(3) Å	(  = 90°

Volume	2229.50(8) Å3

Z	4

Density (calculated)	1.646 Mg / m3

Absorption coefficient	3.527 mm(1

F(000)	1112

Crystal	block; colourless

Crystal size	0.33 ( 0.23 ( 0.09 mm3

( range for data collection	3.01 ( 27.48°

Index ranges	(16 ( h ( 16, (16 ( k ( 16, (18 ( l ( 18

Reflections collected	35179

Independent reflections	5099 [Rint = 0.0752]

Completeness to ( = 27.48°	99.9 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.7419 and 0.3890

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	5099 / 0 / 259

Goodness-of-fit on F2	1.045

Final R indices [F2 > 2((F2)]	R1 = 0.0366, wR2 = 0.0695

R indices (all data)	R1 = 0.0565, wR2 = 0.0758

Largest diff. peak and hole	0.445 and (0.649 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: Sheldrick, G. M. SADABS - Bruker Nonius area detector scaling and absorption correction - V2.10 Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: ORTEP-3 (L.G. Farrugia, J. Appl. Cryst. (1997) 30, 565).

Special details:

All hydrogens fixed using a standard riding model.

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	8001(2)	1746(2)	1653(2)	17(1)	1

C2	7854(2)	1027(2)	872(2)	20(1)	1

C3	8785(3)	560(3)	787(2)	23(1)	1

C4	9820(3)	802(3)	1449(3)	27(1)	1

C5	9954(3)	1505(3)	2217(3)	29(1)	1

C6	9047(3)	1974(3)	2326(2)	25(1)	1

C7	6715(3)	3679(2)	1331(2)	22(1)	1

C8	6345(3)	3557(3)	218(2)	31(1)	1

C9	5822(3)	4196(3)	1632(3)	32(1)	1

C10	7779(3)	4312(3)	1747(3)	31(1)	1

C21	6904(2)	(1485(2)	(1201(2)	18(1)	1

C22	6975(2)	(2181(2)	(1936(2)	16(1)	1

C23	7110(2)	(3273(2)	(1761(2)	19(1)	1

C24	7137(2)	(3696(2)	(872(2)	21(1)	1

C25	7025(3)	(3017(3)	(156(2)	23(1)	1

C26	6928(2)	(1931(3)	(311(2)	22(1)	1

C27	5487(2)	(1842(2)	(3935(2)	18(1)	1

C28	5490(3)	(1505(3)	(4949(2)	24(1)	1

C29	5087(3)	(2980(3)	(3957(2)	25(1)	1

C30	4822(2)	(1067(3)	(3557(2)	23(1)	1

O1	5932(2)	1743(2)	1421(2)	25(1)	1

O2	7257(2)	2524(2)	2950(2)	30(1)	1

O21	7514(2)	(2523(2)	(3484(2)	22(1)	1

O22	7258(2)	(665(2)	(3045(2)	22(1)	1

S3	6912(1)	(1766(1)	(3124(1)	17(1)	1

S4	6904(1)	2366(1)	1894(1)	19(1)	1

Se1	6407(1)	660(1)	(54(1)	21(1)	1

Se2	6826(1)	50(1)	(1393(1)	22(1)	1

Table 3. Bond lengths [Å] and angles [°].

C1(C6	1.400(4)

C1(C2	1.407(4)

C1(S4	1.775(3)

C2(C3	1.397(4)

C2(Se1	1.949(3)

C3(C4	1.388(4)

C3(H3	0.9500

C4(C5	1.384(5)

C4(H4	0.9500

C5(C6	1.383(5)

C5(H5	0.9500

C6(H6	0.9500

C7(C8	1.518(4)

C7(C10	1.530(4)

C7(C9	1.531(4)

C7(S4	1.820(3)

C8(H8A	0.9800

C8(H8B	0.9800

C8(H8C	0.9800

C9(H9A	0.9800

C9(H9B	0.9800

C9(H9C	0.9800

C10(H10A	0.9800

C10(H10B	0.9800

C10(H10C	0.9800

C21(C26	1.396(4)

C21(C22	1.408(4)

C21(Se2	1.948(3)

C22(C23	1.396(4)

C22(S3	1.773(3)

C23(C24	1.382(4)

C23(H23	0.9500

C24(C25	1.390(4)

C24(H24	0.9500

C25(C26	1.382(4)

C25(H25	0.9500

C26(H26	0.9500

C27(C29	1.521(4)

C27(C28	1.531(4)

C27(C30	1.531(4)

C27(S3	1.820(3)

C28(H28A	0.9800

C28(H28B	0.9800

C28(H28C	0.9800

C29(H29A	0.9800

C29(H29B	0.9800

C29(H29C	0.9800

C30(H30A	0.9800

C30(H30B	0.9800

C30(H30C	0.9800

O1(S4	1.443(2)

O2(S4	1.446(2)

O21(S3	1.446(2)

O22(S3	1.448(2)

Se1(Se2	2.3245(4)

C6(C1(C2	120.9(3)

C6(C1(S4	115.7(2)

C2(C1(S4	123.4(2)

C3(C2(C1	117.7(3)

C3(C2(Se1	120.3(2)

C1(C2(Se1	121.9(2)

C4(C3(C2	121.1(3)

C4(C3(H3	119.5

C2(C3(H3	119.5

C5(C4(C3	120.6(3)

C5(C4(H4	119.7

C3(C4(H4	119.7

C6(C5(C4	119.7(3)

C6(C5(H5	120.2

C4(C5(H5	120.2

C5(C6(C1	120.1(3)

C5(C6(H6	120.0

C1(C6(H6	120.0

C8(C7(C10	112.0(3)

C8(C7(C9	110.9(3)

C10(C7(C9	110.3(3)

C8(C7(S4	109.0(2)

C10(C7(S4	109.6(2)

C9(C7(S4	104.7(2)

C7(C8(H8A	109.5

C7(C8(H8B	109.5

H8A(C8(H8B	109.5

C7(C8(H8C	109.5

H8A(C8(H8C	109.5

H8B(C8(H8C	109.5

C7(C9(H9A	109.5

C7(C9(H9B	109.5

H9A(C9(H9B	109.5

C7(C9(H9C	109.5

H9A(C9(H9C	109.5

H9B(C9(H9C	109.5

C7(C10(H10A	109.5

C7(C10(H10B	109.5

H10A(C10(H10B	109.5

C7(C10(H10C	109.5

H10A(C10(H10C	109.5

H10B(C10(H10C	109.5

C26(C21(C22	117.5(3)

C26(C21(Se2	120.9(2)

C22(C21(Se2	121.5(2)

C23(C22(C21	120.8(3)

C23(C22(S3	115.2(2)

C21(C22(S3	124.0(2)

C24(C23(C22	120.5(3)

C24(C23(H23	119.7

C22(C23(H23	119.7

C23(C24(C25	118.9(3)

C23(C24(H24	120.5

C25(C24(H24	120.5

C26(C25(C24	120.9(3)

C26(C25(H25	119.5

C24(C25(H25	119.5

C25(C26(C21	121.2(3)

C25(C26(H26	119.4

C21(C26(H26	119.4

C29(C27(C28	111.0(3)

C29(C27(C30	111.8(3)

C28(C27(C30	111.3(3)

C29(C27(S3	109.2(2)

C28(C27(S3	104.7(2)

C30(C27(S3	108.6(2)

C27(C28(H28A	109.5

C27(C28(H28B	109.5

H28A(C28(H28B	109.5

C27(C28(H28C	109.5

H28A(C28(H28C	109.5

H28B(C28(H28C	109.5

C27(C29(H29A	109.5

C27(C29(H29B	109.5

H29A(C29(H29B	109.5

C27(C29(H29C	109.5

H29A(C29(H29C	109.5

H29B(C29(H29C	109.5

C27(C30(H30A	109.5

C27(C30(H30B	109.5

H30A(C30(H30B	109.5

C27(C30(H30C	109.5

H30A(C30(H30C	109.5

H30B(C30(H30C	109.5

O21(S3(O22	117.55(13)

O21(S3(C22	108.17(13)

O22(S3(C22	107.43(13)

O21(S3(C27	107.32(13)

O22(S3(C27	108.77(13)

C22(S3(C27	107.17(13)

O1(S4(O2	118.30(13)

O1(S4(C1	107.85(14)

O2(S4(C1	106.96(14)

O1(S4(C7	108.83(14)

O2(S4(C7	106.94(15)

C1(S4(C7	107.51(14)

C2(Se1(Se2	101.18(9)

C21(Se2(Se1	102.90(9)

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	21(2) 	14(2)	18(2) 	3(1)	8(1) 	2(1)

C2	24(2) 	14(2)	23(2) 	3(1)	11(1) 	(1(1)

C3	27(2) 	19(2)	26(2) 	2(1)	13(1) 	2(1)

C4	26(2) 	24(2)	34(2) 	8(2)	14(2) 	8(1)

C5	22(2) 	26(2)	34(2) 	6(2)	4(1) 	(2(1)

C6	27(2) 	23(2)	19(2) 	2(1)	3(1) 	(2(1)

C7	28(2) 	16(2)	26(2) 	0(1)	14(1) 	3(1)

C8	46(2) 	23(2)	26(2) 	7(2)	16(2) 	7(2)

C9	32(2) 	32(2)	37(2) 	(1(2)	18(2) 	7(2)

C10	33(2) 	19(2)	45(2) 	1(2)	18(2) 	(4(2)

C21	17(2) 	13(2)	22(2) 	(5(1)	6(1) 	(3(1)

C22	17(1) 	17(2)	14(2) 	(1(1)	4(1) 	(2(1)

C23	21(2) 	16(2)	18(2) 	(1(1)	5(1) 	1(1)

C24	25(2) 	14(2)	24(2) 	3(1)	8(1) 	3(1)

C25	28(2) 	22(2)	17(2) 	3(1)	4(1) 	1(1)

C26	25(2) 	22(2)	18(2) 	0(1)	6(1) 	(1(1)

C27	19(2) 	16(2)	16(2) 	0(1)	5(1) 	1(1)

C28	32(2) 	24(2)	18(2) 	2(1)	11(1) 	(2(1)

C29	25(2) 	22(2)	25(2) 	(1(1)	6(1) 	(4(1)

C30	21(2) 	28(2)	21(2) 	1(1)	8(1) 	4(1)

O1	25(1) 	25(1)	28(1) 	(4(1)	14(1) 	(6(1)

O2	41(1) 	34(1)	18(1) 	1(1)	14(1) 	0(1)

O21	25(1) 	19(1)	26(1) 	(2(1)	14(1) 	2(1)

O22	26(1) 	16(1)	26(1) 	(1(1)	12(1) 	(4(1)

S3	20(1) 	14(1)	18(1) 	0(1)	9(1) 	(1(1)

S4	24(1) 	19(1)	17(1) 	0(1)	10(1) 	(1(1)

Se1	22(1) 	19(1)	22(1) 	(5(1)	8(1) 	(1(1)

Se2	33(1) 	14(1)	20(1) 	(2(1)	11(1) 	(1(1)