|  | Single Crystal X-Ray Diffraction Service National Crystallography Service Contact: Dr S.K.Callear, S.K.Callear@soton.ac.uk |
| --- | --- |

Table 1. Crystal data and structure refinement details.

Identification code 	2009src0216 (RRPSAN02)

Empirical formula 	C14H21ClN3PPdS

Formula weight 	436.22

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	P21/c

Unit cell dimensions	a = 6.2066(3) Å	( = 90°

b = 17.1960(8) Å	( = 90.442(2)°

c = 15.1712(6) Å	(  = 90°

Volume	1619.15(13) Å3

Z	4

Density (calculated)	1.789 Mg / m3

Absorption coefficient	1.535 mm(1

F(000)	880

Crystal	plate; colourless

Crystal size	0.09 ( 0.07 ( 0.01 mm3

( range for data collection	2.94 ( 25.00°

Index ranges	(7 ( h ( 7, (20 ( k ( 19, (18 ( l ( 17

Reflections collected	15933

Independent reflections	2837 [Rint = 0.1108]

Completeness to ( = 25.00°	99.6 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9848 and 0.8742

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	2837 / 0 / 191

Goodness-of-fit on F2	1.168

Final R indices [F2 > 2((F2)]	R1 = 0.0780, wR2 = 0.1363

R indices (all data)	R1 = 0.1154, wR2 = 0.1527

Largest diff. peak and hole	0.851 and (0.779 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: Sheldrick, G. M. SADABS - Bruker Nonius area detector scaling and absorption correction - V2.10 Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: ORTEP-3 (L.G. Farrugia, J. Appl. Cryst. (1997) 30, 565).

Special details:

All hydrogens fixed using a standard riding model.

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	2540(15)	6738(5)	1832(6)	16(2)	1

C2	2038(17)	6916(6)	2687(6)	24(2)	1

C3	3542(18)	6794(6)	3355(7)	29(3)	1

C4	5470(20)	6458(7)	3177(8)	38(3)	1

C5	6006(18)	6217(6)	2343(9)	34(3)	1

C6	4506(17)	6365(6)	1655(7)	24(2)	1

C7	4993(17)	6122(6)	735(7)	28(3)	1

C8	2990(20)	5902(7)	(898(6)	33(3)	1

C9	727(18)	8670(6)	2115(7)	25(2)	1

C11	(2617(19)	9338(7)	2466(8)	35(3)	1

C13	(3356(16)	8194(7)	1611(9)	35(3)	1

C14	(620(20)	8852(6)	368(7)	29(3)	1

C16	(261(17)	9898(6)	1423(7)	27(3)	1

C17	(3750(19)	9480(7)	988(8)	38(3)	1

N10	(344(14)	9437(5)	2239(6)	25(2)	1

N12	(3963(15)	9008(5)	1787(7)	35(2)	1

N15	(1546(15)	9589(5)	693(6)	25(2)	1

P1	(570(4)	8095(2)	1230(2)	18(1)	1

S1	2434(4)	5801(2)	259(2)	24(1)	1

Cl1	(1329(4)	7113(2)	(599(2)	24(1)	1

Pd1	661(1)	6934(1)	748(1)	18(1)	1

Table 3. Bond lengths [Å] and angles [°].

C1(C2	1.370(13)

C1(C6	1.407(14)

C1(Pd1	2.037(9)

C2(C3	1.389(15)

C2(H2	0.9500

C3(C4	1.359(16)

C3(H3	0.9500

C4(C5	1.375(17)

C4(H4	0.9500

C5(C6	1.416(15)

C5(H5	0.9500

C6(C7	1.491(15)

C7(S1	1.825(11)

C7(H7A	0.9900

C7(H7B	0.9900

C8(S1	1.800(10)

C8(H8A	0.9800

C8(H8B	0.9800

C8(H8C	0.9800

C9(N10	1.489(13)

C9(P1	1.847(10)

C9(H9A	0.9900

C9(H9B	0.9900

C11(N12	1.438(16)

C11(N10	1.465(14)

C11(H11A	0.9900

C11(H11B	0.9900

C13(N12	1.475(14)

C13(P1	1.835(11)

C13(H13B	0.9900

C13(H13A	0.9900

C14(N15	1.478(13)

C14(P1	1.846(11)

C14(H14A	0.9900

C14(H14B	0.9900

C16(N15	1.461(13)

C16(N10	1.470(13)

C16(H16A	0.9900

C16(H16B	0.9900

C17(N15	1.455(15)

C17(N12	1.465(15)

C17(H17A	0.9900

C17(H17B	0.9900

P1(Pd1	2.262(3)

S1(Pd1	2.359(3)

Cl1(Pd1	2.400(3)

C2(C1(C6	119.1(9)

C2(C1(Pd1	126.5(7)

C6(C1(Pd1	114.4(7)

C1(C2(C3	120.1(10)

C1(C2(H2	120.0

C3(C2(H2	120.0

C4(C3(C2	120.5(11)

C4(C3(H3	119.8

C2(C3(H3	119.8

C3(C4(C5	122.1(11)

C3(C4(H4	119.0

C5(C4(H4	119.0

C4(C5(C6	117.5(11)

C4(C5(H5	121.3

C6(C5(H5	121.3

C1(C6(C5	120.6(10)

C1(C6(C7	119.3(9)

C5(C6(C7	120.1(10)

C6(C7(S1	105.9(7)

C6(C7(H7A	110.6

S1(C7(H7A	110.6

C6(C7(H7B	110.6

S1(C7(H7B	110.6

H7A(C7(H7B	108.7

S1(C8(H8A	109.5

S1(C8(H8B	109.5

H8A(C8(H8B	109.5

S1(C8(H8C	109.5

H8A(C8(H8C	109.5

H8B(C8(H8C	109.5

N10(C9(P1	111.9(7)

N10(C9(H9A	109.2

P1(C9(H9A	109.2

N10(C9(H9B	109.2

P1(C9(H9B	109.2

H9A(C9(H9B	107.9

N12(C11(N10	115.7(9)

N12(C11(H11A	108.4

N10(C11(H11A	108.4

N12(C11(H11B	108.4

N10(C11(H11B	108.4

H11A(C11(H11B	107.4

N12(C13(P1	112.8(7)

N12(C13(H13B	109.0

P1(C13(H13B	109.0

N12(C13(H13A	109.0

P1(C13(H13A	109.0

H13B(C13(H13A	107.8

N15(C14(P1	111.8(7)

N15(C14(H14A	109.3

P1(C14(H14A	109.3

N15(C14(H14B	109.3

P1(C14(H14B	109.3

H14A(C14(H14B	107.9

N15(C16(N10	114.9(8)

N15(C16(H16A	108.6

N10(C16(H16A	108.6

N15(C16(H16B	108.6

N10(C16(H16B	108.6

H16A(C16(H16B	107.5

N15(C17(N12	114.6(9)

N15(C17(H17A	108.6

N12(C17(H17A	108.6

N15(C17(H17B	108.6

N12(C17(H17B	108.6

H17A(C17(H17B	107.6

C11(N10(C16	107.4(8)

C11(N10(C9	111.0(9)

C16(N10(C9	110.6(8)

C11(N12(C17	108.5(9)

C11(N12(C13	110.9(9)

C17(N12(C13	110.6(10)

C17(N15(C16	108.8(9)

C17(N15(C14	111.3(9)

C16(N15(C14	110.7(9)

C13(P1(C14	98.5(6)

C13(P1(C9	97.4(5)

C14(P1(C9	98.2(5)

C13(P1(Pd1	120.3(4)

C14(P1(Pd1	113.4(4)

C9(P1(Pd1	124.1(3)

C8(S1(C7	100.6(5)

C8(S1(Pd1	108.7(4)

C7(S1(Pd1	91.9(4)

C1(Pd1(P1	94.4(3)

C1(Pd1(S1	81.5(3)

P1(Pd1(S1	171.90(10)

C1(Pd1(Cl1	175.3(3)

P1(Pd1(Cl1	89.37(9)

S1(Pd1(Cl1	94.38(9)

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	16(5) 	15(6)	17(5) 	1(4)	(4(4) 	1(4)

C2	32(6) 	24(6)	15(5) 	7(5)	(4(4) 	(8(5)

C3	41(7) 	23(7)	24(6) 	4(5)	(4(5) 	(11(5)

C4	52(8) 	25(7)	37(7) 	6(6)	(26(6) 	(2(6)

C5	23(6) 	15(6)	65(9) 	8(6)	(14(6) 	3(5)

C6	26(6) 	19(6)	26(6) 	(4(5)	0(5) 	(6(5)

C7	28(6) 	16(6)	41(7) 	5(5)	(1(6) 	2(4)

C8	46(7) 	42(7)	9(5) 	(4(5)	4(5) 	10(6)

C9	36(6) 	17(6)	21(6) 	(11(5)	(9(5) 	6(5)

C11	48(8) 	20(6)	38(7) 	1(5)	30(6) 	12(5)

C13	17(5) 	29(7)	58(8) 	(2(6)	(2(5) 	(3(5)

C14	50(7) 	18(6)	20(6) 	1(5)	(11(5) 	1(5)

C16	22(6) 	19(6)	39(7) 	(4(5)	6(5) 	(12(5)

C17	36(7) 	31(7)	47(8) 	(2(6)	(16(6) 	7(5)

N10	36(5) 	17(5)	21(5) 	(1(4)	(8(4) 	5(4)

N12	30(5) 	21(5)	55(7) 	(3(5)	8(5) 	0(4)

N15	39(6) 	9(4)	25(5) 	3(4)	(8(4) 	0(4)

P1	19(1) 	17(1)	17(1) 	2(1)	0(1) 	0(1)

S1	29(2) 	21(2)	22(1) 	(3(1)	1(1) 	4(1)

Cl1	29(1) 	25(2)	17(1) 	3(1)	(4(1) 	0(1)

Pd1	19(1) 	17(1)	16(1) 	1(1)	0(1) 	1(1)