|  | University of Southampton · School of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	04src0437r

Empirical formula 	C30.50H53Cl3FeP2Pd

Formula weight 	750.27

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	P21/c

Unit cell dimensions	a = 19.4376(15) Å	( = 90°

b = 11.1178(11) Å	( = 91.579(8)°

c = 30.276(3) Å	(  = 90°

Volume	6540.2(10) Å3

Z	8

Density (calculated)	1.524 Mg / m3

Absorption coefficient	1.356 mm(1

F(000)	3112

Crystal	Slab; Red

Crystal size	0.56 ( 0.40 ( 0.16 mm3

( range for data collection	2.94 ( 27.48°

Index ranges	(22 ( h ( 25, (14 ( k ( 14, (39 ( l ( 35

Reflections collected	48804

Independent reflections	14858 [Rint = 0.0337]

Completeness to ( = 27.48°	99.0 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.8122 and 0.5172

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	14858 / 0 / 708

Goodness-of-fit on F2	1.038

Final R indices [F2 > 2((F2)]	R1 = 0.0293, wR2 = 0.0650

R indices (all data)	R1 = 0.0401, wR2 = 0.0689

Largest diff. peak and hole	0.517 and (0.698 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SORTAV (R. H. Blessing, Acta Cryst. A51 (1995) 33(37; R. H. Blessing, J. Appl. Cryst. 30 (1997) 421(426). Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: Cameron - A Molecular Graphics Package. (D. M. Watkin, L. Pearce and C. K. Prout, Chemical Crystallography Laboratory, University of Oxford, 1993).

Special details:

All hydrogen atoms were fixed.

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	1637(1)	5157(2)	8677(1)	13(1)	1

C2	1356(1)	5499(2)	9097(1)	16(1)	1

C3	758(1)	6219(2)	9004(1)	18(1)	1

C4	664(1)	6318(2)	8538(1)	18(1)	1

C5	1204(1)	5684(2)	8332(1)	16(1)	1

C6	699(1)	2741(2)	8637(1)	12(1)	1

C7	433(1)	3035(2)	9066(1)	15(1)	1

C8	(175(1)	3746(2)	8992(1)	17(1)	1

C9	(293(1)	3878(2)	8531(1)	18(1)	1

C10	242(1)	3287(2)	8307(1)	16(1)	1

C11	1602(1)	5252(3)	9561(1)	23(1)	1

C12	333(1)	6826(3)	9342(1)	28(1)	1

C13	90(1)	6977(2)	8303(1)	27(1)	1

C14	1312(1)	5676(2)	7844(1)	21(1)	1

C15	685(1)	2705(2)	9520(1)	21(1)	1

C16	(631(1)	4227(2)	9343(1)	27(1)	1

C17	(905(1)	4472(2)	8314(1)	28(1)	1

C18	275(1)	3196(2)	7815(1)	22(1)	1

C19	2932(1)	5620(2)	8303(1)	18(1)	1

C20	2828(1)	6815(2)	8546(1)	25(1)	1

C21	3695(1)	5343(3)	8262(1)	24(1)	1

C22	2877(1)	3803(2)	9032(1)	16(1)	1

C23	3432(1)	2891(2)	8914(1)	23(1)	1

C24	3198(1)	4746(2)	9344(1)	19(1)	1

C25	909(1)	613(2)	8136(1)	16(1)	1

C26	196(1)	326(2)	8313(1)	21(1)	1

C27	1321(1)	(547(2)	8065(1)	19(1)	1

C28	1799(1)	1018(2)	8934(1)	16(1)	1

C29	2457(1)	325(2)	8816(1)	24(1)	1

C30	1320(1)	187(2)	9187(1)	21(1)	1

P1	2416(1)	4355(1)	8531(1)	11(1)	1

P2	1398(1)	1789(1)	8452(1)	11(1)	1

Cl1	2883(1)	3767(1)	7510(1)	19(1)	1

Cl2	1921(1)	1513(1)	7431(1)	24(1)	1

Fe1	664(1)	4543(1)	8718(1)	11(1)	1

Pd1	2161(1)	2843(1)	8019(1)	11(1)	1

C31	4212(1)	5749(2)	6146(1)	12(1)	1

C32	4234(1)	6486(2)	6541(1)	14(1)	1

C33	4411(1)	7680(2)	6404(1)	16(1)	1

C34	4488(1)	7694(2)	5938(1)	16(1)	1

C35	4365(1)	6510(2)	5775(1)	14(1)	1

C36	2587(1)	6307(2)	6003(1)	12(1)	1

C37	2590(1)	7043(2)	6396(1)	13(1)	1

C38	2738(1)	8250(2)	6265(1)	16(1)	1

C39	2821(1)	8276(2)	5801(1)	17(1)	1

C40	2734(1)	7085(2)	5632(1)	15(1)	1

C41	4103(1)	6195(2)	7013(1)	19(1)	1

C42	4541(1)	8716(2)	6709(1)	22(1)	1

C43	4700(1)	8750(2)	5664(1)	24(1)	1

C44	4438(1)	6147(2)	5304(1)	20(1)	1

C45	2442(1)	6719(2)	6864(1)	18(1)	1

C46	2781(1)	9329(2)	6560(1)	21(1)	1

C47	2947(1)	9386(2)	5533(1)	25(1)	1

C48	2743(1)	6763(2)	5152(1)	21(1)	1

C49	3997(1)	3418(2)	6586(1)	16(1)	1

C50	3755(2)	2110(2)	6532(1)	29(1)	1

C51	4611(1)	3482(2)	6913(1)	22(1)	1

C52	4979(1)	3725(2)	5849(1)	16(1)	1

C53	5575(1)	4488(3)	6032(1)	26(1)	1

C54	5150(1)	2385(2)	5910(1)	28(1)	1

C55	1550(1)	4982(2)	5557(1)	18(1)	1

C56	1061(1)	3907(2)	5529(1)	25(1)	1

C57	1145(1)	6091(2)	5696(1)	27(1)	1

C58	2127(1)	3918(2)	6395(1)	15(1)	1

C59	2046(1)	2568(2)	6290(1)	24(1)	1

C60	1494(1)	4344(2)	6638(1)	20(1)	1

P31	4109(1)	4148(1)	6048(1)	11(1)	1

P32	2366(1)	4744(1)	5892(1)	11(1)	1

Cl31	3984(1)	2527(1)	5140(1)	34(1)	1

Cl32	2425(1)	3155(1)	4981(1)	29(1)	1

Fe31	3516(1)	7093(1)	6091(1)	11(1)	1

Pd31	3224(1)	3692(1)	5541(1)	11(1)	1

C71	3637(2)	587(3)	7590(1)	30(1)	1

Cl71	3429(1)	(876(1)	7777(1)	38(1)	1

Cl72	4079(1)	1407(1)	7998(1)	35(1)	1

Table 3. Bond lengths [Å] and angles [°].

C1(C5	1.447(3)

C1(C2	1.449(3)

C1(P1	1.822(2)

C1(Fe1	2.019(2)

C2(C3	1.432(3)

C2(C11	1.497(3)

C2(Fe1	2.043(2)

C3(C4	1.420(3)

C3(C12	1.496(3)

C3(Fe1	2.060(2)

C4(C5	1.423(3)

C4(C13	1.498(3)

C4(Fe1	2.048(2)

C5(C14	1.500(3)

C5(Fe1	2.036(2)

C6(C10	1.451(3)

C6(C7	1.451(3)

C6(P2	1.822(2)

C6(Fe1	2.020(2)

C7(C8	1.434(3)

C7(C15	1.491(3)

C7(Fe1	2.037(2)

C8(C9	1.417(3)

C8(C16	1.499(3)

C8(Fe1	2.052(2)

C9(C10	1.419(3)

C9(C17	1.497(3)

C9(Fe1	2.066(2)

C10(C18	1.497(3)

C10(Fe1	2.027(2)

C11(H11A	0.9800

C11(H11B	0.9800

C11(H11C	0.9800

C12(H12A	0.9800

C12(H12B	0.9800

C12(H12C	0.9800

C13(H13A	0.9800

C13(H13B	0.9800

C13(H13C	0.9800

C14(H14A	0.9800

C14(H14B	0.9800

C14(H14C	0.9800

C15(H15A	0.9800

C15(H15B	0.9800

C15(H15C	0.9800

C16(H16A	0.9800

C16(H16B	0.9800

C16(H16C	0.9800

C17(H17A	0.9800

C17(H17B	0.9800

C17(H17C	0.9800

C18(H18A	0.9800

C18(H18B	0.9800

C18(H18C	0.9800

C19(C21	1.523(3)

C19(C20	1.534(4)

C19(P1	1.870(2)

C19(H19	1.0000

C20(H20A	0.9800

C20(H20B	0.9800

C20(H20C	0.9800

C21(H21A	0.9800

C21(H21B	0.9800

C21(H21C	0.9800

C22(C23	1.531(3)

C22(C24	1.532(3)

C22(P1	1.844(2)

C22(H22	1.0000

C23(H23A	0.9800

C23(H23B	0.9800

C23(H23C	0.9800

C24(H24A	0.9800

C24(H24B	0.9800

C24(H24C	0.9800

C25(C26	1.532(3)

C25(C27	1.537(3)

C25(P2	1.865(2)

C25(H25	1.0000

C26(H26A	0.9800

C26(H26B	0.9800

C26(H26C	0.9800

C27(H27A	0.9800

C27(H27B	0.9800

C27(H27C	0.9800

C28(C30	1.532(3)

C28(C29	1.543(3)

C28(P2	1.845(2)

C28(H28	1.0000

C29(H29A	0.9800

C29(H29B	0.9800

C29(H29C	0.9800

C30(H30A	0.9800

C30(H30B	0.9800

C30(H30C	0.9800

P1(Pd1	2.3306(6)

P2(Pd1	2.3242(6)

Cl1(Pd1	2.3496(6)

Cl2(Pd1	2.3507(6)

C31(C35	1.443(3)

C31(C32	1.450(3)

C31(P31	1.815(2)

C31(Fe31	2.020(2)

C32(C33	1.435(3)

C32(C41	1.494(3)

C32(Fe31	2.038(2)

C33(C34	1.425(3)

C33(C42	1.492(3)

C33(Fe31	2.066(2)

C34(C35	1.424(3)

C34(C43	1.501(3)

C34(Fe31	2.069(2)

C35(C44	1.493(3)

C35(Fe31	2.036(2)

C36(C37	1.444(3)

C36(C40	1.453(3)

C36(P32	1.819(2)

C36(Fe31	2.016(2)

C37(C38	1.431(3)

C37(C45	1.498(3)

C37(Fe31	2.046(2)

C38(C39	1.418(3)

C38(C46	1.497(3)

C38(Fe31	2.064(2)

C39(C40	1.427(3)

C39(C47	1.500(3)

C39(Fe31	2.064(2)

C40(C48	1.498(3)

C40(Fe31	2.030(2)

C41(H41A	0.9800

C41(H41B	0.9800

C41(H41C	0.9800

C42(H42A	0.9800

C42(H42B	0.9800

C42(H42C	0.9800

C43(H43A	0.9800

C43(H43B	0.9800

C43(H43C	0.9800

C44(H44A	0.9800

C44(H44B	0.9800

C44(H44C	0.9800

C45(H45A	0.9800

C45(H45B	0.9800

C45(H45C	0.9800

C46(H46A	0.9800

C46(H46B	0.9800

C46(H46C	0.9800

C47(H47A	0.9800

C47(H47B	0.9800

C47(H47C	0.9800

C48(H48A	0.9800

C48(H48B	0.9800

C48(H48C	0.9800

C49(C51	1.532(3)

C49(C50	1.537(3)

C49(P31	1.838(2)

C49(H49	1.0000

C50(H50A	0.9800

C50(H50B	0.9800

C50(H50C	0.9800

C51(H51A	0.9800

C51(H51B	0.9800

C51(H51C	0.9800

C52(C53	1.528(3)

C52(C54	1.537(3)

C52(P31	1.871(2)

C52(H52	1.0000

C53(H53A	0.9800

C53(H53B	0.9800

C53(H53C	0.9800

C54(H54A	0.9800

C54(H54B	0.9800

C54(H54C	0.9800

C55(C56	1.528(3)

C55(C57	1.530(3)

C55(P32	1.876(2)

C55(H55	1.0000

C56(H56A	0.9800

C56(H56B	0.9800

C56(H56C	0.9800

C57(H57A	0.9800

C57(H57B	0.9800

C57(H57C	0.9800

C58(C60	1.526(3)

C58(C59	1.541(3)

C58(P32	1.851(2)

C58(H58	1.0000

C59(H59A	0.9800

C59(H59B	0.9800

C59(H59C	0.9800

C60(H60A	0.9800

C60(H60B	0.9800

C60(H60C	0.9800

P31(Pd31	2.3293(6)

P32(Pd31	2.3190(6)

Cl31(Pd31	2.3311(7)

Cl32(Pd31	2.3448(6)

C71(Cl72	1.742(3)

C71(Cl71	1.773(3)

C71(H71A	0.9900

C71(H71B	0.9900

C5(C1(C2	107.50(19)

C5(C1(P1	119.57(17)

C2(C1(P1	132.70(17)

C5(C1(Fe1	69.73(13)

C2(C1(Fe1	69.99(13)

P1(C1(Fe1	129.47(12)

C3(C2(C1	107.2(2)

C3(C2(C11	121.7(2)

C1(C2(C11	131.0(2)

C3(C2(Fe1	70.22(13)

C1(C2(Fe1	68.20(12)

C11(C2(Fe1	128.39(18)

C4(C3(C2	108.8(2)

C4(C3(C12	125.8(2)

C2(C3(C12	125.3(2)

C4(C3(Fe1	69.30(13)

C2(C3(Fe1	68.92(13)

C12(C3(Fe1	130.65(18)

C3(C4(C5	108.6(2)

C3(C4(C13	125.7(2)

C5(C4(C13	125.7(2)

C3(C4(Fe1	70.25(14)

C5(C4(Fe1	69.16(13)

C13(C4(Fe1	126.33(18)

C4(C5(C1	107.9(2)

C4(C5(C14	124.0(2)

C1(C5(C14	128.0(2)

C4(C5(Fe1	70.05(13)

C1(C5(Fe1	68.46(13)

C14(C5(Fe1	130.53(18)

C10(C6(C7	107.13(19)

C10(C6(P2	118.72(17)

C7(C6(P2	133.92(17)

C10(C6(Fe1	69.28(13)

C7(C6(Fe1	69.68(13)

P2(C6(Fe1	129.93(12)

C8(C7(C6	107.3(2)

C8(C7(C15	121.9(2)

C6(C7(C15	130.8(2)

C8(C7(Fe1	70.02(13)

C6(C7(Fe1	68.40(13)

C15(C7(Fe1	127.43(17)

C9(C8(C7	108.7(2)

C9(C8(C16	125.3(2)

C7(C8(C16	125.9(2)

C9(C8(Fe1	70.43(14)

C7(C8(Fe1	68.92(13)

C16(C8(Fe1	128.63(18)

C8(C9(C10	108.8(2)

C8(C9(C17	125.8(2)

C10(C9(C17	125.3(2)

C8(C9(Fe1	69.33(13)

C10(C9(Fe1	68.26(13)

C17(C9(Fe1	131.41(18)

C9(C10(C6	108.0(2)

C9(C10(C18	124.0(2)

C6(C10(C18	127.8(2)

C9(C10(Fe1	71.20(14)

C6(C10(Fe1	68.72(13)

C18(C10(Fe1	129.00(18)

C2(C11(H11A	109.5

C2(C11(H11B	109.5

H11A(C11(H11B	109.5

C2(C11(H11C	109.5

H11A(C11(H11C	109.5

H11B(C11(H11C	109.5

C3(C12(H12A	109.5

C3(C12(H12B	109.5

H12A(C12(H12B	109.5

C3(C12(H12C	109.5

H12A(C12(H12C	109.5

H12B(C12(H12C	109.5

C4(C13(H13A	109.5

C4(C13(H13B	109.5

H13A(C13(H13B	109.5

C4(C13(H13C	109.5

H13A(C13(H13C	109.5

H13B(C13(H13C	109.5

C5(C14(H14A	109.5

C5(C14(H14B	109.5

H14A(C14(H14B	109.5

C5(C14(H14C	109.5

H14A(C14(H14C	109.5

H14B(C14(H14C	109.5

C7(C15(H15A	109.5

C7(C15(H15B	109.5

H15A(C15(H15B	109.5

C7(C15(H15C	109.5

H15A(C15(H15C	109.5

H15B(C15(H15C	109.5

C8(C16(H16A	109.5

C8(C16(H16B	109.5

H16A(C16(H16B	109.5

C8(C16(H16C	109.5

H16A(C16(H16C	109.5

H16B(C16(H16C	109.5

C9(C17(H17A	109.5

C9(C17(H17B	109.5

H17A(C17(H17B	109.5

C9(C17(H17C	109.5

H17A(C17(H17C	109.5

H17B(C17(H17C	109.5

C10(C18(H18A	109.5

C10(C18(H18B	109.5

H18A(C18(H18B	109.5

C10(C18(H18C	109.5

H18A(C18(H18C	109.5

H18B(C18(H18C	109.5

C21(C19(C20	110.8(2)

C21(C19(P1	114.28(17)

C20(C19(P1	113.34(17)

C21(C19(H19	105.9

C20(C19(H19	105.9

P1(C19(H19	105.9

C19(C20(H20A	109.5

C19(C20(H20B	109.5

H20A(C20(H20B	109.5

C19(C20(H20C	109.5

H20A(C20(H20C	109.5

H20B(C20(H20C	109.5

C19(C21(H21A	109.5

C19(C21(H21B	109.5

H21A(C21(H21B	109.5

C19(C21(H21C	109.5

H21A(C21(H21C	109.5

H21B(C21(H21C	109.5

C23(C22(C24	108.58(19)

C23(C22(P1	111.03(16)

C24(C22(P1	117.40(17)

C23(C22(H22	106.4

C24(C22(H22	106.4

P1(C22(H22	106.4

C22(C23(H23A	109.5

C22(C23(H23B	109.5

H23A(C23(H23B	109.5

C22(C23(H23C	109.5

H23A(C23(H23C	109.5

H23B(C23(H23C	109.5

C22(C24(H24A	109.5

C22(C24(H24B	109.5

H24A(C24(H24B	109.5

C22(C24(H24C	109.5

H24A(C24(H24C	109.5

H24B(C24(H24C	109.5

C26(C25(C27	110.8(2)

C26(C25(P2	114.85(16)

C27(C25(P2	113.50(16)

C26(C25(H25	105.6

C27(C25(H25	105.6

P2(C25(H25	105.6

C25(C26(H26A	109.5

C25(C26(H26B	109.5

H26A(C26(H26B	109.5

C25(C26(H26C	109.5

H26A(C26(H26C	109.5

H26B(C26(H26C	109.5

C25(C27(H27A	109.5

C25(C27(H27B	109.5

H27A(C27(H27B	109.5

C25(C27(H27C	109.5

H27A(C27(H27C	109.5

H27B(C27(H27C	109.5

C30(C28(C29	109.5(2)

C30(C28(P2	115.26(16)

C29(C28(P2	112.55(17)

C30(C28(H28	106.3

C29(C28(H28	106.3

P2(C28(H28	106.3

C28(C29(H29A	109.5

C28(C29(H29B	109.5

H29A(C29(H29B	109.5

C28(C29(H29C	109.5

H29A(C29(H29C	109.5

H29B(C29(H29C	109.5

C28(C30(H30A	109.5

C28(C30(H30B	109.5

H30A(C30(H30B	109.5

C28(C30(H30C	109.5

H30A(C30(H30C	109.5

H30B(C30(H30C	109.5

C1(P1(C22	110.52(11)

C1(P1(C19	100.29(11)

C22(P1(C19	107.45(11)

C1(P1(Pd1	110.62(7)

C22(P1(Pd1	113.36(8)

C19(P1(Pd1	113.81(8)

C6(P2(C28	109.26(11)

C6(P2(C25	100.98(10)

C28(P2(C25	106.14(11)

C6(P2(Pd1	111.90(7)

C28(P2(Pd1	114.70(8)

C25(P2(Pd1	112.86(8)

C1(Fe1(C6	107.03(9)

C1(Fe1(C10	124.00(9)

C6(Fe1(C10	42.01(9)

C1(Fe1(C5	41.81(9)

C6(Fe1(C5	121.89(9)

C10(Fe1(C5	106.48(10)

C1(Fe1(C7	122.05(9)

C6(Fe1(C7	41.92(9)

C10(Fe1(C7	70.11(10)

C5(Fe1(C7	159.15(9)

C1(Fe1(C2	41.81(9)

C6(Fe1(C2	124.11(9)

C10(Fe1(C2	162.17(9)

C5(Fe1(C2	69.87(10)

C7(Fe1(C2	106.77(10)

C1(Fe1(C4	69.56(9)

C6(Fe1(C4	157.42(10)

C10(Fe1(C4	120.22(10)

C5(Fe1(C4	40.79(9)

C7(Fe1(C4	158.82(9)

C2(Fe1(C4	69.08(10)

C1(Fe1(C8	158.09(10)

C6(Fe1(C8	69.60(9)

C10(Fe1(C8	68.82(10)

C5(Fe1(C8	158.40(10)

C7(Fe1(C8	41.05(9)

C2(Fe1(C8	121.03(10)

C4(Fe1(C8	121.98(9)

C1(Fe1(C3	69.32(9)

C6(Fe1(C3	160.98(10)

C10(Fe1(C3	155.48(10)

C5(Fe1(C3	68.61(10)

C7(Fe1(C3	123.06(10)

C2(Fe1(C3	40.86(9)

C4(Fe1(C3	40.45(10)

C8(Fe1(C3	106.46(10)

C1(Fe1(C9	160.50(10)

C6(Fe1(C9	69.23(9)

C10(Fe1(C9	40.54(9)

C5(Fe1(C9	122.73(10)

C7(Fe1(C9	68.75(10)

C2(Fe1(C9	156.06(9)

C4(Fe1(C9	106.16(10)

C8(Fe1(C9	40.24(10)

C3(Fe1(C9	120.50(10)

P2(Pd1(P1	96.62(2)

P2(Pd1(Cl1	173.12(2)

P1(Pd1(Cl1	90.09(2)

P2(Pd1(Cl2	89.64(2)

P1(Pd1(Cl2	172.47(2)

Cl1(Pd1(Cl2	83.56(2)

C35(C31(C32	108.02(19)

C35(C31(P31	118.23(17)

C32(C31(P31	133.52(17)

C35(C31(Fe31	69.76(12)

C32(C31(Fe31	69.73(12)

P31(C31(Fe31	129.87(12)

C33(C32(C31	106.6(2)

C33(C32(C41	121.7(2)

C31(C32(C41	131.7(2)

C33(C32(Fe31	70.57(13)

C31(C32(Fe31	68.39(12)

C41(C32(Fe31	125.42(16)

C34(C33(C32	109.2(2)

C34(C33(C42	125.7(2)

C32(C33(C42	125.0(2)

C34(C33(Fe31	69.97(13)

C32(C33(Fe31	68.51(13)

C42(C33(Fe31	130.75(17)

C35(C34(C33	108.2(2)

C35(C34(C43	125.3(2)

C33(C34(C43	126.5(2)

C35(C34(Fe31	68.46(13)

C33(C34(Fe31	69.73(13)

C43(C34(Fe31	130.00(17)

C34(C35(C31	108.0(2)

C34(C35(C44	124.2(2)

C31(C35(C44	127.7(2)

C34(C35(Fe31	70.94(13)

C31(C35(Fe31	68.57(12)

C44(C35(Fe31	129.44(17)

C37(C36(C40	107.61(19)

C37(C36(P32	133.62(17)

C40(C36(P32	118.45(17)

C37(C36(Fe31	70.27(12)

C40(C36(Fe31	69.45(12)

P32(C36(Fe31	130.16(12)

C38(C37(C36	107.4(2)

C38(C37(C45	122.3(2)

C36(C37(C45	130.3(2)

C38(C37(Fe31	70.32(13)

C36(C37(Fe31	68.09(12)

C45(C37(Fe31	128.89(16)

C39(C38(C37	108.9(2)

C39(C38(C46	124.7(2)

C37(C38(C46	126.4(2)

C39(C38(Fe31	69.88(13)

C37(C38(Fe31	68.93(12)

C46(C38(Fe31	128.44(16)

C38(C39(C40	108.7(2)

C38(C39(C47	125.2(2)

C40(C39(C47	126.0(2)

C38(C39(Fe31	69.94(13)

C40(C39(Fe31	68.32(13)

C47(C39(Fe31	129.81(17)

C39(C40(C36	107.5(2)

C39(C40(C48	124.4(2)

C36(C40(C48	128.0(2)

C39(C40(Fe31	70.88(13)

C36(C40(Fe31	68.47(12)

C48(C40(Fe31	129.57(17)

C32(C41(H41A	109.5

C32(C41(H41B	109.5

H41A(C41(H41B	109.5

C32(C41(H41C	109.5

H41A(C41(H41C	109.5

H41B(C41(H41C	109.5

C33(C42(H42A	109.5

C33(C42(H42B	109.5

H42A(C42(H42B	109.5

C33(C42(H42C	109.5

H42A(C42(H42C	109.5

H42B(C42(H42C	109.5

C34(C43(H43A	109.5

C34(C43(H43B	109.5

H43A(C43(H43B	109.5

C34(C43(H43C	109.5

H43A(C43(H43C	109.5

H43B(C43(H43C	109.5

C35(C44(H44A	109.5

C35(C44(H44B	109.5

H44A(C44(H44B	109.5

C35(C44(H44C	109.5

H44A(C44(H44C	109.5

H44B(C44(H44C	109.5

C37(C45(H45A	109.5

C37(C45(H45B	109.5

H45A(C45(H45B	109.5

C37(C45(H45C	109.5

H45A(C45(H45C	109.5

H45B(C45(H45C	109.5

C38(C46(H46A	109.5

C38(C46(H46B	109.5

H46A(C46(H46B	109.5

C38(C46(H46C	109.5

H46A(C46(H46C	109.5

H46B(C46(H46C	109.5

C39(C47(H47A	109.5

C39(C47(H47B	109.5

H47A(C47(H47B	109.5

C39(C47(H47C	109.5

H47A(C47(H47C	109.5

H47B(C47(H47C	109.5

C40(C48(H48A	109.5

C40(C48(H48B	109.5

H48A(C48(H48B	109.5

C40(C48(H48C	109.5

H48A(C48(H48C	109.5

H48B(C48(H48C	109.5

C51(C49(C50	110.1(2)

C51(C49(P31	116.31(17)

C50(C49(P31	111.48(17)

C51(C49(H49	106.1

C50(C49(H49	106.1

P31(C49(H49	106.1

C49(C50(H50A	109.5

C49(C50(H50B	109.5

H50A(C50(H50B	109.5

C49(C50(H50C	109.5

H50A(C50(H50C	109.5

H50B(C50(H50C	109.5

C49(C51(H51A	109.5

C49(C51(H51B	109.5

H51A(C51(H51B	109.5

C49(C51(H51C	109.5

H51A(C51(H51C	109.5

H51B(C51(H51C	109.5

C53(C52(C54	109.6(2)

C53(C52(P31	115.21(17)

C54(C52(P31	113.52(18)

C53(C52(H52	105.9

C54(C52(H52	105.9

P31(C52(H52	105.9

C52(C53(H53A	109.5

C52(C53(H53B	109.5

H53A(C53(H53B	109.5

C52(C53(H53C	109.5

H53A(C53(H53C	109.5

H53B(C53(H53C	109.5

C52(C54(H54A	109.5

C52(C54(H54B	109.5

H54A(C54(H54B	109.5

C52(C54(H54C	109.5

H54A(C54(H54C	109.5

H54B(C54(H54C	109.5

C56(C55(C57	108.7(2)

C56(C55(P32	115.82(18)

C57(C55(P32	113.46(17)

C56(C55(H55	106.0

C57(C55(H55	106.0

P32(C55(H55	106.0

C55(C56(H56A	109.5

C55(C56(H56B	109.5

H56A(C56(H56B	109.5

C55(C56(H56C	109.5

H56A(C56(H56C	109.5

H56B(C56(H56C	109.5

C55(C57(H57A	109.5

C55(C57(H57B	109.5

H57A(C57(H57B	109.5

C55(C57(H57C	109.5

H57A(C57(H57C	109.5

H57B(C57(H57C	109.5

C60(C58(C59	108.9(2)

C60(C58(P32	117.80(17)

C59(C58(P32	109.83(16)

C60(C58(H58	106.6

C59(C58(H58	106.6

P32(C58(H58	106.6

C58(C59(H59A	109.5

C58(C59(H59B	109.5

H59A(C59(H59B	109.5

C58(C59(H59C	109.5

H59A(C59(H59C	109.5

H59B(C59(H59C	109.5

C58(C60(H60A	109.5

C58(C60(H60B	109.5

H60A(C60(H60B	109.5

C58(C60(H60C	109.5

H60A(C60(H60C	109.5

H60B(C60(H60C	109.5

C31(P31(C49	107.74(11)

C31(P31(C52	101.65(10)

C49(P31(C52	107.79(11)

C31(P31(Pd31	113.39(7)

C49(P31(Pd31	112.63(8)

C52(P31(Pd31	112.91(8)

C36(P32(C58	112.63(10)

C36(P32(C55	99.09(10)

C58(P32(C55	106.73(11)

C36(P32(Pd31	113.38(7)

C58(P32(Pd31	109.07(8)

C55(P32(Pd31	115.57(8)

C36(Fe31(C31	106.60(9)

C36(Fe31(C40	42.08(9)

C31(Fe31(C40	122.69(9)

C36(Fe31(C35	122.27(9)

C31(Fe31(C35	41.67(9)

C40(Fe31(C35	106.11(9)

C36(Fe31(C32	122.59(9)

C31(Fe31(C32	41.87(9)

C40(Fe31(C32	160.34(9)

C35(Fe31(C32	70.13(9)

C36(Fe31(C37	41.64(9)

C31(Fe31(C37	122.62(9)

C40(Fe31(C37	70.01(9)

C35(Fe31(C37	159.69(9)

C32(Fe31(C37	106.49(9)

C36(Fe31(C39	69.36(9)

C31(Fe31(C39	159.29(10)

C40(Fe31(C39	40.80(9)

C35(Fe31(C39	122.12(10)

C32(Fe31(C39	157.42(10)

C37(Fe31(C39	68.66(9)

C36(Fe31(C38	69.19(9)

C31(Fe31(C38	159.09(9)

C40(Fe31(C38	68.74(9)

C35(Fe31(C38	157.93(10)

C32(Fe31(C38	121.94(9)

C37(Fe31(C38	40.75(9)

C39(Fe31(C38	40.18(10)

C36(Fe31(C33	159.66(9)

C31(Fe31(C33	68.97(9)

C40(Fe31(C33	157.08(10)

C35(Fe31(C33	68.46(9)

C32(Fe31(C33	40.92(9)

C37(Fe31(C33	122.81(9)

C39(Fe31(C33	121.84(9)

C38(Fe31(C33	107.48(9)

C36(Fe31(C34	158.46(9)

C31(Fe31(C34	69.09(9)

C40(Fe31(C34	121.24(9)

C35(Fe31(C34	40.60(9)

C32(Fe31(C34	69.15(9)

C37(Fe31(C34	158.42(9)

C39(Fe31(C34	106.82(9)

C38(Fe31(C34	122.37(9)

C33(Fe31(C34	40.31(9)

P32(Pd31(P31	96.66(2)

P32(Pd31(Cl31	173.26(2)

P31(Pd31(Cl31	89.87(2)

P32(Pd31(Cl32	89.33(2)

P31(Pd31(Cl32	173.90(2)

Cl31(Pd31(Cl32	84.18(2)

Cl72(C71(Cl71	111.47(15)

Cl72(C71(H71A	109.3

Cl71(C71(H71A	109.3

Cl72(C71(H71B	109.3

Cl71(C71(H71B	109.3

H71A(C71(H71B	108.0

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	12(1) 	11(1)	15(1) 	0(1)	0(1) 	(2(1)

C2	15(1) 	15(1)	17(1) 	(4(1)	2(1) 	(1(1)

C3	17(1) 	14(1)	24(1) 	(6(1)	3(1) 	(1(1)

C4	15(1) 	12(1)	26(1) 	3(1)	3(1) 	1(1)

C5	16(1) 	12(1)	19(1) 	4(1)	2(1) 	(1(1)

C6	12(1) 	11(1)	14(1) 	1(1)	(2(1) 	0(1)

C7	15(1) 	14(1)	17(1) 	3(1)	4(1) 	0(1)

C8	14(1) 	14(1)	24(1) 	0(1)	5(1) 	(2(1)

C9	11(1) 	17(1)	26(1) 	(3(1)	(2(1) 	(1(1)

C10	15(1) 	15(1)	17(1) 	(2(1)	(5(1) 	0(1)

C11	18(1) 	37(2)	14(1) 	(9(1)	1(1) 	0(1)

C12	25(1) 	25(1)	36(2) 	(10(1)	8(1) 	3(1)

C13	22(1) 	20(1)	39(2) 	12(1)	3(1) 	8(1)

C14	17(1) 	28(1)	19(1) 	9(1)	2(1) 	3(1)

C15	28(1) 	21(1)	15(1) 	3(1)	4(1) 	4(1)

C16	22(1) 	23(1)	36(2) 	(2(1)	15(1) 	2(1)

C17	17(1) 	25(1)	41(2) 	(6(1)	(12(1) 	6(1)

C18	26(1) 	23(1)	17(1) 	(2(1)	(9(1) 	5(1)

C19	18(1) 	17(1)	19(1) 	3(1)	2(1) 	(4(1)

C20	30(2) 	16(1)	30(2) 	2(1)	3(1) 	(7(1)

C21	16(1) 	33(2)	23(1) 	1(1)	2(1) 	(8(1)

C22	16(1) 	17(1)	13(1) 	2(1)	(1(1) 	(1(1)

C23	21(1) 	24(1)	24(1) 	(4(1)	(7(1) 	7(1)

C24	19(1) 	22(1)	16(1) 	(3(1)	(4(1) 	0(1)

C25	15(1) 	16(1)	16(1) 	(3(1)	1(1) 	(2(1)

C26	13(1) 	20(1)	30(1) 	(4(1)	1(1) 	(5(1)

C27	21(1) 	16(1)	21(1) 	(6(1)	2(1) 	(1(1)

C28	17(1) 	15(1)	15(1) 	3(1)	(3(1) 	1(1)

C29	17(1) 	24(1)	33(2) 	4(1)	(1(1) 	5(1)

C30	27(1) 	19(1)	18(1) 	5(1)	(1(1) 	(2(1)

P1	10(1) 	13(1)	10(1) 	0(1)	0(1) 	0(1)

P2	11(1) 	11(1)	12(1) 	0(1)	0(1) 	0(1)

Cl1	20(1) 	25(1)	14(1) 	1(1)	6(1) 	(4(1)

Cl2	32(1) 	26(1)	15(1) 	(8(1)	5(1) 	(9(1)

Fe1	10(1) 	12(1)	11(1) 	1(1)	0(1) 	2(1)

Pd1	11(1) 	14(1)	9(1) 	(1(1)	1(1) 	0(1)

C31	9(1) 	13(1)	14(1) 	0(1)	0(1) 	1(1)

C32	12(1) 	14(1)	17(1) 	(2(1)	(2(1) 	1(1)

C33	9(1) 	15(1)	24(1) 	(3(1)	(2(1) 	(1(1)

C34	10(1) 	16(1)	22(1) 	0(1)	2(1) 	(1(1)

C35	11(1) 	16(1)	15(1) 	2(1)	3(1) 	0(1)

C36	10(1) 	14(1)	13(1) 	(1(1)	(1(1) 	0(1)

C37	10(1) 	12(1)	16(1) 	(3(1)	1(1) 	0(1)

C38	11(1) 	13(1)	23(1) 	(2(1)	(1(1) 	3(1)

C39	12(1) 	13(1)	26(1) 	5(1)	(3(1) 	1(1)

C40	13(1) 	17(1)	16(1) 	3(1)	(3(1) 	0(1)

C41	21(1) 	19(1)	16(1) 	(3(1)	(1(1) 	3(1)

C42	20(1) 	15(1)	32(2) 	(8(1)	(3(1) 	(1(1)

C43	22(1) 	16(1)	33(2) 	5(1)	7(1) 	(4(1)

C44	24(1) 	20(1)	16(1) 	1(1)	6(1) 	1(1)

C45	19(1) 	17(1)	18(1) 	(2(1)	3(1) 	(4(1)

C46	18(1) 	13(1)	31(1) 	(5(1)	0(1) 	0(1)

C47	27(1) 	19(1)	30(2) 	10(1)	(6(1) 	(1(1)

C48	25(1) 	22(1)	15(1) 	4(1)	(2(1) 	(1(1)

C49	20(1) 	14(1)	14(1) 	3(1)	0(1) 	(2(1)

C50	40(2) 	17(1)	29(2) 	6(1)	(3(1) 	(8(1)

C51	26(1) 	21(1)	18(1) 	2(1)	(4(1) 	5(1)

C52	14(1) 	18(1)	17(1) 	(2(1)	0(1) 	4(1)

C53	13(1) 	36(2)	28(1) 	(6(1)	(1(1) 	1(1)

C54	31(2) 	24(1)	29(2) 	(2(1)	1(1) 	15(1)

C55	13(1) 	21(1)	19(1) 	(1(1)	(5(1) 	(1(1)

C56	20(1) 	31(2)	24(1) 	(6(1)	(4(1) 	(10(1)

C57	13(1) 	26(1)	43(2) 	(1(1)	(7(1) 	5(1)

C58	17(1) 	14(1)	14(1) 	(2(1)	2(1) 	(1(1)

C59	31(1) 	16(1)	25(1) 	4(1)	9(1) 	(2(1)

C60	16(1) 	24(1)	20(1) 	(4(1)	5(1) 	(4(1)

P31	12(1) 	10(1)	12(1) 	(1(1)	0(1) 	1(1)

P32	11(1) 	11(1)	12(1) 	(2(1)	0(1) 	0(1)

Cl31	17(1) 	47(1)	38(1) 	(30(1)	2(1) 	2(1)

Cl32	24(1) 	43(1)	21(1) 	(17(1)	(10(1) 	8(1)

Fe31	10(1) 	10(1)	13(1) 	0(1)	0(1) 	0(1)

Pd31	12(1) 	12(1)	10(1) 	(3(1)	0(1) 	(1(1)

C71	37(2) 	32(2)	21(1) 	3(1)	2(1) 	4(1)

Cl71	49(1) 	34(1)	31(1) 	4(1)	(1(1) 	(7(1)

Cl72	36(1) 	33(1)	38(1) 	(1(1)	(6(1) 	3(1)

Table 5. Hydrogen coordinates [( 104] and isotropic displacement parameters [Å2 ( 103].

Atom 	x	y	z	Ueq	S.o.f.

H11A	1899	5913	9665	34	1

H11B	1864	4498	9570	34	1

H11C	1206	5184	9753	34	1

H12A	511	7639	9397	43	1

H12B	354	6362	9617	43	1

H12C	(146	6877	9233	43	1

H13A	(308	7019	8494	41	1

H13B	(39	6550	8030	41	1

H13C	242	7793	8231	41	1

H14A	865	5714	7687	32	1

H14B	1550	4935	7762	32	1

H14C	1590	6372	7763	32	1

H15A	612	3381	9721	32	1

H15B	1177	2516	9514	32	1

H15C	431	2001	9622	32	1

H16A	(873	4942	9231	40	1

H16B	(350	4441	9605	40	1

H16C	(966	3611	9421	40	1

H17A	(1280	3886	8279	42	1

H17B	(780	4774	8023	42	1

H17C	(1056	5143	8497	42	1

H18A	(16	2530	7710	33	1

H18B	752	3050	7732	33	1

H18C	112	3950	7681	33	1

H19	2749	5751	7995	21	1

H20A	2997	6737	8853	38	1

H20B	2337	7018	8541	38	1

H20C	3084	7452	8399	38	1

H21A	3902	5934	8065	36	1

H21B	3749	4535	8138	36	1

H21C	3923	5382	8554	36	1

H22	2531	3356	9206	19	1

H23A	3829	3315	8795	34	1

H23B	3246	2329	8692	34	1

H23C	3577	2444	9180	34	1

H24A	3300	4377	9632	28	1

H24B	2874	5413	9379	28	1

H24C	3624	5049	9219	28	1

H25	823	958	7835	19	1

H26A	(56	(188	8101	31	1

H26B	(59	1075	8354	31	1

H26C	248	(94	8597	31	1

H27A	1330	(1023	8338	29	1

H27B	1793	(341	7988	29	1

H27C	1104	(1015	7825	29	1

H28	1948	1664	9145	19	1

H29A	2767	283	9076	37	1

H29B	2687	742	8576	37	1

H29C	2333	(491	8720	37	1

H30A	1275	(583	9031	32	1

H30B	867	564	9207	32	1

H30C	1514	48	9485	32	1

H41A	4538	5992	7166	28	1

H41B	3788	5508	7027	28	1

H41C	3895	6892	7156	28	1

H42A	5012	8671	6831	34	1

H42B	4215	8686	6950	34	1

H42C	4479	9471	6546	34	1

H43A	5196	8713	5618	35	1

H43B	4590	9498	5819	35	1

H43C	4452	8729	5378	35	1

H44A	4288	6809	5110	30	1

H44B	4153	5436	5241	30	1

H44C	4921	5958	5250	30	1

H45A	2722	7221	7065	27	1

H45B	2554	5870	6915	27	1

H45C	1953	6854	6918	27	1

H46A	3175	9825	6479	31	1

H46B	2840	9066	6868	31	1

H46C	2357	9801	6527	31	1

H47A	2506	9773	5457	38	1

H47B	3179	9165	5261	38	1

H47C	3237	9945	5705	38	1

H48A	2288	6912	5016	31	1

H48B	2861	5910	5121	31	1

H48C	3087	7255	5005	31	1

H49	3612	3856	6729	20	1

H50A	4155	1574	6533	43	1

H50B	3497	2024	6251	43	1

H50C	3458	1896	6776	43	1

H51A	4453	3343	7214	33	1

H51B	4825	4278	6897	33	1

H51C	4949	2865	6839	33	1

H52	4962	3868	5522	20	1

H53A	5645	4322	6348	39	1

H53B	5467	5342	5990	39	1

H53C	5995	4290	5876	39	1

H54A	5534	2169	5723	42	1

H54B	4746	1900	5826	42	1

H54C	5278	2230	6220	42	1

H55	1695	5141	5248	21	1

H56A	842	3796	5814	38	1

H56B	1320	3181	5455	38	1

H56C	706	4055	5299	38	1

H57A	750	6208	5493	41	1

H57B	1443	6801	5689	41	1

H57C	982	5976	5997	41	1

H58	2526	3990	6609	18	1

H59A	2092	2102	6564	36	1

H59B	2404	2321	6087	36	1

H59C	1592	2424	6152	36	1

H60A	1077	4079	6477	30	1

H60B	1498	5224	6657	30	1

H60C	1501	4004	6937	30	1

H71A	3924	524	7326	36	1

H71B	3208	1017	7503	36	1