|  | Single Crystal X-Ray Diffraction Service National Crystallography Service Contact: Dr S.K.Callear, S.K.Callear@soton.ac.uk |
| --- | --- |

Table 1. Crystal data and structure refinement details.

Identification code 	2009src0246 (SM 119bis)

Empirical formula 	C6H3ClF3NO

Formula weight 	197.54

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	P21/c

Unit cell dimensions	a = 10.8836(11) Å	( = 90°

b = 8.4697(9) Å	( = 102.651(6)°

c = 7.9738(7) Å	(  = 90°

Volume	717.19(12) Å3

Z	4

Density (calculated)	1.830 Mg / m3

Absorption coefficient	0.533 mm(1

F(000)	392

Crystal	block; colourless

Crystal size	0.33 ( 0.23 ( 0.17 mm3

( range for data collection	3.08 ( 27.47°

Index ranges	(14 ( h ( 14, (10 ( k ( 10, (10 ( l ( 10

Reflections collected	9654

Independent reflections	1630 [Rint = 0.0624]

Completeness to ( = 27.47°	99.9 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9149 and 0.8438

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	1630 / 0 / 109

Goodness-of-fit on F2	1.054

Final R indices [F2 > 2((F2)]	R1 = 0.0513, wR2 = 0.1158

R indices (all data)	R1 = 0.0826, wR2 = 0.1290

Largest diff. peak and hole	0.308 and (0.316 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: Sheldrick, G. M. SADABS - Bruker Nonius area detector scaling and absorption correction - V2.10 Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: ORTEP-3 (L.G. Farrugia, J. Appl. Cryst. (1997) 30, 565).

Special details:

All hydrogens fixed using a standard riding model.

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C2	1974(2)	3820(3)	(264(3)	29(1)	1

C3	2909(2)	4588(3)	837(3)	28(1)	1

C4	2881(2)	6254(3)	894(3)	29(1)	1

C5	1920(2)	7055(3)	(132(3)	27(1)	1

C6	901(2)	6265(3)	(1304(3)	27(1)	1

C7	3957(2)	3690(3)	1920(3)	35(1)	1

N1	1025(2)	4640(2)	(1284(3)	29(1)	1

O6	(2(2)	6919(2)	(2247(2)	36(1)	1

F7B	4237(2)	4201(2)	3540(2)	61(1)	1

F7C	5038(1)	3798(2)	1370(2)	53(1)	1

Cl5	1834(1)	9087(1)	(110(1)	39(1)	1

F7A	3720(2)	2145(2)	1988(2)	51(1)	1

Table 3. Bond lengths [Å] and angles [°].

C2(C3	1.356(4)

C2(N1	1.357(3)

C2(H2	0.9500

C3(C4	1.413(3)

C3(C7	1.481(4)

C4(C5	1.360(3)

C4(H4	0.9500

C5(C6	1.448(3)

C5(Cl5	1.723(2)

C6(O6	1.231(3)

C6(N1	1.383(3)

C7(F7B	1.333(3)

C7(F7A	1.337(3)

C7(F7C	1.346(3)

N1(H1	0.8800

C3(C2(N1	120.5(2)

C3(C2(H2	119.8

N1(C2(H2	119.8

C2(C3(C4	118.8(2)

C2(C3(C7	120.3(2)

C4(C3(C7	120.9(2)

C5(C4(C3	119.9(2)

C5(C4(H4	120.0

C3(C4(H4	120.0

C4(C5(C6	122.5(2)

C4(C5(Cl5	121.88(18)

C6(C5(Cl5	115.61(18)

O6(C6(N1	121.2(2)

O6(C6(C5	125.7(2)

N1(C6(C5	113.1(2)

F7B(C7(F7A	106.5(2)

F7B(C7(F7C	105.2(2)

F7A(C7(F7C	105.7(2)

F7B(C7(C3	112.5(2)

F7A(C7(C3	113.3(2)

F7C(C7(C3	113.1(2)

C2(N1(C6	125.2(2)

C2(N1(H1	117.4

C6(N1(H1	117.4

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C2	30(1) 	27(1)	30(1) 	4(1)	6(1) 	2(1)

C3	25(1) 	32(1)	26(1) 	2(1)	5(1) 	3(1)

C4	28(1) 	30(1)	28(1) 	(4(1)	4(1) 	(6(1)

C5	30(1) 	23(1)	29(1) 	(2(1)	8(1) 	(2(1)

C6	27(1) 	25(1)	30(1) 	2(1)	8(1) 	0(1)

C7	33(1) 	38(2)	32(1) 	3(1)	3(1) 	2(1)

N1	27(1) 	25(1)	31(1) 	(1(1)	(1(1) 	(2(1)

O6	29(1) 	30(1)	42(1) 	4(1)	(4(1) 	5(1)

F7B	64(1) 	76(1)	32(1) 	(8(1)	(12(1) 	27(1)

F7C	30(1) 	66(1)	61(1) 	23(1)	9(1) 	12(1)

Cl5	49(1) 	23(1)	45(1) 	(2(1)	10(1) 	(2(1)

F7A	46(1) 	38(1)	62(1) 	16(1)	(5(1) 	4(1)