|  | Single Crystal X-Ray Diffraction Service National Crystallography Service Contact: Dr S.K.Callear, S.K.Callear@soton.ac.uk |
| --- | --- |

Table 1. Crystal data and structure refinement details.

Identification code 	2009src0345 (SM 144bis)

Empirical formula 	C15H19ClN4O7Si

Formula weight 	430.88

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Orthorhombic

Space group 	Pbca

Unit cell dimensions	a = 6.8700(3) Å	( = 90°

b = 23.3867(14) Å	( = 90°

c = 24.3510(15) Å	(  = 90°

Volume	3912.4(4) Å3

Z	8

Density (calculated)	1.463 Mg / m3

Absorption coefficient	0.302 mm(1

F(000)	1792

Crystal	block; colourless

Crystal size	0.17 ( 0.12 ( 0.05 mm3

( range for data collection	3.05 ( 25.00°

Index ranges	(8 ( h ( 8, (27 ( k ( 27, (28 ( l ( 28

Reflections collected	20043

Independent reflections	3395 [Rint = 0.0832]

Completeness to ( = 25.00°	98.9 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9851 and 0.9504

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	3395 / 0 / 256

Goodness-of-fit on F2	1.271

Final R indices [F2 > 2((F2)]	R1 = 0.1744, wR2 = 0.3437

R indices (all data)	R1 = 0.1940, wR2 = 0.3534

Largest diff. peak and hole	1.266 and (0.517 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: Sheldrick, G. M. SADABS - Bruker Nonius area detector scaling and absorption correction - V2.10 Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: ORTEP-3 (L.G. Farrugia, J. Appl. Cryst. (1997) 30, 565).

Special details:

All hydrogen atoms fixed using a standard riding model.

Hydrogen atoms on water molecule O1w could not be located.

High R values due to unresolved modulation. However, structure can be used to obtain gross connectivity.

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C2	5853(15)	2356(4)	4566(5)	39(3)	1

C3	5559(16)	2430(5)	4024(6)	49(3)	1

C4	5124(16)	1958(4)	3708(6)	41(3)	1

C5	5003(15)	1424(5)	3938(5)	37(3)	1

C6	5364(14)	1340(5)	4497(5)	35(3)	1

C7	6149(17)	1721(4)	5368(5)	41(3)	1

C8	5730(20)	3014(5)	3767(6)	58(4)	1

C22	9485(14)	(192(5)	6181(5)	44(3)	1

C23	9980(17)	(315(6)	6707(5)	51(4)	1

C24	9463(16)	93(6)	7101(5)	46(3)	1

C25	8404(16)	557(6)	6957(5)	45(3)	1

C26	7761(15)	668(5)	6410(5)	37(3)	1

C27	7738(15)	389(4)	5474(4)	34(2)	1

C28	11008(18)	(841(7)	6862(6)	70(5)	1

C31	3282(15)	684(5)	5704(5)	38(3)	1

N1	5756(12)	1823(4)	4789(4)	34(2)	1

N5	4520(13)	942(4)	3573(4)	45(3)	1

N21	8435(12)	283(4)	6043(4)	36(2)	1

N25	7937(17)	974(7)	7386(6)	67(4)	1

O5A	3785(14)	1055(4)	3124(4)	63(3)	1

O5B	4884(12)	465(3)	3740(3)	45(2)	1

O6	5337(10)	871(3)	4754(3)	33(2)	1

O25A	7285(17)	1431(6)	7267(5)	92(4)	1

O25B	8140(20)	834(5)	7854(5)	103(5)	1

O26	6652(11)	1067(4)	6239(3)	47(2)	1

Si1	5746(4)	942(1)	5511(1)	38(1)	1

Cl2	438(4)	1459(1)	4562(2)	52(1)	1

O1W	5334(19)	2664(5)	6528(9)	159(8)	1

Table 3. Bond lengths [Å] and angles [°].

C2(C3	1.346(18)

C2(N1	1.361(13)

C2(H2	0.9500

C3(C4	1.380(18)

C3(C8	1.506(15)

C4(C5	1.371(14)

C4(H4	0.9500

C5(C6	1.396(16)

C5(N5	1.473(16)

C6(O6	1.263(12)

C6(N1	1.362(14)

C7(N1	1.456(14)

C7(Si1	1.875(10)

C7(H7A	0.9900

C7(H7B	0.9900

C8(H8A	0.9800

C8(H8B	0.9800

C8(H8C	0.9800

C22(C23	1.357(17)

C22(N21	1.366(14)

C22(H22	0.9500

C23(C24	1.398(19)

C23(C28	1.468(18)

C24(C25	1.352(18)

C24(H24	0.9500

C25(C26	1.426(16)

C25(N25	1.467(18)

C26(O26	1.275(14)

C26(N21	1.351(15)

C27(N21	1.487(13)

C27(Si1	1.884(10)

C27(H27A	0.9900

C27(H27B	0.9900

C28(H28A	0.9800

C28(H28B	0.9800

C28(H28C	0.9800

C31(Si1	1.858(11)

C31(H31A	0.9800

C31(H31B	0.9800

C31(H31C	0.9800

N5(O5B	1.213(12)

N5(O5A	1.233(13)

N25(O25A	1.195(17)

N25(O25B	1.195(15)

O6(Si1	1.872(8)

O26(Si1	1.901(9)

C3(C2(N1	120.1(11)

C3(C2(H2	119.9

N1(C2(H2	119.9

C2(C3(C4	118.5(11)

C2(C3(C8	120.9(13)

C4(C3(C8	120.7(13)

C5(C4(C3	120.9(12)

C5(C4(H4	119.6

C3(C4(H4	119.6

C4(C5(C6	121.1(12)

C4(C5(N5	117.6(11)

C6(C5(N5	121.3(10)

O6(C6(N1	117.7(10)

O6(C6(C5	127.1(11)

N1(C6(C5	115.2(10)

N1(C7(Si1	108.2(8)

N1(C7(H7A	110.1

Si1(C7(H7A	110.1

N1(C7(H7B	110.1

Si1(C7(H7B	110.1

H7A(C7(H7B	108.4

C3(C8(H8A	109.5

C3(C8(H8B	109.5

H8A(C8(H8B	109.5

C3(C8(H8C	109.5

H8A(C8(H8C	109.5

H8B(C8(H8C	109.5

C23(C22(N21	122.5(13)

C23(C22(H22	118.7

N21(C22(H22	118.7

C22(C23(C24	116.0(13)

C22(C23(C28	122.7(14)

C24(C23(C28	121.3(12)

C25(C24(C23	120.4(11)

C25(C24(H24	119.8

C23(C24(H24	119.8

C24(C25(C26	123.7(13)

C24(C25(N25	117.8(12)

C26(C25(N25	118.5(12)

O26(C26(N21	118.4(10)

O26(C26(C25	128.6(12)

N21(C26(C25	113.0(11)

N21(C27(Si1	107.7(7)

N21(C27(H27A	110.2

Si1(C27(H27A	110.2

N21(C27(H27B	110.2

Si1(C27(H27B	110.2

H27A(C27(H27B	108.5

C23(C28(H28A	109.5

C23(C28(H28B	109.5

H28A(C28(H28B	109.5

C23(C28(H28C	109.5

H28A(C28(H28C	109.5

H28B(C28(H28C	109.5

Si1(C31(H31A	109.5

Si1(C31(H31B	109.5

H31A(C31(H31B	109.5

Si1(C31(H31C	109.5

H31A(C31(H31C	109.5

H31B(C31(H31C	109.5

C2(N1(C6	124.1(10)

C2(N1(C7	121.9(10)

C6(N1(C7	113.9(9)

O5B(N5(O5A	125.3(11)

O5B(N5(C5	117.1(10)

O5A(N5(C5	117.6(10)

C26(N21(C22	124.0(10)

C26(N21(C27	113.3(9)

C22(N21(C27	122.4(10)

O25A(N25(O25B	121.4(17)

O25A(N25(C25	120.3(14)

O25B(N25(C25	118.1(15)

C6(O6(Si1	114.2(7)

C26(O26(Si1	112.8(8)

C31(Si1(O6	94.8(4)

C31(Si1(C7	119.8(5)

O6(Si1(C7	85.7(4)

C31(Si1(C27	116.8(5)

O6(Si1(C27	90.1(4)

C7(Si1(C27	123.4(5)

C31(Si1(O26	96.4(5)

O6(Si1(O26	168.7(4)

C7(Si1(O26	88.6(5)

C27(Si1(O26	85.0(4)

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C2	25(5) 	22(5)	69(9) 	14(5)	0(6) 	(3(4)

C3	30(6) 	36(6)	81(10) 	26(7)	3(6) 	5(5)

C4	32(6) 	23(5)	67(9) 	14(6)	(1(6) 	0(5)

C5	22(5) 	39(6)	48(7) 	13(5)	4(5) 	(5(5)

C6	14(5) 	43(6)	49(7) 	7(6)	1(5) 	(1(4)

C7	34(6) 	30(6)	58(8) 	12(6)	(1(6) 	(8(5)

C8	55(8) 	41(7)	77(10) 	23(7)	15(8) 	10(6)

C22	18(5) 	52(7)	61(8) 	28(6)	(7(5) 	(5(5)

C23	32(6) 	84(10)	36(7) 	23(7)	(8(6) 	(14(6)

C24	29(6) 	83(10)	27(7) 	25(7)	(14(5) 	(21(6)

C25	28(6) 	70(9)	37(7) 	0(6)	(1(5) 	(25(6)

C26	23(5) 	57(7)	29(6) 	12(6)	2(5) 	(16(5)

C27	28(5) 	31(5)	41(7) 	10(5)	3(5) 	(3(4)

C28	32(6) 	96(11)	82(11) 	58(9)	(8(7) 	6(7)

C31	31(6) 	40(6)	44(7) 	15(5)	5(5) 	(1(5)

N1	22(4) 	28(5)	52(6) 	8(4)	(3(4) 	2(4)

N5	32(5) 	48(6)	56(7) 	28(5)	(3(5) 	(18(5)

N21	21(4) 	50(6)	36(6) 	19(5)	(3(4) 	(6(4)

N25	38(7) 	97(11)	66(10) 	9(8)	(10(6) 	(38(7)

O5A	55(6) 	73(6)	60(6) 	38(5)	(13(5) 	(17(5)

O5B	46(5) 	37(4)	52(5) 	9(4)	5(4) 	(4(4)

O6	28(4) 	24(3)	47(5) 	15(3)	(3(3) 	(10(3)

O25A	66(7) 	139(11)	71(8) 	(25(8)	(7(6) 	42(8)

O25B	182(14) 	77(8)	51(7) 	(7(6)	5(8) 	(83(9)

O26	31(4) 	66(6)	44(5) 	6(4)	(2(4) 	2(4)

Si1	26(2) 	40(2)	48(2) 	10(2)	0(2) 	(4(1)

Cl2	32(1) 	52(2)	72(2) 	15(2)	1(2) 	4(1)

O1W	84(9) 	45(7)	350(30) 	65(11)	(37(13) 	(13(6)