Table 1.  Crystal data and structure refinement for 2009src0647.

Identification code 	2009src0647

Empirical formula 	C46 H58 Br2 S3

Formula weight 	866.92

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	P2(1)/n

Unit cell dimensions	a = 11.3163(3) Å	a= 90º.

b = 11.8126(2) Å	b= 99.3500(10)º.

c = 33.2617(7) Å	g = 90º.

Volume	4387.18(17) Å3

Z	4

Density (calculated)	1.313 Mg/m3

Absorption coefficient	2.021 mm-1

F(000)	1808

Crystal size	0.40 x 0.10 x 0.04 mm3

Theta range for data collection	2.93 to 27.50º.

Index ranges	-14<=h<=14, -15<=k<=13, -43<=l<=43

Reflections collected	48089

Independent reflections	10019 [R(int) = 0.0706]

Completeness to theta = 27.50º	99.5 %

Absorption correction	Semi-empirical from equivalents

Max. and min. transmission	0.9235 and 0.4987

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	10019 / 0 / 464

Goodness-of-fit on F2	1.039

Final R indices [I>2sigma(I)]	R1 = 0.0520, wR2 = 0.1138

R indices (all data)	R1 = 0.0762, wR2 = 0.1255

Largest diff. peak and hole	1.560 and -0.651 e.Å-3

Table 2.  Atomic coordinates ( x 104) and equivalent isotropic displacement parameters (Å2x 103)

for 2009src0647.  U(eq) is defined as one third of the trace of the orthogonalized Uij tensor.

________________________________________________________________________________

x	y	z	U(eq)

________________________________________________________________________________

C(1)	7620(3)	3321(3)	-1695(1)	22(1)

C(2)	8258(3)	4213(3)	-1489(1)	21(1)

C(3)	8096(3)	4273(3)	-1076(1)	21(1)

C(4)	7374(3)	3432(3)	-976(1)	23(1)

C(5)	7142(3)	3504(3)	-539(1)	24(1)

C(6)	7874(3)	4577(3)	-406(1)	24(1)

C(7)	8047(3)	5099(3)	-28(1)	24(1)

C(8)	8738(3)	6070(3)	21(1)	26(1)

C(9)	9261(3)	6529(3)	-291(1)	25(1)

C(10)	9120(3)	5991(3)	-669(1)	25(1)

C(11)	8424(3)	5021(3)	-722(1)	21(1)

C(12)	7709(4)	2506(3)	-271(1)	32(1)

C(13)	7176(4)	1345(3)	-373(1)	35(1)

C(14)	7836(4)	448(4)	-83(1)	49(1)

C(15)	7439(4)	-777(3)	-217(1)	45(1)

C(16)	6161(4)	-1038(4)	-198(1)	45(1)

C(17)	5857(5)	-2257(4)	-301(2)	54(1)

C(18)	5804(3)	3667(3)	-522(1)	28(1)

C(19)	5261(3)	4732(3)	-734(2)	43(1)

C(20)	3941(4)	4762(4)	-837(1)	48(1)

C(21)	3400(4)	5852(4)	-1003(2)	53(1)

C(22)	2130(4)	5927(5)	-1172(2)	74(2)

C(23)	1631(5)	7026(4)	-1313(2)	72(2)

C(24)	7774(3)	3271(3)	-2110(1)	22(1)

C(25)	8539(3)	4109(3)	-2208(1)	22(1)

C(26)	8721(3)	4034(3)	-2622(1)	22(1)

C(27)	8081(3)	3171(3)	-2822(1)	23(1)

C(28)	8273(3)	3034(3)	-3258(1)	23(1)

C(29)	9207(3)	3965(3)	-3270(1)	23(1)

C(30)	9774(3)	4258(3)	-3592(1)	27(1)

C(31)	10588(3)	5153(3)	-3537(1)	28(1)

C(32)	10832(3)	5751(3)	-3175(1)	27(1)

C(33)	10255(3)	5454(3)	-2850(1)	24(1)

C(34)	9444(3)	4561(3)	-2898(1)	21(1)

C(35)	7117(3)	3273(3)	-3563(1)	26(1)

C(36)	6583(3)	4440(3)	-3517(1)	34(1)

C(37)	5431(3)	4661(3)	-3809(1)	33(1)

C(38)	4925(3)	5843(3)	-3775(1)	37(1)

C(39)	4555(4)	6110(4)	-3367(1)	42(1)

C(40)	4003(4)	7279(4)	-3352(2)	50(1)

C(41)	8759(3)	1844(3)	-3331(1)	26(1)

C(42)	9897(3)	1505(3)	-3041(1)	30(1)

C(43)	10031(4)	234(3)	-2998(2)	46(1)

C(44)	11157(4)	-148(3)	-2719(1)	38(1)

C(45)	11229(5)	-1409(4)	-2659(2)	89(2)

C(46)	12332(5)	-1816(4)	-2382(2)	65(2)

S(1)	6828(1)	2555(1)	-1381(1)	23(1)

S(2)	9069(1)	4984(1)	-1797(1)	21(1)

S(3)	7255(1)	2399(1)	-2521(1)	23(1)

Br(1)	8954(1)	6820(1)	536(1)	31(1)

Br(2)	11359(1)	5584(1)	-3981(1)	44(1)

________________________________________________________________________________

Table 3.   Bond lengths [Å] and angles [º] for 2009src0647.

_____________________________________________________

C(1)-C(2) 	1.393(4)

C(1)-C(24) 	1.420(4)

C(1)-S(1) 	1.736(3)

C(2)-C(3) 	1.417(4)

C(2)-S(2) 	1.740(3)

C(3)-C(4) 	1.361(5)

C(3)-C(11) 	1.471(4)

C(4)-C(5) 	1.519(4)

C(4)-S(1) 	1.733(3)

C(5)-C(18) 	1.537(5)

C(5)-C(6) 	1.540(5)

C(5)-C(12) 	1.552(5)

C(6)-C(7) 	1.385(4)

C(6)-C(11) 	1.406(5)

C(7)-C(8) 	1.383(5)

C(8)-C(9) 	1.386(5)

C(8)-Br(1) 	1.907(3)

C(9)-C(10) 	1.393(5)

C(10)-C(11) 	1.385(5)

C(12)-C(13) 	1.514(5)

C(13)-C(14) 	1.542(5)

C(14)-C(15) 	1.558(6)

C(15)-C(16) 	1.490(6)

C(16)-C(17) 	1.506(6)

C(18)-C(19) 	1.523(5)

C(19)-C(20) 	1.477(5)

C(20)-C(21) 	1.492(6)

C(21)-C(22) 	1.459(6)

C(22)-C(23) 	1.462(7)

C(24)-C(25) 	1.388(5)

C(24)-S(3) 	1.737(3)

C(25)-C(26) 	1.426(4)

C(25)-S(2) 	1.742(3)

C(26)-C(27) 	1.360(4)

C(26)-C(34) 	1.465(5)

C(27)-C(28) 	1.511(4)

C(27)-S(3) 	1.735(3)

C(28)-C(29) 	1.530(5)

C(28)-C(41) 	1.543(5)

C(28)-C(35) 	1.544(5)

C(29)-C(30) 	1.380(5)

C(29)-C(34) 	1.410(4)

C(30)-C(31) 	1.394(5)

C(31)-C(32) 	1.385(5)

C(31)-Br(2) 	1.900(3)

C(32)-C(33) 	1.396(5)

C(33)-C(34) 	1.391(5)

C(35)-C(36) 	1.522(5)

C(36)-C(37) 	1.517(5)

C(37)-C(38) 	1.520(5)

C(38)-C(39) 	1.519(6)

C(39)-C(40) 	1.520(6)

C(41)-C(42) 	1.531(5)

C(42)-C(43) 	1.514(5)

C(43)-C(44) 	1.519(5)

C(44)-C(45) 	1.503(6)

C(45)-C(46) 	1.506(7)

C(2)-C(1)-C(24)	111.9(3)

C(2)-C(1)-S(1)	112.1(2)

C(24)-C(1)-S(1)	136.0(3)

C(1)-C(2)-C(3)	112.1(3)

C(1)-C(2)-S(2)	112.8(2)

C(3)-C(2)-S(2)	135.1(3)

C(4)-C(3)-C(2)	112.2(3)

C(4)-C(3)-C(11)	109.0(3)

C(2)-C(3)-C(11)	138.7(3)

C(3)-C(4)-C(5)	113.4(3)

C(3)-C(4)-S(1)	113.5(2)

C(5)-C(4)-S(1)	133.0(3)

C(4)-C(5)-C(18)	111.5(3)

C(4)-C(5)-C(6)	98.8(3)

C(18)-C(5)-C(6)	111.9(3)

C(4)-C(5)-C(12)	112.8(3)

C(18)-C(5)-C(12)	113.0(3)

C(6)-C(5)-C(12)	107.9(3)

C(7)-C(6)-C(11)	119.8(3)

C(7)-C(6)-C(5)	128.2(3)

C(11)-C(6)-C(5)	112.0(3)

C(8)-C(7)-C(6)	118.1(3)

C(7)-C(8)-C(9)	122.5(3)

C(7)-C(8)-Br(1)	118.7(3)

C(9)-C(8)-Br(1)	118.8(3)

C(8)-C(9)-C(10)	119.8(3)

C(11)-C(10)-C(9)	118.1(3)

C(10)-C(11)-C(6)	121.6(3)

C(10)-C(11)-C(3)	131.5(3)

C(6)-C(11)-C(3)	106.8(3)

C(13)-C(12)-C(5)	116.6(3)

C(12)-C(13)-C(14)	110.4(3)

C(13)-C(14)-C(15)	111.8(3)

C(16)-C(15)-C(14)	114.6(4)

C(15)-C(16)-C(17)	112.1(4)

C(19)-C(18)-C(5)	114.3(3)

C(20)-C(19)-C(18)	116.3(3)

C(19)-C(20)-C(21)	116.4(4)

C(22)-C(21)-C(20)	121.0(4)

C(21)-C(22)-C(23)	118.9(5)

C(25)-C(24)-C(1)	112.3(3)

C(25)-C(24)-S(3)	112.4(2)

C(1)-C(24)-S(3)	135.3(3)

C(24)-C(25)-C(26)	112.1(3)

C(24)-C(25)-S(2)	112.7(2)

C(26)-C(25)-S(2)	135.1(3)

C(27)-C(26)-C(25)	111.7(3)

C(27)-C(26)-C(34)	108.5(3)

C(25)-C(26)-C(34)	139.6(3)

C(26)-C(27)-C(28)	113.8(3)

C(26)-C(27)-S(3)	113.9(2)

C(28)-C(27)-S(3)	132.3(2)

C(27)-C(28)-C(29)	98.9(2)

C(27)-C(28)-C(41)	111.0(3)

C(29)-C(28)-C(41)	112.6(3)

C(27)-C(28)-C(35)	111.8(3)

C(29)-C(28)-C(35)	111.5(3)

C(41)-C(28)-C(35)	110.5(3)

C(30)-C(29)-C(34)	120.6(3)

C(30)-C(29)-C(28)	127.6(3)

C(34)-C(29)-C(28)	111.8(3)

C(29)-C(30)-C(31)	118.1(3)

C(32)-C(31)-C(30)	122.2(3)

C(32)-C(31)-Br(2)	119.1(3)

C(30)-C(31)-Br(2)	118.6(3)

C(31)-C(32)-C(33)	119.6(3)

C(34)-C(33)-C(32)	119.0(3)

C(33)-C(34)-C(29)	120.5(3)

C(33)-C(34)-C(26)	132.5(3)

C(29)-C(34)-C(26)	107.0(3)

C(36)-C(35)-C(28)	114.1(3)

C(37)-C(36)-C(35)	114.0(3)

C(36)-C(37)-C(38)	113.9(3)

C(39)-C(38)-C(37)	114.7(3)

C(38)-C(39)-C(40)	113.1(4)

C(42)-C(41)-C(28)	115.1(3)

C(43)-C(42)-C(41)	112.4(3)

C(42)-C(43)-C(44)	114.4(3)

C(45)-C(44)-C(43)	113.3(4)

C(44)-C(45)-C(46)	114.7(4)

C(4)-S(1)-C(1)	90.12(16)

C(2)-S(2)-C(25)	90.26(16)

C(27)-S(3)-C(24)	89.89(16)

_____________________________________________________________

Symmetry transformations used to generate equivalent atoms:

Table 4.   Anisotropic displacement parameters (Å2x 103)for 2009src0647.  The anisotropic

displacement factor exponent takes the form: -2p2[ h2a*2U11 + ... + 2 h k a* b* U12 ]

______________________________________________________________________________

U11	U22	U33	U23	U13	U12

______________________________________________________________________________

C(1)	20(2) 	20(2)	24(2) 	-1(1)	0(1) 	4(1)

C(2)	19(2) 	23(2)	19(2) 	1(1)	0(1) 	4(1)

C(3)	20(2) 	22(2)	20(2) 	-1(1)	-1(1) 	7(1)

C(4)	25(2) 	23(2)	21(2) 	0(1)	1(1) 	7(1)

C(5)	27(2) 	22(2)	24(2) 	3(1)	5(1) 	3(1)

C(6)	24(2) 	22(2)	24(2) 	2(1)	2(1) 	6(1)

C(7)	22(2) 	31(2)	19(2) 	0(1)	2(1) 	7(1)

C(8)	24(2) 	28(2)	22(2) 	-4(1)	-4(1) 	9(1)

C(9)	20(2) 	29(2)	25(2) 	-2(1)	-3(1) 	2(1)

C(10)	23(2) 	29(2)	21(2) 	-2(1)	0(1) 	5(1)

C(11)	19(2) 	24(2)	18(2) 	-2(1)	0(1) 	8(1)

C(12)	37(2) 	34(2)	24(2) 	5(2)	-1(2) 	4(2)

C(13)	37(2) 	29(2)	35(2) 	4(2)	-1(2) 	1(2)

C(14)	48(3) 	39(2)	55(3) 	14(2)	-8(2) 	6(2)

C(15)	45(3) 	36(2)	58(3) 	19(2)	20(2) 	16(2)

C(16)	50(3) 	47(3)	37(2) 	8(2)	7(2) 	4(2)

C(17)	66(3) 	41(3)	54(3) 	11(2)	8(2) 	3(2)

C(18)	28(2) 	31(2)	25(2) 	1(1)	7(2) 	-2(2)

C(19)	24(2) 	35(2)	72(3) 	8(2)	13(2) 	3(2)

C(20)	27(2) 	71(3)	47(2) 	15(2)	5(2) 	7(2)

C(21)	30(2) 	48(3)	82(4) 	0(2)	9(2) 	2(2)

C(22)	33(3) 	97(4)	90(4) 	39(3)	3(3) 	5(3)

C(23)	37(3) 	53(3)	125(5) 	18(3)	8(3) 	11(2)

C(24)	19(2) 	24(2)	23(2) 	-3(1)	2(1) 	4(1)

C(25)	20(2) 	21(2)	24(2) 	-3(1)	1(1) 	2(1)

C(26)	21(2) 	23(2)	21(2) 	-3(1)	0(1) 	0(1)

C(27)	20(2) 	24(2)	24(2) 	-4(1)	2(1) 	-1(1)

C(28)	23(2) 	26(2)	18(2) 	-3(1)	2(1) 	-5(1)

C(29)	19(2) 	26(2)	22(2) 	-4(1)	-1(1) 	-1(1)

C(30)	26(2) 	34(2)	20(2) 	-7(1)	2(1) 	-7(2)

C(31)	25(2) 	34(2)	24(2) 	-1(1)	2(1) 	-6(2)

C(32)	22(2) 	29(2)	30(2) 	0(1)	5(1) 	-6(1)

C(33)	25(2) 	24(2)	22(2) 	-6(1)	0(1) 	-1(1)

C(34)	21(2) 	23(2)	21(2) 	-3(1)	5(1) 	0(1)

C(35)	25(2) 	32(2)	21(2) 	-3(1)	1(1) 	-6(2)

C(36)	27(2) 	35(2)	38(2) 	2(2)	-3(2) 	-3(2)

C(37)	27(2) 	43(2)	28(2) 	3(2)	-1(2) 	-7(2)

C(38)	25(2) 	40(2)	43(2) 	13(2)	0(2) 	-3(2)

C(39)	42(3) 	43(2)	40(2) 	2(2)	1(2) 	2(2)

C(40)	39(3) 	42(2)	66(3) 	-8(2)	-3(2) 	-3(2)

C(41)	25(2) 	27(2)	27(2) 	-7(1)	3(1) 	-5(2)

C(42)	26(2) 	29(2)	34(2) 	-9(2)	2(2) 	-4(2)

C(43)	37(2) 	26(2)	68(3) 	-8(2)	-11(2) 	-3(2)

C(44)	37(2) 	28(2)	45(2) 	-8(2)	0(2) 	1(2)

C(45)	61(4) 	30(3)	153(6) 	1(3)	-47(4) 	0(2)

C(46)	61(3) 	37(3)	88(4) 	2(3)	-15(3) 	8(2)

S(1)	26(1) 	22(1)	21(1) 	-1(1)	3(1) 	0(1)

S(2)	21(1) 	23(1)	19(1) 	-4(1)	1(1) 	-1(1)

S(3)	24(1) 	25(1)	20(1) 	-3(1)	3(1) 	-5(1)

Br(1)	31(1) 	37(1)	22(1) 	-8(1)	1(1) 	4(1)

Br(2)	39(1) 	66(1)	29(1) 	-4(1)	11(1) 	-25(1)

______________________________________________________________________________