|  | Single Crystal X-Ray Diffraction Service School of Chemistry - University of Southampton Contact: Dr Mark E Light, light@soton.ac.uk, ex 29429 |
| --- | --- |

Table 1. Crystal data and structure refinement details.

Identification code 	2009src0683a

Empirical formula 	C14H17NO8

Formula weight 	327.29

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Orthorhombic

Space group 	P212121

Unit cell dimensions	a = 4.75500(10) Å	( = 90°

b = 12.4624(3) Å	( = 90°

c = 24.7840(7) Å	(  = 90°

Volume	1468.67(6) Å3

Z	4

Density (calculated)	1.480 Mg / m3

Absorption coefficient	0.123 mm(1

F(000)	688

Crystal	plate; colourless

Crystal size	0.20 ( 0.07 ( 0.01 mm3

( range for data collection	2.96 ( 27.48°

Index ranges	(6 ( h ( 5, (16 ( k ( 16, (32 ( l ( 32

Reflections collected	17643

Independent reflections	1992 [Rint = 0.0617]

Completeness to ( = 27.48°	99.8 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9988 and 0.9758

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	1992 / 1 / 216

Goodness-of-fit on F2	1.099

Final R indices [F2 > 2((F2)]	R1 = 0.0492, wR2 = 0.0863

R indices (all data)	R1 = 0.0618, wR2 = 0.0923

Largest diff. peak and hole	0.266 and (0.273 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit ). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: Sheldrick, G. M. SADABS - Bruker Nonius area detector scaling and absorption correction - V2.10 Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: Cameron - A Molecular Graphics Package. (D. M. Watkin, L. Pearce and C. K. Prout, Chemical Crystallography Laboratory, University of Oxford, 1993).

Special details:

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	4034(7)	9381(2)	8242(1)	16(1)	1

C2	3293(7)	8220(2)	8096(1)	14(1)	1

C3	672(7)	7867(2)	8400(1)	14(1)	1

C4	1261(7)	7972(2)	9001(1)	15(1)	1

C5	2043(7)	9144(2)	9121(1)	17(1)	1

C6	2785(8)	9365(2)	9706(1)	20(1)	1

C7	4615(7)	7546(2)	7200(1)	15(1)	1

C8	4055(7)	7668(2)	6603(1)	15(1)	1

C9	2354(7)	6902(2)	6356(1)	19(1)	1

C10	1662(8)	7010(3)	5814(1)	24(1)	1

C11	2653(8)	7871(3)	5519(1)	24(1)	1

C12	4370(8)	8629(3)	5761(1)	23(1)	1

C13	5073(7)	8532(2)	6306(1)	16(1)	1

C14	6978(8)	9342(2)	6561(1)	20(1)	1

N1	2936(6)	8141(2)	7512(1)	15(1)	1

O1	4457(5)	9461(2)	8809(1)	16(1)	1

O2	1804(5)	10031(2)	8066(1)	17(1)	1

O3	(49(5)	6782(2)	8276(1)	19(1)	1

O4	(1197(5)	7695(2)	9300(1)	20(1)	1

O5	4969(6)	8697(2)	9910(1)	23(1)	1

O6	6411(5)	6908(2)	7372(1)	18(1)	1

O7	8105(5)	9214(2)	6994(1)	23(1)	1

O8	7297(8)	10213(2)	6264(1)	44(1)	1

Table 3. Bond lengths [Å] and angles [°].

C1(O2	1.404(4)

C1(O1	1.424(3)

C1(C2	1.532(4)

C1(H1	1.0000

C2(N1	1.460(3)

C2(C3	1.522(4)

C2(H2	1.0000

C3(O3	1.429(3)

C3(C4	1.521(4)

C3(H3	1.0000

C4(O4	1.427(4)

C4(C5	1.536(4)

C4(H4	1.0000

C5(O1	1.440(4)

C5(C6	1.517(4)

C5(H5	1.0000

C6(O5	1.423(4)

C6(H6A	0.9900

C6(H6B	0.9900

C7(O6	1.243(4)

C7(N1	1.336(4)

C7(C8	1.511(4)

C8(C13	1.390(4)

C8(C9	1.393(4)

C9(C10	1.390(4)

C9(H9	0.9500

C10(C11	1.382(4)

C10(H10	0.9500

C11(C12	1.385(5)

C11(H11	0.9500

C12(C13	1.397(4)

C12(H12	0.9500

C13(C14	1.497(5)

C14(O7	1.209(4)

C14(O8	1.321(4)

N1(H1N	0.985(19)

O2(H2A	0.8400

O3(H3A	0.8400

O4(H4A	0.8400

O5(H5A	0.8400

O8(H8	0.8400

O2(C1(O1	111.8(2)

O2(C1(C2	107.4(3)

O1(C1(C2	109.4(2)

O2(C1(H1	109.4

O1(C1(H1	109.4

C2(C1(H1	109.4

N1(C2(C3	112.1(3)

N1(C2(C1	108.9(2)

C3(C2(C1	110.1(2)

N1(C2(H2	108.5

C3(C2(H2	108.5

C1(C2(H2	108.5

O3(C3(C4	109.7(2)

O3(C3(C2	111.3(2)

C4(C3(C2	108.0(2)

O3(C3(H3	109.3

C4(C3(H3	109.3

C2(C3(H3	109.3

O4(C4(C3	109.7(3)

O4(C4(C5	109.1(2)

C3(C4(C5	108.4(2)

O4(C4(H4	109.8

C3(C4(H4	109.8

C5(C4(H4	109.8

O1(C5(C6	106.2(3)

O1(C5(C4	110.4(2)

C6(C5(C4	114.4(2)

O1(C5(H5	108.5

C6(C5(H5	108.5

C4(C5(H5	108.5

O5(C6(C5	113.7(3)

O5(C6(H6A	108.8

C5(C6(H6A	108.8

O5(C6(H6B	108.8

C5(C6(H6B	108.8

H6A(C6(H6B	107.7

O6(C7(N1	124.5(3)

O6(C7(C8	121.5(3)

N1(C7(C8	113.9(3)

C13(C8(C9	120.1(3)

C13(C8(C7	122.3(3)

C9(C8(C7	117.6(3)

C10(C9(C8	119.7(3)

C10(C9(H9	120.2

C8(C9(H9	120.2

C11(C10(C9	120.4(3)

C11(C10(H10	119.8

C9(C10(H10	119.8

C10(C11(C12	120.1(3)

C10(C11(H11	119.9

C12(C11(H11	119.9

C11(C12(C13	120.0(3)

C11(C12(H12	120.0

C13(C12(H12	120.0

C8(C13(C12	119.7(3)

C8(C13(C14	120.6(3)

C12(C13(C14	119.7(3)

O7(C14(O8	123.5(3)

O7(C14(C13	123.6(3)

O8(C14(C13	112.8(3)

C7(N1(C2	122.8(3)

C7(N1(H1N	122(2)

C2(N1(H1N	115(2)

C1(O1(C5	113.5(2)

C1(O2(H2A	109.5

C3(O3(H3A	109.5

C4(O4(H4A	109.5

C6(O5(H5A	109.5

C14(O8(H8	109.5

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	18(2) 	17(1)	14(1) 	1(1)	2(1) 	1(1)

C2	17(2) 	15(1)	10(1) 	0(1)	0(1) 	1(1)

C3	14(2) 	12(1)	15(1) 	(1(1)	(1(1) 	0(1)

C4	14(2) 	17(2)	15(1) 	1(1)	2(1) 	0(1)

C5	21(2) 	14(1)	16(1) 	1(1)	1(2) 	2(1)

C6	24(2) 	20(2)	16(1) 	(3(1)	(2(2) 	1(2)

C7	18(2) 	13(1)	14(1) 	0(1)	0(1) 	(5(1)

C8	16(2) 	15(1)	14(1) 	0(1)	0(1) 	2(1)

C9	20(2) 	16(1)	22(2) 	1(1)	(2(1) 	(4(1)

C10	29(2) 	22(2)	22(2) 	(3(1)	(5(2) 	(9(2)

C11	32(2) 	23(2)	16(1) 	2(1)	(3(2) 	(4(2)

C12	28(2) 	21(2)	21(2) 	5(1)	(4(2) 	(5(2)

C13	18(2) 	12(1)	20(1) 	1(1)	(1(2) 	2(1)

C14	23(2) 	15(1)	22(2) 	2(1)	(4(2) 	1(1)

N1	16(1) 	17(1)	12(1) 	0(1)	(1(1) 	2(1)

O1	19(1) 	16(1)	15(1) 	1(1)	0(1) 	(2(1)

O2	18(1) 	12(1)	23(1) 	3(1)	(1(1) 	3(1)

O3	23(1) 	13(1)	20(1) 	1(1)	(8(1) 	(2(1)

O4	18(1) 	23(1)	20(1) 	6(1)	2(1) 	0(1)

O5	24(1) 	29(1)	16(1) 	2(1)	(1(1) 	6(1)

O6	22(1) 	15(1)	17(1) 	(1(1)	(4(1) 	7(1)

O7	24(1) 	20(1)	24(1) 	2(1)	(7(1) 	(1(1)

O8	70(2) 	24(1)	37(1) 	14(1)	(29(2) 	(26(2)

Table 5. Hydrogen coordinates [( 104] and isotropic displacement parameters [Å2 ( 103].

Atom 	x	y	z	Ueq	S.o.f.

H1	5797	9595	8050	19	1

H2	4893	7747	8205	17	1

H3	(932	8347	8301	16	1

H4	2851	7489	9105	18	1

H5	421	9612	9018	20	1

H6A	3371	10124	9741	24	1

H6B	1083	9263	9930	24	1

H9	1671	6308	6558	23	1

H10	501	6488	5645	29	1

H11	2155	7944	5150	29	1

H12	5070	9216	5556	28	1

H2A	2421	10642	7986	26	1

H3A	(1041	6768	7996	28	1

H4A	(778	7242	9538	30	1

H5A	6054	8525	9657	34	1

H8	8272	10663	6434	65	1

H1N	1470(70)	8610(30)	7357(15)	52	1

Table 6. Hydrogen bonds [Å and °].

D(H···A	d(D(H)	d(H···A)	d(D···A)	((DHA)

O2(H2A...O6i	0.84	1.89	2.715(3)	165.7

O3(H3A...O6ii	0.84	1.97	2.807(3)	172.6

O4(H4A...O5iii	0.84	1.84	2.674(3)	176.0

O5(H5A...O4iv	0.84	1.89	2.677(3)	156.3

O8(H8...O3i	0.84	1.78	2.614(3)	170.3

N1(H1N...O7ii	0.985(19)	1.99(2)	2.952(3)	166(4)

Symmetry transformations used to generate equivalent atoms:

(i) (x+1,y+1/2,(z+3/2    (ii) x(1,y,z    (iii) x(1/2,(y+3/2,(z+2

(iv)  x+1,y,z

Thermal ellipsoids drawn at the 50% probability level.

# Text boxes

# Single Crystal X-Ray Diffraction Service

School of Chemistry - University of Southampton

Contact: Dr Mark E Light, light@soton.ac.uk, ex 29429