|  | University of Southampton · Department of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	02sot033

Empirical formula 	C18H28N2O2SSi

Formula weight 	364.57

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Monoclinic

Space group 	P21/c

Unit cell dimensions	a = 9.4824(2) Å	( = 90°

b = 22.6655(6) Å	( = 116.1400(10)°

c = 10.0368(3) Å	(  = 90°

Volume	1936.51(9) Å3

Z	4

Density (calculated)	1.250 Mg / m3

Absorption coefficient	0.242 mm(1

F(000)	784

Crystal	block; colourless

Crystal size	0.34 ( 0.18 ( 0.10 mm3

( range for data collection	2.99 ( 27.49°

Index ranges	(12 ( h ( 12, (25 ( k ( 29, (13 ( l ( 13

Reflections collected	12067

Independent reflections	4341 [Rint = 0.0682]

Completeness to ( = 27.49°	97.4 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9762 and 0.9223

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	4341 / 0 / 226

Goodness-of-fit on F2	1.006

Final R indices [F2 > 2((F2)]	R1 = 0.0474, wR2 = 0.1236

R indices (all data)	R1 = 0.0647, wR2 = 0.1348

Extinction coefficient	0.0000(17)

Largest diff. peak and hole	0.609 and (0.603 e Å(3

Diffractometer: Enraf Nonius KappaCCD area detector (( scans and ( scans to fill Ewald sphere). Data collection and cell

refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography,

part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SORTAV (R. H. Blessing,

Acta Cryst. A51 (1995) 33(37; R. H. Blessing, J. Appl. Cryst. 30 (1997) 421(426). Program used to solve structure:

SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Program used to refine structure: SHELXL97 (G. M. Sheldrick

(1997), University of Göttingen, Germany).

Further information:  http://www.soton.ac.uk/~xservice/strat.htm

Special details:

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C11	3395(2)	1025(1)	8002(2)	27(1)	1

C1	(2714(3)	443(1)	342(2)	35(1)	1

C2	(952(2)	490(1)	975(2)	25(1)	1

C3	(245(3)	1002(1)	789(2)	29(1)	1

C4	1377(3)	1057(1)	1407(2)	26(1)	1

C5	2308(2)	596(1)	2246(2)	19(1)	1

C6	1640(2)	80(1)	2446(2)	21(1)	1

C7	15(2)	31(1)	1796(2)	24(1)	1

C8	4704(2)	1943(1)	5716(2)	21(1)	1

C9	5056(2)	1717(1)	7283(2)	23(1)	1

C10	3671(2)	1318(1)	7009(2)	20(1)	1

C12	2658(2)	1301(1)	5332(2)	18(1)	1

C13	1375(2)	1781(1)	4800(2)	19(1)	1

C14	2134(2)	2379(1)	5459(2)	21(1)	1

C15	3638(2)	2489(1)	5277(2)	23(1)	1

C16	(287(3)	1802(1)	6896(2)	34(1)	1

C17	(944(2)	809(1)	4644(2)	24(1)	1

C18	(2078(2)	2060(1)	3609(3)	33(1)	1

N1	4782(2)	967(1)	4816(2)	19(1)	1

N2	3774(2)	1460(1)	4705(2)	18(1)	1

O1	5121(2)	125(1)	3452(2)	23(1)	1

O2	4769(2)	1124(1)	2342(2)	26(1)	1

Si1	(468(1)	1608(1)	5016(1)	20(1)	1

S1	4365(1)	693(1)	3157(1)	18(1)	1

Table 3. Bond lengths [Å] and angles [°].

C11(C10	1.316(3)

C11(H11A	0.9500

C11(H11B	0.9500

C1(C2	1.507(3)

C1(H1A	0.9800

C1(H1B	0.9800

C1(H1C	0.9800

C2(C3	1.393(3)

C2(C7	1.392(3)

C3(C4	1.387(3)

C3(H3	0.9500

C4(C5	1.388(3)

C4(H4	0.9500

C5(C6	1.386(3)

C5(S1	1.7656(19)

C6(C7	1.388(3)

C6(H6	0.9500

C7(H7	0.9500

C8(N2	1.489(2)

C8(C15	1.535(3)

C8(C9	1.544(3)

C8(H8	1.0000

C9(C10	1.517(3)

C9(H9A	0.9900

C9(H9B	0.9900

C10(C12	1.527(3)

C12(N2	1.495(2)

C12(C13	1.542(2)

C12(H12	1.0000

C13(C14	1.542(3)

C13(Si1	1.8950(19)

C13(H13	1.0000

C14(C15	1.536(3)

C14(H14A	0.9900

C14(H14B	0.9900

C15(H15A	0.9900

C15(H15B	0.9900

C16(Si1	1.870(2)

C16(H16A	0.9800

C16(H16B	0.9800

C16(H16C	0.9800

C17(Si1	1.864(2)

C17(H17A	0.9800

C17(H17B	0.9800

C17(H17C	0.9800

C18(Si1	1.864(2)

C18(H18A	0.9800

C18(H18B	0.9800

C18(H18C	0.9800

N1(N2	1.443(2)

N1(S1	1.6527(16)

N1(H1	0.81(3)

O1(S1	1.4407(14)

O2(S1	1.4294(13)

C10(C11(H11A	120.0

C10(C11(H11B	120.0

H11A(C11(H11B	120.0

C2(C1(H1A	109.5

C2(C1(H1B	109.5

H1A(C1(H1B	109.5

C2(C1(H1C	109.5

H1A(C1(H1C	109.5

H1B(C1(H1C	109.5

C3(C2(C7	118.14(18)

C3(C2(C1	120.8(2)

C7(C2(C1	121.1(2)

C4(C3(C2	121.30(19)

C4(C3(H3	119.3

C2(C3(H3	119.3

C3(C4(C5	119.11(19)

C3(C4(H4	120.4

C5(C4(H4	120.4

C6(C5(C4	120.98(18)

C6(C5(S1	120.11(15)

C4(C5(S1	118.80(15)

C5(C6(C7	118.84(18)

C5(C6(H6	120.6

C7(C6(H6	120.6

C6(C7(C2	121.61(19)

C6(C7(H7	119.2

C2(C7(H7	119.2

N2(C8(C15	106.29(15)

N2(C8(C9	104.35(14)

C15(C8(C9	112.29(15)

N2(C8(H8	111.2

C15(C8(H8	111.2

C9(C8(H8	111.2

C10(C9(C8	103.40(15)

C10(C9(H9A	111.1

C8(C9(H9A	111.1

C10(C9(H9B	111.1

C8(C9(H9B	111.1

H9A(C9(H9B	109.0

C11(C10(C9	127.46(18)

C11(C10(C12	125.73(18)

C9(C10(C12	106.79(15)

N2(C12(C10	103.85(14)

N2(C12(C13	106.27(14)

C10(C12(C13	112.40(14)

N2(C12(H12	111.3

C10(C12(H12	111.3

C13(C12(H12	111.3

C14(C13(C12	108.97(15)

C14(C13(Si1	114.35(12)

C12(C13(Si1	116.15(12)

C14(C13(H13	105.5

C12(C13(H13	105.5

Si1(C13(H13	105.5

C15(C14(C13	111.94(15)

C15(C14(H14A	109.2

C13(C14(H14A	109.2

C15(C14(H14B	109.2

C13(C14(H14B	109.2

H14A(C14(H14B	107.9

C8(C15(C14	111.31(15)

C8(C15(H15A	109.4

C14(C15(H15A	109.4

C8(C15(H15B	109.4

C14(C15(H15B	109.4

H15A(C15(H15B	108.0

Si1(C16(H16A	109.5

Si1(C16(H16B	109.5

H16A(C16(H16B	109.5

Si1(C16(H16C	109.5

H16A(C16(H16C	109.5

H16B(C16(H16C	109.5

Si1(C17(H17A	109.5

Si1(C17(H17B	109.5

H17A(C17(H17B	109.5

Si1(C17(H17C	109.5

H17A(C17(H17C	109.5

H17B(C17(H17C	109.5

Si1(C18(H18A	109.5

Si1(C18(H18B	109.5

H18A(C18(H18B	109.5

Si1(C18(H18C	109.5

H18A(C18(H18C	109.5

H18B(C18(H18C	109.5

N2(N1(S1	110.88(12)

N2(N1(H1	113.3(18)

S1(N1(H1	107.6(18)

N1(N2(C8	110.11(14)

N1(N2(C12	110.37(13)

C8(N2(C12	101.98(13)

C17(Si1(C18	109.66(10)

C17(Si1(C16	109.71(10)

C18(Si1(C16	108.41(11)

C17(Si1(C13	109.41(9)

C18(Si1(C13	106.76(9)

C16(Si1(C13	112.81(9)

O2(S1(O1	119.50(8)

O2(S1(N1	108.36(9)

O1(S1(N1	104.61(8)

O2(S1(C5	107.64(9)

O1(S1(C5	109.32(8)

N1(S1(C5	106.74(8)

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C11	18(1) 	30(1)	31(1) 	6(1)	10(1) 	2(1)

C1	21(1) 	54(2)	29(1) 	1(1)	9(1) 	1(1)

C2	19(1) 	36(1)	18(1) 	(3(1)	7(1) 	1(1)

C3	26(1) 	25(1)	27(1) 	3(1)	6(1) 	7(1)

C4	28(1) 	19(1)	28(1) 	2(1)	9(1) 	0(1)

C5	19(1) 	18(1)	22(1) 	(1(1)	11(1) 	(1(1)

C6	22(1) 	20(1)	24(1) 	2(1)	12(1) 	2(1)

C7	23(1) 	28(1)	24(1) 	1(1)	13(1) 	(4(1)

C8	19(1) 	18(1)	26(1) 	(3(1)	10(1) 	(6(1)

C9	18(1) 	24(1)	24(1) 	(1(1)	8(1) 	(3(1)

C10	15(1) 	17(1)	28(1) 	1(1)	10(1) 	3(1)

C12	14(1) 	14(1)	27(1) 	(1(1)	11(1) 	(1(1)

C13	16(1) 	18(1)	23(1) 	(1(1)	9(1) 	0(1)

C14	24(1) 	14(1)	24(1) 	(1(1)	10(1) 	1(1)

C15	28(1) 	16(1)	26(1) 	(2(1)	12(1) 	(5(1)

C16	32(1) 	37(1)	39(1) 	(9(1)	22(1) 	3(1)

C17	21(1) 	25(1)	28(1) 	0(1)	13(1) 	(3(1)

C18	20(1) 	30(1)	46(1) 	7(1)	12(1) 	4(1)

N1	16(1) 	17(1)	25(1) 	1(1)	10(1) 	3(1)

N2	16(1) 	14(1)	27(1) 	(2(1)	11(1) 	(1(1)

O1	22(1) 	18(1)	33(1) 	1(1)	17(1) 	3(1)

O2	29(1) 	21(1)	33(1) 	3(1)	19(1) 	(5(1)

Si1	16(1) 	19(1)	26(1) 	(1(1)	10(1) 	3(1)

S1	18(1) 	16(1)	25(1) 	1(1)	13(1) 	0(1)