Table 1.  Crystal data and structure refinement for 97src216.

      _____________________________________________________

      Empirical formula                 C22 H18 Fe N2

      Formula weight                    366.23

      Temperature                       150(2) K

      Wavelength                        0.71069 A

      Crystal system                    Orthorhombic

      Space group                       P2(1)2(1)2(1)

      Unit cell dimensions              a = 7.5921(11) A
                                        b = 14.9902(9) A
                                        c = 15.372(2) A

      Volume                            1749.4(4) A^3

      Z                                 4

      Density (calculated)              1.390 Mg/m^3

      Absorption coefficient            0.867 mm^-1

      F(000)                            760

      Crystal size                      0.28 x 0.16 x 0.12 mm

      Theta range for data collection   1.90 to 25.04 deg.

      Index ranges                      -8<=h<=7, -17<=k<=17, -17<=l<=16

      Reflections collected             7635

      Independent reflections           2717 [R(int) = 0.0884]

      Refinement method                 Full-matrix least-squares on F^2

      Data / restraints / parameters    2717 / 18 / 226

      Goodness-of-fit on F^2            0.887

      Final R indices [I>2sigma(I)]     R1 = 0.0422, wR2 = 0.0937

      R indices (all data)              R1 = 0.0541, wR2 = 0.0962

      Absolute structure parameter      -0.01(3)

      Largest diff. peak and hole       0.568 and -0.315 e.A^-3

 

   Table 2.  Atomic coordinates ( x 10^4) and equivalent isotropic
   displacement parameters (A^2 x 10^3) for 97SRC216.

   U(eq) is defined as one third of the trace of the
   orthogonalized Uij tensor.

   ________________________________________________________________

		  x             y             z           U(eq)
   ________________________________________________________________

   Fe(1)        3793(1)        789(1)        263(1)       26(1)
   N(1)         5701(4)        912(3)       2916(3)       25(1)
   N(2)         2302(5)       3368(3)       2812(3)       32(1)
   C(1)         4881(6)       1893(3)        802(4)       19(1)
   C(2)         6113(7)       1188(3)        775(3)       23(1)
   C(3)         6371(6)        918(3)       -106(3)       25(1)
   C(4)         5269(6)       1470(3)       -624(3)       23(1)
   C(5)         4368(6)       2064(4)        -66(3)       25(1)
   C(6)         2850(10)      -193(7)       1003(6)       83(3)
   C(7)         3064(8)       -515(4)        171(6)       59(2)
   C(8)         2085(8)        -30(4)       -387(5)       55(2)
   C(9)         1196(8)        588(4)         60(5)       61(2)
   C(10)        1589(10)       508(5)        928(6)       80(3)
   C(11)        4105(6)       2362(3)       1554(3)       22(1)
   C(12)        4553(6)       2308(4)       2394(3)       19(1)
   C(13)        6051(6)       1746(3)       2684(3)       20(1)
   C(14)        7746(7)       2100(4)       2706(4)       30(1)
   C(15)        9128(6)       1539(4)       2937(4)       37(2)
   C(16)        8779(7)        669(4)       3148(3)       36(1)
   C(17)        7039(7)        370(4)       3128(3)       36(2)
   C(18)        3516(6)       2780(3)       3075(3)       20(1)
   C(19)        3773(7)       2586(3)       3958(3)       30(1)
   C(20)        2784(7)       3022(4)       4587(4)       35(2)
   C(21)        1546(7)       3627(4)       4318(4)       33(2)
   C(22)        1366(7)       3771(4)       3428(4)       38(1)
   ________________________________________________________________

 

 
    Table 3.   Bond lengths [A] and angles [deg] for 97src216.
    _____________________________________________________________

    Fe(1)-C(6)             1.993(7)     Fe(1)-C(10)            2.005(6)
    Fe(1)-C(9)             2.018(6)     Fe(1)-C(2)             2.020(5)
    Fe(1)-C(5)             2.025(5)     Fe(1)-C(1)             2.027(5)
    Fe(1)-C(7)             2.036(6)     Fe(1)-C(4)             2.039(5)
    Fe(1)-C(8)             2.046(6)     Fe(1)-C(3)             2.047(5)
    N(1)-C(13)             1.327(6)     N(1)-C(17)             1.341(6)
    N(2)-C(22)             1.329(6)     N(2)-C(18)             1.338(6)
    C(1)-C(2)              1.412(6)     C(1)-C(5)              1.413(7)
    C(1)-C(11)             1.475(7)     C(2)-C(3)              1.426(6)
    C(3)-C(4)              1.420(7)     C(4)-C(5)              1.414(7)
    C(6)-C(7)              1.377(11)    C(6)-C(10)             1.426(10)
    C(7)-C(8)              1.348(10)    C(8)-C(9)              1.337(8)
    C(9)-C(10)             1.372(10)    C(11)-C(12)            1.338(7)
    C(12)-C(13)            1.483(7)     C(12)-C(18)            1.488(7)
    C(15)-C(16)            1.369(8)     C(16)-C(17)            1.395(7)
    C(18)-C(19)            1.401(6)     C(19)-C(20)            1.389(7)
    C(20)-C(21)            1.370(7)     C(21)-C(22)            1.392(7)

    C(6)-Fe(1)-C(10)      41.8(3)       C(6)-Fe(1)-C(9)       68.1(3)
    C(10)-Fe(1)-C(9)      39.9(3)       C(6)-Fe(1)-C(2)      108.1(3)
    C(10)-Fe(1)-C(2)     126.3(3)       C(9)-Fe(1)-C(2)      163.0(3)
    C(6)-Fe(1)-C(5)      156.5(4)       C(10)-Fe(1)-C(5)     120.3(3)
    C(9)-Fe(1)-C(5)      108.2(2)       C(2)-Fe(1)-C(5)       68.3(2)
    C(6)-Fe(1)-C(1)      121.1(3)       C(10)-Fe(1)-C(1)     107.7(2)
    C(9)-Fe(1)-C(1)      125.7(2)       C(2)-Fe(1)-C(1)       40.9(2)
    C(5)-Fe(1)-C(1)       40.8(2)       C(6)-Fe(1)-C(7)       39.9(3)
    C(10)-Fe(1)-C(7)      66.9(3)       C(9)-Fe(1)-C(7)       65.2(3)
    C(2)-Fe(1)-C(7)      123.3(2)       C(5)-Fe(1)-C(7)      161.3(3)
    C(1)-Fe(1)-C(7)      157.4(3)       C(6)-Fe(1)-C(4)      161.6(4)
    C(10)-Fe(1)-C(4)     154.7(3)       C(9)-Fe(1)-C(4)      120.5(2)
    C(2)-Fe(1)-C(4)       68.5(2)       C(5)-Fe(1)-C(4)       40.7(2)
    C(1)-Fe(1)-C(4)       68.9(2)       C(7)-Fe(1)-C(4)      125.7(3)
    C(6)-Fe(1)-C(8)       66.9(3)       C(10)-Fe(1)-C(8)      66.1(3)
    C(9)-Fe(1)-C(8)       38.4(2)       C(2)-Fe(1)-C(8)      157.0(2)
    C(5)-Fe(1)-C(8)      125.5(3)       C(1)-Fe(1)-C(8)      161.4(2)
    C(7)-Fe(1)-C(8)       38.6(3)       C(4)-Fe(1)-C(8)      108.7(3)
    C(6)-Fe(1)-C(3)      124.9(3)       C(10)-Fe(1)-C(3)     163.5(3)
    C(9)-Fe(1)-C(3)      154.8(3)       C(2)-Fe(1)-C(3)       41.0(2)
    C(5)-Fe(1)-C(3)       68.6(2)       C(1)-Fe(1)-C(3)       69.3(2)
    C(7)-Fe(1)-C(3)      109.4(2)       C(4)-Fe(1)-C(3)       40.7(2)
    C(8)-Fe(1)-C(3)      121.8(2)       C(13)-N(1)-C(17)     119.0(4)
    C(22)-N(2)-C(18)     116.9(5)       C(2)-C(1)-C(5)       106.9(5)
    C(2)-C(1)-C(11)      130.2(5)       C(5)-C(1)-C(11)      122.9(4)
    C(2)-C(1)-Fe(1)       69.3(3)       C(5)-C(1)-Fe(1)       69.5(3)
    C(11)-C(1)-Fe(1)     123.1(3)       C(1)-C(2)-C(3)       109.3(5)
    C(1)-C(2)-Fe(1)       69.9(3)       C(3)-C(2)-Fe(1)       70.5(3)
    C(4)-C(3)-C(2)       106.7(5)       C(4)-C(3)-Fe(1)       69.4(3)
    C(2)-C(3)-Fe(1)       68.5(3)       C(5)-C(4)-C(3)       108.1(5)
    C(5)-C(4)-Fe(1)       69.1(3)       C(3)-C(4)-Fe(1)       70.0(3)
    C(1)-C(5)-C(4)       109.0(5)       C(1)-C(5)-Fe(1)       69.7(3)
    C(4)-C(5)-Fe(1)       70.2(3)       C(7)-C(6)-C(10)      105.2(7)
    C(7)-C(6)-Fe(1)       71.7(4)       C(10)-C(6)-Fe(1)      69.6(4)
    C(8)-C(7)-C(6)       109.7(7)       C(8)-C(7)-Fe(1)       71.1(4)
    C(6)-C(7)-Fe(1)       68.3(4)       C(9)-C(8)-C(7)       109.0(8)
    C(9)-C(8)-Fe(1)       69.7(4)       C(7)-C(8)-Fe(1)       70.3(4)
    C(8)-C(9)-C(10)      109.2(7)       C(8)-C(9)-Fe(1)       71.9(4)
    C(10)-C(9)-Fe(1)      69.5(4)       C(9)-C(10)-C(6)      106.8(7)
    C(9)-C(10)-Fe(1)      70.6(4)       C(6)-C(10)-Fe(1)      68.6(4)
    C(12)-C(11)-C(1)     128.7(5)       C(11)-C(12)-C(13)    121.2(5)
    C(11)-C(12)-C(18)    121.1(4)       C(13)-C(12)-C(18)    117.6(4)
    N(1)-C(13)-C(14)     122.5(5)       N(1)-C(13)-C(12)     117.6(4)
    C(14)-C(13)-C(12)    120.0(5)       C(15)-C(14)-C(13)    118.2(5)
    C(16)-C(15)-C(14)    119.4(5)       C(15)-C(16)-C(17)    118.9(5)
    N(1)-C(17)-C(16)     121.9(5)       N(2)-C(18)-C(19)     121.7(4)
    N(2)-C(18)-C(12)     117.7(4)       C(19)-C(18)-C(12)    120.6(4)
    C(20)-C(19)-C(18)    120.1(5)       C(21)-C(20)-C(19)    118.2(6)
    C(20)-C(21)-C(22)    117.9(5)       N(2)-C(22)-C(21)     125.2(5)
    _____________________________________________________________


 
 
    Table 4.   Anisotropic displacement parameters (A^2 x 10^3) for 97SRC216.

    The anisotropic displacement factor exponent takes the form: 
    -2 pi^2 [ h^2 a*^2 U11 + ... + 2 h k a* b* U12 ] 
  
    _______________________________________________________________________ 
  
              U11        U22        U33        U23        U13        U12 
    _______________________________________________________________________ 
  
    Fe(1)    19(1)      23(1)      38(1)      -1(1)       7(1)      -3(1) 
    N(1)     25(2)      29(3)      20(3)       4(2)      -2(2)       8(2) 
    N(2)     45(3)      26(3)      27(3)       4(2)       9(2)      13(2) 
    C(1)     13(3)      18(3)      26(4)       2(3)       3(2)       0(2) 
    C(2)     21(3)      28(3)      20(3)       1(2)       4(3)      -7(3) 
    C(3)     17(2)      31(3)      27(3)       2(3)       5(2)      -7(3) 
    C(4)     25(3)      20(3)      25(4)      -3(3)      -2(2)      -2(2) 
    C(5)     19(3)      33(3)      24(4)       1(2)      -4(2)      -2(2) 
    C(6)     74(5)      91(5)      83(6)      44(5)     -13(4)     -53(4) 
    C(7)     36(3)      25(4)     118(8)       1(4)      12(4)     -10(3) 
    C(8)     38(4)      35(4)      91(6)     -18(5)      14(4)     -16(3) 
    C(9)     24(3)      57(4)     103(6)      -1(4)       6(4)     -15(3) 
    C(10)    71(4)      75(5)      95(5)     -45(4)      68(4)     -51(4) 
    C(11)    18(3)      23(3)      25(3)      -2(2)      -1(2)       2(2) 
    C(12)    20(3)      20(3)      18(3)       0(2)       0(2)       0(2) 
    C(13)    20(3)      20(3)      18(3)      -2(2)       4(2)       5(3) 
    C(14)    31(3)      32(4)      27(4)       1(3)       2(3)      -2(3) 
    C(15)    18(3)      52(4)      40(4)      -4(3)      -4(3)       6(3) 
    C(16)    31(3)      47(4)      30(3)      -1(3)      -2(3)      15(4) 
    C(17)    47(4)      37(4)      25(4)       4(3)      -2(3)       3(3) 
    C(18)    14(3)      20(3)      26(3)      -3(2)       4(2)       3(2) 
    C(19)    21(3)      43(3)      25(3)      -3(3)       2(3)       5(3) 
    C(20)    38(3)      32(4)      35(4)       0(3)       8(3)      -2(3) 
    C(21)    36(4)      26(3)      35(4)       0(3)      17(3)       2(3) 
    C(22)    40(3)      37(3)      36(4)      -2(3)       8(3)      18(3) 
    _______________________________________________________________________ 
 
 

   Table 5.   Hydrogen coordinates ( x 10^4) and isotropic
   displacement parameters (A^2 x 10^3) for 97SRC216.

   ________________________________________________________________

		  x             y             z           U(iso)
   ________________________________________________________________

   H(2)         6682(7)        933(3)       1266(3)       28
   H(3)         7132(6)        460(3)       -307(3)       30
   H(4)         5156(6)       1443(3)      -1239(3)       28
   H(5)         3549(6)       2507(4)       -245(3)       30
   H(6)         3419(10)      -395(7)       1517(6)       99
   H(7)         3792(8)      -1005(4)         14(6)       71
   H(8)         2035(8)       -114(4)       -999(5)       66
   H(9)          416(8)       1016(4)       -184(5)       74
   H(10)        1113(10)       853(5)       1390(6)       96
   H(11)        3160(6)       2755(3)       1423(3)       26
   H(14)        7953(7)       2709(4)       2568(4)       36
   H(15)       10302(6)       1757(4)       2949(4)       44
   H(16)        9707(7)        276(4)       3304(3)       43
   H(17)        6796(7)       -234(4)       3269(3)       44
   H(19)        4626(7)       2155(3)       4125(3)       36
   H(20)        2962(7)       2905(4)       5188(4)       42
   H(21)         833(7)       3937(4)       4725(4)       39
   H(22)         506(7)       4192(4)       3246(4)       45
   ________________________________________________________________