|  | University of Southampton · School of Chemistry EPSRC National Crystallography Service |  |
| --- | --- | --- |

Table 1. Crystal data and structure refinement.

Identification code 	04src0194

Empirical formula 	C44H46Cl4N16Ni2O21

Formula weight 	1394.19

Temperature 	120(2) K

Wavelength 	0.71073 Å

Crystal system 	Orthorhombic

Space group 	Pna21

Unit cell dimensions	a = 25.809(5) Å	( = 90.000(5)°

b = 11.899(5) Å	( = 90.000(5)°

c = 17.357(5) Å	(  = 90.000(5)°

Volume	5330(3) Å3

Z	4

Density (calculated)	1.737 Mg / m3

Absorption coefficient	1.004 mm(1

F(000)	2856

Crystal	Plate; Orange

Crystal size	0.22 ( 0.14 ( 0.03 mm3

( range for data collection	3.01 ( 27.48°

Index ranges	(33 ( h ( 33, (15 ( k ( 15, (22 ( l ( 22

Reflections collected	87747

Independent reflections	12190 [Rint = 0.1260]

Completeness to ( = 27.48°	99.8 %

Absorption correction	Semi(empirical from equivalents

Max. and min. transmission	0.9705 and 0.8093

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	12190 / 823 / 786

Goodness-of-fit on F2	1.069

Final R indices [F2 > 2((F2)]	R1 = 0.0810, wR2 = 0.1720

R indices (all data)	R1 = 0.1288, wR2 = 0.1905

Absolute structure parameter	0.52(3)

Largest diff. peak and hole	1.012 and (0.819 e Å(3

Diffractometer: Nonius KappaCCD area detector (( scans and ( scans to fill asymmetric unit sphere). Cell determination: DirAx (Duisenberg, A.J.M.(1992). J. Appl. Cryst. 25, 92-96.) Data collection: Collect (Collect: Data collection software, R. Hooft, Nonius B.V., 1998). Data reduction and cell refinement: Denzo (Z. Otwinowski & W. Minor, Methods in Enzymology (1997) Vol. 276: Macromolecular Crystallography, part A, pp. 307(326; C. W. Carter, Jr. & R. M. Sweet, Eds., Academic Press). Absorption correction: SORTAV (R. H. Blessing, Acta Cryst. A51 (1995) 33(37; R. H. Blessing, J. Appl. Cryst. 30 (1997) 421(426). Structure solution: SHELXS97 (G. M. Sheldrick, Acta Cryst. (1990) A46 467(473). Structure refinement: SHELXL97 (G. M. Sheldrick (1997), University of Göttingen, Germany). Graphics: Cameron - A Molecular Graphics Package. (D. M. Watkin, L. Pearce and C. K. Prout, Chemical Crystallography Laboratory, University of Oxford, 1993).

Special details:

All hydrogen atoms were fixed.

It was not possible to locate the hydrogen atoms on the solvent water molecules.

Table 2. Atomic coordinates [( 104], equivalent isotropic displacement parameters [Å2 ( 103] and site occupancy factors. Ueq is defined as one third of the trace of the orthogonalized Uij tensor.

Atom 	x	y	z	Ueq	S.o.f.

C1	278(4)	870(8)	5847(6)	27(2)	1

C2	(136(4)	613(8)	6297(6)	26(2)	1

C3	(352(4)	1506(9)	6715(6)	32(2)	1

C4	(147(4)	2568(8)	6629(6)	25(2)	1

C5	256(3)	2743(8)	6122(6)	21(2)	1

C6	508(3)	3843(8)	6031(5)	18(2)	1

C7	340(3)	4865(7)	6319(5)	18(2)	1

C8	624(4)	5768(8)	6160(6)	25(2)	1

C9	1080(4)	5737(7)	5734(5)	17(2)	1

C10	1217(3)	4693(7)	5469(5)	15(2)	1

C11	1676(3)	4429(6)	4964(6)	17(2)	1

C12	2058(4)	2709(8)	3593(5)	20(2)	1

C13	2496(3)	1977(7)	3354(5)	18(2)	1

C14	2609(4)	1613(7)	2651(5)	22(2)	1

C15	3032(4)	904(8)	2498(6)	25(2)	1

C16	3301(4)	587(8)	3154(6)	28(2)	1

C17	3182(3)	957(8)	3884(5)	21(2)	1

C18	3457(3)	724(8)	4617(6)	20(2)	1

C19	3863(4)	7(9)	4666(6)	31(2)	1

C20	4070(4)	(213(9)	5371(6)	32(2)	1

C21	3889(3)	289(8)	6005(7)	30(2)	1

C22	3473(3)	1078(8)	5884(6)	26(2)	1

C31	268(3)	3930(8)	4067(6)	21(2)	1

C32	(127(3)	4154(7)	3546(5)	20(2)	1

C33	(346(3)	3286(8)	3179(6)	25(2)	1

C34	(178(4)	2221(9)	3288(6)	25(2)	1

C35	252(4)	2069(8)	3754(5)	18(2)	1

C36	506(4)	980(8)	3891(6)	22(2)	1

C37	328(4)	(51(8)	3617(6)	29(2)	1

C38	604(3)	(1021(8)	3804(6)	20(2)	1

C39	1055(3)	(918(8)	4235(6)	25(2)	1

C40	1205(3)	123(7)	4476(6)	19(2)	1

C41	1662(3)	381(6)	4935(6)	18(2)	1

C42	2036(4)	2165(8)	6315(5)	19(2)	1

C43	2453(3)	2914(8)	6553(5)	21(2)	1

C44	2559(4)	3286(8)	7314(6)	25(2)	1

C45	2945(4)	4062(8)	7368(5)	24(2)	1

C46	3234(4)	4433(8)	6788(6)	27(2)	1

C47	3116(3)	3964(8)	6060(5)	22(2)	1

C48	3401(3)	4260(7)	5355(5)	17(2)	1

C49	3764(3)	5065(8)	5303(5)	22(2)	1

C50	4019(4)	5284(8)	4621(6)	26(2)	1

C51	3869(4)	4640(8)	3978(6)	26(2)	1

C52	3506(4)	3851(9)	4049(6)	26(2)	1

N1	458(3)	1905(6)	5729(4)	18(1)	1

N2	939(3)	3786(6)	5611(4)	16(1)	1

N3	2071(3)	5112(6)	4994(5)	23(2)	1

N4	1628(2)	3508(6)	4592(4)	14(1)	1

N5	2099(3)	3114(6)	4279(4)	18(1)	1

N6	1671(3)	2855(7)	3138(5)	27(2)	1

N7	2780(3)	1664(6)	3996(4)	21(2)	1

N8	3277(3)	1276(6)	5239(4)	23(2)	1

N31	466(3)	2908(6)	4164(4)	17(1)	1

N32	936(3)	1037(6)	4303(4)	18(1)	1

N33	2083(3)	(254(6)	4915(5)	24(2)	1

N34	1626(3)	1306(6)	5329(4)	23(2)	1

N35	2087(3)	1723(6)	5626(4)	18(1)	1

N36	1629(3)	2002(7)	6789(4)	24(2)	1

N37	2743(3)	3254(6)	5979(4)	18(1)	1

N38	3266(2)	3644(6)	4741(4)	17(1)	1

Ni1	1029(1)	2421(1)	4952(1)	18(1)	1

Ni2	2691(1)	2443(1)	4972(1)	18(1)	1

O1	652(3)	1706(5)	7905(4)	35(2)	1

O2	1356(2)	2573(6)	8465(5)	33(2)	1

O3	748(3)	3618(5)	7815(4)	29(2)	1

O4	527(3)	2825(7)	8991(4)	39(2)	1

Cl1	820(1)	2675(2)	8305(2)	27(1)	1

O11	1367(3)	2450(6)	11519(5)	38(2)	1

O12	546(3)	2216(7)	10999(4)	38(2)	1

O13	638(3)	3289(6)	12113(5)	40(2)	1

O14	769(3)	1360(6)	12167(4)	33(2)	1

Cl11	814(1)	2341(2)	11696(1)	24(1)	1

O21	1215(3)	(2059(6)	7274(4)	37(2)	1

O22	1862(3)	(1036(6)	6652(4)	54(2)	1

O23	1106(4)	(1511(7)	6000(4)	60(2)	1

O24	1074(3)	(207(5)	6968(4)	44(2)	1

Cl21	1345(1)	(1207(2)	6727(1)	30(1)	1

O31	(614(3)	4036(8)	7977(6)	91(3)	1

O32	(1315(4)	2938(6)	7777(5)	61(2)	1

O33	(1399(4)	4854(6)	8025(5)	75(3)	1

O34	(1157(4)	3634(7)	8991(4)	68(3)	1

Cl31	(1149(1)	3856(2)	8194(2)	40(1)	1

O51	2314(3)	7069(6)	5816(4)	39(2)	1

O52	2788(3)	5950(7)	3776(5)	60(2)	1

O53	2575(4)	397(7)	7404(6)	75(3)	1

O54	2150(3)	(2192(7)	4003(4)	49(2)	1

O55	1852(3)	2929(8)	10061(7)	85(3)	1

Table 3. Bond lengths [Å] and angles [°].

C1(N1	1.332(12)

C1(C2	1.359(13)

C1(H1	0.9500

C2(C3	1.403(13)

C2(H2	0.9500

C3(C4	1.378(13)

C3(H3	0.9500

C4(C5	1.380(13)

C4(H4	0.9500

C5(N1	1.316(12)

C5(C6	1.470(13)

C6(N2	1.334(11)

C6(C7	1.383(12)

C7(C8	1.328(13)

C7(H7	0.9500

C8(C9	1.392(13)

C8(H8	0.9500

C9(C10	1.371(11)

C9(H9	0.9500

C10(N2	1.318(11)

C10(C11	1.507(12)

C11(N4	1.279(10)

C11(N3	1.304(10)

C12(N6	1.285(12)

C12(N5	1.288(11)

C12(C13	1.487(12)

C13(C14	1.327(13)

C13(N7	1.383(12)

C14(C15	1.406(13)

C14(H14	0.9500

C15(C16	1.386(14)

C15(H15	0.9500

C16(C17	1.376(13)

C16(H16	0.9500

C17(N7	1.350(11)

C17(C18	1.483(13)

C18(N8	1.346(12)

C18(C19	1.355(13)

C19(C20	1.360(14)

C19(H19	0.9500

C20(C21	1.338(15)

C20(H20	0.9500

C21(C22	1.440(13)

C21(H21	0.9500

C22(N8	1.252(12)

C22(H22	0.9500

C31(N31	1.329(11)

C31(C32	1.389(13)

C31(H31	0.9500

C32(C33	1.338(12)

C32(H32	0.9500

C33(C34	1.352(13)

C33(H33	0.9500

C34(C35	1.386(13)

C34(H34	0.9500

C35(N31	1.345(11)

C35(C36	1.471(13)

C36(N32	1.322(11)

C36(C37	1.394(13)

C37(C38	1.395(13)

C37(H37	0.9500

C38(C39	1.388(12)

C38(H38	0.9500

C39(C40	1.364(13)

C39(H39	0.9500

C40(N32	1.325(11)

C40(C41	1.456(12)

C41(N34	1.299(11)

C41(N33	1.325(10)

C42(N35	1.313(11)

C42(N36	1.350(11)

C42(C43	1.456(13)

C43(N37	1.310(11)

C43(C44	1.419(13)

C44(C45	1.362(13)

C44(H44	0.9500

C45(C46	1.328(14)

C45(H45	0.9500

C46(C47	1.415(13)

C46(H46	0.9500

C47(N37	1.288(11)

C47(C48	1.472(13)

C48(N38	1.339(11)

C48(C49	1.342(13)

C49(C50	1.380(13)

C49(H49	0.9500

C50(C51	1.408(14)

C50(H50	0.9500

C51(C52	1.332(13)

C51(H51	0.9500

C52(N38	1.373(12)

C52(H52	0.9500

N1(Ni1	2.090(8)

N2(Ni1	1.999(7)

N3(H3A	0.8800

N3(H3B	0.8800

N4(N5	1.412(9)

N4(Ni1	2.108(7)

N5(Ni2	2.103(7)

N6(H6A	0.8800

N6(H6B	0.8800

N7(Ni2	1.946(8)

N8(Ni2	2.105(7)

N31(Ni1	2.079(8)

N32(Ni1	2.009(7)

N33(H33A	0.8800

N33(H33B	0.8800

N34(N35	1.389(10)

N34(Ni1	2.136(7)

N35(Ni2	2.109(7)

N36(H36A	0.8800

N36(H36B	0.8800

N37(Ni2	2.001(8)

N38(Ni2	2.101(7)

O1(Cl1	1.414(6)

O2(Cl1	1.414(6)

O3(Cl1	1.420(6)

O4(Cl1	1.423(6)

O11(Cl11	1.466(7)

O12(Cl11	1.401(6)

O13(Cl11	1.415(7)

O14(Cl11	1.430(6)

O21(Cl21	1.429(6)

O22(Cl21	1.355(6)

O23(Cl21	1.451(7)

O24(Cl21	1.442(6)

O31(Cl31	1.448(8)

O32(Cl31	1.380(7)

O33(Cl31	1.381(7)

O34(Cl31	1.408(8)

N1(C1(C2	124.9(9)

N1(C1(H1	117.6

C2(C1(H1	117.6

C1(C2(C3	116.1(9)

C1(C2(H2	122.0

C3(C2(H2	122.0

C4(C3(C2	119.1(9)

C4(C3(H3	120.5

C2(C3(H3	120.5

C3(C4(C5	119.8(9)

C3(C4(H4	120.1

C5(C4(H4	120.1

N1(C5(C4	121.1(9)

N1(C5(C6	116.4(8)

C4(C5(C6	122.4(9)

N2(C6(C7	120.2(8)

N2(C6(C5	112.4(8)

C7(C6(C5	127.4(8)

C8(C7(C6	117.7(8)

C8(C7(H7	121.2

C6(C7(H7	121.2

C7(C8(C9	123.7(9)

C7(C8(H8	118.2

C9(C8(H8	118.2

C10(C9(C8	114.9(8)

C10(C9(H9	122.6

C8(C9(H9	122.6

N2(C10(C9	122.6(8)

N2(C10(C11	111.4(7)

C9(C10(C11	125.9(8)

N4(C11(N3	129.1(8)

N4(C11(C10	113.3(7)

N3(C11(C10	117.5(8)

N6(C12(N5	125.6(9)

N6(C12(C13	119.9(8)

N5(C12(C13	114.5(8)

C14(C13(N7	122.5(8)

C14(C13(C12	127.8(8)

N7(C13(C12	109.6(8)

C13(C14(C15	122.6(9)

C13(C14(H14	118.7

C15(C14(H14	118.7

C16(C15(C14	113.4(9)

C16(C15(H15	123.3

C14(C15(H15	123.3

C17(C16(C15	123.9(9)

C17(C16(H16	118.1

C15(C16(H16	118.1

N7(C17(C16	120.2(9)

N7(C17(C18	111.1(8)

C16(C17(C18	128.6(8)

N8(C18(C19	121.6(9)

N8(C18(C17	115.6(7)

C19(C18(C17	122.8(9)

C18(C19(C20	118.8(9)

C18(C19(H19	120.6

C20(C19(H19	120.6

C21(C20(C19	121.1(10)

C21(C20(H20	119.5

C19(C20(H20	119.5

C20(C21(C22	115.6(10)

C20(C21(H21	122.2

C22(C21(H21	122.2

N8(C22(C21	123.7(10)

N8(C22(H22	118.2

C21(C22(H22	118.2

N31(C31(C32	122.7(9)

N31(C31(H31	118.6

C32(C31(H31	118.6

C33(C32(C31	118.1(8)

C33(C32(H32	121.0

C31(C32(H32	121.0

C32(C33(C34	121.5(9)

C32(C33(H33	119.2

C34(C33(H33	119.2

C33(C34(C35	117.4(9)

C33(C34(H34	121.3

C35(C34(H34	121.3

N31(C35(C34	122.7(9)

N31(C35(C36	112.7(8)

C34(C35(C36	124.5(8)

N32(C36(C37	120.4(8)

N32(C36(C35	114.6(8)

C37(C36(C35	124.9(8)

C36(C37(C38	118.7(9)

C36(C37(H37	120.6

C38(C37(H37	120.6

C39(C38(C37	118.7(9)

C39(C38(H38	120.6

C37(C38(H38	120.6

C40(C39(C38	118.9(8)

C40(C39(H39	120.5

C38(C39(H39	120.5

N32(C40(C39	121.8(9)

N32(C40(C41	112.0(8)

C39(C40(C41	126.2(8)

N34(C41(N33	123.7(8)

N34(C41(C40	114.2(7)

N33(C41(C40	121.9(8)

N35(C42(N36	125.1(9)

N35(C42(C43	115.5(8)

N36(C42(C43	119.4(8)

N37(C43(C44	120.0(9)

N37(C43(C42	113.3(8)

C44(C43(C42	126.7(8)

C45(C44(C43	114.6(9)

C45(C44(H44	122.7

C43(C44(H44	122.7

C46(C45(C44	125.7(9)

C46(C45(H45	117.1

C44(C45(H45	117.1

C45(C46(C47	115.1(9)

C45(C46(H46	122.4

C47(C46(H46	122.4

N37(C47(C46	121.2(9)

N37(C47(C48	116.1(8)

C46(C47(C48	122.8(8)

N38(C48(C49	121.3(9)

N38(C48(C47	113.6(7)

C49(C48(C47	125.1(9)

C48(C49(C50	121.7(9)

C48(C49(H49	119.1

C50(C49(H49	119.1

C49(C50(C51	116.4(9)

C49(C50(H50	121.8

C51(C50(H50	121.8

C52(C51(C50	120.2(9)

C52(C51(H51	119.9

C50(C51(H51	119.9

C51(C52(N38	121.7(10)

C51(C52(H52	119.2

N38(C52(H52	119.2

C5(N1(C1	118.8(9)

C5(N1(Ni1	113.0(6)

C1(N1(Ni1	128.1(7)

C10(N2(C6	120.9(8)

C10(N2(Ni1	119.6(6)

C6(N2(Ni1	116.9(6)

C11(N3(H3A	120.0

C11(N3(H3B	120.0

H3A(N3(H3B	120.0

C11(N4(N5	113.2(7)

C11(N4(Ni1	116.6(6)

N5(N4(Ni1	122.8(5)

C12(N5(N4	114.1(7)

C12(N5(Ni2	116.5(6)

N4(N5(Ni2	122.1(5)

C12(N6(H6A	120.0

C12(N6(H6B	120.0

H6A(N6(H6B	120.0

C17(N7(C13	117.3(8)

C17(N7(Ni2	120.8(6)

C13(N7(Ni2	120.7(6)

C22(N8(C18	119.1(8)

C22(N8(Ni2	127.7(7)

C18(N8(Ni2	113.2(6)

C31(N31(C35	117.1(8)

C31(N31(Ni1	127.4(6)

C35(N31(Ni1	115.3(6)

C36(N32(C40	121.3(8)

C36(N32(Ni1	116.4(6)

C40(N32(Ni1	119.0(6)

C41(N33(H33A	120.0

C41(N33(H33B	120.0

H33A(N33(H33B	120.0

C41(N34(N35	115.9(7)

C41(N34(Ni1	114.6(6)

N35(N34(Ni1	120.7(5)

C42(N35(N34	113.3(7)

C42(N35(Ni2	113.6(6)

N34(N35(Ni2	125.3(6)

C42(N36(H36A	120.0

C42(N36(H36B	120.0

H36A(N36(H36B	120.0

C47(N37(C43	123.1(8)

C47(N37(Ni2	117.6(6)

C43(N37(Ni2	118.4(6)

C48(N38(C52	118.7(8)

C48(N38(Ni2	113.9(5)

C52(N38(Ni2	127.4(6)

N2(Ni1(N32	166.4(2)

N2(Ni1(N31	93.9(3)

N32(Ni1(N31	77.1(3)

N2(Ni1(N1	77.8(3)

N32(Ni1(N1	92.0(3)

N31(Ni1(N1	90.7(2)

N2(Ni1(N4	75.9(3)

N32(Ni1(N4	115.1(3)

N31(Ni1(N4	98.4(3)

N1(Ni1(N4	152.6(3)

N2(Ni1(N34	114.4(3)

N32(Ni1(N34	75.4(3)

N31(Ni1(N34	151.6(3)

N1(Ni1(N34	97.3(3)

N4(Ni1(N34	86.8(2)

N7(Ni2(N37	169.3(2)

N7(Ni2(N38	94.2(3)

N37(Ni2(N38	77.9(3)

N7(Ni2(N5	76.6(3)

N37(Ni2(N5	111.5(3)

N38(Ni2(N5	98.4(3)

N7(Ni2(N8	78.0(3)

N37(Ni2(N8	94.4(3)

N38(Ni2(N8	89.0(2)

N5(Ni2(N8	154.0(3)

N7(Ni2(N35	111.3(3)

N37(Ni2(N35	77.1(3)

N38(Ni2(N35	154.4(3)

N5(Ni2(N35	85.8(2)

N8(Ni2(N35	98.3(3)

O2(Cl1(O1	109.1(4)

O2(Cl1(O3	108.3(4)

O1(Cl1(O3	108.1(5)

O2(Cl1(O4	111.6(5)

O1(Cl1(O4	110.4(5)

O3(Cl1(O4	109.4(5)

O12(Cl11(O13	111.7(5)

O12(Cl11(O14	111.5(5)

O13(Cl11(O14	109.4(5)

O12(Cl11(O11	107.9(5)

O13(Cl11(O11	110.4(5)

O14(Cl11(O11	105.7(4)

O22(Cl21(O21	113.7(5)

O22(Cl21(O24	112.4(4)

O21(Cl21(O24	106.3(5)

O22(Cl21(O23	111.9(5)

O21(Cl21(O23	107.5(5)

O24(Cl21(O23	104.6(5)

O32(Cl31(O33	115.1(6)

O32(Cl31(O34	111.3(6)

O33(Cl31(O34	111.3(6)

O32(Cl31(O31	106.0(6)

O33(Cl31(O31	105.2(6)

O34(Cl31(O31	107.3(7)

Symmetry transformations used to generate equivalent atoms:

Table 4. Anisotropic displacement parameters [Å2( 103]. The anisotropic displacement

factor exponent takes the form: (2( 2[h2a*2U11 + ... + 2 h k a* b* U12 ].

Atom	U11	U22	U33	U23	U13	U12

C1	33(5) 	28(4)	18(5) 	1(4)	3(4) 	(3(4)

C2	26(5) 	31(4)	21(5) 	(8(4)	10(4) 	(2(4)

C3	36(5) 	47(5)	11(4) 	(8(4)	3(4) 	(7(4)

C4	23(5) 	39(5)	13(4) 	(4(4)	1(3) 	1(3)

C5	4(3) 	34(4)	25(4) 	(3(4)	(5(3) 	(2(3)

C6	19(4) 	29(4)	6(4) 	2(3)	0(3) 	5(3)

C7	21(4) 	31(4)	3(4) 	(5(3)	1(3) 	0(3)

C8	32(5) 	26(4)	18(5) 	(4(4)	0(4) 	5(3)

C9	28(4) 	18(4)	6(4) 	2(3)	2(3) 	0(3)

C10	16(4) 	19(3)	11(4) 	0(3)	2(3) 	5(3)

C11	19(4) 	19(3)	14(4) 	8(4)	3(3) 	5(3)

C12	26(4) 	22(4)	11(4) 	5(3)	2(3) 	6(3)

C13	14(4) 	21(4)	20(4) 	(1(3)	0(3) 	1(3)

C14	30(5) 	18(4)	18(4) 	2(3)	1(3) 	(4(3)

C15	23(4) 	25(4)	27(4) 	9(4)	7(3) 	3(3)

C16	23(4) 	35(5)	25(4) 	(6(4)	5(4) 	(1(4)

C17	23(4) 	21(4)	18(4) 	1(3)	2(3) 	1(3)

C18	19(4) 	23(4)	18(4) 	(4(3)	0(3) 	4(3)

C19	21(4) 	39(5)	32(5) 	(2(4)	5(4) 	13(4)

C20	23(5) 	39(5)	36(5) 	8(4)	(2(4) 	5(4)

C21	11(4) 	34(5)	43(5) 	(6(4)	(8(4) 	6(3)

C22	19(4) 	31(5)	28(5) 	(4(4)	1(4) 	8(4)

C31	13(4) 	22(4)	27(5) 	(3(4)	4(3) 	0(3)

C32	20(4) 	28(4)	12(4) 	(1(3)	9(3) 	12(3)

C33	16(4) 	38(4)	20(5) 	2(4)	(9(4) 	1(3)

C34	18(4) 	37(4)	20(5) 	1(4)	(3(3) 	(8(4)

C35	26(4) 	23(4)	6(4) 	1(3)	0(3) 	(2(3)

C36	18(4) 	20(4)	27(5) 	(6(3)	0(3) 	(1(3)

C37	20(5) 	28(4)	41(6) 	(4(4)	(1(4) 	0(3)

C38	15(4) 	21(4)	24(5) 	(3(3)	3(3) 	(1(3)

C39	12(4) 	28(4)	34(5) 	2(4)	2(3) 	1(3)

C40	10(3) 	23(4)	22(5) 	1(3)	8(3) 	4(3)

C41	16(3) 	25(4)	12(4) 	1(4)	10(3) 	4(3)

C42	14(4) 	27(4)	14(4) 	(1(3)	6(3) 	8(3)

C43	18(4) 	31(5)	13(4) 	(2(3)	1(3) 	6(3)

C44	25(5) 	32(5)	18(4) 	2(4)	(2(4) 	0(3)

C45	26(5) 	35(5)	13(4) 	(10(4)	(7(3) 	1(4)

C46	36(5) 	34(5)	12(4) 	(4(4)	(6(4) 	(2(4)

C47	18(4) 	32(4)	15(4) 	(11(3)	1(3) 	2(3)

C48	7(3) 	24(4)	21(4) 	(2(3)	(1(3) 	8(3)

C49	23(4) 	24(4)	19(4) 	(6(3)	1(3) 	2(3)

C50	28(5) 	27(5)	23(4) 	1(4)	6(4) 	(2(4)

C51	39(5) 	29(5)	10(4) 	7(3)	0(4) 	(1(4)

C52	22(5) 	37(5)	18(4) 	(1(4)	5(3) 	2(4)

N1	16(3) 	20(3)	17(3) 	5(3)	(1(3) 	1(3)

N2	12(3) 	21(3)	15(4) 	2(3)	0(2) 	0(2)

N3	22(4) 	32(4)	15(4) 	(7(4)	1(4) 	(1(3)

N4	5(3) 	23(3)	15(3) 	3(2)	4(2) 	4(2)

N5	18(3) 	29(4)	6(3) 	(1(3)	4(2) 	5(3)

N6	14(4) 	32(4)	34(5) 	(5(4)	(3(3) 	10(3)

N7	21(4) 	27(4)	16(3) 	1(3)	4(3) 	(1(3)

N8	22(4) 	23(3)	23(4) 	(3(3)	6(3) 	7(3)

N31	13(3) 	20(3)	17(3) 	(3(3)	7(2) 	0(3)

N32	17(3) 	21(3)	16(4) 	1(3)	6(2) 	(4(3)

N33	20(3) 	22(3)	30(5) 	4(4)	4(4) 	2(3)

N34	18(3) 	27(4)	23(4) 	4(3)	(4(3) 	3(3)

N35	15(3) 	21(3)	19(3) 	(1(3)	2(3) 	3(3)

N36	23(4) 	38(5)	11(4) 	(5(4)	8(3) 	(6(3)

N37	14(3) 	23(3)	17(3) 	(6(3)	6(3) 	3(2)

N38	6(3) 	36(3)	10(3) 	0(3)	5(2) 	2(3)

Ni1	16(1) 	22(1)	15(1) 	(1(1)	2(1) 	1(1)

Ni2	15(1) 	26(1)	13(1) 	(1(1)	1(1) 	2(1)

O1	40(4) 	28(4)	38(4) 	(5(3)	(13(3) 	(1(3)

O2	22(3) 	47(5)	30(5) 	(13(3)	(7(3) 	0(3)

O3	29(4) 	27(4)	31(4) 	2(3)	(1(3) 	(7(3)

O4	50(5) 	40(4)	26(4) 	(5(3)	16(4) 	9(4)

Cl1	19(1) 	24(1)	36(1) 	(5(1)	4(1) 	(1(1)

O11	22(3) 	54(6)	37(5) 	2(3)	(7(3) 	(4(3)

O12	29(4) 	44(4)	42(4) 	0(4)	(27(4) 	3(3)

O13	40(5) 	26(4)	53(5) 	(7(3)	12(4) 	2(3)

O14	40(4) 	29(4)	29(4) 	(3(3)	(11(3) 	(3(3)

Cl11	24(1) 	31(1)	17(1) 	(4(1)	(2(1) 	0(1)

O21	39(4) 	45(4)	28(4) 	16(3)	0(3) 	(8(3)

O22	43(4) 	60(5)	58(5) 	0(4)	24(4) 	1(4)

O23	98(6) 	63(5)	19(4) 	(5(4)	9(4) 	5(5)

O24	34(4) 	25(3)	73(5) 	(10(3)	5(4) 	4(3)

Cl21	38(1) 	25(1)	26(1) 	0(1)	14(1) 	0(1)

O31	68(5) 	95(7)	110(8) 	(39(6)	45(5) 	(22(5)

O32	85(6) 	26(4)	71(6) 	(5(4)	(19(5) 	(16(4)

O33	98(6) 	39(4)	88(7) 	(9(4)	(32(6) 	19(4)

O34	115(8) 	50(5)	41(4) 	7(4)	20(5) 	14(5)

Cl31	59(2) 	29(1)	33(1) 	(2(1)	1(1) 	2(1)

O51	43(4) 	39(4)	34(4) 	(6(3)	(4(3) 	4(3)

O52	33(4) 	76(6)	72(5) 	30(4)	18(4) 	17(4)

O53	74(6) 	72(6)	81(6) 	1(6)	(1(5) 	(24(5)

O54	67(6) 	43(4)	37(5) 	3(3)	7(4) 	19(4)

O55	55(5) 	107(7)	92(7) 	(10(7)	0(6) 	36(5)

Table 5. Hydrogen coordinates [( 104] and isotropic displacement parameters [Å2 ( 103].

Atom 	x	y	z	Ueq	S.o.f.

H1	452	267	5598	32	1

H2	(272	(128	6326	31	1

H3	(636	1380	7054	38	1

H4	(284	3178	6919	30	1

H7	34	4919	6620	22	1

H8	508	6475	6348	30	1

H9	1282	6389	5634	21	1

H14	2394	1841	2234	26	1

H15	3125	666	1994	30	1

H16	3585	85	3097	33	1

H19	4001	(337	4217	37	1

H20	4349	(731	5413	39	1

H21	4025	136	6503	35	1

H22	3341	1470	6319	31	1

H31	402	4531	4366	25	1

H32	(239	4903	3452	24	1

H33	(625	3421	2835	30	1

H34	(348	1602	3053	30	1

H37	24	(92	3309	35	1

H38	486	(1738	3639	24	1

H39	1255	(1563	4361	30	1

H44	2375	3015	7750	30	1

H45	3013	4365	7864	29	1

H46	3501	4974	6858	33	1

H49	3847	5495	5748	26	1

H50	4282	5841	4587	31	1

H51	4028	4768	3492	31	1

H52	3411	3421	3611	31	1

H3A	2354	4959	4732	28	1

H3B	2054	5725	5276	28	1

H6A	1404	3261	3287	32	1

H6B	1673	2548	2676	32	1

H33A	2360	(56	5179	29	1

H33B	2086	(873	4639	29	1

H36A	1370	1570	6643	28	1

H36B	1621	2328	7244	28	1